## Slide 1: Metal Detector Robotic Vehicle
The Supervisor :D. Omer Tamimi
  By: Rimaa Azzam Duha Rasheed Alaa Mehyar

## Slide 2
Page-1
To build autonomous robot with obstacle sensor for detecting metals.
Project objectives & achievements

## Slide 3
Page-2
Metal detector has been built using strong PI Detector (without metal Discrimination).
Project objectives & achievements

## Slide 4
Page-3
Obstacle avoidance algorithmes have been implemented using Arduino UNO Model .
Project objectives & achievements

## Slide 5
Page-4
The models takes distance from ultrasonic sensor and send the motion commend to
H-Bridge .
Project objectives & achievements

## Slide 6
Page-5
H-Bridge drives two PM DC Motors .
Project objectives & achievements

## Slide 7
Page-6
The body of Robot .
Autonomous Robot

## Slide 8
Page-7
The body of Robot .
- Charging circuit
Autonomous Robot

## Slide 9
Page-8
Basic operation of Servo-Motor , Arduino , Ultrasonic sensor .
The servo motor rotation is half cycle (from 30 ˚to 140 ˚).
During this period the Robot is able to scan the area ahead against any obstacle by ultrasonic sensor .
Autonomous Robot

## Slide 10
Page-9
Basic operation of Servo-Motor , Arduino , Ultrasonic sensor .
The ultrasonic scenic is able to detect obstacle at 40 cm range .
There is some disadvantages for ultrasonic as picture below show.
Autonomous Robot
Once the obstacle has been detevted the two motors will immedietly stop and the Robot
will navigate a new root that doesn’t have an abostcal .

## Slide 11
Page-10
Basic operation of Servo-Motor , Arduino , Ultrasonic sensor .
There is some disadvantages for ultrasonic as picture below show.
Autonomous Robot

## Slide 12
Page-11
Arduino and H-Bridge .
H-Bridge circuit –Diagram H-Bridge circuit –Diagram
Autonomous Robot

## Slide 13
Page-12
Arduino and H-Bridge .
How does H-Bridge operate.
Autonomous Robot

## Slide 14
Page-13
The Motion of robot.
Autonomous Robot

## Slide 15
Beat Frequency Oscillation (Bf)
This is among the most basic of metal detectors. This metal detector is considered weak and is the option most commonly used in most electronics shops. It has the ability to find objects located about two feet below ground.
Page-14
Metal detector

## Slide 16
Very Low-Frequency Detectors(VLF)
This is one of the most popular metal detectors currently in use. This is especially so among experienced treasure seekers. The detector can be highly accurate and sensitive.
Page-15
Metal detector

## Slide 17
Pulse Induction(PI)
This is one of the latest innovations in detecting metallic objects. Guards commonly use this type of detectors for detecting concealed weapons at security checkpoints. However, the technology is not very efficient in differentiating the different types of metals.
Page-16
Metal detector

## Slide 18
Page-17
Metal detector
 | BF | VLF | PI
Detection Range | few | medium | wide
cost | More cheap | Expensive | cheap
Metal Discrimination | yes | yes | no
complexity | no | yes | no

## Slide 19
Page-18
Pi polish metal detector circuit.
Metal detector

## Slide 20
Page-19
Circuit.1
feeding cct.
Metal detector

## Slide 21
Page-20
Circuit.2
Generate stream cct.
Metal detector

## Slide 22
Page-21
Signal amplifier
Metal detector

## Slide 23
Page-22
Circuit.3
Shmitt triger cct.
Metal detector

## Slide 24
Page-23
We faced difficulties when we collected all circuits in robot :
1) Wheels were fixed on the robot using a special robot screws.
2) ultrasonic circuit was fixed in front of the robot to detect barriers and avoidance.
3) the batteries , batteries changer , Arduino circuit and H-bridge circuit were fixed on the surface of robot.
4)Wooden arm was fixed on the surface of robot and the metal detector circuit was fixed on this wooden arm To facilitate the tuning circuit
The coil was putted on the end of wooden arm to make it far from the metallic robot
(the coil of metal detector circuit was detected the metal of robot , so we Connected the coil with the wooden arm )
5) we made two circuit but the first circuit didn’t work Efficiently so we built another circuit as we illustrated above
FINAL ASSEMBLING AND TROUBLE SHOOTING :

## Slide 25
Page-24
Advantages :
Saving time and effort.
2) Robots may be used because they are FASTER than people at carrying out tasks.
3) Robots may be used because they can work in places where a human would be in danger.
Application :
Security of buildings such as airport, office, school, prison, etc…
Food processing.
Search for Lost.
To explore for treasures.
Advantages & Application :
:

## Slide 26
Page-25
Future work
the wireless visual system will be used to human monitor the robot vision via mobile. To build the wireless visual system, the wireless camera will be applied on the robot and the wireless camera will transmit the visual around the robot to the receiver on the LCD .
the obstacle sensor will be build that the robot capable to stop moving when there are obstacles detected. To build a robot with ability to detect obstacle, the obstacle sensor will be needed.
Conclusion
Finally after all the difficulties that we have encountered the project has worked well and achieved the goals we set and detect metal .
Future work & Conclusion :