## Slide 1: PRESTRESSED CONCRETE DESING
AL – ERSAL TOWER _ RAMALLAH
Supervisor: Eng. Ibrahim Arman
Prepared By: Areej Younis
  Hana Hamdan
Lubna Abu-Hashyeh
Shefa Salahat

## Slide 2: Layout
Introduction
Preliminary Design
Final design
Visibility Studies

## Slide 3: INTRODUCTION
Project Description
Structural Plans
Materials
Codes and Standards
Gravity and Lateral Loads
Soil Description

## Slide 4: Project Description
  Al-Ersal Tower is a commercial and residential building of 3 basements, a ground floor, and 13 stories
  Location : at al-Ersal .St in Ramallah
  Total area = 26311.66 (m²)
  Structural design systems : - flat plate post tension concrete - flat plate reinforced concrete

## Slide 5: Structural Plans
Structural plan for
basement 3

## Slide 6: Structural Plans
Structural plan for
basement 2

## Slide 7: Structural Plans
Structural plan for
basement 1

## Slide 8: Structural Plans
Structural plan for
ground and 1st floors

## Slide 9: Structural Plans
Structural plan for
2nd – 13th floors

## Slide 10: Materials
Prestressed concrete
f’c= 45 MPa, Ec=31*10³ MPa
Prestressed reinforcing steel
Grade 270 low relaxation strands (Ø12.7mm, Aps=99 mm2)
Reinforced Concrete
f’c= 40 MPa, Ec=29.7*10³ MPa for slabs, beams, stairs and walls
Reinforcing steel for concrete
grade 60
fyp =1676 MPa, Eps = 200GPa, fu= 1862 MPa ,
breaking strength of strand = 184 Mpa
fy =420 MPa
Es=200 GPa
f’c= 45 MPa, Ec=31*10³ MPa for other elements
f’ci=32MPa, Ec=26.58*10³ MPa
Structural materials

## Slide 11: Materials
Tiles
ɣ= 26 KN/m3
Plastering
ɣ= 23 KN/m3
Concrete mortar
ɣ= 23 KN/m3
Aggregates (fine &course)
Masonry stone
ɣ= 26 KN/m3
Block
ɣ= 12 KN/m3
False ceiling
Non-structural materials
ɣ= 18 KN/m3
ɣ= 0.15 KN/m2

## Slide 12: Codes and Standards
ACI 318-08 (American Concrete Institute)
IBC -09 (International Building Code)
ASCE-2005 (American Society of Civil Engineers)
UBC-97 (Uniform Building Code)
PTI (Post-Tension Institute )

## Slide 13: Gravity Loads
Live loads
LL = 3.5 KN/ m2 → For basement 3 and basement 2
Dead loads
DL = 6.25KN/m2→ For Prestressed concrete
Supper Imposed load
SD = 2.5 KN/m2 → For basement 3 and basement 2
LL = 5 KN/ m2 → For other floor
DL = 6.75KN/m2→ For Reinforcement concrete
SD = 4 KN/m2 → For other floor

## Slide 14: Load Combinations
U = 1.4D
U = 1.2D + 1.6L + 0.5L
U = 1.2D + 1.6L+ (1.0L or 0.5W)
U = 1.2D + 1.0W + 1.0L + 0.5L
U = 1.2D + 1.0E + 1.0L + 0.2S
U = 0.9D + 1.0W
U = 0.9D + 1.0E
U = 1.2D + 1.6 L + 1.0 S → For gravity load design

## Slide 15: Lateral Loads
The seismic load factors are as follows:
Seismic zone factor : Z = 0.2
Soil profile: SB (rock) according to IBC-2009
Importance factor: I=1.25
Site class :
The mapped spectral acceleration for a 1-second period: S1 = 0.25
Ss: The mapped spectral acceleration for short periods: S2 = 0.5
Response modification factor : R=4
Seismic Loads

## Slide 16: Lateral Loads
The wind load factors are as follow:
Site is Exposure B category
Gust – effect factor: G = 0.85
External pressure coefficient : Cp: wind ward = 0.8, lee ward = ± 0.5, side wall = - 0.7
Velocity pressure evaluated at height Z above the ground (N/m²): q z
Velocity pressure exposure coefficient evaluated at height Z: Kz from table 27.3-1 at ASCE-05 Code. Which is function of height
Importance factor depends on the structure use: I=1
Topographic factor : Kzt = 1
Wind directionally factor : Kd = 0.85
Basic wind speed (m/s) : V = 120 Km/hr
Wind load

## Slide 17: Soil Description
The soil type is: SB (rock) according to IBC-2009
Soil internal friction angle, Ø = 30°
Soil allowable bearing capacity = 270 KN/m²
Live load (surcharge) = 15 KN/m²
Back filling material is selected by soil (base coarse Ø ≥ 30º
Ko = 0.5
q 1 = 7.5 KN/m²
q 2 = 137 KN/ m²

## Slide 18: Preliminary design
Slab Design
→Flat Plate post-tensioned Slab
Check punching
Check stresses
Losses
Ultimate design method
→Reinforced concrete flat plate
Check punching

## Slide 19: Slab Design
→slab thickness= L/45 = 8.35/45 = 0.186 mm
So, take 250 mm as thickness of slab
Slab thickness checks
Check punching
Check stresses
Prestressed concrete Flat plate

## Slide 20: Check punching

## Slide 21: Check Punching
Use 2Ø12/100 mm
Interior column 13 C
Use 2Ø12/100 mm
Edge column 13 A
No need for shear reinforcement steel
Edge column 11 I
Check punching

## Slide 22
Tendons Layout in Frame G

## Slide 23
Tendons Layout in Frame G

## Slide 24
Initial stage : f(top/bottom)= -(Pi /AC) ± (Munb/St ) Where : Pi : perstressed force before losses , KN Ac : Area of concrete , m2 Munb : Moment due to Wunb at initial stage , KN/m St : Top section modulus , st = Ig /Ct , m3 Ig : Moment of inertia , m4 Ct : distance from the center of concrete section to the top of section , Allowable stress at initial stage ( End support , Mid span) : fti = 0.25 fci`^½ = 1.414 MPa fci = 0.6fci`
= 19.2 MPa
Check Stress

## Slide 25
Check Stress
Final stage: f(top/bottom) = -(Pe/AC) ± ( Munb/St) Where : Munb : Moment due to Wunb at final stage , KN.m
Pe: perstressed force after losses , KN
Allowable stresses at final stage ( End support , mid span ) : ft =0.5 fc`^½ = 0.5 =3.354 MPa fc = 0.45 fc`^½ =-20.25 MPa All stresses are acceptable and within the allowable stresses.

## Slide 26
Δfpes = 11 MPa

## Slide 27: % of Losses in each frame
%[1- (Pe/Pi) ]
26
26
26
26
26
15
24
24
19
18
16
16
18
18
Name of frame
Y(13)
Y(12)
Y(11)
Y(14)
Y(15)
Y (17)
X(A)
X(B)
X(C)
X(D)
X(F)
X(G)
X(H)
X(I)

## Slide 28
Tendons layout in X-direction

## Slide 29
Tendons layout in Y-direction

## Slide 30: Ultimate Design Method
  use minimum steel for ultimate in case of cable cut off
  Check the adequacy of using minimum steel
Ultimate moment – frame 13 (1.2 D + 1.6 L + 1.0 HS)

## Slide 31
Bottom reinforcement steel

## Slide 32
Top reinforcement steel

## Slide 33
Section A-A

## Slide 34: Slab Design
Slab thickness = 0.27 m
d = 0.23 m
Slab thickness checks
Check punching
Reinforced concrete flat plate

## Slide 35
Vu=1601 kN
ØVc=1643 kN
Use 2Ø12/100 mm
Interior column 13 C
Vu=555.94 kN
ØVc=821.87 kN
Use 2Ø12/100 mm
Edge column 13 A
Vu=52.25 kN
ØVc=387.3 kN
No need for shear reinforcement steel
Edge column 11 I
Check Punching

## Slide 36
Flat Plate reinforcement steel in X-Direction
X

## Slide 37
Flat Plate reinforcement steel in Y-Direction

## Slide 38: FINAL DESIGN
Structural Model on SAP
Verifications of Structural Analysis
Columns Design
Beams Design
Stairs Design
Walls Design
Mat Foundation Design
SAP Modeling of Tendons

## Slide 39
Structural Model on SAP
Define:
material :concrete f’c =45 MPa , f’c= 40 MPa
Section :Frame (column and beam ) , Area (slab, walls and mat foundation)
Load : dead, live, super dead, seismic and wind

## Slide 40: Verification of Structure Analyses
Check Compatibility

## Slide 41
Equilibrium Check
% of Difference | Hand calculation (KN) sum of load in Z-direction | SAP (KN) sum of load in Z-direction | Load
2.19% | 256420.93 | 250800.21 | Dead
2.4% | 112490 | 115177.8 | Live
1.85 % | 92530 | 90818 | Super dead

## Slide 42
Lateral Load Checks
 |  | Shear resulted from wind pressure | 
Difference % | Shear from SAP (KN) | Shear calculated manually (KN) | wind pressure
8% | 1796.116 | 1969.248217 | wind x
11% | 2397.277 | 2159.015259 | wind y
 |  | Shear resulted from seismic load | 
Difference % | Base shear from SAP (KN) | Base shear calculated manually (KN) | seismic load
0.9% | 10589.79 | 10693 | X1
0.9% | 10589.79 | 10693 | X2
0.9% | 10589.79 | 10693 | Y1
0.9% | 10589.79 | 10693 | Y2

## Slide 43: Column Design
Reinforcement of column 13
Group no.1
9 ≤ 34 – 12 (-.704/ 5.66) → OK
check slenderness

## Slide 44
General longitudinal
section in column

## Slide 45: General longitudinal section in column

## Slide 46
Beam locations at 2nd – 13th floors
Beam locations at ground and 1st floors
Beams Design

## Slide 47
Beams Design
Item | Moment | h(mm) | b(mm) | d(mm) | As(mm²) | Bar Ø (mm) | # of bars | As for shear
B1 | M+ | 900 | 600 | 830 | 12150 | 32 | 16 | 2Ø12/100
 | M- | 900 | 600 | 830 | 12150 | 32 | 16 | 2Ø12/100
B2 | M+ | 750 | 500 | 680 | 8760 | 32 | 10 | 2Ø12/200
 | M- | 750 | 500 | 680 | 8760 | 32 | 10 | 2Ø12/200
B3 | M+ | 550 | 300 | 490 | 2670 | 25 | 6 | 1Ø12/200
 | M- | 550 | 300 | 490 | 2670 | 25 | 6 | 1Ø12/200

## Slide 48
Longitudinal section in beam 2
Cross section in beam 2

## Slide 49: Stairs Design
Stair -03 plan
Flight :
According to ACI 318-08 code h =0.15 m
WD =3.75 KN/m², WL = 5 KN/m² and
WSD = 4 KN/m²
Landings:
1st : (b=1.61, h=0.15 and L= 2.5) m
2nd: (b=1m, h=0.15 and 2.5) m

## Slide 50
Cross section in stairs

## Slide 51
Stairs reinforcement details

## Slide 52: Basement Wall Design
Basement wall at plan
h = 0.35 m
h = 0.35 m
h = 0.40 m

## Slide 53
Basement wall reinforcement details

## Slide 54
Shear wall Design

## Slide 55
Shear wall loads
Shear Wall Design

## Slide 56
Shear wall reinforcement details
Shear Wall Design

## Slide 57: Mat Foundation Design
→Mat thickness = 1.75 m
d = 1.65 m
Mat thickness check
Check punching

## Slide 58
Vu=29777 kN
ØVc =29331.6 kN
Interior column 13 C
Vu=523.118 kN
ØVc =12728.8 kN
Edge column 13 A
Vu=52.2 kN
ØVc =6780 kN
Corner column 11 I
Check Punching

## Slide 59
Mat foundation reinforcement steel

## Slide 60: SAP Modeling of Tendons
Prestress loads definition

## Slide 61
Hyper static definition

## Slide 62
Tendon section definition

## Slide 63
Tendon profile

## Slide 64
Tendon load

## Slide 65
Tendon eccentricity
ord 2(m) | Coord 1(m) | Point ID
0 | 0 | 1
- 0.015 | 1.235 | 2
0.05 | 2.47 | 3
- 0.035 | 6.295 | 4
0.075 | 10.12 | 5
- 0.04 | 14.295 | 6
0.08 | 18.47 | 7
- 0.04 | 22.645 | 8
0.08 | 26.82 | 9
- 0.065 | 30.995 | 10
0.08 | 35.17 | 11
- 0.04 | 39.345 | 12
0.065 | 43.52 | 13
- 0.02 | 46.345 | 14
0 | 49.17 | 15

## Slide 66
Prestressing moment
Prestressing moment check
% of Difference | 13Frame (KN/m) | 3D SAP (KN/m)
7.42 | 110.53 | 119.4
2.38 | 257.22 | 263.5
10.04 | 155.49 | 141.3
1.07 | 381.85 | 377.8
8.75 | 226.65 | 208.4
0.35 | 379.94 | 381.3
10.94 | 151.4 | 170
2.57 | 325.78 | 334.4
5.36 | 173.19 | 183
4.72 | 313.06 | 328.6
6.84 | 137.18 | 128.4
5.51 | 231.96 | 245.5
9.9 | 68.47 | 62.3

## Slide 67: Visibility Study
Price NIS | Quantity | Item | 
237469 | 521.9 (m³) | Concrete | Reinforced concrete flat plate
205200 | 72 (ton) | Steel | 
164305 | 483.25 (m³) | Concrete | Flat plate post-tensioned slab
62700 | 22 (ton) | Steel | 
130477.5 |  | tendon |