## Slide 1: Graduation Project II Integrated Redesign of School of Fine Art Prepared By: Leena Dwaikat Dina Abu Hamed Asma’ Maslamani Supervised By: Eng. Hasan Mathar

## Slide 2: Outlines:
Introduction
Site analysis
Architectural design
Structural design
Environmental design
Electrical design
Mechanical design
Safety
Quantity Survey

## Slide 3: Introduction:

## Slide 4: Site Analysis:

## Slide 5: Site Analysis:

## Slide 6: Architectural Design

## Slide 7: Main Problems:
Insufficient area of some spaces, such as: classrooms, studios and computer labs.
Insufficient number of W.C’s.
Insufficient number of lifts (the existed are 2, the needed are 3).
Insufficient movements area.
Lack in the music department spaces.

## Slide 9: Architectural Design:
7 Floors – 13500 m²

## Slide 10: Basement Floor 2:
Service Floor – Area = 1440 m²

## Slide 11: Basement Floor 1:
Music Department Floor – Area = 1977 m²

## Slide 12: Ground Floor:
Ground Floor – Area = 2055m²

## Slide 13: First Floor:
Graphic & Interior Design Department– Area = 2055m²

## Slide 14: Second Floor:
Graphic & Interior Design Department– Area = 2200m²

## Slide 15: Third Floor:
Applied Art Department– Area = 2200m²

## Slide 16: Fourth Floor:
Applied Art Department– Area = 1545 m²

## Slide 17: South Elevation:

## Slide 18: North Elevation:

## Slide 19: East Elevation:

## Slide 20: West Elevation:

## Slide 21: Section 1:

## Slide 22: Section 2:

## Slide 23: 3D Model:

## Slide 24: 3D Model:

## Slide 26: 3D Model:

## Slide 27: Structural Design

## Slide 28: Codes and Standards:
ACI -318-14 for reinforced concrete structural design.
UBC -97 for earthquake design.
ASCE for load combinations
For the design of the structure and its elements ETABS , SAP, SAFE and hand calculations were used

## Slide 29: Design data:
Concrete strength, f’c=24 MPa for slabs.
Concrete strength, f’c=28 MPa for other elements.
Steel yield strength fy=420 MPa.
Bearing capacity for soil = 400 kN/m2

## Slide 30: Seismic Design data:
The city of structure is Nablus.
The seismic zone factor. Z=0.2.
The soil profile is type Sc.
The acceleration seismic coefficient Ca=0.24
The velocity seismic coefficient Cv=0.32
The Seismic importance factor is 1
The structural design type is intermediate, R=5.5

## Slide 31: Sections Dimensions:
Structural Element | Dimensions
U-boot Slab | 50 cm
Columns | (60X80) , ( 80X120 ) , ( 90X240)
Beams | ( 50 X50) , (50 X 80 )

## Slide 32: Modeling:

## Slide 33: Verification of the model:
Compatibility check
Equilibrium check
Internal force check

## Slide 34: Compatibility check :

## Slide 35: Equilibrium Check
Load Case | ETABS | Manual | Error % | Status
 | KN |  |  | 
Dead | 110178 | 109746 | 0.4 | ok
Live | 21004 | 20781 | 1.06 | ok
SID | 35006 | 34635 | 1.06 | ok

## Slide 36: Internal Forces Check:
Elements | ETABS | Manual | Error % | Status
 | KN |  |  | 
B1 | 725 | 695 | 4.1 | ok
S2 | 375 | 341 | 9 | ok
Columns | 22048 | 21252 | 3.6 | ok

## Slide 37: Seismic Design checks
Time Period Check
0.695 < (1.4×.578 = .804)
Drift Story Check
44.66 mm < 100 mm
Deflection check
54.4 mm < 56 mm
Modal participating mass ratio check
0.9659 > 0.90
Base shear check
21680 kN > 21653.5 kN
22892 kN > 21653.5 kN

## Slide 38: Slab Reinforcement:

## Slide 39: Beams Reinforcement:

## Slide 40: Columns Reinforcement:

## Slide 41: Footing Reinforcement

## Slide 42: Shear wall Reinforcement

## Slide 43
Environmental Design

## Slide 44: Environmental Design:
Material used.
Thermal design.
Artificial lighting.
Acoustical design.

## Slide 45: Material used and properties:
External walls layers:
(7) cm limestone
(7) cm cast concrete
(6) cm insulation
(20) cm shear wall
(1.5) cm plaster
U value (W/m2-K)= O.468

## Slide 46: Material used and properties:
Internal walls layers:
(2) cm plaster
(10) cm block
(2) cm plaster
U value (W/m2-K)= 2.097

## Slide 47: Material used and properties:
Internal floor layers:
(2) cm Terrazzo
(2) cm mortar
(6) cm insulation
(30) cm cast concrete
(2) cm plaster
U value (W/m2-K)=0.433

## Slide 48: Material used and properties:
Flat Roof layers
(5)cm Asphalt
(15) cm cast concrete
(8)cm insulation
(30) Cm cast concrete
(13)Cm plaster
U value (W/m2-K)=0.316

## Slide 49: Glass Properties:
Double LoE (e2=0.1) clear glass with 6mm/13 mm Argon gas.

## Slide 50: Heating and cooling load analysis:
205.78 kW | Heating design capacity.
435.05 kW | Cooling design capacity.

## Slide 51: Thermal Comfort:
Thermal Comfort with cooling
Thermal Comfort without cooling

## Slide 52: Natural daylight analysis:
DF | Room
2.7 | Classroom
2.6 | Cafeteria
2.2 | Studio
2.3 | offices
2.7 | Theater

## Slide 53: Acoustical Design:
Cafeteria:
The required reverberation time RT60 for the cafeteria is between (0.6 – 1.0)
Reverberation Time:

## Slide 54: Results from ECOTECT

## Slide 55: Sound Transmission Class:

## Slide 56: STC - Classroom:
STC for internal wall
STC for external wall

## Slide 57: Impact Insulation Class
Results from INSUL

## Slide 58
Electrical Design

## Slide 59: Artificial lighting Design :
Classroom:

## Slide 60: Results from DIAlux:
E(lux) recommended | E(lux) from DIAlux
300 | 407

## Slide 61: First floor lighting plan

## Slide 62: Sockets arrangement for ground floor :
Quantity of sockets | Function
4 | Classroom
5 | Studio
6 | Museum
10 | Cafeteria
3 | W.C

## Slide 63: Circuit Breaker Branches:

## Slide 64: Sockets Arrangement for Computer Lab:
quantity of sockets | Function
40 | Computer lab

## Slide 65
Mechanical Design

## Slide 66: Water supply system:

## Slide 67: Water distribution system:

## Slide 68: Drainage system:
Rain water drainage:

## Slide 69: Drainage Layout For Fourth Floor

## Slide 70: HVAC design:
Systems used are VRF
Main components of centralized system are
Outdoor unit (chiller)
Inside unit (fan coil)
Collectors
Ducts.
Diffusers

## Slide 71: Outdoor Unit:
Model of APSc 60-2S with cooling capacity 238KW

## Slide 72: Fan Coil Unit:

## Slide 73: Diffusers:

## Slide 74: HVAC Design for Computer Lab:

## Slide 75: Final duct sizing and distribution of diffusers:

## Slide 76: VRF system in third floor :

## Slide 77: Safety design

## Slide 78: Fire Alarm system:

## Slide 79: Fire Alarm Layout For Ground Floor

## Slide 80: Fire Alarm Layout For First Floor

## Slide 81: Emergency Egress system:

## Slide 82: Cost Survey

## Slide 83
Work | Total Cost (NIS) | Unit Cost (NIS/m²)
Structural work | 3,621,357 | 278.57
Finishes Work | 1,764,000 | 135.69
Mechanical Work | 1,767,122 | 135.93
Electrical Work | 106,166 | 8.17
Total | 7,258,644.06 | 558

## Slide 84: Thank You 

## Slide 85
Work | Total Cost (NIS) | Unit Cost (NIS/m²)
Structural work | 7,242,713 | 557.13
Finishes Work | 1,764,000 | 135.69
Mechanical Work | 1,767,122 | 135.93
Electrical Work | 106,166 | 8.17
Total | 10,880,000.62 | 837