## Slide 1: Evaluation and Redesign of Arab American University Street
Ahmed A. Mara’bi
Omar S. Ahmad
Graduation Project II
Prepared by:
Under Supervision:
Eng. Husain Abu Zant
Notes: يتم عرض هذه الشريحة في بداية المناقشة ومن ثم الترحيب بالممتحنين والحضور

## Slide 2: Outline
Introduction
Methodology
Data Collection
Traffic Studies
Notes: In this presentation we will talk about these points:
1- Introduction to the project
2- Our methodology
3- The data the we collected for this project
4- And then traffic studies and analysis
النقل الى الشريحة التالية والاكمال

## Slide 3
Pavement Design
Geometric Design
Cross Section Elements
Discussion and Conclusions
Notes: 4- The pavement design
5- After that we will talk about the geometric design of this road
6- Then the typical cross sections that we used and their elements
7- Finally the discussion and conclusions.

## Slide 4: Introduction
Background
Study Area
Significance of Work
Notes: 1- Background :
Jenin is one of the major cities in Palestine. According to its importance in the residential, economical, and educational aspects. Therefore, an efficient road network connects between its surrounding parts becomes very important. The road network should be studied well and improved continuously to be efficient and active. One of the main roads in this network is Arab American University (AAU) Street which extends from Qabatya to the AAU. It is about 6.5 km ,
let us take a walk along the road
يتم النقل على شريحة جديد لعرف فيديو تصوير جوي للطريق من البداية حتى النهاية ويتم الحديث خلال العرض عن ال
Study area and Significance of Work.

## Slide 5
Notes: بعد انتهاء الفيديو يتم الحديث عن الاهداف في الشريحة التالية

## Slide 6: Objectives
Evaluate the existing geometric and pavement conditions.
Evaluate the existing and forecast traffic conditions.
Redesign and improve the geometric, traffic, and pavement issues.
Notes: The objectives of this study are the following:
- Evaluate the existing geometric and pavement conditions.
- Evaluate the existing and forecast traffic conditions.
Redesign and improve the geometric, traffic, and pavement issues.
بعد الانتهاء ... يبدأ عمر بشرح ال :
Methodology , Data collection , and Traffic studies.

## Slide 7: Methodology
Reconnaissance Visit
Performing Traffic Studies
Standards and Specifications
Evaluation of the Existing Conditions
Notes: يبدأ عمر بالشرح
To achieve the objectives of this project, the following steps were being applied:
1- we visited the site of the road and make the inventory study in order to have a clear idea about the alignment, the terrain, the existing geometric conditions of the road, and the traffic types and quantity. Collect the maps and data records of the study area
2- Then conducting traffic count for 6 hours ; three hours in the morning ( 7:00 – 10:00 AM ) and other three hours in the evening ( 12:00 – 3:00 PM ) in order to determine the peak hour at the road , and analyze the traffic volumes , and determine the LOS
3- The project based on the standards and the specifications of the American Association of State Highway and Transportation Officials (AASHTO 2011).
4- Then Evaluation of the Existing Conditions such as
- horizontal alignment based on horizontal curves
- Pavement conditions based on the structural performance which is related to the physical conditions such as cracks.
- Cross section elements based on the AASHTO 2011 standards.
- Traffic control devices, marking, and other traffic controls.
Conducting the CBR test in order to determine the conditions for the sub-grade.
نقل للشريحة التالية لاكمال الشرح

## Slide 8
Pavement Design
Performing Geometric Design
Traffic Control
Bill of Quantity Report
Notes: Then performing the pavement design based on AASHTO 1993 guide
Then performing the geometric design
And design the traffic control devices required along the road to give the most comfortable and safe drive.
Finally prepare Bill of Quantity Report
نقل للشريحة التالية

## Slide 9: Data Collection
Maps and Contour
Horizontal alignment and Grades
Soil Test
Traffic Counting
Notes: Gathering data is the primary requirement to perform any study, the following data were collected to complete this project:
1- Maps and contour: The contour maps were collected from the civil engineering department at An-Najah National University, and the other information about the study area like the path of the road is obtained by using GIS maps and aerial photos from Google Earth
2- The horizontal alignment of the road is obtained by using GIS ( ArcMap Software ) , and then converted the produced shape file to AutoCAD file and then get the length of the road and the horizontal curves and there radii to compare them with the standards
In addition, the information about the grades on the road obtained from Civil 3D software and Google Earth program and compared them with the standards.
3- Then the soil samples were collected from the site and conducting the (CBR) test for the sub-grad layer and determined the liquid and plastic limits for the sample, and made the sieve analysis test. In order to determine the classification of the soil and its classification was:
A-2-6 (Silty or clayey gravel and sand)
A-7-5 ( Clayey soil)
4- Finally To study the current situation on Arab American University Street, traffic was performed on the main intersection on the road; Haddad Tourism Village intersection. And calculate the LOS
نقل للشريحة التالية

## Slide 10: Traffic Studies
LOS at Intersection
The LOS at the intersection was B
Notes: The results of LOS at the intersection by using HCS 2000 software were as shown in the following Table and the LOS was B
نقل للشريحة التالية

## Slide 11
LOS on Road Links
Notes: To evaluate the LOS on the road links, the road was divided into two parts; the first part was Qabatya side and the second one was Arab American University side, and then using HCM 2010 tables and equations to evaluate the LOS. The following table shows the traffic on the two parts:
شرح بسيط عن العناصر الموجودة داخل الجدول
The LOS was C for the existing traffic volumes.
نقل لشريحة التالية

## Slide 12
Future Level of Service
Notes: The study area serves many facilities, such as AAU, the American school, Ro’ya Stadium, and Haddad Tourism Village. According to these facilities the traffic volumes will be increased in the future, so to forecast the future PHV and calculate the future LOS, the growth rate (i) of the traffic is needed.
After plotting the relation between the # of vehicles and Years for the data taken from the Palestinian Central Bureau of Statistics (PCPS) the following graph is determined ant it is showing from the graph that the growth rate was 3.2% and the full calculation is shown in the report between your hands.
Then we calculated the future PHV for a design period of 20 years and 3.2% growth rate and the future LOS was D
نقل للشريحة التالية
( ابدأ انا بالحديث )

## Slide 13: Pavement Design
Notes: أبدأ بالشرح عن الطبقات الموجودة في الصورة ومن ثم الطبقات التي استخدمناها

## Slide 15: Geometric Design
Horizontal Alignment
Horizontal Curves
Vertical Alignment
Vertical Curves
Notes: The design of this road is done by AutoCAD Civil 3D software and all tables of results obtained from the software.
1- Horizontal alignment
* Determine the classification of the road.
* Design speed.
* Determine a reasonable maximum superelevation rate.
* Find the maximum side-friction factor.
* Calculate the minimum radius for the horizontal curve.
* Make sure that the stopping sight distance is provided throughout the length of the curve.
2- V.A
The topics discussed under vertical alignment can be divided into two categories: the design of highway sections that have ascending or descending grades, and the design of vertical curves that connect these segments of ascending and descending grades.

## Slide 16: Cross Section Elements
Notes: شرح عن الصور الموجودة

## Slide 19: Discussion and Conclusion
Redesign of all aspects relating to cross sectional area.
This road is efficient and the LOS was calculated in two sections. The results appears LOS to be (C) for the existing road under current traffic volumes, and the LOS is (D) within a period of 20 years.

## Slide 20
The studied intersection which called (Haddad Intersection) was within LOS (B). This intersection needs more attention for the geometric aspects. The intersection was designed to be “Roundabout“.

## Slide 21
After road condition survey, some parts of the road suffer from many distresses. Such distresses are alligator cracks and longitudinal cracks. So, it is highly recommended to manage these defects to overcome the road distresses.
The Traffic Control Devices (TCD) were studied. It is obvious from the study that there is a lack for good TCD’s.