## Slide 1: Air Hockey Robot
An-Najah National University
Facility Of Engineering
Computer Engineering Department
Students:
Abdullah Ahmad & Moath Omar
Supervisor:
Dr. Samer Arandi

## Slide 2: شكر وتقدير

## Slide 3: مي_وملح#

## Slide 4: Outline
Introduction: Air Hockey Game.
The Project idea.
Components and apparatus.
System modules.
Background.
Design and implementation
  Table.
  Axis and conveyers.
  motors.
  Trajectory module.
  Air flow implementation.
Future work
References.
Demo.

## Slide 5: Air hockey game
Played by two players, each try to maximize his score.
Score gained by entering the puck in the opponent goal.
Play ground: a low friction table.

## Slide 6: Project Idea
To design a robot that plays the game.
Challenge & knowledge domain:
  To apply hardware and software design knowledge:
    Motor interfacing.
    Puck tracking “image processing”.
    Problem solving.
  To play the game with single player.

## Slide 7: Components & apparatus
Wood boards for Air Hockey Table.
Arduino Uno.
Pic 16F877A.
stepper motors , dc motors and servo motors.
motor cables and connections.

## Slide 8: Components & apparatus
Aluminum rods.
Belt for the axis.
8*5 LED matrix.
Resistors, capacitors, transistor and many other IC’s.

## Slide 9: Components & apparatus
Power supply.
PC or Laptop.
Webcam .
Small Fans.
Drill .

## Slide 10: System components
Table and Air flow System
Robot and Motors
Camera and Tracking System
Scoring System

## Slide 11: Background

## Slide 12: Arduino
The Arduino Uno is a microcontroller board based on the ATmega328 .It contains everything needed to support the microcontroller; simply connect it to a computer with a USB cable or power it with an AC-to-DC adapter or battery to get started

## Slide 13: OpenCV
OpenCV (Open Source Computer Vision Library) is an open source computer vision and machine learning software library.

## Slide 14: Motors
Stepper Motor
DC Motor
Servo Motor

## Slide 15: Stepper motor
Advantages :
Precise step, usually 1.8 degree => position control.
Good torque.
Through micro stepping, it can be pushed to high speed.

## Slide 16: Stepper motor
Disadvantages :
Need a driving circuit.
Need a high/ mid power usually more than 10 watts.
No feedback.
Can lose some steps!
Can be categorized as heavy “heavier than servo!’.

## Slide 17: Servo motor
Advantages
It gives you feedback.
High torque. Very light. Internal driving circuit.
Mid speed up to 150 RPM.
Doesn’t consume pins from the controller.

## Slide 18: Servo motor
Disadvantages:
Limited speed, hard to turn around.
A limited range of freedom “180 degree angle.
Hard to find in local stores.

## Slide 19: DC motor
Low cost, found everywhere.
Very high speeds “given high power”, in term of thousand of RPMs.

## Slide 20: DC motor
Disadvantages:
Low torque.
Nonlinear control. Has a very sharp start and stop transient !
Need a feedback circuit.
Brush based, broken soon.
May Need a braking system.

## Slide 21: Design and implementation

## Slide 22
Robot

## Slide 23: X and Y axes or carriages
We need X and Y axes or carriages that provide easy and fast movement of our robot with minimum friction

## Slide 24: X and Y axes or carriages

## Slide 25: X and Y axes or carriages

## Slide 26: Motors belt
We need belts that have small section and lightweight.

## Slide 27: Motors

## Slide 28: Stepper motor
Uni-polar motor

## Slide 29: Stepper motor
bi-polar stepper

## Slide 30: DC Motor
As we mentioned earlier, the DC motor tend to be very fast usually, but it is not linear, voltage dependent , and in our case it must be used within a closed loop system which mean a feedback circuit.

## Slide 31: DC Motor

## Slide 32: Servo motor:
Although they are always great for robotics, due to their size, low power, high torque, high stability, and given feedback. The bad news was there limited speed, which was up to 150 rpm “the high speed versions!!!”, moreover, the available motors were limited in the degree of movement, to 180 degree only.

## Slide 33: Stepper Motor again
Uni-polar as bi-polar Stepper Motor:

## Slide 34
Tracking system

## Slide 35: Tracking system
Our tracking system consist of Camera, c++ application combined with openCV libraries. That use the camera to detect the puck, then track it and do the suitable calculation
The camera we used is –Logitech c570-.
we initially setup the camera to take 640*480px frames, to obtain 30fps.

## Slide 36: Tracking system
Full frame size captured by camera

## Slide 37: Tracking system
Cropping frame since we interested only with the area inside the table

## Slide 38: Tracking system
smooth the frame using Gaussian algorithm

## Slide 39: Tracking system
convert the image from RGB to HSV

## Slide 40: Tracking system
apply threshold filter to detect RED color (puck color)

## Slide 41: Tracking system
Each time we take two consecutive frames, calculate the position of the puck and its speed.
using mathematical and Trigonometry equations we developed algorithm to predicate the puck direction and the path
Trajectory prediction

## Slide 42: Tracking system
Trajectory prediction with angle

## Slide 43: Tracking system
Trajectory prediction without angle

## Slide 44: Tracking system
Memory management
Object size problem
Problems

## Slide 45
Scoring system

## Slide 46: Scoring system
Responsible for detecting and counting goals scored by each side.
Displaying the result on a 5*8 led matrix.
We used an Infrared transmitter and receiver, line of sight, that fire a signal when crossed by the Puck.

## Slide 47: Scoring system

## Slide 48
Table

## Slide 49: Table
Air Hockey table is the base of our project, after searching for a suitable size of our table we get the dimensions from a previous project. The dimension of our Table is 110cm * 60cm

## Slide 50: Table
Table First design

## Slide 51: Table
Air System

## Slide 52: Table
Air System

## Slide 53: Table
Air System

## Slide 54: Future Work
Use faster Motors.
Enhance tracking system.
Intelligence playing mode.

## Slide 55: References
[1] Air hockey image, www.Mastergames.com.
[2]OpenCV library, Opencv.org.
[3]ArduinoArduino.cc.

## Slide 56: Demo

## Slide 57: Any Questions ???...!

## Slide 58: Thanks For Listening 