## Slide 1: Graduation Project 2 Structural Analysis and Design of and commercial Building by software sap (2000) in Nablus
Prepared by:
Aseel Ahmad Ali
Mais hijab
Nirmeen Issam Natour
Supervised by:
Dr. Riyad Awad
An-Najah National University Nablus - Palestine
Faculty of Engineering Civil Engineering Department
2021

## Slide 2: Outline
Project Description
Building structural system
Codes and Standards
Materials
Software
Load Types
Load Combinations
Preliminary Dimensions
Modeling
Irregularities
Checks
Design of structural elements

## Slide 5: Project Description

## Slide 6
This is a graduation project to redesign the structural elements of the building for gravitational and lateral loads.
This structure is the building of Abdalhameed al Sosa in Nablus. The building will be analyzed and deigned using the primary principles of structural design. Also one of the most modern software programs to analyze reinforced concrete structures was used.
The project will give a summary of the design principles of different structural elements in the structure, and finally it will introduce practical design drawings for implementation.

## Slide 7: Building Structural System

## Slide 8: Building Structural System
The structural system of the building is formed of two types: two-way solid slabs without beams (flat plate slabs) and two way ribbed slabs, one-way ribbed slab x-direction and one-way ribbed slab y-direction with hidden interior beams
The beams are supported by columns, which are the main vertical structural elements.
We will discuss design of structural element like slab and beam and other elements: such as columns, shear walls, retaining wall and footings.

## Slide 9
Floor | Area (m2) | Height (m) | Use of floor
Basement 2 | 525.96 | 2.60 | Car Parking
Basement 1 | 525.96 | 2.60 | Car Parking
Ground floor | 317.75 | 4.5 | Stores
Typical Floors (6 floors) | 317.75 | 2.95 | Offices

## Slide 10: Plan for First Basement

## Slide 11: Plan for second Basement

## Slide 12: Plan for Ground Floor

## Slide 13: Plan for Typical Floor

## Slide 14: Materials
Materials for structural elements:
Concrete (f’c = 28 MPa) E = 24870. MPa, γ = 25 kN/m3
Reinforcing Steel (ASTM A615, Grade 50) Fy = 420 MPa, Fu = 450 MPa Es = 200 GPa

## Slide 15: Materials
Materials for non- structural elements:
Material | 𝛾 𝑖𝑛 kN/𝑚3
Block | 12
Tiles | 25
Plastering | 23
Filling Material | 18
Concrete mortar | 23

## Slide 16: Codes
ACI 318-11: For sections design and detailing.
IBC–2017: Were used for gravity live load .
UBC-1997: We used it for Earthquake load

## Slide 17: Software
SAP2000 19.
AUTOCAD 2017.

## Slide 18: Loads Load patterns can be classified in this structure into two categories 1-Gravity loads, including dead, live, and super imposed dead loads. 2-Lateral loads, which include seismic loads.

## Slide 19: Gravity load Types
Dead Loads
It is mainly the own weight of the structural elements, which can be defined as the loads that does not change with time progressing.
Superimposed Dead Loads
These loads are mainly created by the non-structural elements of the building as tiles, stones, partitions, filling materials and plastering and so on

## Slide 20: Section in a slab

## Slide 21
Superimposed dead load = weight of tiles + weight of mortar + weight of filling material
+ weight of plaster + weight of partitions
𝑊𝑆𝐷 = 0.01*25 + 0.02*23 + 0.15*18 + 0.015*23 + 1 = 4.75KN/m2 = 5 KN/m2
*For garage parking area:
𝑊𝑆𝐷 = 0
Story No. or Use | S. D (kN/m2)
Parking Floors | 0
Stores | 5
Offices | 5
Super imposed dead load summarized in Table .

## Slide 22: Section in the external wall
Layer | Thickness(cm)
Stone | 5
Concrete | 10
Isolation | 4
Block | 10
Plaster | 1.5
Material thickness

## Slide 23: Wall weight
Usually the used isolation is polystyrene rolls with unit weight of 0.3 KN/ m3, the first story height is 4.5m and the second story high is 2.95 m
So, the wall weight per unit length were calculated as follows for 4.5 m
Wall weight in ground floor = (0.05*27 + 0.10*23 + 0.04*0.3 + 0.1*12 + 0.015*23) * 4.5 = 23.43 kN/m
Wall weight in typical floor = 5.207 * 2.95 = 15.36 kN/m
Wall weight in roof floor = 5.207 * 1.2 = 6.25 kN/m

## Slide 24: Load Types
Live Loads
Live loads are temporary loads, of short duration, or the load to which a structure is subjected in addition to its own weight, such as, people, furniture, cars…etc.
In our structure, there are many live loads depending on use of every floor according to ASCE 7- 10.
Distribution of live load on the slabs are summarized in Table 1.5.
Story No. or Use | Live (kN/m2)
Parking Floors | 5
Stores | 5
Offices | 2.5

## Slide 25: Seismic load
to determine the seismic load value the requirements of UBC97 code will be
Applied Mapped spectral response acceleration parameters: .
These parameters can be obtained in the maps of risk-target maximum considered earthquake accelerations at 10% of critical damping. Seismic hazard map of spectral response accelerations
Zone factor value is Z = 0.20

## Slide 26: Soil profile type:
Bearing capacity for soil (qall) equal 210 kN/m2 To check the site class, average undrained shear strength is applied.
Su = qall /2 = 210 2 = 105 kpa.
The soil profile is ‘Sc’ .

## Slide 27: Importance factor and risk category
The risk category was decided to be (4), so the importance factor is equal to 1.00 according to UBC97, see Figure.

## Slide 28: Seismic Coefficients for Response Spectrum Design

## Slide 29: Load Combinations
According to the “ACI 318-11” code section 9.2.1, the following loading combinations may be considered:
U=1.4D
U= 1.2D + 1.6L
U = 1.2D + 1.0E + 1.0L
U=1.2D + 1.0E - 1.0L
U= 0.9D + 1.0E
U = 0.9D - 1.0E
Where:
U: ultimate load D: dead load
L: live load
E: earthquake Load

## Slide 30: Preliminary Dimensions

## Slide 31: Flat plate thickness slab in the Basements Floors according to table ACI 318-14 h soiled = Where: 𝐿 n= 6.5 m h soiled = = .216 m take it 250 mm

## Slide 32: Ribbed slab thickness in typical floors and ground floor

## Slide 33
ℎ Ribbed two way =
Thickness of two way ribbed slab
𝑳
𝟑𝟑

## Slide 34
Thickness of one way ribbed slab:

## Slide 35
𝟖
ℎ ribbed one way = 𝑳 or
𝑳
𝟏𝟖.𝟓
Where:
𝐿 = 2.40 m (cantilever)
𝐿 = 3.55 m (one end continuous)
h ribbed = 𝟐.𝟒𝟎
𝟖
𝟏𝟖.𝟓
or 𝟑.𝟓𝟓 = 0.30 or 0.19
take it 300 mm.

## Slide 37
After Graduation project I, the last ribbed slab section

## Slide 38
Beams dimensions

## Slide 39
The selected beam has a length equals 6.52 m

## Slide 40
𝟐𝟏
H beam = 𝟔.𝟓𝟐 = 0.31
take it 300 mm
The width of the beam will be taken approximately as the following relation:
Width (B) = 𝑳𝒆𝒏𝒈𝒕𝒉
𝟐𝟎
𝟐𝟎
B beam = 𝟔.𝟓𝟐 = 0.326 m
take it 400 mm
.
Beam groups | Dimension (mm)
Main Beams | 400*300
Secondary Beams | 400*300

## Slide 41
Columns, shear walls and retaining walls dimensions
After assuming vertical members, their dimensions shall be checked proper or not by SAP2000.
Vertical Structural Members | Dimensions (mm)
Columns | 300*800
Retaining walls | 300
Shear walls 1 | 300
Shear walls 2 | 250

## Slide 42: Modeling

## Slide 43: Flat plate slab definition

## Slide 44: Flat plate slab modifiers

## Slide 45: One way ribbed slab X-Direction Slab defntion

## Slide 46
One way ribbed slab X-Direction Slab modifires

## Slide 47: One way Y-Direction Slab deffintion

## Slide 48
One way Y-Direction Slab modifiers

## Slide 49: Two way ribbed slab definition

## Slide 50: Two way ribbed slab modifiers

## Slide 51: Beams definition and modifiers

## Slide 52: Column definition and modifiers

## Slide 53: Shear wall 30 cm definition and modifiers

## Slide 54: Shear wall 25 cm definition and modifiers

## Slide 55: Retaining Wall definition and modifiers

## Slide 56: Loud pattern

## Slide 57: Model checks

## Slide 58: Compatibility check model one

## Slide 60: Model two

## Slide 62: Equilibrium check model one

## Slide 63: All error < 5% ok
Load type | Manual results (kN) | SAP2000 results (kN) | Error %
Live | 4470.66 | 4389.15 | 1.8
Dead | 11718.99 | 11668.66 | 0.43
SD | 2629.80 | 2581.72 | 1.8
Wall | 1407.13 | 1406.89 | 0.02

## Slide 64: Model two
Load type | Manual results (kN) | SAP results (kN) | Error %
Live | 5190.15 | 5189.49 | 0.01
Dead | 20019.48 | 19507.48 | 2.55
SD | 10380.30 | 10378.99 | 0.02
Wall | 6737.15 | 6789.01 | 0.77
All error < 5% ok

## Slide 65: Stress strain check model one
P (SD) = 112.06 kN
P (SD) theo = 97.53 KN
%Error = 14.89 % >10% (this is because there are shear walls in addition to columns)

## Slide 66: model two
P (live) = 344.12 kN
P (live) theo = 341.33 kN
%Error = 0.82 % <10%  OK

## Slide 67: Punching shear check flat plate
Vc,p < 2.46 Mpa
< 1.004 Mpa
< 1.76 Mpa
From saap = .95 < 1.004 ok

## Slide 68: shear check Model one Shear capacity of flat plate slab = Distribution of shear in x-direction
145.52 kN/m

## Slide 69: Distribution of shear in y-direction

## Slide 70: Shear capacity new section slab = 46.16 KN/m shear in x-direction from saap = 35.58 KN/m 35.58 < 46.16 ok
Model two

## Slide 71: Shear in y-direction
shear in y-direction from saap 12.61 KN/m < 46.16 KN /m ok
The result from saap show that the slab is adequate for shear instead of balacons that need shear reinforcement

## Slide 72: Deflection Check model one

## Slide 73: Model two
Δ allowable = = = 14.04 mm
= 13.72 mm > 14.04 mm OK

## Slide 74: Period check T ≤ 1.4 Ta Ta = .49 second
Building is too soft in x-direction

## Slide 75: Mass participation ratio for model analysis

## Slide 76: Base shear check
base shear by hand = 38434.46 kN

## Slide 77: After edit the scale factor
All values are more than 85% of base shear from equivalent static

## Slide 78: Torsion Irregularity check
The maximum story drift from earthquake in X- direction.

## Slide 79
Ratio = max/avg = 13.05/12.42 = 1.05 < 1.20 OK

## Slide 80: The maximum story drift from earthquake in y- direction

## Slide 81
 All ratios in two directions less than 1.2 then no Torsional Irregularity.

## Slide 82: Drift check Story drift calculations due to earthquake load in X-direction
Story Number | Displacement (Δs’) | Relative Displacement (Δs) | Drift (ΔM) | hs | Δ allowable
1 | 5.95 | 5.95 | 27.0725 | 4500 | 112.5
2 | 13.05 | 7.10 | 32.305 | 2950 | 73.75
3 | 21.13 | 8.08 | 36.764 | 2950 | 73.75
4 | 29.28 | 8.15 | 37.0825 | 2950 | 73.75
5 | 37.03 | 7.75 | 35.2625 | 2950 | 73.75
6 | 44.19 | 7.16 | 32.578 | 2950 | 73.75
7 | 50.61 | 6.42 | 29.211 | 2950 | 73.75

## Slide 83: Story drift calculations due to earthquake load in Y-direction
Story Number | Displacement (Δs’) | Relative Displacement (Δs) | Drift (ΔM) | hs | Δ allowable
1 | 3.33 | 3.33 | 15.15 | 4500 | 112.5
2 | 5.54 | 2.21 | 10.06 | 2950 | 73.75
3 | 8.48 | 2.94 | 13.38 | 2950 | 73.75
4 | 11.6 | 3.12 | 14.20 | 2950 | 73.75
5 | 14.75 | 3.15 | 14.33 | 2950 | 73.75
6 | 17.75 | 3 | 13.65 | 2950 | 73.75
7 | 20.39 | 2.64 | 12.01 | 2950 | 73.75
 All values of drift are Ok

## Slide 84
Design of Structural Elements
Notes: Design results of program was verified on all structural elements, so final design results were taken directly from the program.

## Slide 85: Design of flat plate slab
The ultimate minimum moment in both direction X and Y:
• depth of slap (H) = 250 mm
• Width of slap section (B) = 1000 mm.
• Effective depth of the slap (d) = 220 mm.
• 𝜌min = 0.0018 and 𝜌 max = 0.018
• As min = 0.0018 x 1000 x 250 = 450 mm2
a =7.94mm
40.83 kN. m

## Slide 86: Check for the ultimate moment in x- direction (M11):

## Slide 87
Check for the ultimate moment in x- direction (M11):
As shown in Figure there are two type of zone where the moment is more than the minimum moment.
Distribution of moment in X- direction (M11) for ground floor.

## Slide 89
Note: Steel of flat plate slab in x- direction:
• Use bottom steel equal ∅12/200mm in zone A.
• Use top steel equal ∅12/140 mm in zone B.
• Use bottom and top steel equal ∅10/200mm for the other zones.

## Slide 90
Check for the ultimate moment in y- direction (M22):
Distribution of moment in y- direction (M22) for ground floor.

## Slide 91
Note: Steel of flat plate slab in y- direction:
• Use bottom steel equal ∅12/200mm in zone A.
• Use top steel equal ∅12/140 mm in zone B.
• Use bottom and top steel equal ∅10/200mm for the other zones.

## Slide 92: Design of flat plate
floor | Bottom steel in direction X Zone A | Top steel in direction X Zone B | Bottom steel in direction Y Zone A | Top steel in direction Y Zone B | Other Zone Minimum steel
Slab of first basement | ∅12/200mm | ∅12/140 mm | ∅12/200mm | ∅12/140 mm | ∅10/200mm
Slab of second basement | ∅12/200mm | ∅12/140 mm | ∅12/200mm | ∅12/140 mm | ∅10/200mm

## Slide 93: Design of ribbed slab

## Slide 94: Design of ribbed slab

## Slide 95: Check for the ultimate moment in x- direction (M11):
As shown in Figure there are two type of zone where the moment is more than the minimum moment.

## Slide 96
The ultimate moment in zone B (x-direction).

## Slide 97
• Note: Steel of ribbed slab in x- direction:
• Use bottom steel equal 2∅12/rib in zone A.
• Use top steel equal 2∅20/rib in zone B.
• Use bottom and top steel equal 2∅10/rib for the other zones.

## Slide 98: Check for the ultimate moment in y- direction (M22):
As shown in Figure there are two type of zone where the moment is more than the minimum moment.

## Slide 99
The ultimate moment in zone B (y-direction).

## Slide 100
Note: Steel of ribbed slab in y- direction:
    Use bottom steel equal 2∅12/rib in zone A.
    Use top steel equal 2∅25/rib in zone B area No.1.
    Use top steel equal 2∅18/rib in zone B area No.2.
    Use top steel equal 2∅12/rib in zone B area No.3.
    Use top steel equal 2∅12/rib in zone B area No.4.
    Use bottom and top steel equal 2∅10/rib for the other zones.

## Slide 101: Shear Design of ribbed Slab :
As per discussed later when we do check, some areas need shear reinforcement to increase efficiency of slab to resist shear loads.
Figure shows the highest three values of slab shear.
Vu1 = 49.51 kN/m
Vu2 = 71.67 kN/m
Vu3 = 59.59 kN/m
We will design shear for maximum value and choose Vu2 = 71.67 kN/m.

## Slide 102: Design of Beams
Figure show Beams distribution in typical floors

## Slide 103: Flexure Design for Beams
Beams only in the typical floors distributed as figure Then, sap results for beams are shown in the Figure.

## Slide 104
There are red beams suffering from shear and torsion problems, then we should increase the section as per message from SAP .

## Slide 105
We will try to increase size section as per Figure 4.20 that shown final dimensions of beams.
*Three type of beams mentioned (B400*300, B700*300 and B900*300)

## Slide 106
Longitudinal reinforcing area for beams is shown in the Figure 4.

## Slide 107: Shear Design for Beams
Shear reinforcing ratio for beams is shown in the Figure 4

## Slide 108: Torsion Design for Beams
Torsion reinforcing for beams is shown in the Figure .

## Slide 109: Design of Beams
General beam longitudinal section.

## Slide 110: Design of Beams
Let’s take the same beam named in the AutoCAD drawings B8 in Figure .

## Slide 112: Design for Columns:
Flexure Design for columns
Longitudinal steel reinforcement check:
The rebar percentages for columns from SAP2000 are shown Figure

## Slide 113
Any column with rebar percentage less than 3%,
column pass Any column more than 3% (selected in the Figure 4.29), column size to be enlarge.

## Slide 114
New rebar percentages for columns from ETABS after changing size are shown Figure

## Slide 116
Column Name | Width (mm) | Length(mm) | % of rebar | Longitudinal Bars
C1 | 300 | 800 | 3.5% | 18Ø25
C2 | 300 | 1000 | 3.45% | 22 Ø25
C3 | 300 | 1200 | 3.5% | 256 Ø
C4 | 400 | 1200 | 3.84% | 24 Ø32
summery of reinforcement of columns.
Longitudinal steel for columns
Spacing requirements for shear reinforcement for columns.
Column-Name | Ls(mm) | Lo(mm) | So(mm) | S1(mm)
C1 | 650 | 800 | 150 | 250
C2 | 650 | 1000 | 150 | 250
C3 | 650 | 1200 | 150 | 250
C4 | 800 | 1200 | 150 | 250

## Slide 117: Design of Shear walls
Sample Design and Detailing for Shear Walls

## Slide 118
Internal forces in shear wall: Vu = 25 kN/m
Mu = 20 kN.m/m
Pn = 1700 kN
Design for shear.
For horizontal shear reinforcement: Use 2Ф10/250mm
For vertical shear reinforcement: Use 2Ф10/250mm
special boundary elements check.
Special boundary elements are needed if the stress σ > 0.2 f'c
σ = 0.2 x 24 = 4.8 MPa Vu = 25 kN/m Mu = 20 kN.m/m Pn = 1700 kN

## Slide 120: Design for Retaining walls:

## Slide 122: Design of Mat Footing

## Slide 123: Deflection:
Deflection is the main criterion for the design of footing. Figure shows maximum deflection on mat footing from envelope combination

## Slide 124: Stress under the base:

## Slide 125: Thickness of footing Punching shear

## Slide 126: Thickness of footing One-way shear

## Slide 127: Design of mat footing
Design footing in x-direction.
Description | Moment value (kN.m/m) |  | Area of steel (mm2/m) | Min. area of steel (mm2/m)
Bottom steel | 888 | 0.0041 | 3075 | 1440
Top steel | 314 | 0.0016 | 1292 | 1440
Description | Moment value (kN.m/m) |  | Area of steel (mm2/m) | Min. area of steel (mm2/m)
Bottom steel | 888 | 0.0041 | 3075 | 1440
Top steel | 314 | 0.0016 | 1292 | 1440
Design footing in y-direction.
Description | Moment value (kN.m/m) |  | Area of steel (mm2/m) | Min. area of steel (mm2/m)
Bottom steel | 888 | 0.0041 | 3075 | 1440
Top steel | 314 | 0.0016 | 1292 | 1440
Description | Moment value (kN.m/m) |  | Area of steel (mm2/m) | Min. area of steel (mm2/m)
Bottom steel | 888 | 0.0041 | 3075 | 1440
Top steel | 314 | 0.0016 | 1292 | 1440

## Slide 128: Thank you