## Slide 1: Reconfigurable Antenna by Ahmed Alawneh, Mohammed Mansour and Alaa Rawajbeh The supervisor: Dr. Allam Mousa 2014
An-Najah National University
Fuculty of Engineering
Telecommunication Engineering Department

## Slide 2: Overview
the reconfigurable antenna is a new technology for next generation of wireless network
it has the ability to modify its geometry and behavior
adapt the changes in environmental conditions or system requirements
such as:
enhanced bandwidth, change in operating frequency, polarization, radiation pattern etc.

## Slide 3: Objectives
Type of the Reconfigurable antennas
Implement reconfigurable antenna
Frequency reconfigurable antenna
Channel hopping in Wi-Fi
Pattern reconfigurable antenna
BER Improvement

## Slide 4
Types of Reconfigurable antenna

## Slide 5: Types of Reconfigurable antenna
Types | Process | Applications
Frequency Reconfigurable Antennas | Change the surface current distribution | WLAN, GSM, UMTS, PCS, Bluetooth, Cognitive Radio
Pattern Reconfigurable Antennas | Change the radiating edges, slots or the feeding network | MIMO, Software Defined Radio,
Polarization Reconfigurable Antennas | Change the antenna surface structure or the feeding network | Satellite Communication, MIMO, Cognitive Radio

## Slide 6
In this project we work on two reconfigurable types:
1- Frequency reconfigurable antenna
2- Pattern reconfigurable antenna

## Slide 7: Frequency Reconfigurable antenna
The Problem:
A single wireless device such as laptop and mobile need to support a number of communication standards ( e.g. WIMAX,3G ,Bluetooth ,GPS ,Wi-Fi, UWB)

## Slide 8: The Solutions:
Individual antenna for each standard ( lack of space and the strong coupling between radios)
multiband antennas (more filters , large space)
Frequency reconfigurable antenna (less space and filters)

## Slide 9: Our Design of frequency RA
We used HFSS program to design a Microstrip reconfigurable antenna to operate in two scenarios:
Single-band 2.4 GHz.
Dual-band 2.4 &3.5 GHz.

## Slide 10
Parameter | Value/mm
Width of Patch (W) | 42
Length of Patch (L) | 28.73
Width of Ground (WG) | 52
Length of Ground (LG) | 50
Width of Feed Line (WF) | 2.7
Length of Feed Line (LF) | 31.735
Patch & Ground Thickness (M) | 0.05
Substrate Thickness (H) | 1.6
Insert Width (X) | 2
Insert Length (Y) | 4.8
Vertical Slot Width(S1) | 20
Vertical Slot Length(S2) | 1.5
Horizontal Slot Width(S3) | 20
Horizontal Slot Length (S4) | 1
PIN Diode Switch (P) | 12
Re-configurability Implementation
horizontal and vertical slots with ON/OFF PIN diode switch are used to allow the reconfigurable antenna to operate in two scenarios

## Slide 11
When PIN diode is in ON mode the resonant frequency measured at 2.4 GHz with return loss -16.5 and gain of 5.5 dB as illustrated in Figures below .

## Slide 12
When PIN diode is in OFF mode the resonant frequencies measured at 2.4 and 3.5 GHz with return loss -14.6 & -16.5dB respectively as shown in the figure below.

## Slide 13: Frequency channel hopping on Wi-Fi

## Slide 14: Wireless InSite Simulation Design for Faculty of Engineering

## Slide 15: Power(dB) of various Wi-Fi channel

## Slide 17: Frequency channel hopping on Wi-Fi

## Slide 19: Pattern Reconfigurable antenna
The Problem:
multipath fading in indoor propagation model for
Wi-Fi technology.
The solution:
Pattern Reconfigurable antenna

## Slide 20: Fading and Multipath
Fading refers to the distortion that comes form the Multipath

## Slide 21: Beam for Dipole Antenna L/2, L

## Slide 22: Wireless InSite Simulation Design for Faculty of Engineering

## Slide 23: Received signal power in (dBm) for different antenna radiation patterns Vs. Distance points

## Slide 24: The Communication System
Generate bits
Convolutional Coding
BPSK modulation
Channel
Demodulation
Decoding
BER Calculations

## Slide 25: BER improvement

## Slide 26: Results
frequency reconfigurable antenna its possible to make a multiband with one antenna
Reconfigurable with Wi-Fi channel improve the BER
Patten reconfigurable antenna reduce the the transmit power needed by nearly 10 db

## Slide 27: Future Vision
Reconfigurable antenna will see the light up with new generations of Wireless technology.

## Slide 28: Thank you