## Slide 1: An-Najah National University Engineering & IT Faculty Civil Engineering Department
Structural Analysis And Design of Baitona Building
By: Anan Barahmeh (11105757)
Saleh Qundos (11212226) Galeb Daragmeh (11210069)
Under supervision of : Dr. Munther Diab

## Slide 2: Outline:
Introduction.
Gravity and Lateral loads.
3D modeling using ETABS.
Design of Slab.
Design of Beams.
Design of Columns and Shear walls.
Design of Footings.

## Slide 3
INTRODUCTION

## Slide 4
Baitona Building
Location : Makhfia-Nablus
9 Floors.
Floor area : about 550 m²
Total Area : about 5750 m²

## Slide 5
Floors consists:
Three floors is Residential.
Three floors offices.
The basement for parking the ground and the attic for storage .

## Slide 6
Codes
ACI 318 (American Concrete Institute)
IBC-2012 (International Building Code)
ASCE-2010 (American Society of Civil Engineers).

## Slide 7
GRAVITY & LATERAL
LOADS

## Slide 8
Loads
Gravity
Lateral
Seismic
Dead
live
Superimposed

## Slide 9: Preliminary Design The choice of the system for slab in the building is very important to resist the internal forces and stability.
In our project we use one way solid slab system.
As the solid slab is better for resisting seismic loads.

## Slide 11
Intermediate moment resisting frame system

## Slide 12
SDS=2/3*SMS
SMS= Fa * Ss
R
System
I
Fa→ site class(B), Ss
Ss= 2.5 *Z
Z→ site class(B)→ soil type
Risk category (I)
Use of Buildings and Structures

## Slide 13
Response spectrum
  A response spectrum is a plot of the maximum response amplitude (displacement, velocity, or acceleration) versus the modal period

## Slide 14: Seismic design factors
R= Modification factor

## Slide 15
Code | Value of base shear (Hand Calc.)(kN)
IBC-2012 | 2769.9

## Slide 16
Load combinations
U = 1.4D
U = 1.2D + 1.6L + 0.5(Lr or S or R)
U = 1.2D + 1.6(Lr or S or R) + (1.0L or 0.5W)
U = 1.2D + 1.0W + 1.0L + 0.5(Lr or S or R)
U = 1.2D + 1.0E + 1.0L + 0.2S
U = 0.9D + 1.0W
U = 0.9D + 1.0E

## Slide 17
THREE DIMENSIONAL STRUCTURAL ANALYSIS

## Slide 18
Modifiers for each element
Modifier | Element
0.7 | Column
0.35 | Beam
0.25 | Slab
0.7 | Shear wall

## Slide 21
Rebar percentage
All is okay
Shear & torsion
No red elements
No problems
Strength check

## Slide 22
Compatibility of structural model

## Slide 23
Equilibrium
Load type | Hand results kN | Etabs results kN | Difference %
Dead | 57446 | 60408 | 4.9
SD | 18844 | 21203.8 | 11
Live | 14133 | 14135 | 0

## Slide 24
Slab moments
The difference percentage is 22 %, which is less than 25%, OK
Stress Strain relationship
(internal equilibrium)

## Slide 25
Lateral loads check
Seismic load, IBC
Direction | Hand calculation base shear(kN) | Etabs base shear (kN)
X | 2769.9 | 2455.2

## Slide 26
Period and modal participation ratio

## Slide 28
DESIGN OF SLAB

## Slide 29
Solid slab.
Thickness = 25 cm.
Shear on slab:
Max Vu = Vc =
138.9 >29.8 so,
shear is OK

## Slide 30
Steel reinforcement:
Using a uniform steel mesh with 4Ø12/ 1m (Top and Bottom) for all floors and roof.

## Slide 31
DESIGN OF BEAMS

## Slide 32
ACI318-14 Code requirements:
The value of moment and shear
computed by taking twice the
earthquake load in the load
combinations.
The first hoop shall be located not more than 50 mm from the face of a supporting member.
  .

## Slide 33
For shear and torsion |  | For flexure
 |  | As = ρbd
For shear and torsion |  | For flexure
 |  | As = ρbd
Equations:

## Slide 34
Beam ID | Dimension(h/d) | Longitudinal Steel |  | transverse steel until 2h(S1) | transverse steel (S2)
B1 | (900/250) | Top | 6Ø16 | Ø8/10 cm | Ø8/10 cm
 |  | Bottom | 4Ø16 |  | 
B2 | (400/250) | Top | 4Ø10 | Ø8/10 cm | Ø8/10 cm
 |  | Bottom | 4Ø10 |  | 
B3 | (300/600) | Top | 4Ø16 | Ø8/10 cm | Ø8/10 cm
 |  | Bottom | 3Ø16 |  | 
Tie beams | (300/500) | Top | 3Ø14 | Ø8/10 cm | Ø8/10 cm
 |  | Bottom | 3Ø14 |  | 

## Slide 35
DESIGN OF COLUMNS AND SHEAR WALLS

## Slide 37
All columns in the building is used 90*30 cm
Design methodology:-
Using ETABS to get the axial force and moments on each column.
Choosing the proper steel ratio.
Determining the spacing between hoops.

## Slide 38
ACI318-14 code requirements:
Hoops Equations

## Slide 39
For All columns Steel Ratios is used 1%
So As = 2700 mm2

## Slide 40
Hoops:
For All columns: provide Ø10/10 cm at a distance of 90 cm for the whole Column
Start with hoops at a distance of 5 cm from the face of supports.
Provide a lap splice length = 50 cm.
The splicing of bars is made on the middle of columns.

## Slide 41
Design of shear wall :

## Slide 42
Minimum reinforcement in shear walls according to ACI318-14
Minimum ratio of vertical reinforcement area, ρ shall be:
  0.0015 as minimum rebar ratio with Fy not less than 420 MPa.
Minimum ratio of horizontal reinforcement area, ρ, shall be:
  0.0025 as minimum rebar ratio with Fy not less than 420 MPa.
Vertical and horizontal reinforcement shall not be spaced farther apart than three times the wall thickness, nor farther apart than 450 mm.

## Slide 43: Rebar for Shear walls
The design output from ETABS is 1300 mm2 /meter run  for vertical rebar
For horizontal rebar use minimum steel

## Slide 44
Use total cover = 40 mm.
.2 from ETABS
, therefore, there is no need for shear reinforcement

## Slide 45: DESIGN OF FOOTING

## Slide 46
Soil type : Rock.
Allowable Bearing Capacity: 350 kN/m²

## Slide 47
Group | Dim | Footing No.
F1 | 2.8*2.8*.75 | 1,2,3
F2 | 2.7*2.7*.75 | 4,5,6
F3 | 2.6*2.6*.75 | 7,8,9,10
F4 | 2.5*2.5*.75 | 11,12,13
F5 | 2.4*2.4*.75 | 14,15,16,17,18,19
F6 | 2.3*2.3*.75 | 19-24