## Slide 1: Graduation Project II Structural Analysis and Design of building in Nablus city -Palestine.
An-Najah National University Faculty of Engineering Civil Engineering Department
جامعة النجاح الوطنية
كلية الهندسة ونكنولوجيا المعلومات
By
Adham Adnan Ashour
Under supervision of: Dr.Mahmoud Dwaikat.

## Slide 2: Outline : 1. General Description 2. Preliminary Design 3.Three-Dimensional Modeling and Analysis 4.Design 5.Footing

## Slide 3: General Description

## Slide 4: General Description
Location
It is located in Nablus – Palestine, and the coordinates of the project according to the palestinian coordinate system are 181080″N, 175535″E. Location elevation (site level) is +662m AMSL (above mean sea level).

## Slide 6: General Description
All supports are Pin supporter in the 3D.
As for the external walls, part of them are made of glass walls and the other part are stone walls, and they are added as dead loads on the external beams.
The slab system is two-way solid slab.
In preliminary design chapter, a quick preliminary was performed, so the thicknesses of retaining and shear walls were taken from architectural plans.
Seven checks were made include compatibility check, equilibrium check, stress-strain check, time period, base shear ,story drift , and P-delta.
Assumptions

## Slide 7: General Description
Height and Area For Each Floor

## Slide 8: General Description
Codes and Standard.
ASCI 318-14 (American Concrete Institute)
ACI 318-19 (American Concrete Institute)

## Slide 9: General Description
Ultimate load combinations:
1.4D
1.2D + 1.6L
1.2D + 1.6L + 0.5(Lr or S or R)
1.2D + 1.6(Lr or S or R) + (1.0L or 0.5W)
1.2D + 1.0W + 1.0L + 0.5(Lr or S or R)
1.2D + 1.0E + 1.0L + 0.2S
0.9D + 1.0W
0.9D + 1.0E
Service load combinations:
D + L
D + 0.75L
D + 0.7E
D + 0.75L + 0.75(0.7E)
0.6D + 0.7E
Load Combinations

## Slide 10: General Description
Ultimate load combinations: (lateral load)
1.4D
1.2D + 1.6L
1.29D + L + Ex
1.29D + L - Ex
1.29D + L + Ey
1.29D + L - Ey
0.9D + 1.0Ex
0.9D - 1.0Ex
0.9D + 1.0Ey
0.9D - 1.0Ey
Load Combinations

## Slide 11: General Description
Unit weight, ɣ | 25 (kN/m 3)
Compressive strength, fc | 28 Mpa
Linear modulus of Elasticity,Ec | 4700 = 24870 Mpa
Unit weight, ɣ | 25 (kN/m 3)
Compressive strength, fc | 28 Mpa
Linear modulus of Elasticity,Ec | 
Construction Materials
Structural Elements

## Slide 12: General Description
Non- Structural Elements :
Material | Unit weight ɣ(KN/m3)
Masonry stone | 26
Cement mortar &Plaster | 23
Partition blocks | 12
Filing material aggregate | 14
Glass | 25
Tiles | 26
Ytong Block | 5
Reinforce concrete | 25
Construction Materials.

## Slide 13: General Description
Gravity loads :
Dead load
Super imposed dead load
Live load
Lateral loads :
Soil load
Seismic load
Loads

## Slide 14: General Description
The floor layers:
Finishing materials weight = Σ (thickness of layer × unit weight for each layer)
Element | Thickness (cm) | Unit weight (KN/m^3)
Filling | 5 | 14
Mortar | 2 | 23
Tiles | 1.5 | 26
Ytong Block | 17 | 5
Plaster | 1.5 | 23
SD= Tile weight + Mortor weight + Filling weight + Block weight + Plaster weight + SD of Partitions
SD = 5 KN/m2
Superimposed Dead load calculation

## Slide 15: General Description
Exterior wall load
-Stone wall :
SD masonry wall = unit weight × thickness
=18KN/M

## Slide 16
Live Load

## Slide 17
Lateral Load
Seismic loads:

## Slide 18
Lateral Load
Seismic loads:
According to ASCE 7-10 code to seismic analysis for this structure:
- Risk category: risk category of the building is III

## Slide 19
Lateral Load
Importance factor : (Ie) = 1.25
Zone factor (Z) for Nablus = 0.2
- Mapped acceleration parameters Ss & S1 :
From Palestine seismic map:
Ss= 0.6
S1 = 0.14
Site Class
Site classification is C

## Slide 20
Site Coefficients
- The values of Fa and Fv According to the site class in this project are 0.90 ,0.80 respectively.

## Slide 21
Seismic Design Category
-The maximum considered earthquake Spectral Response Acceleration
Parameters SMS and SM1:
Fa = 1.1652 Fv = 1.7
Sms = 1.1652* 0.6 = 0.7
Sm1 = 1.7 * 0.14 = 0.238
Sds = 2/3 * 0.7= 0.47
Sd1 = 2/3 * 0.238 = 0.16

## Slide 22
Lateral Force Resisting System
Type of the lateral forces resisting system :
Ordinary reinforced concrete shear walls
Response Modification Factor (R) = 5
Over-strength Factor (Ωo) = 2.5
Deflection Amplification Factor (Cd) = 4.5

## Slide 23
Structural Period
Ta = Ct hn x =Ta = 0.0488 * (3.2m * 9n)^0.75 = 0.6 sec
T from ETABS ≤ Ta Cu
The period is limited to Tu = Ta Cu= T max at X and Y = 1.37 * 0.6= 0.82sec

## Slide 24: General Description
Computer Programs

## Slide 25: Structural Preliminary Design

## Slide 26: 1. Slab System 2.Beam System 3. Column System 4. Wall System
Preliminary Design
Structural Systems for analysis and design

## Slide 27: Slab Preliminary dimensions

## Slide 28: Using two-way solid slab,
Preliminary Design
Slab System
By referring to Table 8.3.1.1 in ACI-318-19:
h = 250mm
Slab thickness assumption is not correct but:
H = 250 mm > 125 mm assume is correct.

## Slide 29
Preliminary Design
Slab System
Check Slab for shear
Slab
Maximum Shear force in X-Direction from Etabs = 60kN
Maximum Shear force in Y-direction from Etabs = 100 kN

## Slide 30: Beams Layout

## Slide 31
Preliminary Design
Beam Layout

## Slide 32
Preliminary Design
Beam System

## Slide 33: Column Layout

## Slide 35
Preliminary Design
Column System
R: Rectangular column
Column | Type | Dimension
C1 | R | 700*700

## Slide 36: Wall Layout

## Slide 37
Preliminary Design
Types of walls in this structure will be used:
1. Shear walls
From architectural plans, elevators and staircase walls have an walls have an thickness equal to 300 mm
Wall System
Wall name | Wall thickness (mm)
Wall 1 | 300

## Slide 38: 3D-Modeling and Analysis

## Slide 39: 3D-Modeling and Analysis

## Slide 40: Verification of Structural Analysis

## Slide 41: 3D-Modeling and Analysis
Compatibility Check

## Slide 42: 3D-Modeling and Analysis
Equilibrium Check
Live load
Live load = 3 kn/m2
Total Slab area = 306 – 18 = 288 m2
Total live load = 288*3*9 = 7776 kN
Total live load from Etabs = 7654.7 kN

## Slide 43: 3D-Modeling and Analysis
Stress Strain Load

## Slide 44: 3D-Modeling and Analysis
Deflection Check

## Slide 45: 3D-Modeling and Analysis
Seismic Analysis Methods
1.Equivalent lateral force method (ELF).
Seismic loading in Y-direction
Seismic loading in X-direction

## Slide 46: 3D-Modeling and Analysis
Seismic Analysis Methods
  2.Modal response spectrum method (MRS).
Definition of MRS in ETABS

## Slide 47: 3D-Modeling and Analysis
Period

## Slide 48: 3D-Modeling and Analysis
Base Shear Check
→ V manually = Cs * Building weight
-Where:
V: seismic base shear.
Cs: seismic response coefficient.
W: effective weight.

## Slide 49: 3D-Modeling and Analysis
Base Shear Check

## Slide 50: 3D-Modeling and Analysis
Response spectrum
→ Define load case in both directions (Ex and Ey initial)
Factor=9810*I/R = 9810*I/5 =2452.5 See figure
The values of dynamic earthquake forces must be approximately equal to the value of earthquake forces in the static method. However, the values were not equal, which led to a change in the scale factor for each of the dynamic earthquake forces in X and Y.

## Slide 51: 3D-Modeling and Analysis

## Slide 52: 3D-Modeling and Analysis
Story Drift
𝜕𝑥 =𝐶𝑑 ∗ 𝜕𝑥𝑒/𝐼𝑒
The allowable drift = 0.02 hx

## Slide 53: 3D-Modeling and Analysis
Story Drift
Drift in X-Direction |  |  |  |  | 
Story | Delta(elastic) | H | Drift | allowable | 
9 | 0.00205 | 4.5 | 0.01128 | 0.06 | OK
8 | 0.00206 | 4.5 | 0.01133 | 0.06 | OK
7 | 0.00203 | 4.5 | 0.01118 | 0.06 | OK
6 | 0.00193 | 4.5 | 0.01064 | 0.06 | OK
5 | 0.00177 | 4.5 | 0.00974 | 0.06 | OK
4 | 0.00125 | 4.5 | 0.00687 | 0.09 | OK
3 | 0.00027 | 4.5 | 0.0015 | 0.055 | OK
2 | 8.70E-05 | 4.5 | 0.00048 | 0.08 | OK
1 | 2.10E-05 | 4.5 | 0.00012 | 0.09 | OK

## Slide 54: 3D-Modeling and Analysis
Story Drift
Drift in Y-Direction |  |  |  |  | 
Story | Delta(elastic) | H | Drift | allowable | 
9 | 0.00205 | 4.5 | 0.01128 | 0.06 | OK
8 | 0.00206 | 4.5 | 0.01133 | 0.06 | OK
7 | 0.00203 | 4.5 | 0.01118 | 0.06 | OK
6 | 0.00193 | 4.5 | 0.01064 | 0.06 | OK
5 | 0.00177 | 4.5 | 0.00974 | 0.06 | OK
4 | 0.00125 | 4.5 | 0.00687 | 0.09 | OK
3 | 0.00027 | 4.5 | 0.0015 | 0.055 | OK
2 | 8.70E-05 | 4.5 | 0.00048 | 0.08 | OK
1 | 2.10E-05 | 4.5 | 0.00012 | 0.09 | OK

## Slide 55: 3D-Modeling and Analysis
Effect of P-delta
The values of θ in X direction less than 0.1neglect effect of P-delta.
𝜃 =𝑃𝑥∗ ∆ / 𝑉𝑥∗ℎ𝑥

## Slide 56: 3D-Modeling and Analysis
Effect of P-delta
The values of θ in Y direction less than 0.1neglect effect of P-delta.
𝜃 =𝑃y∗ ∆ / 𝑉y∗ℎy

## Slide 57: Design

## Slide 58: Design
Design of Slab

## Slide 59: Design
Design of beam

## Slide 60: Design
Design of beam
 |  |  |  |  | Area steel |  |  |  |  |  | 
 | b | d | d^2 | Mu+ | Mu- | ƿ+ | ƿ- | Fy | Fc | As+ | As-
Beam 1 | 400 | 520 | 270400 | 151 | 151 | 0.00382 | 0.00382 | 420 | 28 | 793.646 | 793.646
Beam 2 | 400 | 240 | 57600 | 30 | 30 | 0.00355 | 0.00355 | 420 | 28 | 340.81 | 340.81
As min = 0.00333*400*520 = 788.5 m2

## Slide 61: Design
Design of columns
Column at grid (5G) has been selected. See figure:
Axial load from ETABS = 4122.63 KN See figure:

## Slide 62: Design
Design of columns
0.7*0.7

## Slide 63: Footing

## Slide 64: Footing
This project is a design for some types of footing, which the Mat foundation and Wall Footing
Ultimate load combinations:
1.4D
1.54D
1.2D + 1.6L
1.32D+1.76L
1.1D+1.1L (Service load)

## Slide 65: Footing
Mat foundation Layout (AutoCAD drawing): See Figures:
→Allowable bearing capacity of soil = 250 Kn/m2
→

## Slide 66: Footing
Mat Foundation and Wall footing checks :
Check soil pressure :
The pressure must be less than q allowable =250kn/m2. → Ok. See figure:

## Slide 67: Footing
Check Punching shear :
Check punching shear for mat foundation (less than (1) to get a high factor of safety ). OK. See figure:

## Slide 68: Footing

## Slide 69: Footing

## Slide 70: Plans