## Slide 1: Design of foundation for multistory building considering seismic loads
Prepared by :
Baha’a Adel Irshaid
Jad-alhaq Muhammed Zamzam
Muhammed Husni Weld Ali
Muhammed Maher khilfeh
Mahmoud Abd-alnaser al-kharraz
Under supervision of :
Dr. Issam Jardaneh

## Slide 2: Outline
Preview
Effect of increasing number of floors on:-
*Foundation type
*Foundation dimension
*Foundation cost
considering seismic loads

## Slide 3: Preview
Soil type of the site is brownish silty-clay
Soil’s bearing capacity = 120 kN/m2
The soil was being improved using three layers of compacted base coarse, after this improvement soil’s bearing capacity = 180 kN/m2

## Slide 4: Soil layers of the site

## Slide 5: Geological section of site

## Slide 6: Seismic Zone Factor (Z)
This is an estimation of the site peak ground acceleration expressed as a function of the gravity acceleration g
Z factor in Nablus = 0.2g

## Slide 7: Soil response spectra
From the figure below we noticed maximum spectral acceleration is 0.78 g

## Slide 8: Modeling

## Slide 9: Analysis
Formulation the model into 3D using analysis software (ETAPS 2016), which can provide static and dynamic with seismic analysis, and then the results from ETAPS are discussed for several factors.

## Slide 10
Material
The compressive strength at 28days, 𝒇'c= 350kg/cm² ( 28 MPa.)
The yield strength of steel bars, ℱy=420 mPa (high strength steel).

## Slide 11: Loads
Dead load (DL) due to the own weight of the building component.
-Super Imposed Dead load (SID) = 4.5 kN/m2
-Live load (LL) due to moving loads expected through the function of the building=3 kN/m2.
Response spectrum

## Slide 12: -Response spectrum as function

## Slide 13
Checks
Compatibility

## Slide 14: Equilibrium
% of difference dead
% of difference live
% of difference SD

## Slide 15: Result of Etabs Analysis

## Slide 16
Chart: 
| 4 | 8 | 12 | 16 | 20
loads without seismic consideration (kN) | 42455 | 76152 | 109453 | 142339 | 174850
loads with seismic consideration(kN) | 41133 | 77476 | 116415 | 157430 | 200230
Comparison between total columns loads and number of floors

## Slide 17: Design
CODES
For Design will Use ACI 318-11 code
For Seismic Design UBC 97 Code
LOAD COMBINATIONS
Wu=1.4 D
Wu=1.2 D +1.6 L
Wu=1.2D.L +1.0L.L ±1.0E
Wu=0.9 D ±1.0 E

## Slide 18: Foundation Design Options
Single footing
Combined footing
Mat foundation
Piles foundation
Mat over Piles foundation

## Slide 19
Isolated and combined footing option
Isolated and combined footing option fails due to huge overlap between footings since the net area of footings is greater than two thirds of building’s area. as shown in the figure below

## Slide 20: Mat foundation Option
Mat foundation meets the building and soil requirements, so Mat foundation was being adopted in this project .

## Slide 21: Design of Mat Foundation
Soil defined with bearing capacity as simple springs under the Mat Foundation

## Slide 22
Applied Loads

## Slide 23: Selecting of mat thickness
Vu = 1150 KN
Vc =
Vc = 1092 KN
Vc =
Vc =
Vc =
Vc =
Vu<∅Vc  OK

## Slide 24
Etabs Results
MAT THICKNESS (mm) | Seismic load consideration | FLOOR No.
700 | Yes | 4
700 | No | 
1100 | Yes | 8
1000 | No | 
1500 | Yes | 12
1200 | No | 
1900 | Yes | 16
1500 | No | 
2200 | Yes | 20
1600 | No | 

## Slide 25
Check Stress under the Mat Foundation
q = - - y - x
Because the building was symmetric there is no eccentricity which means
ex = ey = 0
Mx = P ey = 0
My = P ey = 0
P = ∑ Forces
Area = A = 20*18.85 = 377 m2

## Slide 26: Mat displacement

## Slide 27: Mat Reinforcement
Calculating the moment in X-direction

## Slide 28: Calculating area of steel for M11
For M11
X= 3.7 Y = 14.67 b =3.6m
Xstart = Xend = 2.9
Y start =12.87 Y end = 16.47
M = 3200 KN.m
ρ=
ρ= 0.00198< ρmin
Use ρmin
As =ρbd
As = 0.00333*1000*1100= 3663
# of bars == 8 bars
1φ25mm/12cm

## Slide 29: Mat Reinforcement
Calculating the moment in Y-direction to find Area of steel required

## Slide 30: Calculating area of steel for M22
For M22
X= 3.7 Y = 14.67 b =3.08m
Xstart = 2.05 Xend = 5.35
Y start = Y end =14.02
M = 3770 KN.m
ρ=
ρ= 0.027< ρmin
Use ρmin
As =ρbd
As = 0.00333*1000*1100= 3663
# of bars == 8 bars
1φ25mm/12cm

## Slide 31: Mat Reinforcement in case of Seismic consideration

## Slide 32: Mat Reinforcement in case of without Seismic consideration

## Slide 34: Cost calculations
This is for 8-floor without seismic consideration
Total weight of steel = 17983 kg
Steel price = 50352.98 Nis
Volume of concrete = 245m3
Concrete price = 36750 Nis
Total price = 87103 Nis

## Slide 35: Cost calculations

## Slide 36
Recommendations
Soil Improvement
The characteristic of the soil can be improved in many ways, the most common way is compaction by adding base course with good characteristics and compact it.
2. Mat Foundation
The effect of the earthquake can be reduced at the edges of the mat foundation by adding 20 cm reinforced concrete around the mat.

## Slide 37
3. Number of floors
Depend in the study of the soil in eastern region of Nablus at Al-Hisbeh Street , it is recommended that the height of the building around eight floor because the effect of the earthquake is minimum which is almost constant till eight floor, after that steep increase in the effect of the earthquake.