## Slide 1: Structural analysis and design of Husam Quresh building
By:
Qais Ghannam
Aws Radwan
Amr Abed
Supervisor:
Eng. Hind Tbaileh

## Slide 2: INTRDUCTION
Project description
Materials
Soil investigation
Codes and standard
  Seismicity of Site and Structure
Loads
Load combination

## Slide 3: PROJECT DESCRIPTION
This project is about a Private commercial multi-storey building in Nablus city, rafedia region, and this building is under construction.
The building is over looking on two streets, a major street in the south and a Minor street on the east, and its away 3m from the major street, and 2m from the minor one.

## Slide 4
The building is about ten floors, three of them are underground floors, the lowest two floors (B3 and B2) will be Garages, the first underground storey (B1) will be depository, the ground floor will be Stores, the ground floor has an attic 3 meters in height, the first and second floors will be Wedding Hall and museum respectively, and the remaining floors designed to be offices.

## Slide 5
Total area of building = 5300
The area of each floor:
Floor | B3 | B2 | B1 | G | attic | 1-6
Floor | B3 | B2 | B1 | G | attic | 1-6

## Slide 6
The height and elevation of each floor :

## Slide 7: materials
Concrete

## Slide 8
Steel

## Slide 9
Non-structural materials

## Slide 10: Soil investigation
An investigation about the soil was done in the location of the project to get on the bearing capacity of the soil and condition around the site of work, with contact with civil engineer make studies about this region and he out with , Then will be using this value in analysis and design of the foundation of the structure.

## Slide 11: Codes and standard
ACI 318-14
ASCE7-10
IBC 2012

## Slide 12: Seismicity of Site and Structure

## Slide 13
Z for Nablus = 0.2
SS = 2.5 × Z = 2.5 × 0.2 = 0.5
S1 = 1.25 × Z =1.25 × 0.2 = 0.25

## Slide 14
Site class  Stiff Soil (C)

## Slide 15
Site Coefficient Fa = 1.2

## Slide 16
Site Coefficient Fv (by interpolation) = 1.55

## Slide 17
SMS = Fa × SS = 0.6
SM1 = Fv × S1 = 0.3875
SDS = SS = 0.6
SD1 = S1 = 0.3875

## Slide 18
Risk Category = II

## Slide 19
Seismic design category =D

## Slide 20: loads
Gravity Loads
  Dead Load: Weight of structural members.
  SD Load: 4.5 KN/.
  Live load:

## Slide 21
Lateral Load
The method used in determination the effect of earthquake load is modal response method.
Verified by ELF

## Slide 22: Load combination
Ultimate Load Combinations:
1.4 D
1.2D +1.6L
1.32D +L +1.3EQx +0.39EQy
1.32D +L +1.3EQy +0.39EQx
0.78D +1.3EQx +0.39EQy
0.78D +1.3EQy +0.39EQx

## Slide 23
Service Load Combinations:
D+L
1.084 D+0.91EQx+0.273EQy
1.084 D+0.91EQy+0.273EQx
1.063D +0.75L +0.683EQx +0.205EQy
1.063D +0.75L +0.683EQy +0.205EQx
0.516D+0.91EQx+0.273EQy
0.516D+0.91EQy+0.273EQx

## Slide 24: PRELIMINARY DIMENTIONS
Slabs
Beams
Columns

## Slide 25: slab thickness
We have a two way system that used:
1) two way solid slab : it used for B3 slab.
2) two way U-boot slab: it used for all floors except B3 slab.

## Slide 27
For solid slab :
assuming :

## Slide 28
For U-BOOT SLAB :
U-boot dimensions :
Height = 20 cm
Width = length = 52 cm
total depth of slab = 32 cm .

## Slide 29: Beams dimensions
for one end continues beam with
L = 8.4 m .
Try h =0.6 m
b= 0.3m

## Slide 30
for one end continues beam with
L = 8.4 m .
Try h = 0.6 m
b = 0.3m

## Slide 31: Column dimensions
column dimensions found by
tributary area method
The dimension of column is (1400 × 500)

## Slide 32: MODELING & CHECkES
ETABs 2016, will be used.
Process of modeling
checks of modeling

## Slide 33: Process of modeling
1) Define of material
- Concrete
concrete was used with
ɣ=25KN/m3 and
F'c =28 MPa
So Ec = 4700×√(f'c) =
4700× √28=
24870 MPA

## Slide 34: - Steel (rebar)
ɣ=78.5 KN/m3
Fy=420 Mpa
Es= 200 000 MPa

## Slide 35: 2) Define of sections
Columns & Beams sections
Shear & Retaining walls sections
Slabs sections

## Slide 36: Columns & Beams sections

## Slide 37: Beams sections
Main beam
Secondary beams

## Slide 38: Beams modifiers

## Slide 39: Columns modofires

## Slide 40: Shear & Retaining walls sections

## Slide 41: Slabs sections
U- boot section
solid slab

## Slide 42
U-boot slab

## Slide 43: Modifiers for U-boot slab:
F11 = F22 = F12 = = = 0.5149

## Slide 44
M11 =M22 =M12=( =(
= 0.1897
V13 = V23 = = 0.22388
Mass modifire = Weight modifire =
= () = 0.62353

## Slide 46: Solid slab
Solid slab section & modifiers

## Slide 47: 4)Define of load and load combinations

## Slide 48: Steps to define lateral load
1)Define function with type of response spectrum with value of SDS 0.60
And SD1 =0.3875

## Slide 49: Steps to define lateral load
2) Define load cases in two directions with type of response spectrum using the function that defined in step 1
The scale factor = ( g ×I)/R= (9810 ×1)/5=1962

## Slide 50: Steps to define lateral load
3) Define equivalent lateral static force in X and Y directions.

## Slide 51: Steps to define lateral load
4) Define mass source for blocks which will be used to find seismic weight of structure.
5) Define diaphragms for each story and it will be semi rigid diaphragm.

## Slide 52: Checks of model
Compatibility check.
Equilibrium check.
Stress strain check.
Deflection check.
Modal mass participate ratio check(MPMR)
Base shear check
Drift check
P-delta check

## Slide 53: Compatibility check to confirm that the structural elements connect together.

## Slide 54: Equilibrium check
This check is to confirm that weight of structure from ETABS are approximately equal to weight of structure by hand calculations.
Max. allowable error in this chick 5%
ETABs result:

## Slide 55: Calculations - Live load
Equilibrium check for total live load |  |  | 
Story | Live load (KN/m^2) | Area (m^2) | Total live load (KN)/story
B2 | 3 | 608.82 | 1826.46
B1 | 5 | 608.82 | 3044.1
G | 5 | 564.46 | 2822.3
Attic | 5 | 337.39 | 1686.95
1 | 5 | 426.3 | 2131.5
2 | 3 | 426.3 | 1278.9
3 | 3 | 426.3 | 1278.9
4 | 3 | 426.3 | 1278.9
5 | 3 | 426.3 | 1278.9
6 | 3 | 426.3 | 1278.9
roof | 3 | 426.3 | 1278.9
Stair slab | 2 | 75.46 | 150.92
Sum. |  |  | 19335.63
ETABs Result |  |  | 19091.74
Error |  |  | 1.26135016
max. allowable error |  |  | 5%
OK |  |  | 

## Slide 56: - SID load
Equilibrium check for total SID load |  |  |  | 
Story | SID load (KN/m^2) | Area (m^2) | Exterior walls on beams | Total SID/story
B2 | 4 | 608.82 | 0 | 2435.28
B1 | 4.3 | 608.82 | 0 | 2617.926
G | 4.3 | 564.46 | 630 | 3057.178
Attic | 4.3 | 337.39 | 1265 | 2715.777
1 | 4.3 | 426.3 | 1220 | 3053.09
2 | 4.3 | 426.3 | 1220 | 3053.09
3 | 4.3 | 426.3 | 1220 | 3053.09
4 | 4.3 | 426.3 | 1220 | 3053.09
5 | 4.3 | 426.3 | 1220 | 3053.09
6 | 4.3 | 426.3 | 1220 | 3053.09
roof | 4.3 | 426.3 | 1220 | 3053.09
Stair slab | 3 | 75.46 | 0 | 226.38
total SID |  |  |  | 32424.171
ETABs Result |  |  |  | 32180.2
Error |  |  |  | 0.752435583
Error < 5% … OK |  |  |  | 

## Slide 57: Dead load
Solid slab dead load = 0.22 × 1 ×1 × 25 = 5.5 KN/m2
To find Unit weight for U-Boot slab, use this figure

## Slide 58: Dead load from slabs
Equilibrium check for Dead load |  |  | 
SLABs Dead load |  |  | 
Story | Slab weight (KN/m^2) | Area (m^2) | Total Slabs load/story
B2 | 5.5 | 608.82 | 3348.51
B1 | 4.989 | 608.82 | 3037.40298
G | 4.989 | 564.46 | 2816.09094
Attic | 4.989 | 337.39 | 1683.23871
1 | 4.989 | 426.3 | 2126.8107
2 | 4.989 | 426.3 | 2126.8107
3 | 4.989 | 426.3 | 2126.8107
4 | 4.989 | 426.3 | 2126.8107
5 | 4.989 | 426.3 | 2126.8107
6 | 4.989 | 426.3 | 2126.8107
roof | 4.989 | 426.3 | 2126.8107
Stair slab | 5.5 | 75.46 | 415.03
Sum = |  |  | 26187.94753

## Slide 59: Dead load from beams
Beams | Section area (m^2) | avg. length (m) | # of beams | weight (KN)
B1 (70X40) | 0.28 | 7.1 | 210 | 10437
B2 50X40 | 0.2 | 2.1 | 30 | 315
B3 22X40 | 0.088 | 1.9 | 4 | 16.72
B4 22X60 | 0.132 | 3.2 | 10 | 105.6
B5 32X40 | 0.128 | 4.8 | 102 | 1566.72
B6 32X60 | 0.192 | 4.4 | 35 | 739.2
B7 (70X30) | 0.21 | 6.8 | 38 | 1356.6
Sum = |  |  |  | 14536.84

## Slide 60: Dead load from columns
Columns Dead Load |  |  |  | 
Story | Section area | Length | No. in each story | Weight
B2 | 0.35 | 2.5 | 11 | 240.625
B1 | 0.35 | 2.5 | 11 | 240.625
G | 0.35 | 3 | 11 | 288.75
Attic | 0.35 | 3.27 | 11 | 314.7375
1 | 0.35 | 3.06 | 11 | 294.525
2 | 0.35 | 3.25 | 11 | 312.8125
3 | 0.35 | 3.25 | 11 | 312.8125
4 | 0.35 | 3.06 | 11 | 294.525
5 | 0.35 | 3.06 | 11 | 294.525
6 | 0.35 | 3.06 | 11 | 294.525
roof | 0.35 | 3.06 | 11 | 294.525
Stair slab | 0.35 | 3.32 | 4 | 116.2
 |  |  | Sum= | 3299.188

## Slide 61: Dead load from walls: Total dead load = (1640+5163.3+3299.188+14536+26187) =50827.575 KN From ETABS= 50005 %error = ( = 1.62% < 5% so it's ok
Retaining Walls | 5163.6
Shear Walls | 1640
Total Dead Load | 50827.57503
ETABs Reading | 50005
Error | 1.618363712
1.62% < 5% ….. >>> OK | 

## Slide 62: Stress strain check
Check moment in frame
Check moment in beam
Check axial on column
Check shear in slab

## Slide 63: moment in frame
Live load used to calculate moment in frame in B3-floor
So live load = 3 KN/m2= q
Ln=width of frame = ( )
= 7m
L=length of frame = 7.4
M==
= 143.7 KN.m

## Slide 64: moment in frame
Section cut at start of frame
M at start of frame
= 34.6 KN.m

## Slide 65: moment in frame
Section cut at mid of frame
M at mid of frame
= 81.4 KN.m

## Slide 66: moment in frame
Section cut at end of frame
M at end of frame
= 69.3 KN.m

## Slide 67: moment in frame
So M=( + M at mid )
M= ( + 81.4 ) = 133.35 KN.m
Hand calculation: M=== 143.7 KN.m
%error = = 7.2%
7.2% < 10 % ⇛ so it's an acceptable value

## Slide 68: Moment in beam
This check will be done for B1 (70×40) and will be calculated from live load (3 KN/m2), as shown in the figure:
Tributary area
for B1

## Slide 69: Moment in beam
L= 7.7 m
A= ( 0.5 × 7.7 × ) + (0.5 ×6.3 ×2
Load = 29.25 × 3 = 87.75 KN
W =
So : M= = = 84.48 KN.m

## Slide 70: Moment in beam M at second edge = 52.7 KN M at first edge = 25.38 KN.m

## Slide 71: Moment in beam M at mid of beam = 51.7 KN.m

## Slide 72: Moment in beam
M at first edge = 25.38 KN.m
M at second edge = 52.7 KN.m
M at mid of beam = 51.7 KN.m
M from ETABS = ( +51.7) = 90.74KN.m
Hand calculation: M= = = 84.48 KN.m
% error = (

## Slide 73: check axial on column
For column (C8) in 6th floor
Tributary area = 6.9×4.1 = 28.2 m2.
P (live) = live load × Area
P = 3 KN/ m2 × 28.2 m2 = 84.6 KN

## Slide 74: check axial on column
From ETABS(P) = 80.3 KN.
Difference percentage = (84.6 – 80.2655)/ 84.6 × 100% = 5.12 %, OK

## Slide 75: check shear for slab
Shear Capacity of slab = ФVc
ФVc = Ø × (1/6 ) × √(f'c) ×bw × d
= 0.75 × 1/(6 ) × √(28 ) ×150 × 280 × 1.1 = 30.558 KN/rib
ФVc = 30.558/0.67 = 45.61 KN/ m

## Slide 76: check shear for slab
Check of the shear force in x-direction (V13):

## Slide 77: check shear for slab
Check of the shear force in y-direction (V23):

## Slide 78: Deflection check
Deflection at first panel:
First panel will be checked in first floor
Immediate deflection =
deflection in the middle of the panel –
average deflection of the four beams

## Slide 79: Deflection check
from dead load:
Average deflection of beams
= = 7.85 mm.
Deflection at mid of panel = 12 mm
The deflection = 12 – 7.85 = 4.15 mm

## Slide 80: Deflection check
From SID:
Average deflection of beams
= = 6.175 mm
Deflection at mid of panel = 9.3 mm
The deflection = 9.3 - 6.175= 3.15 mm

## Slide 81: Deflection check
From live load:
Average deflection of beams
= = 4.35mm
Deflection at mid of panel= 8 mm
The deflection = 8 – 4.35 = 3.65 mm

## Slide 82: Deflection check
Immediate deflection = ΔDL + ΔSID + ΔLL = 11.25 mm
Long term deflection = 2 ×Δd+2×Δsid +1.5 Δl = 20.7 mm
The following table shows the allowable deflection:
Allowable immediate deflection = = 21.3 mm > 11.25 mm It's ok.
Allowable long term deflection = mm > 20.7 mm it's ok .

## Slide 83: Mpmr check
to find if response spectrum analysis can be made for seismic design. So The MPMR must be greater than 90% to use response spectrum analysis.

## Slide 84
Case | Mode | Period sec | UX | UY | UZ | Sum UX | Sum UY
Modal | 1 | 1.500 | 0.4507 | 0.0322 | 0 | 0.4507 | 0.0322
Modal | 2 | 1.420 | 0.0309 | 0.4896 | 0 | 0.4816 | 0.5217
Modal | 3 | 1.003 | 0.0384 | 1.236E-05 | 0 | 0.52 | 0.5217
Modal | 4 | 0.383 | 0.1078 | 0.002 | 0 | 0.6278 | 0.5237
Modal | 5 | 0.364 | 0.0023 | 0.1151 | 0 | 0.6301 | 0.6389
Modal | 6 | 0.281 | 0.0019 | 0.0154 | 0 | 0.6321 | 0.6543
Modal | 7 | 0.185 | 0.0461 | 0.0012 | 0 | 0.6781 | 0.6555
Modal | 8 | 0.167 | 0.0025 | 0.0577 | 0 | 0.6807 | 0.7132
Modal | 9 | 0.162 | 0.0001 | 0.0016 | 0 | 0.6807 | 0.7147
Modal | 10 | 0.139 | 0.019 | 0 | 0 | 0.6998 | 0.7147
Modal | 11 | 0.135 | 0.0001 | 0.0025 | 0 | 0.6998 | 0.7173
Modal | 12 | 0.124 | 0.0016 | 0.0131 | 0 | 0.7014 | 0.7304
Modal | 13 | 0.116 | 1.91E-05 | 1.281E-05 | 0 | 0.7014 | 0.7304
Modal | 14 | 0.111 | 0.0005 | 0.0434 | 0 | 0.702 | 0.7738
Modal | 15 | 0.105 | 0.0486 | 0.0001 | 0 | 0.7505 | 0.774
Modal | 16 | 0.099 | 0.0022 | 0.0001 | 0 | 0.7528 | 0.774
Modal | 17 | 0.088 | 0.0007 | 0.051 | 0 | 0.7535 | 0.8251
Modal | 18 | 0.082 | 0.0734 | 0.0014 | 0 | 0.8269 | 0.8265
Modal | 19 | 0.076 | 0.0085 | 0.0409 | 0 | 0.8355 | 0.8674
Modal | 20 | 0.069 | 0.0429 | 0.0002 | 0 | 0.8783 | 0.8676
Modal | 21 | 0.066 | 0.0074 | 0.0329 | 0 | 0.8858 | 0.9005
Modal | 22 | 0.061 | 0.0014 | 0 | 0 | 0.8871 | 0.9005
Modal | 23 | 0.059 | 0.0067 | 0.0018 | 0 | 0.8939 | 0.9023
Modal | 24 | 0.059 | 0.0005 | 0.0122 | 0 | 0.8944 | 0.9145
Modal | 25 | 0.058 | 0.0066 | 0.0015 | 0 | 0.901 | 0.9161

## Slide 85: Base shear check
Will be make on result of modal response spectrum , response spectrum shall be multiplied by at least 0.85
Base shear manually : V = Cs × W
W = weight of structure = 89927 KN .
Cs = minimum of : ,
SDs = 0.6 , R= 5 , Ie = 1
Ta= Ct ×
T = Ta×Cu

## Slide 86: Base shera check
Value of Ct and x taked from code so :
Ct = 0.02 ×
X = 0.75
hn = 36.37 m
Cu = 1.4
So : T =
Period For fundamental in ETABS = 1.5
So use T = 1.018 s

## Slide 87: Base shear check
Then Cs=0.07598.
V=Cs × w = 0.07598 × 89927 = 6832 KN.

## Slide 89: Drift check
This check on drift ( horizontal displacement of storey )
Allowable drift = 0.02 × hnx
From ETABS we take the value of drift multiply by

## Slide 90: In x - direction

## Slide 91: In y -direction

## Slide 92: P-delta check
In this check we show the eddect of P –delta effect by calculation stability coefficient and compare it with allowable limit which equal 0.1
Theta =

## Slide 93: Theta in x –direction

## Slide 94: Theta in Y -direction

## Slide 95: DESIGN AND DETAILING
Flexural design for U-boot slab:
>> use 414 /m in two direction

## Slide 96
Beams Design:

## Slide 97
Shear reinforcing design for beams:

## Slide 98
Example of beams design:

## Slide 99
Column design:
From ETABS we find that rebar Percentage >> OK.
use 36 14
For shear design >> Use 5∅10/20 cm

## Slide 100
Shear wall design:
Vu from ETABS = 53.3 KN
ΦVc = 91.9KN/m >> Vu so thickness is ok.
vertical steel: Mu=64 KN.m/m .. As = 6.08×10-3×1000×250 =
1520mm2 > As min .. use 114/10 cm
Horizontal steel .. Mu=33. 6 KN.m/m .. As = 4.1×10-3 ×1000×150 =
615 mm2 .. So Use 1Φ12 /15 cm on each side

## Slide 102
Footing design
Using safe program
K= factor × qall
K=120×300 = 36000
Check for punching shear :
There is no punch on the footing
as we see on picture.

## Slide 103
Check bearing capacity:
As we see on the picture there is no regions on footing
that above bearing capacity

## Slide 104
For footing we use:
Q = 300 KN/m^2 .. H = 600 mm .. D = 520 mm ..
Ex :
More and more detailing
in AutoCAD drawing
and word report