## Slide 1: Structural design of al-manarah center in ramallah city
Prepared by : Ghadeer G. Mukhemar
Nada A. Jaradat
Shireen A. Ktaifan
Under supervision of: Ibrahim Mohammad
An-Najah National University
Faculty of Engineering
Civil Engineering Department

## Slide 2
1. Introduction.
2. Preliminary design.
3. Three dimensional analysis and design of structural elements using ETABS.

## Slide 3
3D Architectural Model
Figure 1.1 : 3D architectural model
Introduction

## Slide 4
Project Location
Figure 1.2: Project location
Introduction

## Slide 5
This project consists of fifteen floors of an approximate area of 25,578, including five basements, a ground floor, eight top floors and a roof with a total height of 52.0m. The building has three main gates in the fifth basement, first basement and in the ground floor.
General description
Introduction

## Slide 6
AutoCAD architectural plans
Figure 1.3: Fourth Basement architectural plan
Introduction

## Slide 7: AutoCAD architectural plans
Figure 1.4: Ground floor architectural plan
Introduction

## Slide 8
AutoCAD architectural plans
Figure 1.5: Fifth floor architectural plan
Introduction
The following table shows floors usage, areas and center to center heights.

## Slide 9
Floor Name | Floor Usage | Floor Area(m2) | Floor Height C/C(m)
Fifth Basement | Parking and police office | 1886 | 3.12
Forth Basement | Parking and police office | 1875 | 3.12
Third Basement | Parking and police office | 1875 | 3.12
Second Basement | Parking and police office | 1882 | 3.12
First Basement | Parking and police office | 1986 | 3.9
Ground Floor | Shops, offices and police office | 1895 | 3.76
First Floor | Shops, offices and police office | 1939 | 3.52
Second Floor | Offices and police office | 1908 | 3.64
Third Floor | Offices | 1732 | 3.12
Fourth Floor | Offices | 1491 | 3.12
Fifth Floor | Offices | 1732 | 4.68
Sixth Floor | Offices | 1482 | 3.38
Seventh Floor | Offices | 1419 | 3.38
Eighth Floor | Offices | 1193 | 3.38
Roof | Offices | 1193 | 3.64
Staircase floor |  | 90 | -
Total |  | 25,578 | 48.62
Table 1.1: Floors Description
Introduction

## Slide 10
American Concrete Institute (ACI318M-14): Building code requirements for structural concrete and commentary.
American Society of Civil Engineers (ASCE7-10).
American Society of Civil Engineers (ASCE41-13).
International Building Code (IBC2012).
Jordanian Code_2006.
Unified Facilities Criteria (UFC3-301-1).
Israeli Standard SI413.
Codes and standards
Introduction

## Slide 11
Structural materials
Concrete.
Concrete B400 for columns, shear walls and foundation.
concrete B350 for slabs and beams.
Reinforcing steel.
Other materials (non-structural materials).
Materials
Introduction

## Slide 12
Properties | B350 | B400
Unit weight (KN/m3) | 25 | 25
Concrete Compressive Strength fc (MPa) | 28 | 32
Concrete Flexural Strength/ Capacity (MPa) | 3.28 | 3.51
Concrete Tensile Strength /capacity (MPa) | 1.75 | 1.87
Modulus of Elasticity (MPa) | 24870 | 26587
Poisson Ratio | 0.2 | 0.2
Properties | B350 | B400
Unit weight (KN/m3) | 25 | 25
 | 28 | 32
 | 3.28 | 3.51
 | 1.75 | 1.87
 | 24870 | 26587
Poisson Ratio | 0.2 | 0.2
Concrete
Table 1.2: Concrete proprieties
Introduction

## Slide 13
Reinforcing steel
Property | Value
Yield Strength (MPa) | 420
Tensile Strength (MPa) | 620
Modulus of Elasticity (MPa) | 
Property | Value
Yield Strength (MPa) | 420
Tensile Strength (MPa) | 620
Modulus of Elasticity (MPa) | 
Table 1.3 steel properties:
Introduction

## Slide 14
Nonstructural material | Unit weight (KN/m3)
Tiles | 27
Mortar and Plastering | 23
Gravel | 18
Block | 12
Masonry Stone | 27
Polystyrene (insulation) | 0.3
Non-structural materials
Table 1.4: Unit weight for nonstructural material
Introduction

## Slide 15
Gravity loads (dead, super imposed dead, live and snow loads).
Lateral loads (earthquake, wind and soil loads).
Loads
Introduction

## Slide 16
Dead load
The dead load includes the self-weight of the structural elements.
Superimposed dead load
1.Weight of tiles
2.Weight of mortar
3.Weight of gravel
4.Weight of plastering
5.Weight of false ceiling
6.Weight of partitions
Gravity loads
Introduction

## Slide 17
Material | Unit weight in (KN/m3) | Thickness (t) in (m) | (KN/m2)
Tiles | 27 | 0.03 | 0.81
Mortar | 23 | 0.02 | 0.46
Gravel | 18 | 0.1 | 1.8
Plastering | 23 | 0.02 | 0.46
Total |  |  | 3.53
Material |  | Thickness (t) in (m) | 
Tiles | 27 | 0.03 | 0.81
Mortar | 23 | 0.02 | 0.46
Gravel | 18 | 0.1 | 1.8
Plastering | 23 | 0.02 | 0.46
Total |  |  | 3.53
Gravity loads
Superimposed dead load from partitions ranges from 1 to 1.5, use 1.5 KN/m2 and assume false ceiling weight equals 0.2 KN/m2.
From Ground to Ninth floor:
Total superimposed dead load =3.53+1.5+0.2 = 5.23 ≈ 5.3 KN/m2
For basement floors superimposed dead load =( thickness of pavement slab ɣ concrete ) + false ceiling weight =( 0.8 25) + 0.2 = 2.2 KN/m2
Table 1.5: Superimposed dead load calculations
Introduction

## Slide 18
Superimposed dead load on perimeter walls
The weight of perimeter walls will differ for each floor based on the thickness, height and materials used and it will be presented as line load on the perimeter of the building.
Wall weight =(weight of stone +weight of mortar +weight of RC+ weight of insulation +weight of block + weight of plastering ) floor height
Gravity loads
Introduction
Figure 1.6: Section in exterior wall

## Slide 19
Name of Floors | Weight of Perimeter Walls (KN/m) | Weight of perimeter walls (KN/m2) | Weight of perimeter walls – weight of RC (KN/m2)
Fifth to Second Basements | 32.38 | 10.379 | 4.129
First Basement | 40.478 | 10.379 | 4.129
Ground Floor | 39.025 | 10.379 | 4.129
First Floor | 36.53 | 10.379 | 4.129
Second Floor | 37.78 | 10.379 | 4.129
Third and Fourth floors | 32.38 | 10.379 | 4.129
Fifth Floor | 48.57 | 10.379 | 4.129
Sixth and Seventh | 35.08 | 10.379 | 4.129
Gravity loads
Table 1.6: Weight of perimeter walls
Introduction

## Slide 20
For eighth and ninth floors we have curtain walls:
The range of load /m2 for curtain wall is 0.4- 0.6 KN/m2
Load per meter for curtain walls in the eighth and ninth floors = 0.6 floor height
=0.6 × 3.38 =2.028 = 2.1 KN/m
Gravity loads
Introduction

## Slide 21
Live load
In this project live load will differ according to the floor usage, the following live load values from ASCE7-10 are shown below
Gravity loads
Floor usage | Live load (KN/m2)
Parking | 3
Shops | 5
Offices | 2.4
Balconies | 4.8
Table 1.7: Live Load values
Introduction

## Slide 22
Snow load
Pf =0.7
Where:
Pf: Flat roof snow load KN/
Ce: Exposure factor Table 7-2 (ASCE7-10)
Ct: Thermal factor Table 7-3 (ASCE7-10)
Is: Importance factor Table 1.5-2(ASCE7-10)
Pg: Ground snow load
Ce=1
Ct=1
Is=1.1
Gravity loads
Introduction

## Slide 23
In snow load:
The value of Pg is taken from the Jordanian Code, it depends on the height of the building above mean sea level which equals 866.64 in our case.
Gravity loads
Structure height above mean sea level h in (m) | Snow load (KN/m2)
h<250 | 0
250<h<500 | (h-250)/800
500<h<1500 | (h-400)/320
Table 1.8: Pg value for snow load calculations (Jordanian Code Table5-3)
Introduction

## Slide 24
Pg()= = 1.458125 KN/m2.
Snow load = 0.7Ct Ce Is Pg
= 0.7 1.1226 KN/m2.
To compare it with minimum snow load Pm according to ASCE7-10
Pm= 0.96 = 0.96 = 0.96 KN/ m2
Since okay
Gravity loads
Introduction

## Slide 25
Earthquake load
Risk category (Ш)
“Buildings and other structures, the failure of which could pose a substantial risk to human life”.
Importance factor (Ie) = 1.25 (ASCE 7-10 Table 1.5-2)
Acceleration parameters S1 and Ss from Israel standard SI413.
Lateral loads
Introduction

## Slide 26
Ss = 0.5
S1= 0.12
Figure 1.7: Mapped acceleration parameter S1 and Ss
Introduction

## Slide 27
Site classification “B” Rock (ASCE7-10 Table 1.3)
Site Coefficients Fa and Fv
Fa = short-period site coefficient.
Fv = long-period site coefficient.
Fa=1 (ASCE7-10 Table 11.4-1)
Fv =1 (ASCE7-10 Table 11.4-1)
Spectral response acceleration parameters SMS and SM1
SMS = Fa ×SS (ASCE7-10 equation11.4-1)
SMS= 1× 0.5=0.5
SM1 = Fv ×S1 (ASCE7-10 equation11.4-2)
SM1= 1×0.12 =0.12
Lateral loads
Introduction

## Slide 28
Seismic Design Category “D” (ASCE7-10 Table 11.6-1 and 11.6-2 )
Since SDC is “D” Response Spectrum and Seismic Response History are permitted while Equivalent Lateral Force is not permitted. ( ASCE7-10 Table 12.6-1)
Response factor R, over strength factor and deflection amplification factor Cd ( ASCE7-10 Table 12.2-7)
R=7
Cd=5.5
=2.5
Lateral loads
Introduction

## Slide 29
Response spectrum period versus acceleration curve
Lateral loads
Figure 1.8: Response spectrum period vs. acceleration curve
Introduction

## Slide 30
Wind load
Where:
P: Design internal pressure to be used in determination of wind load for buildings (N/m2) from equation 27.4-1 ASCE7-10.
G: Gust – effect factor, for a rigid building or other structure is permitted to be taken as 0.85 or it can be calculated using the formula (26.9-6) in ASCE7-10, and it’s taken as 0.85.
Cp: External pressure coefficient to be used in determination of wind loads for buildings from figure 27.4-1 according to ASCE7-10, and it is taken as 0.8 for windward, -0.354 for leeward and -0.7 for sideward.
Lateral loads
Introduction

## Slide 31
qz: Velocity pressure evaluated at height Z above the ground (N/m) from equation 27.3-1in ASCE7-10.
Kz: Velocity pressure exposure coefficient evaluated at height Z Table 27.3-1 in ASCE7-10.
Kzt: Topographic factor from equation 26.8-1 in ASCE7-10, and it is taken as one.
Kd: wind directionality factor from Table 26.6-1 in ASCE7-10, and it is taken as 0.85.
V: Basic wind speed (m/s). Three-second gust speed at 33ft (10m) above the ground in Exposure C. It can be determined in two ways
1- From Jordanian Code and IBC2012, V= 39.44 m/s
2- From UFC3-301-1, V= 51.4 m/s
Z = height above ground level, in (m).
Lateral loads
Introduction

## Slide 32
Wind Pressure in X and Y-direction (Windward)
Lateral loads
Table 1.9:Wind Pressure in X and Y-direction (Windward)
Introduction

## Slide 33
Wind Pressure in X and Y-direction (Leeward)
Lateral loads
Table 1.10:Wind Pressure in X and Y-direction (Leeward)
Introduction

## Slide 34
Wind Pressure in X and Y-direction (Sideward)
Lateral loads
Table 1.11:Wind Pressure in X and Y-direction (Sideward)
Introduction

## Slide 35
Soil pressure
= +
Where:
Δp = additional earth pressure caused by seismic shaking, which is assumed to be a uniform pressure.
= soil pressure due to surcharge load in KN/
= soil pressure due to soil and surcharge load in KN/
kh = horizontal seismic coefficient in the soil, which may be assumed equal to
SXS /2.5.
γt = total unit weight of soil.
Hrw = height of the retaining wall.
SXS = spectral response acceleration parameter.
Lateral loads
Introduction

## Slide 36
: Coefficient of lateral earth pressure used for a level ground deposit with zero lateral strain in the soil.
Q allowable: allowable bearing capacity of soil in KN/m2.
Soil: unit weight of soil in KN/m3.
W: is surcharge load on the soil (weight of vehicles) and it’s assumed to be 12 KN/m2
Q allowable =473 KN/m2
Site Class: B
=300
=20 KN/m3
SXS =0.5
=0.2
Lateral loads
Introduction

## Slide 37
Since there are two levels of mat, two cases of soil pressure is obtained.
Lateral loads
 | Case 1 | Case 2
Height of wall in m | 14.04 | 12.48
in KN/m2 | 22.464 | 19.968
in KN/m2 | 6 | 6
in KN/m2 | 146.4 | 130.8
 | Case 1 | Case 2
Height of wall in m | 14.04 | 12.48
 | 22.464 | 19.968
 | 6 | 6
 | 146.4 | 130.8
Table 1.12: Soil pressure cases
Introduction

## Slide 38
Ultimate load combinations
Load combinations
Table 1.13: Ultimate load combinations
Introduction

## Slide 39
Service load combinations (ASCE7-10)
1. D
2. D + L
3. D + (Lr or S or R)
4. D + 0.75L + 0.75(Lr or S or R)
5. D + (0.6W or 0.7E)
6a. D + 0.75L + 0.75(0.6W) + 0.75(Lr or S or R)
6b. D + 0.75L + 0.75(0.7E) + 0.75S
7. 0.6D + 0.6W
8. 0.6D + 0.7E
Load combinations
Introduction

## Slide 40
Where:
D: Dead load.
L: Live load.
Lr: Roof live load.
S: snow load.
R: Rain load.
W: Wind load.
E: Earthquake load.
H: load due to lateral earth pressure, ground water pressure, or pressure of bulk materials.
Load combinations
Introduction

## Slide 41
Analysis and Design assumptions:
The foundation is mat.
Exterior walls will be modeled as shear walls, in order to have seismic resistance building.
Interior walls and partitions will not be modeled but there load has been taken in consideration as superimposed dead load of 1.5 KN/m2.
There are no tie beams since mat foundation is used.
The ultimate strength design method will be used in the design process of this project. In the strength design method, actual loads or working loads are multiplied by load factor to obtain the ultimate design loads. The load factor represents a high percentage of factors for safety required in the design.
A three dimensional model will be used with all accurate dimensions.
Beams and columns are represented by line elements while slabs and walls are represented by area elements.
The masonry cladding will be applied external reinforced concrete walls as superimposed dead load.
Response spectrum method will be used for seismic forces computations.
Analysis and design principles
Introduction

## Slide 42
Slab preliminary design:
Two panels were chosen, as follows:
Panel 1
Preliminary design
Figure 2.1: Panel 1 in ground floor.
Preliminary Design

## Slide 43
Assume fm < 2
Moments of inertia were found for slab and beams as follows
I-beam-T = 3.412528 × 10-3 m4.
I-beam-L = 3.185796 × 10-3 m4.
I-slab –x- int = b h3 = × 6.15 × 0.173 = 2.52 × 10-3 m4.
I-slab –x- ext = b h3 = × 2.05 × 0.173 = 8.39 × 10-4 m4.
I-slab –y1- int = b h3 = × 8.2 × 0.173 = 3.36× 10-3 m4.
I-slab –y2- int = b h3 = × 6.95 ×0 .173 = 2.85 × 10-3 m4.
Preliminary design of slab
Preliminary Design

## Slide 44
fm
fm 1 = = = 1.354.
fm 2 = = = 1.015.
fm 3 = = = 3.79.
fm 4 = = = 1.19.
fm avg = 1.8 < 2 ok
H should not be less than H = ≥ 125
H= 114<125 , Assume h =0.17m
Preliminary design of slab
Preliminary Design

## Slide 45
Panel 2
Preliminary design of slab
Figure 2.2: Panel 2 in ground floor.
Preliminary Design

## Slide 46
Assume fm < 2
I-beam-T = 1.4389866 × 10-2 m4.
I-beam-L = 1.2924039 × 10-2 m4.
I-slab –x = b h3 = × 6.15 × 0.253 = 8 m4.
I-slab –y1-int = b h3 = × 9.45 × 0.253 =12.3 m4.
I-slab –y2-int = b h3 = × 9.45 × 0.253 =10.67 m4.
fm =
Preliminary design of slab
Preliminary Design

## Slide 47
fm 1 = = = 1.8
fm 2 = = = 1.17
fm 3 = = = 1.8
fm 4 = = = 1.35
fm avg = 1.53 < 2 ok
H should not be less than:
H = ≥ 125
H = 0.239, use h slab = 0.25m.
Preliminary design of slab
Preliminary Design

## Slide 48
Minimum depth of non prestressed beam according to ACI318-14 Table 9.3.1.1 = = = 51 cm , use 55 cm as preliminary beams depth
The width of beams can be assumed or L/20 can be used as an indication, = = 53.5 cm, to be conservative width of 80 cm was used.
Preliminary design of beams
Figure 2.3: Frame C-C in x-direction in second floor.
Preliminary Design

## Slide 49
Preliminary design of columns
Figure 2.4: Columns plan in fourth basement.
Preliminary Design

## Slide 50
Column 39 was chosen as representative for interior columns preliminary dimensions.
Preliminary design of columns
Figure 2.5: Column 39 location and tributary area.
Preliminary Design

## Slide 51
Tributary area around the column =
Total dead and superimposed dead load =5456.25 + 850.5 + 701.1 +4626.9=11634.75 KN.
To take columns own weight into consideration we multiply total dead load by 1.10.
Total dead load = 11634.75 1.1=12798.225 KN.
Total live load = 2572.44KN.
Preliminary design of columns
Preliminary Design

## Slide 52
Ultimate load = 1.2D +1.6L
= (1.212789.225) +(1.62572.44)= 19473.774 KN
=
Where:
Pu : Ultimate axial strength of cross section.
Fc : Concrete compressive strength.
Fy : Steel yield strength.
: Rebar percentage assumed to be 1%
: Strength reduction factor =0.65 .
Ag=Gross area of concrete section .
= =1203082.928 mm2
=1096.8 mm
Column dimension = 1100 mm
Preliminary design of columns
Preliminary Design

## Slide 53
Column C5 was chosen as representative of edge columns.
Preliminary design of columns
By following the same procedure edge columns preliminary dimensions were 700 700 mm.
Figure 2.6: Column 5 location and tributary area.
Preliminary Design

## Slide 54
Columns preliminary dimensions are shown in the following table (referring to columns plan).
Preliminary design of columns
Table 2.1: Columns dimensions.
Preliminary Design

## Slide 55
In this project there was three types of walls
Exterior walls: Made of reinforced concrete with masonry stone cladding with a preliminary thickness of 350 mm, (250 mm reinforced concrete + 60 mm plain concrete + 40 mm stone).
Interior walls: Surrounding elevators and staircases, these have a preliminary thickness of 300 mm.
Basement walls: In preliminary design, the thickness of walls are assumed to be 400 mm for fifth and fourth basements, 350 mm for third and second basements and 300 mm for first basement.
Preliminary design of walls
Preliminary Design

## Slide 56
Preliminary design
Figure 2.7: Fourth basement floor framing plan.
Preliminary Design

## Slide 57
Preliminary design
Figure 2.8: Ground floor framing plan.
Preliminary Design

## Slide 58
Preliminary design
Figure 2.9: Fifth floor framing plan.
Preliminary Design

## Slide 59
Three Dimensional Analysis and Design
Figure 3.1: Three dimensional model of the building.
3D Analysis and Design

## Slide 60
Modifiers
Three Dimensional Analysis and Design
Figure 3.3: Modifiers used in column sections.
Figure 3.2: Modifiers used in beam sections.
3D Analysis and Design

## Slide 61
Three Dimensional Analysis and Design
Figure 3.4: Modifiers used in slab sections.
Figure 3.5: Modifiers used in wall sections.
3D Analysis and Design

## Slide 62
Load patterns and cases
Three Dimensional Analysis and Design
Figure 3.6: Load patterns.
Figure 3.7: Load cases.
3D Analysis and Design

## Slide 63
Springs and mass source
Three Dimensional Analysis and Design
Figure 3.9: Mass Source.
Figure 3.8: Spring assignment.
3D Analysis and Design

## Slide 64
Load pattern | Hand result (KN) | ETABS result (KN) | Difference %
Dead load | 311002.4324 | 304141.9225 | 2.2
Superimposed load | 125316.374 | 123796.7829 | 0.722
Live load | 57704.81 | 57671.927 | 0.057
Snow load | 1489.8 | 1489.7902 | 0
Soil Pressure | 17173.45 | 17177.94 | 0.026
Wind load X | 1065.77 | 1069.27 | 0.33
Wind load Y | 1603.19 | 1441.48 | 10
Seismic load X | 18481.66 | 18443.89 | 0.204
Seismic load Y | 15792.13 | 15766.73 | 0.16
Verification of Structural Analysis
Equilibrium checks
Table 3.1: Equilibrium Check.
3D Analysis and Design

## Slide 65
Story forces from wind load
Verification of Structural Analysis
Floor | Hand result (KN) | ETABS result (KN) | Difference %
Sixth floor X | 97.49 | 104.29 | 6.88
Sixth floor Y | 150.13 | 160.48 | 6.89
Seventh floor X | 100.15 | 118.59 | 18.4
Seventh floor Y | 105.82 | 103.25 | 2.42
Table 3.2: Story forces from wind load.
3D Analysis and Design

## Slide 66
Story forces from seismic load
The lateral seismic force (Fx) in KN induced at any level shall be determined from the following equations:
And
Where
Cvx = vertical distribution factor
V = total design lateral force or shear at the base of the structure (KN)
wi and wx = the portion of the total effective seismic weight of the structure (W) located or assigned to level i or x and it was taken from the mass source in KN
hi and hx = the height (m) from the base to level i or x
k = an exponent related to the structure period, as follows:
For structures having a period of 0.5 s or less, k = 1.
For structures having a period of 2.5 s or more, k = 2.
Since the period in x direction =0.718 sec, interpolation was obtained to get the value of Kx
Kx= 1.109
Verification of Structural Analysis
3D Analysis and Design

## Slide 67
Story forces from earthquake load
Verification of Structural Analysis
Story | Story force from hand calculation (KN) | Story force from ETABS (KN) | %Difference
Stair Case 35.6 | 170.83 | 170.59 | 0.142
ROOF 31.98 | 1326.12 | 1325.11 | 0.076
8th Floor 28.6 | 1614.98 | 1613.6 | 0.085
7th Floor 25.22 | 1916.83 | 1915.3 | 0.079
6th Floor 21.84 | 2071.47 | 2069.8 | 0.080
5th Floor 17.16 | 1882.90 | 1881.3 | 0.084
4th Floor 14.61 | 1842.27 | 1840.3 | 0.107
3rd Floor 10.92 | 1775.77 | 1775 | 0.043
2nd Floor 7.28 | 1532.38 | 1531 | 0.089
1st Floor 3.76 | 1325.93 | 1325 | 0.070
Ground Floor 0.00 | 963.91 | 963 | 0.094
1st Basement -2.34 | 389.49 | 389 | 0.125
1st Basement -3.9 | 359.91 | 353 | 1.919
2nd Basement -5.46 | 330.72 | 331 | 0.084
2nd Basement -7.02 | 288.13 | 288 | 0.044
3rd Basement -8.58 | 234.50 | 234 | 0.211
3rd Basement -10.14 | 190.62 | 190 | 0.325
4th Basement -11.7 | 136.88 | 137 | 0.090
4th Basement -13.26 | 90.26 | 90 | 0.287
Table 3.3: Story forces from earthquake load.
3D Analysis and Design

## Slide 68
Equivalent static versus dynamic response spectrum
Before modification of scale factor
In the X direction =
In the Y direction =
After modification
In the X direction =
In the Y direction =
Verification of Structural Analysis
3D Analysis and Design

## Slide 69
Period was calculated in three different ways
1- An approximate fundamental period, Ta, is determined according to equation (12.8-7) ASCE7-10
Ta = Ct
Where:
hn is the structural height.
Ct and x are coefficients determined from Table 12.8-2 ASCE7-10 as shown below
Ct =0.0488
x= 0.75
hn= 52 m
Ta=0.0488 =0.945 second.
2- From ETABS results in x and y directions
Period in x = 0.718 sec.
Period in y = 0.84 sec.
Verification of Structural Analysis
3D Analysis and Design

## Slide 70
3- From Rayleigh
In X direction
Tn=2
Where
W: Weight of floor from mass source in KN.
: Average displacement in each floor.
F: Force in each floor from ETABS in KN, after applying a force of 1 KN/m2 in each floor.
Tn= 0.582 sec.
Verification of Structural Analysis
3D Analysis and Design

## Slide 71
% Difference between Rayleigh and ETABS = 100 %
= 100% = 23.36 %
In Y direction
Tn = 2 = 0.674 sec.
% Difference between Rayleigh and ETABS = 100 %
= 100% = 24.29 %
Verification of Structural Analysis
3D Analysis and Design

## Slide 72
Mass participation ratio for modal analysis
Verification of Structural Analysis
Figure 3.2: Periods in x and y directions from ETABS.
3D Analysis and Design

## Slide 73
Verification of Structural Analysis
Figure 3.3: Sum Ux and Uy from ETABS.
3D Analysis and Design

## Slide 74
1- Horizontal structural irregularities
Structural irregularities
Table 3.4: Horizontal structure irregularities.
3D Analysis and Design

## Slide 75
2- Vertical structural irregularities
Structural irregularities
Table 3.5: Vertical structure irregularities.
3D Analysis and Design

## Slide 76
Slabs and beams
Shear check for slab:
For 250 mm slab thickness
∅𝑉𝑐 = × Ø× √𝑓′𝑐 ×𝑏𝑤×𝑑
Where
∅𝑉𝑐: shear capacity in KN.
∅: shear modification factor =0.75.
𝑓′𝑐: concrete compressive strength in MPa.
bw: width of slab section in mm.
d: effective depth in mm .
∅𝑉𝑐 = × 0.75× √28 × ×210= 138.9 KN.
For 170 mm slab thickness
∅𝑉𝑐= × Ø× √𝑓′𝑐 ×𝑏𝑤×𝑑
= × 0.75× √28 × ×130= 86 KN.
    Verification of internal forces
3D Analysis and Design

## Slide 77
    Verification of internal forces
V13 for 250 mm slab , <
Figure 3.4: V13 for 250 mm slab (KN).
3D Analysis and Design

## Slide 78
    Verification of internal forces
V13 for 170 mm slab , <
Figure 3.5: V13 for 170 mm slab (KN).
3D Analysis and Design

## Slide 79
Moment check:
Frames in x and y directions were chosen, moments by hand and from ETABS were obtained and compared.
    Verification of internal forces
Figure 3.6: Frames in x and y directions.
3D Analysis and Design

## Slide 80
M live, hand = = = 106 KN.m
M live, ETABS = + Moment at middle of span
=+ 47.3484 =107.1 KN.m
% Difference in moment 11 = 100 % =
= 100 % = 1.03 %
    Verification of internal forces
3D Analysis and Design

## Slide 81
Columns
Column C38 was chosen to check axial loads from dead, superimposed, live and snow loads, the column and its tributary area
    Verification of internal forces
Figure 3.7: Column C38 used for internal force check.
3D Analysis and Design

## Slide 82
Pultimate = 1.2 Dead +1.2 SD + 1.6 Live +0.5 Snow
From ETABS ultimate axial load = 11038.5888 KN
% Difference in axial load on column 38 = 100 %
=
    Verification of internal forces
3D Analysis and Design

## Slide 83
Immediate and long term deflections
Here, immediate deflection due to live load and long term deflection will be checked according to ACI 318-14.
Long term deflection:
𝛥LT= 𝛥L + 𝜆∞ 𝛥D+𝜆t 𝛥LS
Where
𝛥LT: long term deflection.
𝛥L: Immediate deflection due to live load.
𝛥D: Immediate deflection due to dead load.
𝛥LS: Immediate deflection due to sustained live load.
𝜆∞: Time dependent multiplier for infinite duration of sustained load.
𝜆t: Time dependent multiplier for limited load duration.
    Deflection Check
3D Analysis and Design

## Slide 84
𝜆 =
𝜆t= 𝜆∞= = 2
𝛥LT= 𝛥L + 2 𝛥D+ (2 𝛥LS = 2 𝛥D + 1.5 𝛥L
Deflection check for slab thickness 250 mm
D at center = 21.698 mm.
Avg. D at corners = = 7.6215 mm.
D = D at center - Avg. D at corners = 14.0765 mm.
    Deflection Check
3D Analysis and Design

## Slide 85
    Deflection Check
Figure 3.8: Deflection from dead load for slab thickness 250 mm (mm).
3D Analysis and Design

## Slide 86
LT, max = (2 + (1.5 = 35.75 mm.
LT, allowable =
Where
LT, allowable: allowable long term deflection, L: longest span length.
LT, allowable = = 44.58 mm LT, max  Adequate
Immediate deflection:
L, max = 5.0655 mm.
L, allowable =
Where
L, allowable: allowable deflection due to live load ,L: longest span length.
L, allowable = = 29.72 mm > L, max  Adequate.
    Deflection Check
3D Analysis and Design

## Slide 87
There are two types of drifts.
1. Elastic drift.
2. Inelastic drift.
According ASCE 7-10
Plastic = elastic
Plastic drift in each story should be smaller than the allowable story drift according to ASCE 7-10 which equals 0.015
    Story drift, elastic and plastic deflection
3D Analysis and Design

## Slide 88
For all stories elastic max < allowable  Adequate.
Table 3.6: The values of plastic and elastic drifts.
3D Analysis and Design

## Slide 89
    Design of Slabs
14 Slabs.
Two slab thicknesses:
Slab 250 mm.
Slab 170 mm.
Column and middle strips were taken into consideration in directions x and y.
Second Floor was taken as a sample
3D Analysis and Design

## Slide 90
Figure 3.9: Strips Moment for second floor slab in x-direction (KN.m).
    Design of Slabs
3D Analysis and Design

## Slide 91
    Design of Slabs
Figure 3.10: Strips Moment for second floor slab in y-direction (KN.m).
3D Analysis and Design

## Slide 92
    Design of Slabs
Figure 3.11: Area of steel for second floor from ETABS in direction x and y (.
3D Analysis and Design

## Slide 93
    Design of Slabs
Figure 3.12: Slab reinforcement for second floor in x direction.
3D Analysis and Design

## Slide 94
Figure 3.13: Slab reinforcement for second floor in y direction.
    Design of Slabs
3D Analysis and Design

## Slide 95
    Design of Beams
14 floors.
Different beam sections (width × depth) :
800 × 550 mm.
800 × 500 mm.
300 × 550 mm.
Beams are in x and y directions.
Beam B4 in fifth floor was taken as a sample.
3D Analysis and Design

## Slide 96
    Design of Beams
Figure 3.14: Beam B4 in fifth floor
3D Analysis and Design

## Slide 97
    Design of Beams
Figure 3.15: Longitudinal reinforcement in B4 (
3D Analysis and Design

## Slide 98
    Design of Beams
Figure 3.16: Transverse reinforcement in B4.
3D Analysis and Design

## Slide 99
    Design of Beams
Figure 3.17: Beam B4 reinforcement in fifth floor.
3D Analysis and Design

## Slide 100
    Design of Columns
14 floors.
Columns dimensions ranges from (700 × 700) mm to (1300 × 1300) mm, as follows :
Column C23 in first floor was taken as a sample.
Table 3.7: Columns dimensions.
3D Analysis and Design

## Slide 101
    Design of Columns
Figure 3.18: Columns layout in first floor.
3D Analysis and Design

## Slide 102
    Design of Columns
Figure 3.19: Column C23 reinforcement in first floor from ETABS (.
3D Analysis and Design

## Slide 103
    Design of Columns
Figure 3.20: Column C23 reinforcement in first floor.
3D Analysis and Design

## Slide 104
    Design of Walls
14 floors.
Different walls sections :
W400 mm.
W350 mm.
W300 mm.
W200 mm.
W3 was taken as a sample.
Figure 3.21: Walls in the structure.
3D Analysis and Design

## Slide 105
    Design of Walls
Figure 3.22: Longitudinal reinforcement in W3 (.
Figure 3.23: Shear reinforcement in W3 (.
3D Analysis and Design

## Slide 106
    Design of Walls
Figure 3.24: Wall W3 location.
3D Analysis and Design

## Slide 107
    Design of Walls
Figure 3.25: Wall W3 reinforcement details.
3D Analysis and Design

## Slide 108
    Design of Footings
Area of floor = 1886 .
=
in addition there is the earthquake effect so
mat foundation is used.
The maximum ultimate compression force on columns equals 18453 for column C24.
Assume mat foundation thickness h= 1500 mm and d=1400 mm.
The punching shear force Vult = 18453 KN
The punching shear capacity Vc is given by:
Area of footing = =
3D Analysis and Design

## Slide 109
Vu should be less than or equals .
,
.
Adequate
= 1408 KN.m
= 41.7 mm.
    Design of Footings
3D Analysis and Design

## Slide 110
Where:
: Yielding strength of steel in Mpa.
: Concrete compressive strength in MPa
Mu: Ultimate moment in KN.m.
b: Width of strip in footing in mm.
d: Effective depth of footing section in mm.
Area of steel in mm2.
: Strength factor =0.9.
minimum area of steel was used =
area of steel used = .
    Design of Footings
3D Analysis and Design

## Slide 111
    Design of Footings
Figure 3.26: Mat foundation from ETABS
3D Analysis and Design

## Slide 112
    Design of Footings
Figure 3.27: Ultimate moment M11 on Mat (KN.m).
3D Analysis and Design

## Slide 113
    Design of Footings
Figure 3.28: Ultimate moment M22 on Mat (KN.m).
3D Analysis and Design

## Slide 114
    Design of Footings
Figure 3.29: Reinforcement of mat in X direction.
3D Analysis and Design

## Slide 115
    Design of Footings
Figure 3.30: Reinforcement of mat in Y direction.
3D Analysis and Design

## Slide 116
There are 3 different staircases.
    Design of Stairs
Figure 3.31: Staircases 1, 2 and 3.
3D Analysis and Design

## Slide 117
    Design of Stairs
3D Analysis and Design
W Dead =3.75 KN/m2.
W Live according to table 4.1 ASCE7-10 = 5 KN/m2.
W Superimposed dead = 5.3 KN/m2.
W ultimate =1.2(WD+WSD )+1.6(WL )
W ultimate =1.2(3.75+5.3)+1.6(5)=18.86 KN
M ultimate = = 32.3 KN.m

## Slide 118
    Design of Stairs
Figure 3.32: Section A-A in staircases 1 detailing.
3D Analysis and Design

## Slide 119
Beams and slabs
1- Shear
Vu was taken from ETABS.
Vc = ʎ bw d
Vs = – Vc
=
min = max of ( , )
    Design Verification
3D Analysis and Design

## Slide 120
Where:
𝑉𝑐: shear capacity in KN.
Vu: ultimate shear force in KN.
Vs: nominal shear strength provided by shear reinforcement.
Av: area of vertical legs in stirrup.
S: spacing between stirrups.
Fyt: steel yield strength of stirrups.
∅: shear modification factor =0.75.
𝑓′𝑐: concrete compressive strength in MPa.
bw: width of slab section in mm.
d: effective depth of reinforced concrete section in mm
    Design Verification
3D Analysis and Design

## Slide 121
2- Moment
Mu was taken from ETABS.
= (1- )
= max of ( )
=
As = x b x d
    Design Verification
3D Analysis and Design

## Slide 122
Where:
Mu: Ultimate moment in KN.m
Fc`: Compressive strength of concrete in Mpa.
Fy: Yielding strength of steel in Mpa.
b: Width of slab in mm.
d: Effective depth of slab section in mm.
: Area of steel in mm2
Ultimate moment in KN
: Strength factor =1
= steel ratio.
    Design Verification
3D Analysis and Design

## Slide 123
    Design Verification
3- Torsion
Tu was taken from ETABS.
Tth = Ø ʎ
=
Where:
Tth = Threshold torsion
Acp = Area enclosed by outermost perimeter of concrete cross section in mm2
Pcp = Outside perimeter of concrete cross section in mm
ʎ = Factor to account for light weight concrete, in this case we have normal weight concrete ,ʎ =1
Ao = Area enclosed by centerline of the outermost closed transverse torsional reinforcement in mm2.
3D Analysis and Design

## Slide 124
    Design Verification
Walls and Columns
Axial and moment
Pu and Mu1,2 were taken from ETABS.
Bresler reciprocal load method :
= + -
Where:
: Axial capacity of column section in KN.
: Axial capacity of column section in direction x at first end of the column in KN corresponding to Mux1
: Axial capacity of column section in direction x at second end of the column in KN
corresponding to Mux2
: Axial capacity of column section in direction y at first end of the column in KN
corresponding to Muy1
: Axial capacity of column section in direction y at second end of the column in KN corresponding to Muy2
3D Analysis and Design

## Slide 125
    Design Verification
Foundation
1- Punching shear
Vu was taken from ETABS.
Where:
Short side of column dimensions / long side of column dimension.
: Concrete compressive strength in MPa
: The perimeter of the critical section, for interior column:
= .
40 for interior column, 30 for edge column, 20 for corner column
: Effective depth
3D Analysis and Design

## Slide 126
    Design Verification
2- Moment : as in beams.
3- Soil pressure under the foundation
Soil pressure from ETABS < Q allowable , the values of soil pressure under the mat foundation is less than allowable bearing capacity of the soil so the area is adequate
3D Analysis and Design

## Slide 127
    Seismic provisions for detailing
1- Beams
At both ends of the beam, hoops shall be provided over lengths not less than 2h measured from the face of the supporting member toward mid span. The first hoop shall be located not more than 50 mm from the face of the supporting member. Spacing of hoops shall not exceed the smallest of (a) and (b);
(a) d/4 (b) 150 mm.
Where
h : depth of beam section.
d : effective depth of beam section
Beams shall have at least two of the longitudinal bars continuous along both the top and bottom faces. These bars shall be developed at the face of support.
Clear spacing between longitudinal bars shall be at least the greatest of
(25 mm , db , dagg )
3D Analysis and Design

## Slide 128
    Seismic provisions for detailing
2- Columns
Length lo shall not be less than the largest of (a), (b), and (c):
(a) One-sixth of the clear span of the column.
(b) Maximum cross-sectional dimension of the column.
(c) 450 mm.
Beyond the length lo, the column shall contain hoop reinforcement not exceeding the smallest of (a) through (c):
(6 db , 48 ds , Least column dimension , 150 mm)
Where:
db: diameter of bar.
ds: diameter of stirrup.
3D Analysis and Design

## Slide 129
    Seismic provisions for detailing
Spacing of transverse reinforcement shall not exceed the smallest of (a) to (c):
(a) One-fourth of the minimum column dimension
(b) Six times the diameter of the smallest longitudinal bar
(c) So as calculated by:
So = 100 +
Where
hx: largest distance between stirrups legs
The value of So shall not exceed 150mm and need not be taken less than 100mm.
3D Analysis and Design

## Slide 130
Thank you for listening