## Slide 1: Environmentally friendly bike lane network in Nablus
An-Najah National University
  Faculty of Engineering and Information Technology
Prepared by:
Diala Juma
Batool Al-Tanbour
Under supervision of:
Dr. Khaled Al-Sahili

## Slide 2: Objectives
Designing a network of bicycles or electric bikes lanes between the two campuses of An-Najah National University (old and new campuses) to the city center area.
To know the range of people who use bicycles or electric bicycles or their willingness to use them, specifically An-Najah National University students.
To assess the suitability of the existing road network to the use of bicycles or electric bicycles, and based on that, to set standards for designing an appropriate bicycle network.
The General objectives
The particular objectives

## Slide 3: Methodology
Specifying Study Area
Collection of Data
Data Analysis
Network Design

## Slide 4: Specifying the Study Area

## Slide 5: Data Collection
Traffic Volume Study
Obtain Maps
Inventory Study
Questionnaire

## Slide 6: Vehicular Peak Hour Volume
Traffic Volume Study
Total (veh/hr) | Westbound (veh/hr) | Eastbound (veh/hr) | Peak hour | Street name
2056 | 895 | 1161 | 7:15-8:15 Am | Rafedia Street
426 | --- | 426 | 7:15-8:15 Am | Al-Shwetreh Street
1971 | 952 | 1019 | 7:15-8:15 Am | Omar Ibn Al-Khattab Street
1120 | --- | 1120 | 7:15-8:15 Am | Ghernatah Street
1031 | 1031 | --- | 7:15-8:15 Am | Palestine Street

## Slide 7: Intersections' Level of Service
Rafedia Street |  |  |  |  |  |  |  |  |  |  | 
Intersection # | 1 | 2 | 3 |  | 4 | 5 | 6 | 7 | 8 |  | 9
LOS | A | A | F |  | C | F | F | F | B |  | D
Intersection # | 10 | 11 | 12 |  | 13 | 14 | 15 | 16 | 17 |  | 18
LOS | F | F | D |  | F | B | A | E | F |  | A
Omar Ibn Al-Khattab Street |  |  |  |  |  |  |  |  |  |  | 
Intersection # | 1 | 2 | 3 |  | 4 | 5 | 6 | 7 | 8 |  | 9
LOS | E | A | F |  | A | A | F | F | F |  | F
Ghernatah Street |  |  |  |  |  |  |  |  |  |  | 
Intersection # | 1 |  |  |  |  |  | 2 |  |  |  | 
LOS | C |  |  |  |  |  | F |  |  |  | 
Palestine Street |  |  |  |  |  |  |  |  |  |  | 
Intersection # | 1 |  |  | 2 |  |  | 3 |  |  | 4 | 
LOS | F |  |  | F |  |  | F |  |  | C | 
Al Shwetreh Street |  |  |  |  |  |  |  |  |  |  | 
Intersection # | 1 |  |  |  |  |  | 2 |  |  |  | 
LOS | A |  |  |  |  |  | C |  |  |  | 

## Slide 8: Inventory Study
Pavement condition
No. of lanes
Traffic Signals and Signs
Parking
Sidewalks

## Slide 9
Questionnaire Analysis

## Slide 10
Questionnaire Analysis

## Slide 11
Design Criteria
Functional Classification
Design Vehicle
Elements of Design
Bike Lanes
On-Street Parking
Signs and Marking
Grades
Drainage
Drainage

## Slide 12: Rafedia Street (An-Najah National University Street (New Campus)) Design

## Slide 13: Rafedia Street(At Rafedia Old Mosque) Design

## Slide 14: Al-Shwetreh Street Design

## Slide 15: Omar Ibn Al-Khattab Street (Near An-Najah National University (Old Campus)) Design

## Slide 16: Ghernatah Street Design

## Slide 17: Palestine Street Design

## Slide 18: Conclusions
Difficulties
The Work Process
Vehicles Reduction

## Slide 19: the end Thank you for listening