## Slide 1
Single Phase PV-STATCOM Using Multilevel Inverter

## Slide 2
Outline
Overview.
Power factor.
photovoltaic system.
Static synchronous compensator.
Control techniques.
Methodology and results.
-P.V system design .
-Design and simulation of DSTATCOM.
-H-bridge with PI PWM.
-H-bridge with hysteresis. -H-5 with PI PWM.
-Cascaded H-bridge with PI Level shifted PWM.
Recommendation and future work.

## Slide 3
Overview.
power systems are facing a number of power quality problems that classified as voltage and current quality problems. There are a number of current power quality problems such as :-
  Poor power factor .
  Poor voltage regulation.
  Harmonics .

## Slide 4
Power Factor.
Problem of poor power factor:
    High current for suppling the load.
    high cost of equipment's .
    High losses .
    Drop voltage.
P.F is the ratio of the real power absorbed by the load to the apparent power.

## Slide 5
Power factor improvement.
1)Static VAR compensator.
is a set of electrical devices for providing fast-acting reactive power using capacitors and controller . Disadvantage: -Slow response time.
-High power loss. -Low elimination for harmonics -Reactive power decreases when grid voltage . decreases. -Switching transient
-Harmonics causing capacitor overheating.

## Slide 6
SYNCHRONOUS CONDENSERS.
A synchronous condenser is a synchronous device that produces reactive power which leads real power by 90.
Disadvantage . - Higher energy losses. -Limited voltage support.
-Produces noise.
- Maintenance cost is high. -Except in sizes above 500 kVA.
-No self-starting torque. - Losses in the motor.

## Slide 7
STATCOM.
A regulating device used on alternating current electricity transmission networks. Advantage: -Fast response time . -Lower power losses -Can filter the harmonics. -Not effected with drop voltage. -Can interfaced with real power sources.

## Slide 8
Photovoltaic System.
- is an energy system that is designed to transform the energy from the sun into electricity by means of photovoltaics. -Solar PV has specific advantages as an energy source: once installed, its operation generates no pollution and no greenhouse gas emissions.

## Slide 9
MPPT
Perturbation and Observation
2. IC Method

## Slide 10
Static Synchronous Compensator (STATCOM) is a reactive power compensation device that is shunt connected to the AC transmission and distribution systems.
STATCOM.

## Slide 11
Layout system.

## Slide 12
Control techniques.
The main objective of a control algorithm of DSTATCOMs is to estimate the reference currents
using feedback signals.
There are many control algorithms of DSTATCOMs such as:
    -SRF(d-q) -IRPT(-)

## Slide 13
SRF(d-q).

## Slide 14
IRPT(-).

## Slide 15
Gating controlling
PI controller with PWM

## Slide 16
Hysteresis controller
Gating controlling

## Slide 17
Methodology and results.
P.V system design.

## Slide 18
D-Statcom
H bridge PI PWM
Night Mode Linear
Night Mode Nonlinear
H bridge Hysteresis
Cascaded H bridge
H5
Nonlinear Load
Linear Load
Nonlinear Load
Linear Load
Night Mode Linear
Night Mode Nonlinear
Nonlinear Load
Linear Load
Night Mode Nonlinear
Linear Load
Nonlinear Load
Night Mode Linear
Design of DSTATCOM.

## Slide 19: H-bridge PI PWM with Linear Load
Methodology and results.

## Slide 23: H-bridge With PI PWM Non Linear Load

## Slide 26: Night mode PWM with Linear load

## Slide 29: Night mode PWM with non linear load

## Slide 32: H-bridge hysteresis With Linear Load

## Slide 35: H-bridge hysteresis with non linear load

## Slide 38: Night Mode hysteresis With linear load

## Slide 41: Night mode hysteresis with nonlinear load

## Slide 44
H-5 bridge.

## Slide 45: H5 PI PWM With Linear Load

## Slide 48: H5 PI PWM with nonlinear load

## Slide 51
Cascaded H-bridge.

## Slide 52: Cascaded H-bridge Multilevel inverter Level Shifted PWM with linear load

## Slide 55: Cascaded H-bridge Multilevel inverter Level Shifted PWM with non linear load

## Slide 58: Night Mode Cascaded H-bridge Multilevel inverter with linear load

## Slide 61: Night Mode Cascaded H-bridge Multilevel inverter with nonlinear load

## Slide 64
Recommendations & future work.
Building the H-Bridge with PI PWM and its gate drives and control this H-Bridge using MATLAB Simulink and Arduino controller.