## Slide 1: Analysis and design of the conference center of the Islamic university
Abd Alrahman Qadri Abu Eideh Izzideen Qaysar Yaish Manar Abd Alhameed Abu Zahra
Mohammed Zidan Masri Sabeeh Zidan Masri

## Slide 2: Contents
Introduction
Preliminary Design
3D Static Analysis and Design
3D Dynamic Analysis and Design
Concrete design
Steel design

## Slide 3: Project Description
Location
It is located at west of Nablus at 800 m elevation above mean sea level. It’s extended over an area 7800 m2
Stories and usage
Floor Name | Function | Area () | Hieght (m)
Basement | VIP Restaurant | 7820 | 6.3
Ground | main conference hall | 7679 | 7.5
First | Manager Secretarial | 7409 | 4.7
Floor Name | Function |  | Hieght (m)
Basement | VIP Restaurant | 7820 | 6.3
Ground | main conference hall | 7679 | 7.5
First | Manager Secretarial | 7409 | 4.7

## Slide 5: Codes and Standards
American Concrete Institute (ACI 318-14).
American Society of Civil Engineers (ASCE 7-10).
American Institute of Steel Construction (AISC 360-16).

## Slide 6: Materials
Reinforcement Concrete
Rebar Steel
Structural Steel
Roof Sheeting
Glass
Bolts
Weld

## Slide 7: Loads Types
Dead Load
Superimposed dead load
Live Load
Snow Load
Wind Load
Earthquake load

## Slide 8: SD Load
In our structure, it is about these elements:
SD on concrete Slabs (tiles, partitions, false ceiling,…etc)
Steel Roof (solar panels, lighting and HVAC system)

## Slide 9: Wind Load
Z (qz) = 0.0613 * Kz * Kzt * Kd * V2 *I
Kd: Directionality factor. Kzt: Topographic factor. Kz: Pressure-exposure coefficient depends on roughness, exposure and the height. I: Importance factor depends on occupancy type. v: basic wind speed (m/sec)

## Slide 10: Wind Load
Kd = 0.85 Kzt = 1 v = 140 km/hr = 36.11 m/sec I = 1.25
Kz= 1.25 (Roughness C and Exposure C)
P design = P ext - P int
Pint or ext = qz* G * Cp
G: Gust factor.
Cp: pressure coefficient.

## Slide 11: Loads values
Superimposed dead load
4 kN/m2
Live load
Slabs = 4.8 kN/m2
Stadium = 5 kN/m2
Steel roof = 1 kN/m2
Snow load
Steel roof = 1 kN/m2
Wind X-direction
Walls = -0.95 kN/m2
Roof = -1.16 kN/m2
Wind Y-direction
Wind ward = 1.06 kN/m
Lee ward = -0.64 kN/m
Roof =-0.75 kN/m

## Slide 12: Combinations
Strength Combinations
Service Combinations

## Slide 13: Preliminary Design
Slabs
Columns
Beams

## Slide 14: Beams
Critical span is 9.6 m long.
h (beams) = 9.6/18.5 = 0.51 m.
but due to deflection requirements, the selected depth of the beam is 800 mm.

## Slide 15: Slab
Starting by 25 cm thickness solid slab.
For deflection requirements, the depth of the slab is 36 cm.
For practical application, the slab is decided to be U-boot slab with total thickness of 40 cm

## Slide 16: Columns
Assume ρ = 1%
Pult =9900 kN
Area = =685774mm2
 1000*800 mm rectangular column

## Slide 17: 3D Static Analysis and Design
Modeling in SAP2000 and Etabs
Analysis Verifications
Deflection
Results

## Slide 18: Modeling
blocks 1&3
block4

## Slide 19
Block 2
block 6

## Slide 20
Block 5

## Slide 21: Analysis Verifications
Compatibility check
Deflection
Equilibrium check
Internal Forces
Dead Load
Superimposed Dead Load
Live Load

## Slide 22: Compatibility check
From the figure, it is clear that the component of the structure looks compatible with each other.
blocks 1&3
block4

## Slide 23: Compatibility check
Block 2
block 6
block 5

## Slide 24: Deflection Computations
Block 4
-Critical slab is 9.96 m long.
-Max Deflection = 35.9 mm
-Allowable deflection = L/240
=9960/240 = 41.5 mm
-Max < allowable (OK)

## Slide 25: Deflection Computations
Steel deflection limit:
Live load deflection =
Snow and wind load deflection =
Dead +Live deflection =

## Slide 26: Deflection Computations for large truss
Live load deflection :
Δallowable = 319 mm.
From SAP  Δ = 29 mm (OK)
Snow and wind load deflection :
Δallowable = 319 mm.
From SAP  Δsnow = 30 mm (OK)
Δwind = 22.80 mm (OK)
(Dead + Live) deflection :
Δallowable = 479 mm.
From SAP  Δ = 53 mm (OK)

## Slide 27: Check For Equilibrium
All blocks satisfy the equilibrium check

## Slide 28: For block 1 & 3

## Slide 29: Internal forces For block 5

## Slide 30: 3D Dynamic Analysis and Design
Mass source definition
Mass participation ratio
Period check
Seismic analysis
Seismic checks
Results

## Slide 31: Mass source definition
All SD load and 25% of live load considered as permanent mass.

## Slide 32: Mass participation ratio
the modal participation mass ratio in X and Y more than 90% after 46 Modes.

## Slide 33: Period check
 | SAP | manual | 
Block 1 & 3 | 0.43 | 0.75 | 
Block 2 | 0.64 | 0.75 | 
Block 4 & 6 | 0.52 | 0.75 | 
Block 5 | 0.54 | 0.75 | 

## Slide 34: Seismic analysis
Seismic parameters
Equivalent static definition
Response spectrum definition

## Slide 35: Seismic parameters
Site classification “B”
Seismic importance factor I = 1.25
Response modification factor R = 5
Based on Ss = 0.375, S1 = 0.1875
Fa = 1.2
Fv = 1.6125
SDS = 0.25
SD1 = 0.05
Seismic design category “B”

## Slide 37: Equivalent static definition
According to IBC-2012

## Slide 38: Response spectrum definition

## Slide 39: Seismic checks
Base shear
 | V sap (kN) | V manual (kN) | Error %
Block 1 & 3 | 2000 | 2089 | 4.5
Block 2 | 1274 | 1320 | 3.4
Block 4 & 6 | 1452 | 1406 | 3.2
Block 5 | 1916 | 1957 | 2.1

## Slide 40: Siesmic checks-Drift check
Cd =5 , I = 1.25

## Slide 41: Seismic checks
Drift check
Block 1 & 3
Block 2
 | h story | max displacement | drift | cd | cd* drft | drft allow | check
basement | 6 | 0.0001 | -0.0009 | 5 | -0.0045 | 0.12 | ok
Ground floor | 6 | 0.001 | -0.001 | 5 | -0.005 | 0.12 | ok
story1 | 6 | 0.002 | 0.002 | 5 | 0.01 | 0.12 | ok
Allowable (m) | ᶋxe | height | cd | ᶋx(m) | 
0.227 | .063 | 6.31 | 4.5 | 5.3 *10-5 | Story1
0.27 | .075 | 7.5 | 4.5 | 0.000169 | Story2
0.178 | .05 | 4.95 | 4.5 | 0.000219 | Story3

## Slide 42: Seismic checks
Allowable(m) | ᶋx(m) | height | cd | ᶋxe | 
0.06316 | 0.0034 | 6.316 | 5 | 0.00086 | Story1
0.075 | 0.0052 | 7.5 | 5 | 0.0013 | Story2
0.047 | 0.0047 | 4.7 | 5 | 0.00119 | Story3
Block 4 & 6
(m) Allowable | ᶋx(m) | height | cd | ᶋxe | 
0.1262 | 4.24E-4 | 6.31 | 2.5 | 0.000212 | Story1
0.098 | 6.92E-4 | 4.9 | 2.5 | 0.000346 | Story2
0.052 | 5.18E-5 | 2.6 | 2.5 | 0.000259 | Story3
Block 5

## Slide 43: Results
Slabs (U-Boot) | 
All | 0.4
Shear Wall | 
All | 0.3
Steel sections resulting | 
For large truss | 
Top cord | HSS 3-1/2*1-1/2*1/8
Bottom cord | HSS 10*10*5/8
Inclined | HSS 7*5*3/16
columns | HSS 9*5*3/16
Purlins | W 8*40
Bracing | HSS 4*4*1/8
Steel sections resulting | 
For small truss | 
Top cord | HSS 2*1*1/8
Bottom cord | HSS 2*2*1/8
Inclined | HSS 2*2*1/8
columns | HSS 2-1/4*2-1/4*1/8
Purlins | W 6*15
Bracing | HSS 3*3*1/8

## Slide 44: Stadium

## Slide 45: Stadium
Arches
Arches

## Slide 46: Concrete design
Slabs
Beams
Columns
Shear walls
Footings

## Slide 47: Slabs
We design 1st floor at level Z=6.316m (part 4+6)
Slab design on the X – direction :
Mu (bottom) Max on this panel = 57 KN.m
As = 758mm2/unit
design For tension , As top = As bottom = 86mm2
As=970 mm2 /unit =4ø18/unit
Mu (top) Max on this rooms = 110KN.m
As=970 mm2 /unit =4ø18/unit

## Slide 48
Slab design on the Y – direction :
Mu (bottom) Max on this panel = 53 KN.m
So As =758mm2/unit
Design for tension , As top = As bottom = 125.6mm2
As =883mm2/unit=4ø18/unit
Mu (top) Max on this rooms = 105KN.m
As=1009mm2/unit =4ø18/unit

## Slide 49: Beams
One-end continuous

## Slide 50: Beams
Two-end continuous

## Slide 51: Columns

## Slide 55: Shear walls
Vertical rebar
As = = = 375 mm2/m  Use 4Ø12/m in each side.
Horizontal rebar
As = = = 375 mm2/m  Use 4Ø12/m in each side.

## Slide 56: Footings

## Slide 57: Steel Roofs
Large Roof Truss
53,7 * 37.5 m
Truss Depth 3m
Small Roof Truss
29.2 * 16.2 m
Truss Depth 2m

## Slide 58
Large Truss

## Slide 59
Small Truss

## Slide 60: Steel member design
Tension Capacity
Compression Capacity
Moment Capacity
Lateral Torsional Buckling

## Slide 61: Tension Capacity
ØTn = Ø * Fy * Ag
ØTn: Tension capacity for the member.
Ø: Reduction factor. In tension Ø = 0.9
Fy: Yielding stress of steel.
Ag: Gross sectional area of the member.
Group | Sections Name | Etabs | 
 |  | ØTn(kN) | Tu(kN)
Top cord | HSS 3-1/2*1-1/2*1/8 | 154 | 16
Bottom cord | HSS 10*10*5/8 | 3026 | 0
inclined | HSS 7*5*3/16 | 574 | 349
column | HSS 9*5*3/16 | 674 | 380
purlins | W 8*40 | 1686 | 0
Bracing | HSS 4*4*1/8 | 255 | 30

## Slide 62: Compression Capacity
Group | Sections Name | Etabs | 
 |  | ØPn(kN) | Pu(kN)
Top cord | HSS 3-1/2*1-1/2*1/8 | 115 | 0
Bottom cord | HSS 10*10*5/8 | 2924 | 1656
inclined | HSS 7*5*3/16 | 458 | 423
column | HSS 9*5*3/16 | 542 | 33
purlins | W 8*40 | 813 | 0
Bracing | HSS 4*4*1/8 | 63 | 33

## Slide 63: Lateral Torsional Buckling
Bottom cord (HSS 10*10*5/8):
Lp = 1.76*ry* Lp = 1.76*96.6* /1000 = 4.8 m
Lb = 2.46 m <Lp.
So, no lateral torsional buckling.

## Slide 64: Moment capacity
Group | Sections Name | Etabs | 
 |  | ØMn(kN.m) | Mu(kN.m)
Top cord | HSS 3-1/2*1-1/2*1/8 | 5 | 0
Bottom cord | HSS 10*10*5/8 | 268 | 0
inclined | HSS 7*5*3/16 | 35 | 0
column | HSS 9*5*3/16 | 50 | 0
purlins | W 8*40 | 146 | 12
Bracing | HSS 4*4*1/8 | 9 | 0

## Slide 65: Steel Connections Design
Steel Connections Design

## Slide 70: Weld Design
For HSS 10*10*5/8 members:
y
L= 270 mm
For HSS 7*5*3/16 members:
y
L= 20 mm
Use L= 100 mm

## Slide 74: Base Plate Connection
Bolts material is
F1554 Gr36.

## Slide 75: At the END ..

## Slide 76: THANK YOU
THANK YOU