## Slide 1
An-Najah National University Faculty of Engineering Building Engineering Department
Graduation Project – 2
Integrated Design of Academic Library
Arab American University Library – Jenin
Prepared By: Odai BaniOdeh
Ali Khuffash
Kassab Jaber
Bader Bozeyh Project supervisor: Dr. Ahmad Saleh

## Slide 2
CONTENTS
Introduction
Selected Site
Architectural Design
Structural Design
Environmental Design
Electrical Design
Mechanical Design
Safety Design
Estimated Cost

## Slide 3: INTRODUCTION
The project is designing a library building in Arab American University – Jenin (AAUJ). This project is significant because the university campus lacks to an independent library.
The main concept of our project was to design an integrated Academic library(AAUJ), and our focus has been on Structure, Environmental, Electrical, Mechanical and Safety design to make a comfortable Library.

## Slide 4: Selected Site
Site Area : 8443 m2
The suggested land locates at the middle of the university campus to insure that the students can easily arrive the library building from any faculty.

## Slide 5: Selected Site

## Slide 6: Section A-A
Selected Site
The slope of the site is about
5% as the contour lines and section A-A show below.

## Slide 7: Selected Site

## Slide 8
Sun path at winter and the location of the sun
at 11:00 am in 21/12
Sun path at summer and the location of
the sun
at 11:00 am in 21/6
Selected Site

## Slide 9: ARCHITECTURAL DESIGN

## Slide 10: Site Plan

## Slide 11: Ground Floor

## Slide 12: First Floor

## Slide 13: Second Floor

## Slide 14: Third Floor

## Slide 15: Elevations
South-Elevation

## Slide 16: Elevations
West-Elevation

## Slide 17: Elevations
North-Elevation

## Slide 18
East-Elevation
Elevations

## Slide 19
Section A-A
Sections

## Slide 20: Sections
Section B-B

## Slide 21: Sections
Roof section
Floor and wall section

## Slide 22: STRUCTURAL DESIGN

## Slide 23
Design Codes
American Society of Civil Engineers (ASCE).
The American Concrete Institute code (ACI 318).
Uniform Building Code (UBC-97).

## Slide 24
Compressive strength of Concrete “f′c” :
    For columns and slabs f′c = 32 Mpa
    For all other elements in structure such as blinding and bracing f′c = 12 Mpa
Yielding strength of steel fy = 420 MPa.
Material Property
Soil bearing capacity = 300 KN/m2

## Slide 25
Jenin Seismic Zone is 2B, Seismic Factor Z= 0.2
Importance Factor I = 1
Stiffness Factor R = 5.5
Seismic Coefficient (Cv) = 0.2
Seismic Coefficient (Ca) = 0.2
Soil profile = SB
Seismic Design Data

## Slide 26
Super Imposed dead load (SI): 4 KN/m2
Live Load (L.L): 7 KN/m2 (for reading area) 3 KN/m2 (for other areas)
Lateral loads consider earthquake load.
Loads

## Slide 27: Design and Reinforcement of Structural Elements

## Slide 28
3D Models - Etabs

## Slide 29
Model Checks
Compatibility

## Slide 30
Model Checks
Equilibrium

## Slide 31
Model Checks
Internal Forces

## Slide 32
Cv = 0.2
Ca = 0.2
Seismic design
I = 1
R = 5.5
Base shear ( V ) = 3550 KN
Soil profile SB
Z =0.2
From Etabs
Mass participation ratio is larger than 90% in X, Y .

## Slide 33
Slab Reinforcement Details

## Slide 34
Beam Reinforcement Details

## Slide 35
Column Reinforcement Details

## Slide 36
Footing Reinforcement Details
Single Footing

## Slide 37
Shear Wall Details

## Slide 38
Stair Reinforcement Details

## Slide 39: Environmental Design

## Slide 40: Shading
Sun path and shadow on the building
shadow (8 am-18 pm) and annual sun path for the building using Ecotect

## Slide 41
Shading Devices
shadow (11am) 21st June South and east elevation
shadow (2am) 21st June west elevation

## Slide 42
Environmental Analysis
External wall layers and properties

## Slide 43
Internal wall layers and properties

## Slide 44
Floor layers and properties

## Slide 45
Ceiling layers and properties

## Slide 46
Roof layers and properties

## Slide 47
Thermal Analysis
heating and cooling loads
Monthly heating and cooling load all visible thermal zones

## Slide 49
Daylight Analysis (DF%)
Glass type used
BLUE (SGG COOL-LITE KS 746 II) with properties as follow

## Slide 50
Avg DF= 5.35%
Avg Level = 454.35 lux
Electronic library (DF%)

## Slide 51
Avg DF= 5.51%
Avg Level = 467.96 lux
Reading area 2nd floor (DF%)

## Slide 52
Summary (DF%)

## Slide 53
Acoustical Design
Sound Transmission Class (STC)
Impact Insulation Class (IIC)
STC for external wall
STC for internal wall

## Slide 54
    Acoustical Design
    Reverberation Time (RT60)
    Range RT60 for Library 0.5-1.2sec
    RT60 values for Reading area before improving :

## Slide 55
    Acoustical Design
    Improving RT60 by add Perforated metal panels

## Slide 56
    Acoustical Design
    Reverberation Time (RT60)
    RT60 values for Reading area after improving (35% of ceiling area):

## Slide 57: Electrical Design

## Slide 58: Artificial Lighting
The simulation analysis and design by “DIALux Evo 5”

## Slide 59
Entrance hall 3ed floor

## Slide 60
Reading area

## Slide 61
Discussion room

## Slide 62
Class room

## Slide 63
Ground floor lamps distribution

## Slide 64: Sound reinforcement System
Distribution of loudspeakers in multipurpose hall
Type of used loudspeaker- Control 322C

## Slide 65
    Sockets Arrangement
Ground Floor

## Slide 66
Mechanical DESIGN

## Slide 67
    Water Supply Design

## Slide 68
    Water Supply Design

## Slide 69
    Water Supply Design

## Slide 70
    Water Supply Design

## Slide 71
    Drainage System

## Slide 72
    Drainage System
    Ground Floor

## Slide 73
    Drainage System
    First Floor

## Slide 74
    Drainage System
    Second Floor

## Slide 75
    Drainage System
    Third Floor

## Slide 76
    Roof Drainage System

## Slide 77
    Storm water Drainage System

## Slide 78
    H-VAC System
    Max Cooling: 250 KW at 14:00 on 15th August
    The dimension from main duct = (1300*2400) mm

## Slide 79
    H-VAC System
    Air to Air System
    Distribution of ducts in reading area

## Slide 80
    H-VAC System
    Distribution of ducts in entrance hall
ceiling diffuser

## Slide 81
    H-VAC System
Zone | Area (m2) | Number of diffuser
Reading area first floor | 433.13 | 20
Entrance hall ground floor: | 193 | 10

## Slide 82
Safety DESIGN

## Slide 83
    Safety Design
    Ground floor movement escape

## Slide 84
    Safety System

## Slide 85
Estimated Cost

## Slide 86
Estimated Cost
The total cost of the LIBRARY is about 13.5 million NIS.
The total cost per meter square for the Library is about 2400 NIS.