## Slide 1: Redesign the Faculty of Arts at Al-Najah National University Prepared by : Anas Hatoo Isam Subhi Mohannad B’ara Under the supervision of : Dr.Sameh Mona

## Slide 2: Contents:
Introduction
Site Analysis
Architectural Design
Structural Design
Passive Design
Mechanical Design
Electrical Design
Cost survey
Conclusion

## Slide 3: Introduction

## Slide 4: Site Analysis: The site is located in Nablus city at Al- Junied region which is located 32°13'8.00" to the north and 35°14'24.05" to the east with an area around 2391.05m2 and a periphery of 196.82m.

## Slide 5: Site Plan and Parking

## Slide 6: 21/12 21/7

## Slide 7: Architectural Design

## Slide 8: The Architectural Plans

## Slide 9: The existing Ground Floor plan

## Slide 10: The new design of Ground floor

## Slide 11: The existing First Floor Plan

## Slide 12: The new Design of the First Floor

## Slide 13: The existing Second Floor Plan

## Slide 14: The New Design of Second Floor

## Slide 15: The New Third Floor Plan

## Slide 16: The Existing Fourth Floor :

## Slide 17: The new design of the fourth Floor

## Slide 18: The existing Basement Floor

## Slide 19: The new Design of Basement Floor

## Slide 20: Elevations

## Slide 21: The Existing South Elevation

## Slide 22: The new south Elevation

## Slide 23: The existing North Elevation

## Slide 24: The New north Elevation

## Slide 25: The existing East Elevation

## Slide 26: The new East Elevation

## Slide 27: The existing West elevation

## Slide 28: The new West Elevation

## Slide 29: Sections

## Slide 30: Section A-A

## Slide 31: Section B-B

## Slide 32: Structural Analysis

## Slide 33: Codes used:
The

## Slide 34: Concrete Materials:
Reinforced concrete :
Grade 25
Grade 30
Plain concrete
Grade 15
Grade 20

## Slide 35: Foundations:
Isolated Footing
Strap Footing

## Slide 36: Columns

## Slide 37: SLAB DESIGN

## Slide 38: WALLS

## Slide 39: BEAMS
Inverted Beams
Hidden Beams
Drop Beams
  Strap Beams

## Slide 40: Detailing

## Slide 41: STEEL COVERING

## Slide 42: SEISMIC
Nablus city is located in zone 2B
and so the Z factor equals to 0.20

## Slide 43: Environmental Analysis

## Slide 44: Environmental Analysis:
Design Builder Software were used to calculate the U values for both walls and roof , calculate heating and cooling loads and the daylight factor.
Heating & Cooling Loads
Simulation
Comfort

## Slide 45: Table1:U-Values Table2: Heating & Cooling Loads
Item | U-Value
External Walls | 2.9
Roof | 1.34
Heating Load | 245.5 KW
Cooling Load | 355.5 KW
Winter | 42.21
Summer | 188.56
Table3: Energy per Conditioned Building Area (KW/m2) Table4: Direct Heating & Direct Cooling (KWH)
Direct Heating | 42812.55
Direct Cooling | 48325.02

## Slide 46: Comfort Analysis:
In Summer | 2820
In Winter | 2305
Table5: Hours of Heat Dissatisfaction

## Slide 47: Ventilation:
1) Create openings in the drum of the courtyard and so circulation. 2) Enlarge Openings

## Slide 48: Solar Photovoltaic Design :
PV Syst software was used to reach best design for the system, solar cells was chosen
The available area on the roof is about 1500 m2
And the building is widely open to the south

## Slide 49: Specification of the Modules used :

## Slide 50: Detailing and Dimensions of the modules

## Slide 51: The inverter Used in the design

## Slide 52: The distribution of the Modules on the Roof :
The capacity of the system = 117*350 = 40 KWp
Area of input module the system = 117*0.99*1.96 = 230 m2
The angle of the Modules “ tilt” = 22

## Slide 53: The main simulation results :
The possible loss diagram for the whole year

## Slide 54: Cost of the PVs System
Cost of modules = 350*117 = 40950$
Cost of Inverters = 7475*2 = 14950$
Cost of Installation = 1200*2 $ = 2400 $
For 1500 m2 roofing area, 1200 meter length needed for the system,
assume 2$ each worker need for each meter length needed for the
system.
4. Operation Cost = 1400 $
Every 6 months maintenance done with 700 $, so it costs 1400 $ per
year.
Summary:
Initial cost of the PV system= 40950+ 14950+ 2400= 58300$
Operation costs= 1400 $/year.
Electricity production = 72700 KWh/yr.
Annual saving = 72700 * 0.17 = 12359 $/yr.
Payback Period = 59700/12359 = 4.83 years.

## Slide 55
3D view of the Distribution

## Slide 56: Acoustical Analysis

## Slide 57: Acoustical Analysis:
RT60
STC & IIC
NC & Background Noise
Reverberation Time Values
Sound Transmission Class Values
Noise Criteria Values

## Slide 58: Reverberation Time:
Three samples of rooms were taken to calculate the reverberation time at all frequencies these rooms are a class room in the ground floor, an office in third floor and a music class in the first floor.
The calculations are going to be performed in three cases:
a.When the space is zero occupied.
b.When the space is 50% occupied.
c.When the space is 100% occupied.

## Slide 59: Class Room RT60 :

## Slide 60: Using Autodesk Ecotect the RT60 values at 500 Hz in the three cases are larger than the limit which is in the range of 0.4 and 0.6 sec. So We Need Absorbers

## Slide 61: Music Room RT60

## Slide 62
Using Autodesk Ecotect the RT60 values at 500 Hz in the three cases are in the range of the standard which is 0.9 - 1.2 sec

## Slide 63: Office RT60

## Slide 64
Using Autodesk Ecotect the RT60 values at 500 Hz in the three cases are in the range of 0.4 and 1.7 sec

## Slide 65: Sound Transmission Class
STC for the external wall: The resulted STC = 40 db.
STC for the internal wall: The resulted STC = 51 db.

## Slide 66: Impact Insulation Class:
IIC for the Ceiling: The resulted IIC = 46 db.

## Slide 67: Background Noise:
Space | Back Ground Noise inside(db.) | Back Ground Noise Outside(db.)
Class Room | 50 | 80
Music Class | 42 | 62
Labor Office | 43 | 70

## Slide 68: Mechanical Analysis

## Slide 69: DRAINAGE SYSTEM

## Slide 70: WATER SUPPLY SYSTEM

## Slide 71: Roof Drainage Layout:

## Slide 72: FIREFIGHTING SYSTEM

## Slide 73: RAINWATER STOREGE

## Slide 74: FUEL SUPPLY

## Slide 75: ELEVATORS

## Slide 76: HVAC SYSTEM

## Slide 78: Roof plan HVAC ducting layout

## Slide 79: ELECTRICAL SYSTEM ANALYSIS

## Slide 80: Electrical System:

## Slide 81: circuit breaker calculations and distribution
zone | Number of Z44 LED 61W 4000K DALI | Number of gbs 300 4*18W | Socket of (2 AMP)
A*3 | 24 | - | 72
B*5 | 60 | - | 15
C*5 | - | 60 | 3
D*21 | 42 | - | 19
WC *2 | - | 11 | 2
Tottal power (watt) | 7686 | 5112 | -
Tottal AMP | 34 | 23 | 222

## Slide 82: Lighting Analysis

## Slide 83: Main Lighting Characteristics
1.Intincity
2.Glare Index(UGR)
3.Uniformity
4.Color Irradiation

## Slide 84: For Example : Classroom
The Unites :
3D view

## Slide 85: Results:

## Slide 86: CONSUMPTION

## Slide 87: 1.Water Consumption 2.Energy Consumption

## Slide 88: Case Study

## Slide 89: Site Analysis:

## Slide 90: GALEF CENTER FOR FINE ARTS, OTIS COLLEGE

## Slide 91: Architectural:

## Slide 92: Otis Architectural:

## Slide 93: Passive Design:

## Slide 94: Structural:

## Slide 95: Electromechanically:

## Slide 96: CONCLUSION

## Slide 97: 1.Architectural aspects 2.Passive aspects 3.Structural aspects 4.Mechanical aspects 5.Electrical aspects 6.Lighting aspects 7.Consumption
Aspects: