## Slide 1: An-Najah National University Faculty Of Engineering Civil Engineering Department Graduation Project II
Evaluation of the water runoff and culvert structures at Wadi AL-Teen in Tulkarm district
Prepared By : Ahmad Amjad Rashid Amr Barqawi
Mohammed Bayan Ali
Yazan Abu-Haniya
Supervision of Dr. Hamees Tubeileh

## Slide 2: Evaluation of the water runoff and culvert structures at Wadi AL-Teen in Tulkarm district.

## Slide 3: Objectives :
Determine the amount of runoff in the Wadi AL-Teen .
Analyze the existing culverts and redesign a new one if needed .
Design a storm system for the adjacent road.
Estimate the cost of the project

## Slide 4: Study Area

## Slide 5: Wadi Al-Teen

## Slide 6: Topography
According to given contour maps Wadi Al-teen lies on four mountains it has an average height of 65 m on sea level and reaches to 70 m on some regions with slow variance in elevation from site to site, with sharp slope.

## Slide 7: Contour map for Wadi Al-Teen.

## Slide 8: Area and Land Use
The size of Wadi Al-Teen catchment area is estimated at 80 km2, has a percent of impervious regions arrives 9.6 %.

## Slide 9: Rainfall readings
The average annual rainfall in Wadi Al-Teen is 680 mm according to Palestinian Statistics center.
From Palestinian Metrologic Center :
year | 2013/2014 | 2014/2015 | 2015/2016 | 2016/2017 | 2017/2018
Annual depth(mm) | 460.5 | 720.3 | 427.5 | 418.7 | 547.3
Maximum day depth (mm) | 90 | 117 | 50 | 90 | 56

## Slide 10: Analysis and evaluation of the existing situation of the drainage system (culvert)

## Slide 11: Existing situation of the drainage system:

## Slide 12: Existing situation of the drainage system:

## Slide 13: Methodology
The following data is collected: the amount of rainfall for 10 years, information about culverts and location, data about the adjacent roads and their sections and coordinates , and the geographical nature of the surrounding area .
Then from these data we analyze, find the amount of runoff water in the Wadi AL-Teen by using HEC-HMS software, and analyze the current culverts and evaluate their efficiency by using HY-8 software .

## Slide 14: Steps of the work
Finding location of culverts by site visit and GIS .

## Slide 15
Determining the catchment regions and data for each catchment on each culvert Using GIS.

## Slide 16: Catchments Data by GIS.

## Slide 17: Sample Calculation for Lag Time.
*Lag time for catchment (Shufa).
Lag Time=0.6*Tc
Tc=0.01947*〖5700〗^0.77*〖0.072〗^(-0.385)=41.8min
Lag time=0.6*41.8=25.1 min

## Slide 18: Using IDF curve for 10-year return period.
There were no data for Wadi Al-Teen to make IDF curve, Nablus taken for design.
Nablus city which is 20 KM eastern Wadi Al-Teen, has an annually rainfall of 660.1 mm which is very near of Wadi Al-Teen which is 680 mm, so it is acceptable to take this IDF curve for design

## Slide 19: IDF Curve used.
Chart: Duration(min)
| 10 | 20 | 30 | 40 | 50 | 60 | 120 | 180 | 240
 | 51.5 | 42.5 | 34.7 | 28.2 | 24.6 | 21.9 | 14.6 | 11.7 | 10.3

## Slide 20: IDF Curve analysis.

## Slide 21: Mass curve
Chart: Duration(min)
| 0 | 10 | 30 | 60 | 120 | 240 | 360
Accumilative depth(mm) | 0 | 8.58 | 22.95 | 37.1 | 55.35 | 80.25 | 96.55

## Slide 22: Partial duration depth required for HEC-HMS Inserting

## Slide 23: Curve Number
Wadi Al-Teen Catchments have a clay soil so it has soil type of “C” ACCORDING TO Curve Number classification.
Wadi Al-Teen Catchments have an urban area with impervious < 12 % (the areas of buildings and paved roads).
According to this table it will have a curve number of 77.

## Slide 24: Curve Number Table.

## Slide 25: Simulation By HEC-HMS

## Slide 26: Results from HEC-HMS

## Slide 27: Results from HEC-HMS

## Slide 28: Results from HEC-HMS

## Slide 29: By HY-8 .
Culvert 1

## Slide 30
Culvert 2

## Slide 31
Culvert 3

## Slide 32: Results From HY-8
Crossing Discharge Data For Culvert 1
Discharge Selection Method: Specify Minimum, Design, and Maximum Flow
Minimum Flow: 0 cms
Design Flow: 32.944 cms
Maximum Flow: 40 cms

## Slide 33: Summary of Culvert Flows at Crossing: Crossing 1

## Slide 34: Rating Curve Plot for Crossing: Crossing 1

## Slide 35: Culvert Summary Table: Culvert 1

## Slide 36: Water Surface Profile Plot for Culvert: Culvert 1

## Slide 37: Summary of Culvert Flows at Crossing: Crossing 2
Headwater Elevation (m) | Total Discharge (cms) | Culvert 1 Discharge (cms) | Roadway Discharge (cms) | Iterations
62.17 | 0.00 | 0.00 | 0.00 | 1
62.79 | 5.00 | 5.00 | 0.00 | 1
63.15 | 10.00 | 10.00 | 0.00 | 1
63.44 | 15.00 | 15.00 | 0.00 | 1
63.75 | 20.00 | 20.00 | 0.00 | 1
64.05 | 25.00 | 25.00 | 0.00 | 1
64.39 | 30.00 | 30.00 | 0.00 | 1
64.84 | 35.00 | 35.00 | 0.00 | 1
65.25 | 40.00 | 38.34 | 1.66 | 4
65.47 | 43.49 | 39.08 | 4.43 | 3
65.84 | 50.00 | 39.34 | 10.66 | 4
65.00 | 36.72 | 36.72 | 0.00 | Overtopping

## Slide 38: Culvert Summary Table: Culvert 2
Total Discharge (cms) | Culvert Discharge (cms) | Headwater Elevation (m) | Inlet Control Depth (m) | Outlet Control Depth (m) | Flow Type | Normal Depth (m) | Critical Depth (m) | Outlet Depth (m) | Tailwater Depth (m) | Outlet Velocity (m/s) | Tailwater Velocity (m/s)
0.00 | 0.00 | 62.17 | 0.000 | 0.000 | 0-NF | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000
5.00 | 5.00 | 62.79 | 0.617 | 0.204 | 1-S2n | 0.266 | 0.362 | 0.277 | 0.688 | 2.462 | 1.453
10.00 | 10.00 | 63.15 | 0.978 | 0.542 | 1-S2n | 0.425 | 0.575 | 0.455 | 1.095 | 3.000 | 1.827
15.00 | 15.00 | 63.44 | 1.273 | 0.957 | 1-JS1t | 0.563 | 0.754 | 1.020 | 1.450 | 2.009 | 2.069
20.00 | 20.00 | 63.75 | 1.537 | 1.576 | 1-S1t | 0.692 | 0.913 | 1.349 | 1.779 | 2.025 | 2.248
25.00 | 25.00 | 64.05 | 1.789 | 1.879 | 1-S1t | 0.815 | 1.059 | 1.662 | 2.092 | 2.054 | 2.390
30.00 | 30.00 | 64.39 | 2.042 | 2.223 | 4-FFf | 0.934 | 1.196 | 1.830 | 2.394 | 2.240 | 2.506
35.00 | 35.00 | 64.84 | 2.307 | 2.671 | 4-FFf | 1.050 | 1.326 | 1.830 | 2.689 | 2.613 | 2.604
40.00 | 38.34 | 65.25 | 2.496 | 3.075 | 4-FFf | 1.126 | 1.409 | 1.830 | 2.976 | 2.862 | 2.688
43.49 | 39.08 | 65.47 | 2.539 | 3.301 | 4-FFf | 1.142 | 1.427 | 1.830 | 3.175 | 2.917 | 2.740
50.00 | 39.34 | 65.84 | 2.555 | 3.675 | 4-FFf | 1.148 | 1.433 | 1.830 | 3.538 | 2.937 | 2.826

## Slide 39: Water Surface Profile Plot for Culvert: Culvert 2

## Slide 40: Summary of Culvert Flows at Crossing: Crossing 3
Headwater Elevation (m) | Total Discharge (cms) | Culvert 1 Discharge (cms) | Roadway Discharge (cms) | Iterations
56.50 | 0.00 | 0.00 | 0.00 | 1
57.10 | 5.00 | 5.00 | 0.00 | 1
57.46 | 10.00 | 10.00 | 0.00 | 1
57.76 | 15.00 | 15.00 | 0.00 | 1
58.02 | 20.00 | 20.00 | 0.00 | 1
58.26 | 25.00 | 25.00 | 0.00 | 1
58.52 | 30.00 | 30.00 | 0.00 | 1
58.77 | 35.00 | 35.00 | 0.00 | 1
59.01 | 40.00 | 40.00 | 0.00 | 1
59.16 | 43.30 | 43.30 | 0.00 | 1
59.48 | 50.00 | 50.00 | 0.00 | 1
60.00 | 61.00 | 60.99 | 0.00 | Overtopping

## Slide 41: Culvert Summary Table: Culvert 3
Total Discharge (cms) | Culvert Discharge (cms) | Headwater Elevation (m) | Inlet Control Depth (m) | Outlet Control Depth (m) | Flow Type | Normal Depth (m) | Critical Depth (m) | Outlet Depth (m) | Tailwater Depth (m) | Outlet Velocity (m/s) | Tailwater Velocity (m/s)
0.00 | 0.00 | 67.66 | 0.000 | 0.000 | 0-NF | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000
4.00 | 4.00 | 68.12 | 0.459 | 0.076 | 1-S2n | 0.149 | 0.272 | 0.173 | 0.522 | 2.569 | 1.277
8.00 | 8.00 | 68.39 | 0.729 | 0.313 | 1-S2n | 0.230 | 0.432 | 0.290 | 0.817 | 3.061 | 1.631
12.00 | 12.00 | 68.62 | 0.955 | 0.585 | 1-S2n | 0.299 | 0.566 | 0.394 | 1.070 | 3.385 | 1.870
16.00 | 16.00 | 68.81 | 1.154 | 0.842 | 1-JS1t | 0.361 | 0.685 | 0.979 | 1.299 | 1.815 | 2.052
20.00 | 20.00 | 69.00 | 1.335 | 1.093 | 1-JS1t | 0.418 | 0.795 | 1.195 | 1.515 | 1.860 | 2.201
24.00 | 24.00 | 69.21 | 1.505 | 1.549 | 1-S1t | 0.471 | 0.898 | 1.400 | 1.720 | 1.904 | 2.325
28.00 | 28.00 | 69.40 | 1.667 | 1.745 | 1-S1t | 0.522 | 0.995 | 1.598 | 1.918 | 1.947 | 2.433
32.00 | 32.00 | 69.60 | 1.825 | 1.941 | 1-S1t | 0.571 | 1.088 | 1.790 | 2.110 | 1.986 | 2.527
32.94 | 32.94 | 69.65 | 1.862 | 1.987 | 1-S1t | 0.583 | 1.109 | 1.835 | 2.155 | 1.995 | 2.548
40.00 | 40.00 | 70.02 | 2.138 | 2.359 | 1-S1f | 0.665 | 1.263 | 2.000 | 2.481 | 2.222 | 2.687

## Slide 42: Water Surface Profile Plot for Culvert: Culvert 3

## Slide 43: REDESIGN CULVERTS

## Slide 44: Culvert 1 :

## Slide 45: Culvert Summary Table: Culvert 1
Total Discharge (cms) | Culvert Discharge (cms) | Headwater Elevation (m) | Inlet Control Depth (m) | Outlet Control Depth (m) | Flow Type | Normal Depth (m) | Critical Depth (m) | Outlet Depth (m) | Tailwater Depth (m) | Outlet Velocity (m/s) | Tailwater Velocity (m/s)
0.00 | 0.00 | 67.66 | 0.000 | 0.000 | 0-NF | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000
4.00 | 4.00 | 68.12 | 0.459 | 0.076 | 1-S2n | 0.149 | 0.272 | 0.173 | 0.522 | 2.569 | 1.277
8.00 | 8.00 | 68.39 | 0.729 | 0.313 | 1-S2n | 0.230 | 0.432 | 0.290 | 0.817 | 3.061 | 1.631
12.00 | 12.00 | 68.62 | 0.955 | 0.585 | 1-S2n | 0.299 | 0.566 | 0.394 | 1.070 | 3.385 | 1.870
16.00 | 16.00 | 68.81 | 1.154 | 0.842 | 1-JS1t | 0.361 | 0.685 | 0.979 | 1.299 | 1.815 | 2.052
20.00 | 20.00 | 69.00 | 1.335 | 1.093 | 1-JS1t | 0.418 | 0.795 | 1.195 | 1.515 | 1.860 | 2.201
24.00 | 24.00 | 69.21 | 1.505 | 1.549 | 1-S1t | 0.471 | 0.898 | 1.400 | 1.720 | 1.904 | 2.325
28.00 | 28.00 | 69.40 | 1.667 | 1.745 | 1-S1t | 0.522 | 0.995 | 1.598 | 1.918 | 1.947 | 2.433
32.00 | 32.00 | 69.60 | 1.825 | 1.941 | 1-S1t | 0.571 | 1.088 | 1.790 | 2.110 | 1.986 | 2.527
32.94 | 32.94 | 69.65 | 1.862 | 1.987 | 1-S1t | 0.583 | 1.109 | 1.835 | 2.155 | 1.995 | 2.548
40.00 | 40.00 | 70.02 | 2.138 | 2.359 | 1-S1f | 0.665 | 1.263 | 2.000 | 2.481 | 2.222 | 2.687

## Slide 47: Culvert 2 :

## Slide 48: Culvert Summary Table: Culvert 2
Total Discharge (cms) | Culvert Discharge (cms) | Headwater Elevation (m) | Inlet Control Depth (m) | Outlet Control Depth (m) | Flow Type | Normal Depth (m) | Critical Depth (m) | Outlet Depth (m) | Tailwater Depth (m) | Outlet Velocity (m/s) | Tailwater Velocity (m/s)
0.00 | 0.00 | 62.17 | 0.000 | 0.000 | 0-NF | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000
5.00 | 5.00 | 62.67 | 0.501 | 0.129 | 1-S2n | 0.207 | 0.294 | 0.220 | 0.602 | 2.274 | 1.383
10.00 | 10.00 | 62.97 | 0.796 | 0.368 | 1-S2n | 0.323 | 0.467 | 0.357 | 0.947 | 2.803 | 1.760
15.00 | 15.00 | 63.21 | 1.042 | 0.690 | 1-JS1t | 0.423 | 0.612 | 0.813 | 1.243 | 1.844 | 2.011
20.00 | 20.00 | 63.45 | 1.255 | 1.277 | 1-S1t | 0.514 | 0.741 | 1.085 | 1.515 | 1.844 | 2.201
25.00 | 25.00 | 63.67 | 1.452 | 1.500 | 1-S1t | 0.599 | 0.860 | 1.340 | 1.770 | 1.865 | 2.354
30.00 | 30.00 | 63.91 | 1.636 | 1.740 | 1-S1t | 0.680 | 0.972 | 1.585 | 2.015 | 1.893 | 2.482
35.00 | 35.00 | 64.15 | 1.814 | 1.978 | 1-S1t | 0.758 | 1.077 | 1.821 | 2.251 | 1.922 | 2.591
40.00 | 40.00 | 64.39 | 1.990 | 2.224 | 1-S1f | 0.834 | 1.177 | 2.000 | 2.481 | 2.000 | 2.687
43.49 | 43.49 | 64.60 | 2.113 | 2.433 | 4-FFf | 0.886 | 1.245 | 2.000 | 2.639 | 2.175 | 2.747
50.00 | 50.00 | 65.02 | 2.347 | 2.847 | 4-FFf | 0.980 | 1.366 | 2.000 | 2.927 | 2.500 | 2.847

## Slide 50
The difference before and after the design for culvert 1.
After Redesign | Before Redesign | 
3 | 3 | Number of Barrels
3000 | 2500 | Span (mm)
2000 | 1340 | Rise (mm)
70.30 m | 70.00m | Crest Elevation
69.65 m | 70.43m | Head Water Elevation

## Slide 51
The difference before and after the design for culvert 2.
After Redesign | Before Redesign | 
4 | 4 | Number of Barrels
2500 | 1830 | Span (mm)
2000 | 1830 | Rise (mm)
65.30 m | 65.00m | Crest Elevation
64.60 m | 65.47 m | Head Water Elevation

## Slide 52: STORM NETWORK FOR FAR'OUN STREET

## Slide 53: The problem of storm water on Far'oun street

## Slide 54: Methodology
Finding the storm data
Preparing data as layers of the street
Using storm cad to design the network depending on layers of (contour ,and road)
Checking the design to admire the criteria of velocity and cover.

## Slide 55: Criteria of design
Design period(years) | 20
Maximum velocity in conduits(m/s) | 3
Minimum velocity in conduits (m/s) | 0.6
Maximum allowable cover (m) | 5
Minimum allowable cover(m) | 0.8
Minimum allowable slope (%) | 1
Maximum allowable slope (%) | 15
Conduit Material | Concrete

## Slide 56: Suggested Outfalls

## Slide 57: Steps Done
First: Adding Data

## Slide 58
Second : Delineation the Catchments and Drawing manholes, Catch Basin, and conduits

## Slide 59
Third: Define storm data

## Slide 60
Fourth: Inserting Elevation for each Manhole and Catch Basin .

## Slide 61
Fifth: Calling conduit catalog

## Slide 62
Sixth: Calling Inlet Catalog

## Slide 63
Seventh: Defining design constrains

## Slide 64
Eighth : Inserting Conduit Type ,Material and Size For Each conduit

## Slide 65
Ninth : Inserting Runoff Coefficient and Time of Concentration for each Catchment

## Slide 66
Tenth : Base Calculation Option

## Slide 67: Results
The conduits we used .
Diameter (in) | Length (m)
8 | 1593.6
10 | 1313.6
12 | 614.4
15 | 193.8

## Slide 68
Velocities in pipes

## Slide 69
Cover Start

## Slide 70
Cover Stop

## Slide 71
Slope

## Slide 72
Profile of storm network

## Slide 73
Profile of drop manhole .

## Slide 74: Cost Estimate

## Slide 75
Cost of project
The total cost = 590410 $
 | Unit price | Quantity | Cost
Manholes | 600$/unit | 46 unit | 27600$
Catch basin | 250$/unit | 22 unit | 5500$
Conduits | 150 $/m | 3715.4 m | 557310$

## Slide 76: Discussions and Recommendations.

## Slide 77: Discussions of Culverts Analysis
According to the results of analysis of culverts we noticed the efficiency of culvert 1 is very bad so that need to redesigned , also culvert 2 has a bad efficiency and need to redesigned , culvert 3 has a good efficiency .
The region of Wadi Al-Teen is very close to Nablus , it has a close annual rainfall depth.
The efficiency of culverts affected by the surrounding area as illustrated in image .

## Slide 78: Discussions of Storm Network
We use Rational Method to design a storm system .
The Runoff Coefficient (C) used is 0.7
We determine the time of concentration for each catchment by :
C: The Rational Coefficient . L: overland flow length in ft . S: surface slope in % .

## Slide 79
THANK YOU