## Slide 1
Mulit functional
Building design
Graduation Project “2”
Prepared by:
Supervisor :
Dr. Nermeen Al-barq
Orouba Abdullah
Qutaiba Yaseen
Ruba ammar
Yusra AbuMohsen

## Slide 2
Introduction
Structural Design
Quantity Surveying and Cost Estimation
Environmental Design
Mechanical Design
Electrical Design
Architectural Design
Safety Design
Outline:

## Slide 3
Architectural Design

## Slide 4
Architectural Design:
1 site plan
2- the plans
3- sections

## Slide 6
Site plan:
Notes: The main entrance of the restaurant is from Jamal Abdel Nasser Park, the secondary entrance of parking, management, and services are from Yafa Street as shown in the figure below.
The site contains parking which the capacity of it about 36 car, and there are two ramps the first one for entrance, and the second one for exit

## Slide 7
Ground Floor
Area=1025m^2
Architectural Design:
Notes: The ground floor contains the reception and cashier, coat room, kitchen, dining area, mechanical and electrical rooms and storage

## Slide 8
First Floor Area=1300m^2
Architectural Design:

## Slide 9
secand Floor Area=1300m^2
Architectural Design:

## Slide 10
third Floor Area=1300m^2
Architectural Design:

## Slide 11: Elevation(North )

## Slide 12
Elevation (suoth)
Architectural Design:

## Slide 13: Elevation(east )

## Slide 14: Elevation(North )

## Slide 15
Structural Design

## Slide 16
Structural Design:
1- Design codes
2- Loads
3-ETABS model and checks
4- Structural elements and detailing

## Slide 17
Design Codes:
ACI -318-08 (American Concrete Institution) for reinforced concrete structural design.
UBC-97 (Uniform Building Code) for earthquake load computations.
ASCE (American Society Of Civil Engineers) for design loads.
Structural Design:

## Slide 18
Loads:
Structural Design:
Type of loads | Load (KN/m2)
Live load | 5KN/m2
Super imposed | 6.1KN/m2
Exterior walls | 25KN/m

## Slide 19: Seismic Design Data:
Location …Tubas
Zone ….2B
CV=0.4
CA=0.28
Z= 0.2
Soil type….SD

## Slide 20
Structural System:
The system of the slab is one way ribbed slab(40 cm thickness ) with Drop beams.

## Slide 21
ETABS models:

## Slide 22
Checks for models :
1. Compatibility check and Deflection check :
U z from ETABS= 19mm < U max= 30mm
Notes: compatibility had achieved as shown in the figure

## Slide 23
2. Equilibrium check:
Load | Manual | ETABS | Error
Dead load | 48440.9 KN | 49000KN | 1.5 %
Live load | 20315.5 KN | 20316.5KN | 0.0043 %
Super imposed | 29502 KN | 29502.5 KN | 0.003 %

## Slide 24: 3. Internal Forces Check:
Difference | ETABS | Manual | Load
0.8% | 5028.2KN | 5071 KN | axial load for column
0.15% | 400.5 KN . m | 342 KN | Moment for beam
0.077%. | 83.2KN | 90kN.m | Moment for Slab (interior span)

## Slide 25: 4. Period Check:
ETAB < 1.3 T manual | ETABS | Manual
o.039<0.65 | 0.039 | 0.5
5. equivalent static check:
ETABS>MANUAL | ETABS | Manual
OK | EQ x= 10742 EQ y= 11742 | V max = 10637.7KN

## Slide 26: · Drift CHECK:
∆(in elastic)=19mm …< 112.5mm

## Slide 27
Design of Slab: One-Way Ribbed Slab

## Slide 28
Beam Design:

## Slide 29: Concrete Beam Scheduale :

## Slide 30
Column Design:

## Slide 31: Column Design:

## Slide 32
Footing Design:

## Slide 33: Shear Wall Design:

## Slide 34
Environmental Design

## Slide 35
Environmental Design:
1- The layers for the elements
2- Thermal analysis
3- Daylight factor
4- Shading design

## Slide 36
Thermal Analysis ( Jawwal )
Total floor area = 417 m2 – full occupancy – Full air conditioned

## Slide 37
Materials :
External wall of U = 0.41 W/m2.K

## Slide 38
Internal wall of U = 0.64 W/m2.K

## Slide 39
Ceiling: 0.27 W/m2.K

## Slide 40
Ground floor : U-value = 0.38 W/m2.K

## Slide 41
Glass material :
Glass in Jawwal and the Bank U = 1.5 W/m2.K

## Slide 42
Jawwal
Breakdown analysis :

## Slide 43
Heating/cooling loads (Jawwal)
Max Heating: 5.075 KW at 12:00 on 18th January
Max Cooling: 21.856 KW at 19:00 on 30th July

## Slide 44: Outline
Architectural Design
Structural Design
Environmental Design
Mechanical Design
Electrical Design
Safety Design
BOQ
Site location
Water supply system
Drainage system
HVAC

## Slide 45: Shading Design
@9:00 AM @11:00 AM
@
@11:00 AM
9:00 AM

## Slide 46
Shadow rang every
½ hour from 9:00-17:00 – June 21

## Slide 47
For east window we used Vertical adjustable louvers
Fixed-cantilever for south window

## Slide 48: Average Daylight Values
Zone | Floor |  | DF-Value | Uniformity distribution | Picture
jawwal | Ground floor |  | 4.5% | 72% | 
bank | Ground floor |  | 3.7% | 64.6% | 
resturant | 1st Floor |  | 4.12% | 60.2% | 
shop | 1st floor |  | 3.7% | 60.4% | 
office | 2st floor |  | 5% | 65.7% | 

## Slide 49: Figure : daylight bank(by daylox)

## Slide 50
Mechanical design:
1. Water supply
2. Water drainage
3. Safety
5. HVAC system

## Slide 51: Water supply system:

## Slide 52: Drainage water systems design:
The purpose of drainage lines design:
1-easy flow of sewage water.
2- no return of gases.

## Slide 53: By dividing the building in to zones : Drainage lines distribution in zoneA1

## Slide 54: Number of dfu’s in zone A1 : The total number of fixture units = 66 dfu Stack diameter = 4" Diameters of the pipes = 2 " , 3 " and 4" (horizontal).
Mechanical Design
      Black water: W.CS & Kitchen sink
      Grey water: Lavatory.

## Slide 55: Drainage system roof shows manhole lines
Mechanical Design

## Slide 56
1.safety signs for fire
2.Manual Systems
3. Sprinkler system
4. Smoke detectors
Safety system:
Mechanical Design

## Slide 57
Safety system:

## Slide 58: Sprinkler distribution-3rd floor

## Slide 60
Uc =0.270W/m2.C
Uw =0.410 W/m2.C
Uadj =0.640 W/m2.C
HVAC Design Data for (Jawwal ) :
Max Cooling: 21.856 KW@ 19:00 on 30th of July.
Uglass =1.50 W/m2.C
Ufloor =0.380 W/m2.C

## Slide 61
Main Duct sizing :
v=1.3 m3/s , vA-B=7 m/s ,then (Δ𝑝/𝐸𝐿)=1.1
Duct size | Volumetric flow rate | d | V m/s | ϪΡ/EL
A-B | 1.3 | .5 | 7 | 1.1
B-C | 1.021 | .45 | 6.5 | 1.1
C-D | .835 | .4 | 6.2 | 1.1
D-E | .649 | .4 | 6 | 1.1
E-F | .463 | .35 | 5.5 | 1.1
F-G | .279 | .3 | 4.9 | 1.1
G-H | .183 | .25 | 4.5 | 1.1
H-I | .093 | .2 | 2.5 | 1.1

## Slide 62
Diffuser selection :
23 x23 cm ceiling diffusers
such that the volumetric rate = 175 L/s and its throw 3-7.3m
A fixed carbon
dioxide sensor
Diffusers (return).
Square diffusers (supply).

## Slide 63
Diffusers distribution:
Jawwal
Bank

## Slide 64
Electrical Design

## Slide 65
General Artificial Lighting used:
LAMP 6441213 PLAT LED 3600 LM LAMP 6442213 PLAT LED 3600 LM
LAMP 6444000 DINAMIC DECO 4X14/24W
Artificial lighting for dinning
Notes: Dialux program were used in our analysis to get a helpful and useful allocation of the artificial lighting, two different spaces were chosen to test and those were, manager ,dinning, kitchen, employee area and storage.
a targeted value of U (uniformity) and (unified glare rating) UGR shall be achieved for each space where U >0.6 and UGR should not exceed 19, so to get these values suitable paint, tile, color of furniture and appropriate type of lamp have to be applied.[25]

## Slide 66: Artificial lighting for some zone
*Bank Branch

## Slide 67: Artificial lighting & socets for some zone
*jawwal Branch

## Slide 68: Artificial lighting for some zone
*main hall in resturant

## Slide 69
RT60 Values for bank in GF floor before modifications
Acostical design
Notes: As it's shown in the standards, the reverberant time inside the Dining room does not match the specifications of restaurants that is ( 0.8 – 1.2 ) s

## Slide 70: To improve RT60 we use

## Slide 71
RT60 Values for resturant in first floor after modifications
RT60 Values for offeic
in secand floor after
modifications
Notes: All values lies in the range (0.8-1.2) Which is suitable for Dining rooms.

## Slide 72
STC Calculations
Required STC 50-55
80

## Slide 73
STC Calculations
Required STC 50-55
51.63

## Slide 74
Speakers:
Sound system calculations for the restaurant were only made for the dining halls.

## Slide 75
The distribution of loudspeakers in resturant

## Slide 76
The distribution of loudspeakers in Bank

## Slide 77
Quantity surveying and cost estimation

## Slide 78: Bill of Quantities Bowling - Sample Structural
Total cost of structural elements per meter square = 150 JD
Total Cost of the Bowling center = 993,750 JD