## Slide 1: Indoor Propagation Modeling
Prepared by:
Ashraf Zetawe
Derar Mu’alla
Osama Dragmeh
Supervisor:
Dr. Yousef Dama

## Slide 2: Outlines
1- Why Project
2- Literature Review
3- Measurements Procedure
4- Clustering.
5- Channel Capacity.
6- Authentication Of Data
7- INDOOR RADIO PROPAGATION MODEL

## Slide 3: Why???
Number of research
Design propagation model in an indoor environment.
How to plan for reliable wireless system
Number of companies in middle east

## Slide 4: Literature Review
802.11n is a IEEE standard .
MIMO System
PROPAGATION MODELS.
Multipath propagation

## Slide 5: Study Area

## Slide 6: Wireless Insite

## Slide 7: Implemented model

## Slide 8: Site Description
Material type | thickness | Used in | Height
concrete | 35 Cm | floor and ceiling | 3m
dielectric material | 3 Cm | second ceiling | 2.5m
concrete | 35 Cm | Out walls | ____
concrete | 22 Cm | inner walls | ____
concrete | 15 Cm | inner walls | ____
brick | 12.5 Cm | inner walls | 
wooden and metal door | 3 Cm | door | ____
one-layer glass | 0.3 Cm | windows | ____

## Slide 9: Transmitter and receiver locations

## Slide 10: MIMO Equipment
Transmitter
The transmitter used is TP-link TD-W8961n access point MIMO system.
Number of antenna | 2
Transmission power | 20dBm
Antenna gain | Antenna 1 3dBi Antenna 2 3dBi
Type of the antenna | external
Maximum bitrate | 300Mbit/s

## Slide 11: MIMO Equipment
Number of antenna | 2
Transmission power | 15dbm
Antenna gain | Antenna 1 gain ≤3dbi Antenna 2 gain ≤4dbi
Type of the antenna | Internal
Maximum bitrate | 300Mbit/s
Receiver
We use two receiver
Cisco Mimo receiver
Spectrum Analyzer

## Slide 12: RSSI Measurement Setup
insider 2.0
Receiver

## Slide 13: RSSI simulation
Running number | High of the transmitter (m) | Transmitting power (dBm) | Number of reflection | Number of transmissions | Number of diffraction
1 | 0.5 | 11dbm | 6 | 6 | 0
2 | 1 | 11dbm | 6 | 6 | 0
3 | 1.5 | 11dbm | 6 | 6 | 0
4 | 0.5 | 17dbm | 6 | 6 | 0
5 | 1 | 17dbm | 6 | 6 | 0
6 | 1.5 | 17dbm | 6 | 6 | 0
7 | 0.5 | 20dbm | 6 | 6 | 0
8 | 1 | 20dbm | 6 | 6 | 0
9 | 1.5 | 20dbm | 6 | 6 | 0
10 | 1.5 | 20dbm | 6 | 6 | 1
Notes: Received Signal Strength Indicator

## Slide 14: TX Height selection
Transmitters
Notes: Thank u osama
As osama said we performed many simulations to our study area using wireless insite tool
We performed the simulation on three tx heights 0.5 1 and 1.5 m to see the effect of height on the received signal power
We can see clearly that the received power is in its highest value when the tx is on height of 1.5m
Based on that for the rest of our work we will be using the 1.5m tx height

## Slide 15: RSSI ANALYSIS FOR SIMULATED AND MEASURED VALUES
Chart: Measurement Power vs. Simulated power Tx2 Rx1&2
| 32.200000000000003 | 32.200000000000003 | 32.200000000000003 | 32.200000000000003 | 32.200000000000003 | 32.4 | 32.46 | 32.6 | 32.65 | 32.9 | 33 | 33.4 | 33.9 | 34.4 | 35.200000000000003 | 35.700000000000003 | 36.6 | 37.200000000000003 | 38.1 | 38.5 | 39.5 | 40 | 41 | 41.5 | 42.5 | 43 | 43.9 | 44.4 | 45.3 | 45.8 | 46.8 | 47.3 | 48.3 | 48.8 | 49.8 | 50.2 | 51.3 | 51.7 | 52.7 | 53.1 | 54.2 | 54.3 | 54.3 | 54.3 | 54.3 | 54.4 | 54.4 | 54.5 | 54.5 | 54.5 | 54.6 | 54.8 | 55 | 55.2 | 55.4
Simulation | -71.1533 | -64.2467 | -49.7467 | -49.79 | -56.4667 | -57.1633 | -70.7467 | -65.7767 | -58.9433 | -52.3433 | -61.9167 | -52.93 | -53.5133 | -45.5433 | -75.8133 | -50.3333 | -79.2967 | -47.39 | -76.6733 | -46.1667 | -74.5467 | -50.6167 | -82.3 | -52.2933 | -85.9567 | -64.5833 | -96.6667 | -61.8267 | -95.4833 | -62.6333 | -94.4833 | -67.4567 | -90.22 | -64.4867 | -90.7267 | -65.6167 | -90.6067 | -67.12 | -98.94 | -61.2867 | -97.2967 | -99.6633 | -95.52 | -76.2833 | -100 | -99.5667 | -100 | -99.47 | -93.5633 | -64.06 | -95.6533 | -78.8833 | -75.69 | -77.6767 | -72.23
Measurement | -79 | -80 | -81 | -78 | -78 | -79.5 | -79 | -82 | -74.5 | -69 | -87 | -69 | -65 | -70 | -86 | -73 | -93.5 | -72.5 | -93.5 | -67.5 | -100 | -69 | -100 | -69.5 | -100 | -72.5 | -100 | -72.5 | -100 | -70.5 | -100 | -74 | -100 | -75 | -100 | -78 | -100 | -80.5 | -100 | -83 | -100 | -100 | -100 | -96.5 | -96.5 | -100 | -96.5 | -100 | -95 | -83.5 | -100 | -94.5 | -93 | -86.5 | -87
Chart: Measurements Power vs. Simulation Power Tx3 Rx1&2
| 16.600000000000001 | 17.5 | 17.8 | 18.7 | 19 | 19.8 | 20.2 | 21.1 | 21.4 | 22.3 | 22.7 | 23.5 | 24.1 | 24.8 | 25.3 | 26.2 | 26.8 | 27.5 | 28.1 | 28.8 | 29.5 | 30.2 | 31 | 31.6 | 32.299999999999997 | 33 | 33.700000000000003 | 35.200000000000003 | 35.299999999999997 | 36 | 36.6 | 37.299999999999997 | 37.299999999999997 | 37.799999999999997 | 38.1 | 38.4 | 39 | 39.1 | 39.700000000000003 | 39.799999999999997 | 40.4 | 40.6 | 41.1 | 41.65 | 41.9 | 42.6 | 42.8 | 43.6 | 43.6 | 44.6 | 44.6 | 45.6 | 45.6 | 46.6 | 46.7
Simulation | -50.9633 | -53.09 | -55.9233 | -51.1167 | -55.5267 | -65.73 | -47.4733 | -63.42 | -51.38 | -52.11 | -48.94 | -54.13 | -46.5033 | -55.7733 | -46.5867 | -54.08 | -50.0833 | -49.4 | -46.5133 | -44.7233 | -64.9833 | -59.5967 | -63.11 | -65.8867 | -66.17 | -65.4033 | -64.0133 | -72.95 | -52.7667 | -77.88 | -94.34 | -95.1467 | -70.71 | -99.7333 | -100 | -100 | -100 | -100 | -100 | -100 | -99.3467 | -100 | -100 | -100 | -100 | -100 | -100 | -100 | -100 | -100 | -100 | -100 | -100 | -100 | -100
Measurement | -63.5 | -62 | -61 | -69.5 | -69.5 | -66 | -72.5 | -61 | -67.5 | -68.5 | -72.5 | -67 | -68.5 | -73.5 | -74.5 | -72 | -74 | -77 | -74.5 | -73 | -77.5 | -77.5 | -75 | -75.5 | -74 | -80.5 | -78 | -72.5 | -84 | -87 | -88.5 | -86.5 | -83.5 | -85 | -87 | -93.5 | -89.5 | -92.5 | -92.5 | -95 | -92.5 | -97 | -95.5 | -93.5 | -95 | -95.5 | -95 | -95.5 | -95 | -95.5 | -96 | -95.5 | -95.5 | -96 | -93
Notes: We then plotted the simulated received power against tx-rx distance along with the measured power to compare between them we got these results
Its clear that there is a good agreement between the simulation results and the measured results
But still, we have a difference that can reach 20 dB which is too much
So we decided to change the parameters of the materials in the simulator to enhance the results

## Slide 16: Measurements vs. Simulation after Modification
Chart: Measurement Power vs. Simulated power Tx2 Rx1&2
| 32.200000000000003 | 32.200000000000003 | 32.200000000000003 | 32.200000000000003 | 32.200000000000003 | 32.4 | 32.46 | 32.6 | 32.65 | 32.9 | 33 | 33.4 | 33.9 | 34.4 | 35.200000000000003 | 35.700000000000003 | 36.6 | 37.200000000000003 | 38.1 | 38.5 | 39.5 | 40 | 41 | 41.5 | 42.5 | 43 | 43.9 | 44.4 | 45.3 | 45.8 | 46.8 | 47.3 | 48.3 | 48.8 | 49.8 | 50.2 | 51.3 | 51.7 | 52.7 | 53.1 | 54.2 | 54.3 | 54.3 | 54.3 | 54.3 | 54.4 | 54.4 | 54.5 | 54.5 | 54.5 | 54.6 | 54.8 | 55 | 55.2 | 55.4
Measurement | -79 | -80 | -81 | -78 | -78 | -79.5 | -79 | -82 | -74.5 | -69 | -87 | -69 | -65 | -70 | -86 | -73 | -93.5 | -72.5 | -93.5 | -67.5 | -100 | -69 | -100 | -69.5 | -100 | -72.5 | -100 | -72.5 | -100 | -70.5 | -100 | -74 | -100 | -75 | -100 | -78 | -100 | -80.5 | -100 | -83 | -100 | -100 | -100 | -96.5 | -96.5 | -100 | -96.5 | -100 | -95 | -83.5 | -100 | -94.5 | -93 | -86.5 | -87
Simulation | -80.1533 | -73.2467 | -58.7467 | -58.79 | -65.4667 | -66.1633 | -79.7467 | -74.7767 | -67.9433 | -61.3433 | -70.9167 | -61.93 | -62.5133 | -54.5433 | -84.8133 | -59.3333 | -88.2967 | -56.39 | -85.6733 | -55.1667 | -83.5467 | -59.6167 | -91.3 | -61.2933 | -94.9567 | -73.5833 | -105.6667 | -70.8267 | -104.4833 | -71.6333 | -103.4833 | -76.4567 | -99.22 | -73.4867 | -99.7267 | -74.6167 | -99.6067 | -76.12 | -107.94 | -70.2867 | -106.2967 | -108.6633 | -104.52 | -85.2833 | -109 | -108.5667 | -109 | -108.47 | -102.5633 | -73.06 | -104.6533 | -87.8833 | -84.69 | -86.6767 | -81.23
Chart: Measurements Power vs. Simulation Power Tx3 Rx1&2
| 16.600000000000001 | 17.5 | 17.8 | 18.7 | 19 | 19.8 | 20.2 | 21.1 | 21.4 | 22.3 | 22.7 | 23.5 | 24.1 | 24.8 | 25.3 | 26.2 | 26.8 | 27.5 | 28.1 | 28.8 | 29.5 | 30.2 | 31 | 31.6 | 32.299999999999997 | 33 | 33.700000000000003 | 35.200000000000003 | 35.299999999999997 | 36 | 36.6 | 37.299999999999997 | 37.299999999999997 | 37.799999999999997 | 38.1 | 38.4 | 39 | 39.1 | 39.700000000000003 | 39.799999999999997 | 40.4 | 40.6 | 41.1 | 41.65 | 41.9 | 42.6 | 42.8 | 43.6 | 43.6 | 44.6 | 44.6 | 45.6 | 45.6 | 46.6 | 46.7
Measurement | -63.5 | -62 | -61 | -69.5 | -69.5 | -66 | -72.5 | -61 | -67.5 | -68.5 | -72.5 | -67 | -68.5 | -73.5 | -74.5 | -72 | -74 | -77 | -74.5 | -73 | -77.5 | -77.5 | -75 | -75.5 | -74 | -80.5 | -78 | -72.5 | -84 | -87 | -88.5 | -86.5 | -83.5 | -85 | -87 | -93.5 | -89.5 | -92.5 | -92.5 | -95 | -92.5 | -97 | -95.5 | -93.5 | -95 | -95.5 | -95 | -95.5 | -95 | -95.5 | -96 | -95.5 | -95.5 | -96 | -93
Simulation | -61.9633 | -64.09 | -66.9233 | -62.1167 | -66.5267 | -76.73 | -58.4733 | -74.42 | -62.38 | -63.11 | -59.94 | -65.13 | -57.5033 | -66.7733 | -57.5867 | -65.08 | -61.0833 | -60.4 | -57.5133 | -55.7233 | -75.9833 | -70.5967 | -74.11 | -76.8867 | -77.17 | -76.4033 | -75.0133 | -83.95 | -63.7667 | -88.88 | -105.34 | -106.1467 | -81.71 | -110.7333 | -100 | -100 | -100 | -100 | -100 | -100 | -99.3467 | -100 | -100 | -100 | -100 | -100 | -100 | -100 | -100 | -100 | -100 | -100 | -100 | -100 | -100
Notes: And so we did
We can see that after modifying the parameters the results has became more close and the difference became around 8 db which is acceptable

## Slide 17: Clustering
Notes: In order to make sure that our simulation results are reasonable we want to link the simulation results to an existing indoor propagation model called Saleh venzuela model…
In this model the multipath components are received in groups called clusters or in rays within a cluster.
This model indicates that If we plot the power received against time of arrival for each cluster the power will decay exponentially for each cluster and the power of the ray also will decay exponentially as u can see here
So we first plotted the received power against ToA and AoA then used the k-means method to find the clusters as shown here.

## Slide 18: Applying Saleh-Valenzuela to our simulation
c1
c2
c3
c4
Received power
Time of arrival
Notes: Now for each cluster we plotted the received power against time to get these results
We can see that the simulation satisfy saleh venzuela model
Now we know that our simulation is reasonable

## Slide 19: Channel Capacity
Find the channel matrix (c)
Apply Shannon formula to find the capacity
Notes: Now we want to find the channel capacity for our model to find the channel capacity we first need to find the channel matrix for each receiver so for simplicity we reduced the number of receivers to 7 distributed as shown and then to apply Shannon formula to find the capacity.

## Slide 20: Channel Matrix
Where
  hij : Complex impulse response
  M: the number of paths that reach the receiver
  Pk: Received power
  : Time of arrival
Receiver | Impulse response from Tx1 | Impulse response from Tx2
Rx1 | -7.40093056075077 - 34.6670097082566i | -7.65846296427752 - 69.8691692718261i
Rx2 | 28.1743154669248 + 26.9513899296517i | -30.6190873871329 - 4.56461270998886i
Rx3 | 10.6921361812571 - 13.1170984207187i | 3.09790836802025 - 42.7003439250243i
Rx4 | -32.8817540839863 + 5.31237602910812i | -20.2232527602618 + 26.8334011113775i
Rx5 | 10.4563509419887 - 28.8690152926596i | -48.7581299569394 - 22.4828547780491i
Rx6 | 15.9382117568367 + 38.0980291519978i | 70.2075964238675 - 22.6445746986406i
Rx7 | -37.2976965132879 - 28.5465557836052i | 16.6591355583433 - 32.6566288477936i
Notes: Since were dealing with a 2x1 MIMO system the dimension of the channel matrix should be 2x1 for each receiver and it should be on this form
Where h11 is the complex impulse response from the 1st transmitter antenna to the receiver antenna and h21 is the complex impulse response from the 2nd transmitter antenna to the receiver antenna
And they can be found by this formula where M: is the no. of pathes pk: is the received power for each path
Theta k : is the angle of arrival for each path
F0: is the operating frequency
And taw k: is the time of arrival for each path
We found the h matrix for our model it was like this

## Slide 21: Channel Capacity
52.4041 bits/sec/Hz.
Where
  n : number of receiving antennas (1 in our case)
  SNR: the average signal-to-noise ratio at each receiver
  I : the identity matrix (1 in our case since its 2x1 MIMO system)
  H : is the normalized channel matrix
: transpose of H
Notes: Now we want to apply this formula to find the capacity this is call Shannon formula we applied it to get of capacity 52.4 bits\sec\hz we will continue with ashraf

## Slide 22: INDOOR RADIO PROPAGATION MODEL
The aim of this part
Indoor propagation model
Keenan Motley model
Saleh-Venezuela model
Choose the model
Keenan Motley model

## Slide 23: Keenan Motley model
Where:
= mean received power (dB)
= transmitted power (dB)
L = clutter loss (dB)
d = Tx/Rx separation (m)
n = signal decay rate

## Slide 24: Indoor Environment scenarios
Line of sight
Non Line of sight (Tx and Rx in the same floor)
Non Line of sight (Tx and Rx in different floor)

## Slide 25: Measurements setup
Transmitter | Route number
P1 , F1 | Route 2
F2 | Route 1
P2 | Route 3
F3 | Route 4
P3 , F4 | Route 5
P4 , F5 | Route 6
P5 | Route 1 ,4

## Slide 26: authentication

## Slide 27: Free space attenuation factor
TX(P5)*RX(route 1) |  |  | 
#rx | distance | Measurements | path los
1 | 1.3 | -26 | 46
2 | 2.8 | -32 | 52
3 | 4.3 | -34 | 54
4 | 5.8 | -39 | 59
5 | 7.3 | -38 | 58
6 | 8.8 | -41 | 61
7 | 10.3 | -43 | 63
8 | 11.8 | -41 | 61
9 | 13.3 | -43 | 63
10 | 14.8 | -48 | 68
11 | 16.3 | -47 | 67
12 | 17.8 | -49 | 69
13 | 19.3 | -48 | 68
Tx and Rx location | mean square error
TX(P5)*RX(route 1) | 4.661236828
TX(P5)*RX(route 4) | 4.790544655
TX(P1)*RX(route 2) | 5.451917858
TX(P2)*RX(route 3) | 4.904359128
TX(P3)*RX(route 5) | 4.240786069
TX(P4)*RX(route 6) | 4.706875779
Where = path loss at 1 meter

## Slide 28: Floor factor
Where = number of the floor
= floor factor
The value of Based on our measurements is 42
Tx and Rx location | mean square error
TX(F2)*RX(route 1) | 8.19718704
TX(F1)*RX(route 2) | 7.469590457
TX(F3)*RX(route 4) | 122.6622818
TX(F4)*RX(route 5) | 132.7651097
TX(F5)*RX(route 6) | 324.5090622

## Slide 29: nearby building effect
Tx and Rx location | mean square error | mean square error
TX(F3)*RX(route 4) | 122.6622818 | 9.148314508
TX(F4)*RX(route 5) | 132.7651097 | 6.519320026
TX(F5)*RX(route 6) | 324.5090622 | 9.019084557
Modeling the Effects of Nearby Buildings on Inter-Floor Radio-Wave Propagation.

## Slide 30: Wall factors
Wall type | Attenuation due to wall
Brick | 8 dBm
Concrete | 12 dBm
Where:
= number of wall types
= number of walls traversed of category
= attenuation per wall of category

## Slide 31: conclusion
the benefit of the project
for the university
In general

## Slide 32
Remember: Questions are the
main reason for world war II
So any Question