## Slide 1: Graduation Project II Structural Analysis and Design of Indonesian Rehabilitation Hospital in Nazareth city -Palestine.
An-Najah National University Faculty of Engineering Civil Engineering Department
جامعة النجاح الوطنية
كلية الهندسة ونكنولوجيا المعلومات
By
Ahmad Shammout
Deema Safadi
Masa Awad
Rahaf Abu Omar
Zaid Abu Zahra
Under supervision of: Ibrahim Arman.

## Slide 2: Outline: 1. General Description 2. Preliminary Design 3. 3-D Modeling and Analysis 4. Verification of Structural Design 5. Structural Design

## Slide 4: General Description
Location
It is located in Nazareth – Palestine, and the coordinates of the project according to the global coordinate system WGS are 32°42′08″N, 35°17′52″E. Location elevation (site level) is +347m AMSL (above mean sea level).

## Slide 6: General Description
Floor Number | High of each floor (m) | Area of each floor (m2)
B2 | 4 | 1853.65
B1 | 4 | 1853.65
GF | 4 | 1387
F1 | 4 | 1308.96
F2 | 4 | 1230.05
Roof | 4 | 1137.11
Height and Area For Each Floor
Stair-Case | 3 | 28.84

## Slide 7: General Description
All supports are fixed supporter in the 3D.
As for the external walls, part of them are made of glass walls and the other part are stone walls, and they are added as dead loads on the external beams.
The slab system is two-way solid slab with drop beams .
In preliminary design chapter, a quick preliminary was performed, so the thicknesses of retaining and shear walls were taken from architectural plans.
Eight checks were made include compatibility check, equilibrium check, stress-strain check, time period, base shear ,story drift , story forces , structural irregularity and P-delta.
Assumptions

## Slide 8: Floor Plans

## Slide 9: Besement two

## Slide 10: Besement One

## Slide 11: Ground Floor

## Slide 12: Floor One

## Slide 13: Floor Two

## Slide 14: Roof Floor

## Slide 15: General Description
Codes and Standard.
ASCE 7-22 (American Society of Civil Engineers
ACI 318-19 (American Concrete Institute)
ASTM 2016 (American Society for Testing and Materials)

## Slide 16: General Description
Unit weight, ɣ | 25 (kN/m 3)
Compressive strength, f’c | 28 Mpa (B350) 40 Mpa (B500)
Linear modulus of Elasticity,Ec | 4700 = 24870 Mpa
Unit weight, ɣ | 25 (kN/m 3)
Compressive strength, f’c | 28 Mpa (B350) 40 Mpa (B500)
Linear modulus of Elasticity,Ec | 
Construction Materials
Structural Materials:

## Slide 17: General Description
Non- Structural Materials:
Material | Unit weight ɣ(KN/m3)
Masonry stone | 26.5
Cement mortar &Plaster | 23
Partition blocks | 15
Filing material aggregate | 18
Glass | 25
Marble Tiles | 27
Aluminium | 26
False celling | 0.2 (KN/m2)
Sand | 23
Reinforce concrete | 25
Construction Materials.

## Slide 18: General Description
Gravity loads :
Dead load
Super dead load
Live load
Snow load
Lateral loads :
Soil load
Seismic load
Water load
Loads

## Slide 19: General Description
Floor Number | Super-imposed load (KN/m2 ) on the slab
Basement 2 | 4.1
Basement 1 | 4.5
Ground Floor | 7
Floor 1 | 7.5
Floor 2 | 7.5
Roof | 7
Superimposed dead load

## Slide 20: General Description
Occupancy | Live Load (KN/m2 )
Parking | 3
Store 1st Floor | 5
Store under 1st Floor | 6
Store above 1st Floor | 4
W.C | 2
Audiology room | 6
X-Ray room | 6
Stairs | 5
Gym | 5
Laboratories | 3
Balconies | 5
Patient room | 2
Office use | 2.5
Kitchen | 5
Pharmacy | 6
Clinic room | 5
Corridor at GF | 5
Corridor above 1st Floor | 4
Roof live Load( Lr) | 1
1.92 KN/m2
Live Load
Snow Load

## Slide 21: General Description
Lateral Load
Soil Load:
Water Load:

## Slide 22: General Description
Seismic loads:
According to ASCE 7-22 code to seismic analysis for this structure:
- Risk category: risk category of the building is IV
Lateral Load

## Slide 23: General Description
Importance factor : (Ie) = 1.5
Lateral Load

## Slide 24: General Description
- Mapped acceleration parameters Ss & S1 :
From Palestine seismic map:
Lateral Load
Ss = 0.7 g
S1 = 0.14 g
TL = 8 sec

## Slide 25: General Description
Site classification is C
Site Class

## Slide 26: General Description
- The values of Fa and Fv According to the site class in this project are 1.12, 1.66, respectively.
Site Coefficients

## Slide 27: General Description
-The maximum considered earthquake Spectral Response Acceleration
Parameters SMS and SM1:
SMS =Fa SS = 1.12 × 0.7 = 0.784
SM1 = Fv S1= 1.66 × 0.14= 0.2324
Design spectral acceleration :
SDS= SMS ×1.0 = 0.784
SD1= SM1× 1.0 = 0.2324
Seismic Design Category :
Seismic design category D
Seismic Design Category

## Slide 28: General Description
Type of the lateral forces resisting system :
Building frame system: special shear walls .
Response Modification Factor (R) = 6
Over-strength Factor (Ωo) = 2.5
Deflection Amplification Factor (Cd) = 5
Lateral Force Resisting System

## Slide 29: General Description
Type of the lateral forces resisting system :
Moment – resisting frame: special reinforced concrete moment frames.
Response Modification Factor (R) = 8
Over-strength Factor (Ωo) = 3
Deflection Amplification Factor (Cd) = 5.5
Lateral Force Resisting System

## Slide 30: General Description
for building frame system :
Ta = Ct hn x = 0.0488 × 16 0.75 = 0.39 sec
T from ETABS ≤ Ta Cu
The period is limited to Ta Cu= 0.3904 × 1.4676= 0.57 sec
Structural Period

## Slide 31: General Description
for Moment – resisting frame:
Ta = Ct hn x = 0.0466 × 16 0.9 = 0.565 sec
T from ETABS ≤ Ta Cu
The period is limited to Ta Cu= 0.565× 1.4676= 0.83 sec
Structural Period

## Slide 32: General Description
For building- frame system :
V = Cs W
Cs= 0.17
Cs min = 0.0517
Cs max = 0.101  V = 0.101 W
For Moment – resisting frame:
V = Cs W
Cs= 0.147
Cs min = 0.0517
Cs max = 0.052  V = 0.052 W
Seismic base shear

## Slide 33: General Description
Computer Programs

## Slide 34: Structural Preliminary Design

## Slide 35: 1. Slab System 2.Beam System 3. Column System 4. Wall System
Preliminary Design
Structural Systems for analysis and design

## Slide 36: Slab Layout

## Slide 37: Using two-way solid slab, must
Preliminary Design
Slab System
By referring to Table 8.3.1.2 in ACI-318-19,
Assuming αfm > 2:
h min = 200mm

## Slide 38
Slab System
Check Slab for shear
Preliminary Design

## Slide 39
Preliminary Design
Slab System
Check Slab for shear

## Slide 40: Beam Layout

## Slide 41
Preliminary Design
Beam Layout

## Slide 42
Preliminary Design
Beam System
Beam number | Height (mm) | Width (mm)
B1 | 600 | 200
B2 | 600 | 400
B3 | 600 | 800

## Slide 43: Column Layout

## Slide 45
Preliminary Design
Column System
R: Rectangular column
C: Circular column

## Slide 46: Wall Layout

## Slide 47
Preliminary Design
Two types of walls in this structure will be used:
1. Basement retaining walls.
2. Elevators and staircase walls. (Shear walls).
From architectural plans, elevators and staircase walls have an initial thickness equal to 200 mm. In contrast, retaining walls have an initial thickness equal to 300 mm.
Wall System
Wall name | Wall thickness (mm)
SW 200 | 200
SW 300 | 300

## Slide 49: 3D-Modeling and Analysis

## Slide 50: 3D-Modeling and Analysis

## Slide 51: 3D-Modeling and Analysis

## Slide 52: 3D-Modeling and Analysis

## Slide 53: 3D-Modeling and Analysis
Basic ultimate load combinations:
1.4D
1.2D + 1.6L + 0.5(Lr or S or R)
1.2D + 1.0E + L + 0.2S
0.9D + 1.0E
0.9 D+ 1.0 W
1.2D+1.6 (Lr or S or R )+(L or 0.5W )
1.2 D+1.0 W+L +0.5 (Lr or S or R )
Basic service load combinations:
D
D + L
D +(0.6W or 0.7E)
D + 0.75L + 0.75(0.7E) + 0.75S
0.6D + 0.7E
Load Combinations

## Slide 54: 3D-Modeling and Analysis
Ultimate load combinations:
1.4DL+1.4SID
1.2DL+1.2SID+1.6LL + 0.5S
1.2DL+1.2SID+1.0 LL + 1.6 S
1.36 DL + 1.36 SID + 1.0 LL + 1.3 Eqx + 0.39 Eqy + 0.2S
1.36 DL + 1.36 SID + 1.0 LL + 1.3 Eqy + 0.39 Eqx + 0.2S
0.9DL+0.9SID
0.74 DL+ 0.74 SID + 1.3Eqx + 0.39Eqy
Service load combinations:
1.0 DL + 1.0 SID
1.0 DL + 1.0 SID + 1.0 LL
1.0 DL + 1.0 SID + 1.0 S
1.0 DL +1.0 SID +0.75 LL + 0.75 S
1.1 DL + 1.1 SID + 0.91Eqx + 0.273Eqy
1.1 DL + 1.1 SID + 0.91Eqy + 0.273Eqx
1.0 DL + 1.0 SID +0.75 LL + 0.75 S
Load Combinations

## Slide 55: 3D-Modeling and Analysis
Ultimate load combinations:
1.4DL+1.4SID
1.2DL+1.2SID+1.6LL + 0.5S
1.2DL+1.2SID+1.0 LL + 1.6 S
1.36 DL + 1.36 SID + 1.0 LL + 1.3 Eqx + 0.39 Eqy + 0.2S
1.36 DL + 1.36 SID + 1.0 LL + 1.3 Eqy + 0.39 Eqx + 0.2S
0.9DL+0.9SID
0.74 DL+ 0.74 SID + 1.3Eqx + 0.39Eqy
Service load combinations:
1.0 DL + 1.0 SID
1.0 DL + 1.0 SID + 1.0 LL
1.0 DL + 1.0 SID + 1.0 S
1.0 DL +1.0 SID +0.75 LL + 0.75 S
1.1 DL + 1.1 SID + 0.91Eqx + 0.273Eqy
1.1 DL + 1.1 SID + 0.91Eqy + 0.273Eqx
1.0 DL + 1.0 SID +0.75 LL + 0.75 S
Load Combinations

## Slide 56: Verification of Structural Analysis

## Slide 57: 3D-Modeling and Analysis
Compatibility Check

## Slide 58: 3D-Modeling and Analysis
Equilibrium Check
Load type | Difference percentage for block A | Difference percentage for block B
Dead |  | 1.6
Superimposed | 0.34 | 4.4
Stone | 0.2 | 1.7
Glass | 2.05 | -
Water | 0 | -
Live | 3.7 | 0.6
snow | 0.356 | 1.3
Soil X | 0.5 | 4.4
Soil Y | 2.36 | 4.9
Load type | Difference percentage for block A | Difference percentage for block B
Dead |  | 1.6
Superimposed | 0.34 | 4.4
Stone | 0.2 | 1.7
Glass | 2.05 | -
Water | 0 | -
Live | 3.7 | 0.6
snow | 0.356 | 1.3
Soil X | 0.5 | 4.4
Soil Y | 2.36 | 4.9
All the differences are < 5%  ok.

## Slide 59: 3D-Modeling and Analysis
Verification of the preliminary design

## Slide 60: 3D-Modeling and Analysis
Permitted Analytical Procedures
In this project, the seismic design category is D and the structure characteristics is all other structures.
The permitted analytical procedures is response spectrum and seismic response history.
The equivalent lateral force method using response spectrum analysis was used in this project to check the base shear.

## Slide 61: 3D-Modeling and Analysis
Seismic loading in Y-direction
Seismic Analysis Methods
1.Equivalent lateral force method (ELF).
Seismic loading in X-direction

## Slide 62: 3D-Modeling and Analysis
Seismic Analysis Methods
  2.Modal response spectrum method (MRS).
Definition of MRS in ETABS

## Slide 63: 3D-Modeling and Analysis
Base Shear
The values of dynamic earthquakes forces must be approximately equal to the value of earthquakes forces in the static method. However, the values were not equal, which led to change the scale factor for each of the dynamic earthquake forces in X and Y.
V manually = Cs final * Building weight
-Where W = D+ SD+ 0.25 L
Load case | Difference percentage A | Difference percentage B
EQX static | 3.85 | 1.5
EQY static | 4.7 | 1.8
Different Percentage Between Manual and Static

## Slide 64: 3D-Modeling and Analysis
Base Shear
Modification factor in X direction = 1.35 Modification factor in Y direction = 1.82
Modification factor in X direction = 1.414 Modification factor in Y direction = 1.378
Block A 
Block B 
Load case | Block | Old | New
EDX | Block A | 2451.75 | 3432.45
EDY |  | 2451.75 | 4315.08
EDX | Block B | 2451.75 | 3430.57
EDY |  | 2451.75 | 3344.24

## Slide 65: 3D-Modeling and Analysis
Scale factor modification in X-dir

## Slide 66: 3D-Modeling and Analysis
Scale factor modification in Y-dir

## Slide 67: 3D-Modeling and Analysis
Story Forces
Story | K | H(m) =hx | Weight Accumulative | Weight for Individual Floor (KN) Wx | Wx*(hx)^k | Cvx | Csx final | Vx = Csx * Total W kN | F(X) Force (KN)
StairCase | 1.1745 | 27.03 | 1066.394 | 1066.39 | 51241.4 | 0.03859 | 0.196 | 12231.06 | 471.975
Roof | 1.1745 | 24 | 7252.902 | 6186.51 | 258526 | 0.19469 | 0.196 | 12231.06 | 2381.23
F2 | 1.1745 | 20 | 17122.16 | 9869.25 | 332923 | 0.25071 | 0.196 | 12231.06 | 3066.49
F1 | 1.1745 | 16 | 27775.7 | 10653.5 | 276524 | 0.20824 | 0.196 | 12231.06 | 2547.01
GF | 1.1745 | 12 | 39318.93 | 11543.2 | 213710 | 0.16094 | 0.196 | 12231.06 | 1968.45
B1 | 1.1745 | 8 | 51398.77 | 12079.8 | 138912 | 0.10461 | 0.196 | 12231.06 | 1279.49
b2 | 1.1745 | 4 | 62403.35 | 11004.6 | 56065.2 | 0.04222 | 0.196 | 12231.06 | 516.406
Sum |  |  |  | 62403.4 | 1327902 | 1 |  |  | 12231.1
story | output case | Vx(KN) accumulative | Force(KN)
StairCase | Eqx static | -313.9961 | -313.9961
Roof | Eqx static | -2327.7166 | -2013.7205
F2 | Eqx static | -5454.7112 | -3126.9946
F1 | Eqx static | -8151.7722 | -2697.061
GF | Eqx static | -10336.5546 | -2184.7824
B1 | Eqx static | -11756.0812 | -1419.5266
b2 | Eqx static | -12411.5922 | -655.511
sum |  |  | 12411.592
For X-dir:

## Slide 68: 3D-Modeling and Analysis
Story Forces
Story | K | H(m) =hy | Weight Accumulative | Weight for Individual Floor(KN) Wx | Wy*(hy)^k | Cvy | Csy | Vy kN | F(y) Force(kN)
Staircase | 1.1745 | 27.03 | 1066.394 | 1066.39 | 51241.4 | 0.03859 | 0.136385 | 8510.88 | 328.42
Roof | 1.1745 | 24 | 7252.902 | 6186.51 | 258526 | 0.19469 | 0.136385 | 8510.88 | 1656.96
F2 | 1.1745 | 20 | 17122.16 | 9869.25 | 332923 | 0.25071 | 0.136385 | 8510.88 | 2133.79
F1 | 1.1745 | 16 | 27775.7 | 10653.5 | 276524 | 0.20824 | 0.136385 | 8510.88 | 1772.32
GF | 1.1745 | 12 | 39318.93 | 11543.2 | 213710 | 0.16094 | 0.136385 | 8510.88 | 1369.73
B1 | 1.1745 | 8 | 51398.77 | 12079.8 | 138912 | 0.10461 | 0.136385 | 8510.88 | 890.325
B2 | 1.1745 | 4 | 62403.35 | 11004.6 | 56065.2 | 0.04222 | 0.136385 | 8510.88 | 359.337
sum |  |  |  | 62403.4 | 1327902 | 1 |  |  | 8510.88
story | output case | Vy(KN) acummulative | Force(KN)
Staircase | Eqy Static | -219.1716 | -219.17
Roof | Eqy Static | -1624.7636 | -1405.592
F2 | Eqy Static | -3807.4292 | -2182.66
F1 | Eqy Static | -5689.9979 | -1882.56
GF | Eqy Static | -7214.9923 | -1524.99
B1 | Eqy Static | -8205.8325 | -990.8402
B2 | Eqy Static | -8663.384 | -457.5515
sum |  |  | 8663.384
For Y-dir:

## Slide 69: 3D-Modeling and Analysis
Story Forces
Story | Force X Manually kN | Force X ETABS kN | Force Y Manually | Force Y ETABS
Staircase | 471.975 | -313.9961 | 328.42 | -219.1716
Roof | 2381.23 | -2013.7205 | 1656.96 | -1405.592
F2 | 3066.49 | -3126.9946 | 2133.79 | -2182.6656
F1 | 2547.01 | -2697.061 | 1772.32 | -1882.5687
GF | 1968.45 | -2184.7824 | 1369.73 | -1524.9944
B1 | 1279.49 | -1419.5266 | 890.325 | -990.8402
b2 | 516.406 | -655.511 | 359.337 | -457.5515
Sum | 12231.1 | 12411.592 | 8510.88 | 8663.384
Difference error % | 1.45 |  | 1.76 | 

## Slide 70: 3D-Modeling and Analysis
Period
T limit = Cu*Ta,
Ta = Ct (hn)x
Tx final is the Min of Ta and Tx
Ty final is the Min of Ta and Ty
Tx ETABS | 0.233
Ty ETABS | 0.426
T Manually | 0.84901
Tx Final | 0.233
Ty Final | 0.426
Sample Calculation For Block B

## Slide 71: 3D-Modeling and Analysis
Type of Lateral structural system
Percentage of Loads Resisting by Walls | Type
Less than 25% | Moment Resisting Frame System
25% to 75% | Dual System
More than 75% | Shear wall Resisting System

## Slide 72: 3D-Modeling and Analysis
Type of Lateral structural system
Total vertical reactions in X direction
Walls vertical reactions in X direction
Sample calculation For Block A in X-Direction

## Slide 73: 3D-Modeling and Analysis
Type of Lateral structural system
Total vertical reactions in Y direction
Walls vertical reactions in Y direction
Sample calculation For Block B in Y-Direction

## Slide 74: 3D-Modeling and Analysis
Type of Lateral structural system
Percentage of Loads Resisting by Walls | Type
Less than 25% | Moment Resisting Frame System
25% to 75% | Dual System
More than 75% | Shear wall Resisting System
Block A | Difference in X %
 | Difference in Y %
Block B | Difference in X %
 | Difference in Y %
59 | Dual System
81 | Shear Wall Resisting System
91 | Shear Wall Resisting System
91 | Shear Wall Resisting System

## Slide 75: 3D-Modeling and Analysis
Model Participation
Case | Mode | SumUX | SumUY
Modal | 1 | 0.4566 | 0
Modal | 2 | 0.4598 | 0.0546
Modal | 3 | 0.4601 | 0.5238
Modal | 4 | 0.4837 | 0.5296
Modal | 5 | 0.5704 | 0.5319
Modal | 6 | 0.5721 | 0.5331
Modal | 7 | 0.5795 | 0.5422
Modal | 8 | 0.6057 | 0.5602
Modal | 9 | 0.6124 | 0.5697
Modal | 10 | 0.6129 | 0.5897
Modal | 11 | 0.6166 | 0.6742
Modal | 12 | 0.6167 | 0.6861
Modal | 13 | 0.6392 | 0.7712
Modal | 14 | 0.6583 | 0.8177
Modal | 15 | 0.6585 | 0.8197
Modal | 16 | 0.9156 | 0.82
Modal | 17 | 0.9162 | 0.82
Modal | 18 | 0.9268 | 0.8366
Modal | 19 | 0.928 | 0.8396
Modal | 20 | 0.9316 | 0.8694
Modal | 21 | 0.9324 | 0.8895
Modal | 22 | 0.9324 | 0.8896
Modal | 23 | 0.9328 | 0.9084
Modal | 24 | 0.9332 | 0.9302
Modal | 25 | 0.9365 | 0.9329
Modal | 26 | 0.9387 | 0.9342
Modal | 27 | 0.9401 | 0.9353
Modal | 28 | 0.9401 | 0.9442
Modal | 29 | 0.9434 | 0.9445
Modal | 30 | 0.9478 | 0.9452
Case | Mode | SumUX | SumUY
Modal | 1 | 0.0003 | 0.6613
Modal | 2 | 0.6907 | 0.6617
Modal | 3 | 0.6937 | 0.6974
Modal | 4 | 0.6938 | 0.872
Modal | 5 | 0.8468 | 0.8733
Modal | 6 | 0.8488 | 0.919
Modal | 7 | 0.8633 | 0.9382
Modal | 8 | 0.8742 | 0.9384
Modal | 9 | 0.877 | 0.9554
Modal | 10 | 0.904 | 0.9624
Modal | 11 | 0.9156 | 0.9628
Modal | 12 | 0.9362 | 0.963
Number of modes required is the one where 90% must be achieved from both X and Y direction
Block A
Block B

## Slide 76: Structural irregularity:

## Slide 77
Horizontal irregularity:
Structural irregularity:

## Slide 78
Vertical irregularity:
Structural irregularity:

## Slide 79: Verification of structural design

## Slide 80
Beam design verification
Verification of structural design
* Flexural design verification:
Beam cross section 1100*600
Beam length = 15.7 meter
located in the second floor.
ETABS result :
The area of steel for this beam due to the ultimate negative moment = 2124 mm2.

## Slide 81
Beam design verification
Verification of structural design
Manual calculation:
Mu =419.95 KN.m
Cover =60 mm
d=600-60 =540 mm
b=1100 mm
Difference percentage equal to 0.16% < 5%...OK

## Slide 82
Beam design verification
Verification of structural design
* Shear design verification:
Beam cross section 400*600
Beam length = 5.35 m
located in the second floor.
ETABS result :

## Slide 83
Beam design verification
Verification of structural design
Manual calculation:

## Slide 84
Beam design verification
Verification of structural design
 | ETABS result | Manual result | Different percentage
ΦVc | 142.35 | 142.4 | 0.035%
ΦVs | 3.62 | 3.6 | 0.56%
Vp | 85.12 | 85.2 | 0.093%
Av/s | 21.65 | 21.16 | 2.31%

## Slide 85
Column design verification
Verification of structural design
Axial load capacity :
cross section =600*900
length = 4m
located in the third floor.

## Slide 86
Column design verification
Verification of structural design
Chart: Phi,Mn3
| 0 | 809.50810000000001 | 1182.1718000000001 | 1493.6143999999999 | 1763.1745000000001 | 2027.3152 | 2339.2705000000001 | 2577.4443000000001 | 2207.6266000000001 | 1434.1229000000001 | 0
 | 10011.1671 | 10011.1671 | 8862.6328 | 7509.9252 | 5936.2707 | 4008.7361 | 3075.6967 | 1751.1646 | -79.6422 | -2479.0723 | -6106.2402
 | 4629

## Slide 87
Column design verification
Verification of structural design

## Slide 88
Walls design verification
Structural design
Shear Wall
Pier
Spandrel

## Slide 89
Structural design
Spandrel- Coupling beam:
Walls design verification

## Slide 90
Structural design
Spandrel- Coupling beam:
Walls design verification

## Slide 91
Structural design
Spandrel- Coupling beam:
Design of section:
Walls design verification

## Slide 92: Structural design

## Slide 93
Design of slabs
Structural design

## Slide 94
Design of slabs
Structural design
Manual calculation:
(Roof slab)

## Slide 95
Design of slabs
Structural design

## Slide 96
Design of beams
Structural design
* Area of steel from ETABS: (mm2)
* Longitudinal reinforcement:
* Shear area of steel from ETABS:(mm2/mm)
* Shear reinforcement:

## Slide 97
Design of beams
Structural design

## Slide 98
Design of beams
Structural design
* Cross section:
* Longitudinal section:

## Slide 99
Design of columns
Structural design
* Weak beam – strong column concept:

## Slide 100
Design of columns
Structural design
* ETABS results:

## Slide 101
Design of columns
Structural design
Cross section:

## Slide 102
Design of Walls
Structural design
Spandrel- Coupling beam:
Flexural Design:
As Top = 3014 mm
As Bot = 3014 mm
As final = 3014 mm
Use 4Փ32 Top and Bot
Ah Left = 1000 mm
Ah Right = 1000 mm
As final = 1000/2 = 500 mm
Use Փ12/200 mm
Av Left = 3050 mm
Av Right = 3200 mm
As final = 3.2 mm /mm
Use 2legs Փ12 Stirrups/70mm
Diagonal reinforcement:
Adia Left = 3050 mm
Adia Right = 3200 mm
As final = 3.2 mm /mm
Use 6Փ32
Shear Design:

## Slide 103
As Top = 3014 mm
As Bot = 3014 mm
As final = 3014 mm
Use 4Փ32 Top and Bot
Flexural Design:

## Slide 104
Ah Left = 1000 mm
Ah Right = 1000 mm
As final = 1000/2 = 500 mm
Use Փ12/200 mm
Shear Design:

## Slide 105
Av Left = 3050 mm
Av Right = 3200 mm
As final = 3.2 mm /mm
Use 2legs Փ12 Stirrups/70mm
ShearDesign:

## Slide 106
Adia Left = 3050 mm
Adia Right = 3200 mm
As final = 3.2 mm /mm
Use 6Փ32
Diagonal reinforcement :

## Slide 107
Design of Walls
Structural design
Spandrel- Coupling beam:
Cross section

## Slide 108
Design of Walls
Structural design
Pier Design:
Design of section:

## Slide 109
Design of Walls
Structural design
Pier Design:
Design of section:
Development length:
Transverse reinforcement:
Smax, is min of:
<
<
<

## Slide 110
Design of Walls
Structural design
Pier Design:
Cross Section

## Slide 111
Design of Footing:
Structural design
Mat foundation:
Thickness = 1000 mm
Wide beam shear(One-way shear ):
Maximum shear (at distance d from face of wall) = 3430.4 KN/m

## Slide 112
Design of Footing:
Structural design
Shear design:

## Slide 113
Design of Footing:
Structural design
Mat foundation:
Check punching shear
Maximum punching shear =0.46 .
Max. Punching shear demand /capacity ration equal to 0.46 < 1

## Slide 114
Design of Footing:
Structural design
Mat foundation:
Check stresses under footings
Max. Stress equal to 530 KN/m2which larger than
bearing capacity (350KN/m2), so piles will be used in this Zonee.

## Slide 115
Design of Footing:
Structural design
Piles :
A 0.8 m diameter pile with two different depths was used piles 8 m deep and 12 m deep.
Deeper piles have been used in the central area where loading is higher, so larger capacities are required .
After put the piles, Max. Stress under the mat foundation is equal to 290KN/m2, which smaller than 350 KN/m2.

## Slide 116
Design of Footing:
Structural design

## Slide 117
Design of stairs
Structural design
Stairs :
Flight Slab :
Riser height = 170 mm
Width of Tread =300 mm
Loads :
SD =3.96 KN
LL = 5 KN

## Slide 118
Design of stairs
Structural design
Stairs :
Flight Slab:
Preliminary thickness of concrete :
H = = = 180 mm
Try H = 180 mm

## Slide 119
Design of stairs
Structural design
Stairs :
Flight Slab :
Live load on stairs = 5 KN
Sd load on stairs = 3.96 KN
Dead Load = .18 X 25 = 4.5 KN
Wu = 1.2 x DL + 1.6 x LL
Wu = 1.2 x ( 4.5 + 3.96) + 1.6 x 5 = 18.15 KN \

## Slide 120
Design of stairs
Structural design
Stairs :
Flight Slab :

## Slide 121
Design of stairs
Structural design
Flight Slab:
Shear Check :

## Slide 122
Design of stairs
Structural design
Stairs :
Landing Slab:

## Slide 123
Design of stairs
Structural design
Stairs :
Landing :

## Slide 124
Design of stairs
Structural design
Stairs :
Landing:

## Slide 125
Design of stairs
Structural design
Stairs :
Landing :

## Slide 126
Design of diaphragms and collectors:
Structural design

## Slide 127
Design of diaphragms:
Structural design

## Slide 128
Fpx Calculation:
Structural design

## Slide 129
Fpx Calculation:
Structural design

## Slide 130
Modeling:
Structural design

## Slide 131
Modeling:
Structural design
Maximum bending moment
Maximum shear force

## Slide 132
Diaphragm width calculation:
Structural design

## Slide 133
Design of collector:
Structural design
Axial force in the collector

## Slide 134
Design of collector:
Structural design

## Slide 135
Non-Structural Elements
Structural design
The exterior walls contain 3cm of stone and 7cm of unreinforced concrete, the stones must be attached and fixed in the horizontal and vertical directions.
It was decided to stack four rows of stone units vertically together. Each stone is 25 cm high.
Exterior walls:

## Slide 136
Non-Structural Element
Structural design
Exterior walls:

## Slide 137
Non-Structural Materials
Structural design
Partition walls:

## Slide 138: The End

## Slide 139
Finally, I’m an engineer now