## Slide 1: Smart parking system
Prepared by : fatheyah faqih
Supervisor:Dr.Falah Hassn

## Slide 2: OUTLINE
Introduction
Why the ultrasonic sensor
Features of project
Our working
Hardware
Conclusion

## Slide 3: Introduction
With the increase in vehicle production and world population, more and more parking spaces and facilities are required. In this project a new parking system called Smart Parking System (SPS) is proposed to assist drivers to find vacant spaces in a car park in a shorter time

## Slide 4: Why the ultrasonic sensor
Ultrasonic sensors are used to detect movement of targets and to measure the distance to targets in many process plants. Sensors with an on or off digital output are available for detecting the movement of objects, and sensors with an analog output which varies proportionally to the sensor to target separation distance are commercially available

## Slide 5
Active ultrasonic sensors generate high frequency sound waves and evaluate the echo which is received back by the sensor, measuring the time interval between sending the signal and receiving the echo to determine the distance to an object. Passive ultrasonic sensors are basically microphones that detect ultrasonic noise that is present under certain conditions, convert it to an electrical signal, and report it to a LCD display.

## Slide 6: Ultrasonic instead of light sensor
In graduation project 1 our searching about using the light sensor instead of the ultrasonic
What is the reasons ????????????

## Slide 7: Working
Our proposed SPS detection system is based on ultrasonic sensors. For each individual car park, this would require one sensor fixed on the ceiling above each parking space. Ultrasonic sensors work based on echo-location. The sensor transmits a sound, which hits a solid object (car or ground) and is reflected back to the sensor. The time between the sent pulse and the returned echo is used to calculate distance. In a vacant space, the time between transmitted sound and reflection is longer than in an occupied space, hence the sensor can detect when a space is occupied.

## Slide 8: Working
In our project , the distance was the ultrasonic sensor sensing is 50 cm , when the car existing , the distance that is felt by the sensor will be reduced then the time that the signal take to reflect also decrease then the LCD will show that this space “FULL” , and when the car leave its space the distance will become bigger then the time of reflection also increase then the LCD will show on the screen that this space was “empty”.

## Slide 9: The circuit diagram for the work

## Slide 10: Hardware used
Arduino UNO
LCD Display
LEDs
Ultrasonic sensor
Batteries

## Slide 11: conclusion
The main contribution of this project is to introduce the most significant parking problem —., finding an empty space — and propose a solution. Ultrasonic sensors can be used both for parking space detection and improper parking detection. The proposed architecture for a parking detection system would decrease searching time for vacant spaces and reduce instances of single cars improperly parking across two spaces. Future research might examine car park booking procedures and optimization of sensor usage. Cost effectiveness and marketing could be studied as well.