## Slide 1
Automated Student Hostel
Prepared by:
Ghroob Suwan
Mayas Dawod
Rusul Maqboul
Walaa AbuSoad
An-Najah National University
Faculty of Engineering & Information Technology
Building Engineering Department
Graduation Project 2
Supervised by:
Dr. Mutassem Baba

## Slide 2: Outline
Introduction
Architectural Design Chapter
Structural Design Chapter
Environmental Design Chapter
Mechanical Design Chapter
Electrical Design Chapter

## Slide 3: INTRODUCTION

## Slide 4: 1. Introduction
The land of the project is located at the south-east of an An-Najah National University (the new campus), in the western part of the city of Nablus. The site of the project it is far from the city center about 5 km, and about 300 m from the main streets (RAFEDIA). The building is surrounded by the Residential Buildings from the east, bystreets from south west and west, and surrounded by nothing from the north .
1.1 Site Location:

## Slide 5: 1. Introduction
About (530-540)m above sea level and 5 kilometers away from city center.
Site has a total area of 5583m2
Near Serviceable streets width equals 10 m.
1.2 Site Location:

## Slide 6: 1. Introduction
Environmental Site Analysis depends on many variables:
Solar analysis.
Noise analysis.
Wind analysis.
Climate analysis
1.2 Site Location:

## Slide 7: 1. Introduction
Environmental Site Analysis depends on many variables:
Noise analysis.
Most of the noise is towards the street.
Highest value doesn’t exceed 59 dB.
Climate analysis
1.2 Site Location:
Summary of annual temperatures | 
average monthly temperature in the summer | (21-24) ° C.
average monthly temperature in the winter | (9.5-11.5) ° C.
maximum temperature reaches | (39-40.5) ° C.
lowest temperature reaches | (-1-1.4) ° C.)

## Slide 8: 1. Introduction
Environmental Site Analysis depends on many variables:
Solar analysis.
Sun path as shows in picture
Wind analysis.
Wind direction is mostly to the north-west.
1.2 Site Location:

## Slide 9: 1. Introduction
1.2 Site Analysis :
Site Advantages :
The slop of land can be handled.
Away from traffic rush.
Has a quiet surrounding environment.
Very close to An-Najah National University (the new campus), that may increase number of coming students.
Good Northern view.
1.2 Site Location:
Site Disadvantages :
Bit away from the public transportation, so poor accessibility.

## Slide 10: ARCHITECTURAL Design CHAPTER

## Slide 11: 1. Architictula
2.1 Site Plan for the project:

## Slide 12: 2. Architectural Design
2.1 Site for the project:

## Slide 13: 2. Architectural Design
2.1 Site for the project:
    2.1.1 Swimming pool
A swimming pool with an area of 230 m2
was built on the north east side of the land and was about 10 meters below the 0.0 level

## Slide 14: 2. Architectural Design
2.1 Site for the project:
    2.1.2 Playgrounds
Basketball and the other for Tennis, with an area of 140 m2 for each.

## Slide 15: 2. Architectural Design
2.1 Site for the project:
    2.1.3 Seating area
The site was also provided with 120 m2 of outdoor seating

## Slide 16: 2. Architectural Design
2.1 Site for the project:
    2.1.3 Seating area

## Slide 17: 2. Architectural Design
2.2 Basement Floor
Basement Floor
( AREA = 700 SM )
The basement Floor includes a car parking with two ramps and service rooms

## Slide 18: 2. Architectural Design
2.3 Ground Floor
Ground Floor
( AREA = 1230 SM )
The ground floor includes the public facilities
reception, secretarial, waiting room, cafeteria, gym, Study rooms, lounge and services.

## Slide 19: 2. Architectural Design
2.4 First Floor
First Floor
( AREA = 1253 SM )
The first floor is symmetry It contains shared student rooms, two living rooms, two kitchens and services.

## Slide 20: 2. Architectural Design
2.5 Second Floor
Second Floor
( AREA = 1273 SM )
The first floor is symmetry It contains shared student rooms, two living rooms, two kitchens and services.

## Slide 21: 2. Architectural Design
  2.8 Spaces and Functions
    2.8.4 Students’ Bed Rooms:
1st Floor & 2nd Floor
Average Rooms Area = 28 SM

## Slide 22: 2. Architectural Design
2.6 Third Floor
Third Floor
( AREA = 1273 SM )
The third floor consists of suites, each suite has a bedroom in addition to a cooking area and a private bathroom. Each one accommodates two students The floor is also symmetrically divided

## Slide 23: 2. Architectural Design
  2.8 Spaces and Functions
    2.8.5 Students’ Bed Rooms:
Average Rooms Area =37 SM
Area =3 SM
Area = 8 SM
Area = 26 SM
3rd Floor

## Slide 24: 2. Architectural Design
2.7 Fourth Floor
Fourth Floor
( AREA = 1300 SM )
The third floor consists of suites, each suite has a bedroom in addition to a cooking area and a private bathroom. Each one accommodates two students The floor is also symmetrically divided

## Slide 25: 2. Architectural Design
  2.8 Spaces and Functions
    2.8.6 Students’ Bed Rooms:
4th Floor
Average Rooms Area = 30 SM
Area = 7 SM
Area = 20 SM
Area = 4 SM

## Slide 26: 2. Architectural Design
  2.8 Spaces and Functions
    2.8.1 Main Entrance

## Slide 27: 2. Architectural Design
  2.8 Spaces and Functions
    2.8.2 Main Lobby
Space | Area (m2)
Reception | 19.5
Secretary | 8.7
Guard room | 15.3
Waiting Area | 76.35

## Slide 28: 2. Architectural Design
  2.8 Spaces and Functions
    2.8.3 Study Rooms
Study rooms are designed in hostel for group study or student projects, five rooms located on the west side of the ground floor
With an area of ​​15.5 m2 per room

## Slide 29: 2. Architectural Design
  2.8 Spaces and Functions
    2.8.7 Living rooms & kitchens in 1st Floor
Kitchen Area = 36 SM
Living Room Area = 38 SM

## Slide 30: 2. Architectural Design
  2.8 Spaces and Functions
    2.8.7 Living rooms & kitchens in 1st Floor
Kitchen Area = 36 SM
Living Room Area = 38 SM

## Slide 31: 2. Architectural Design
  2.8 Spaces and Functions
    2.8.7 Living rooms & kitchens in 4th Floor

## Slide 32: 2. Architectural Design
  2.9 Elevations
    2.9.1 South elevation
Smart facade

## Slide 33: 2. Architectural Design
  2.9 Elevations
    2.9.2 North elevation

## Slide 34: 2. Architectural Design
  2.9 Elevations
    2.9.3 West elevation
Smart facade

## Slide 35: 2. Architectural Design
  2.9 Elevations
    2.9.4 East elevation
Smart facade

## Slide 36: STRUCTURAL CHAPTER

## Slide 37: 3.Structurtural Design
The structural design for the automated hostel, consisting of five floors and a basement/parking.
The building is separated into 3 blocks for the seismic design by expansion joints, with the left and right blocks being almost identical.

## Slide 38: 3.Structurtural Design
Design codes used :
Building code requirements for reinforced concrete – ACI 318M-11
Uniform building code – UBC 97 – for the earthquakes loads
Material used:
Reinforced concrete B300- for structural elements, with concrete compressive strength fć=24 Mpa
Plain concrete B200 for blinding's
Reinforcement – deformed high yielding steel Fy=420 Mpa
Bearing capacity for soil: The bearing capacity for soil is 300 KN/m²

## Slide 39: 3.Structurtural Design
Design loads:
SID load from filling materials is 4 KN/m² + 1.5 KN/m² block = 5.5 KN/m²
Live load is for residential buildings is 2.5 KN/m² and 5 KN/m² for large spaces and halls
Slab load:
Slab load coming from own weight of one way ribbed slab 32 cm is approximately = 8.5 KN/m²
Slab load coming from own weight of two way ribbed slab 32 cm is approximately = 10 KN/m²

## Slide 40: 3.Structurtural Design
Structural system for center block:
Two system used for the center block slabs
One way ribbed slab
Two way ribbed slab
Thickness of slabs
For one way ribbed slab L*/21 = 4600/21 = 22 cm
For two way ribbed slab ((L1 + 0.76XL1) + (2XL2))/ 140 = 24
Cantilever one way ribbed slab L / 8 = 2500/8 = 31.2
Use slab thickness of 32 cm
* Where L is the longest span

## Slide 41: Structural design
Beam dimension for center block:
Columns:
Type | Dimension
Main beam | Beam 300 x 700
Secondary beam | Beam 800 x 320
Internal column | C 600 x 600
Edge column | C 700 x 300

## Slide 42: Structural design
Footings dimension for center block:
for the center block there are multiple footings used, example mentioned in the table below
Type | Dimension (M)
Isolated footing | F16- 3.40 X 3.40 X 0.70
Combined footing | Comb1- 3.70 x 2.0 x 0.50

## Slide 43: 3.Structurtural Design
Beam sections and column
distribution for centered block
Is shown in the figure

## Slide 44: 3.Structurtural Design
3D model for the
centered block using
ETABS

## Slide 45: 3.Structurtural Design Checks
Compatibility check

## Slide 46: Checks for structural analysis
Equilibrium check
Manual | Approximately 2032 Kn
ETABS | Approximately 2772 Kn

## Slide 47: 3.Structurtural Design Checks:
Seismic design - W total seismic load
Soil type is SB
Ct = 0.0731 for reinforced concrete moment resisting frames
Z= 0.2 , I = 1, R = 8.5
Cv= 0.2, Ca = 0.2
T = Ct (hn)^3/4 = 0.0731 x (22)^3/4 = 0.74
V = Cv * I * W / R * T = 0.0376 W

## Slide 48: Checks for structural analysis
Natural period – T
 | T in seconds
Manual | 0.74
From ETABS | 1.9

## Slide 49: 3.Structurtural Design
Slab design
The slab design for the center
Block for the one way ribbed
Slab section

## Slide 50: 3.Structurtural Design
Slab design
Slab design for the center
Block for the two way ribbed
Slab section

## Slide 51: 3.Structurtural Design
Main Beam design

## Slide 52: 3.Structurtural Design
Column design for internal column
Column design for edge column

## Slide 53: 3.Structurtural Design
Footings design for
center block

## Slide 54: 3.Structurtural Design
Footings
design
– comb1

## Slide 55: ENVIROMENTAL CHAPTER

## Slide 56: 4.Environmental CHAPTER
Orientation:
Orientation of the building is very important for all environmental aspects of:
Ventilation
Daylight
Passive heating and cooling.

## Slide 57: 4.Environmental CHAPTER

## Slide 58: 4.Environmental CHAPTER
Sun Path
Sun Path is very important factor affects on all environmental aspects:
Daylight
Passive Heating and Cooling
And affects on PV system that will be illustrated on next slides.

## Slide 59: 4.Environmental CHAPTER
Sun Path Diagram at Nablus(Lat.32.22N,Long.35.25E,Alt.552m)

## Slide 60: 4.Environmental CHAPTER
Shading
Design Builder SOFTWARE was used to view sun path and its effect on the hostel.
The two design days of year was taken (21/January and 21/June), with three different times during the day (8:00 am,12:00 pm and 4:00 pm)

## Slide 61: 4.Environmental CHAPTER
Summer (21/June)
At 8:00 am:

## Slide 62: 4.Environmental CHAPTER
At 12:00 pm:

## Slide 63: 4.Environmental CHAPTER
At 4:00 pm:

## Slide 64: Winter (21/January)
At 8:00 am:
4.Environmental CHAPTER

## Slide 65: 4.Environmental CHAPTER
At 12:00 pm:

## Slide 66: 4.Environmental CHAPTER
At 4:00 pm:

## Slide 67: Acoustics
Reverberation Time (RT60)
Sound Transmission Class (STC)
Loudspeaker System.
4.Environmental CHAPTER

## Slide 68: Reverberation Time (RT60)
Students’ Bedrooms: Recommended RT60 → 0.5 - 0.9 second.
Study Rooms: Recommended RT60 → 0.8 – 1.0 second.
GYM: Recommended RT60 → 1.2 – 1.6 second.
Cafeteria: Recommended RT60 → 0.8 – 1.2 second.
4.Environmental CHAPTER

## Slide 69: Sound Transmission Class (STC)
INSUL Software Results:
Exterior Wall: STC = 28 dB
4.Environmental CHAPTER

## Slide 70: 4.Environmental CHAPTER
2. Interior Wall: STC = 48 dB

## Slide 71: 4.Environmental CHAPTER
3. Floor : STC = 68 dB

## Slide 72: Loudspeaker System
EXTRON company was chosen to select a suitable audio system.
CS1226T PLUS loud speaker system was selected.
The Calculations and Results are shown below:
4.Environmental CHAPTER

## Slide 73: 4.Environmental CHAPTER

## Slide 74: 4.Environmental CHAPTER

## Slide 75: Photovoltaic system design
This system was very effective due to the large area of the roof and the first large building consumption.
This part is a passive solar system made to save energy consumption in the Hostel.
4.Environmental CHAPTER

## Slide 76
PVSYST6.7 Software was used to design the system for the hostel.
Use LG Company to select PV cells, with a capacity of 300 WP and 36 V.
used Sofa Solar Company to Select Inverter for system, the system need 10 inverters with 30KW capacity
4.Environmental CHAPTER

## Slide 77
The module for design PV cell is (1640*1000) mm.
Active area = # of modules * Area of module = 609 × (1.64*1.00) = 998.76 m2
Total Capacity = 183 KWp
Initial Cost = 609* 1200$ = 304500$
Operation Cost = 0.015* 304500 = 4567.5 $
Electricity Production = 337300 KWh/yr.
    Cost of the system:
Annual Saving = 337300* 0.17 = 57341 $/yr.
Payback Period = 309067.5/57341 = 5 years.
4.Environmental CHAPTER

## Slide 78: 4.Environmental CHAPTER
System Layout:

## Slide 79: Thermal Analysis
Heating load and losses in the building:
4.Environmental CHAPTER

## Slide 80: 4.Environmental CHAPTER
Cooling load for the building in 15 July

## Slide 81: 4.Environmental CHAPTER
Simulation of thermal comfort in the building.

## Slide 82: MECHANICAL CHAPTER

## Slide 83: 5.Mechanical CHAPTER
Water Supply System
Water demand= 23 m3/day

## Slide 84: 5.Mechanical CHAPTER
Water Supply tank
4 tanks for cold water(cap= 6m3)
2 tanks for Firefighting system(cap= 5m3)
4 tanks for hot water(cap= 2m3)

## Slide 85: 5.Mechanical CHAPTER

## Slide 86: Grey and rainwater system
Rain Water Tank size = 1000 m3
grey Water Tank size = 20 m3
5.Mechanical CHAPTER

## Slide 87: (SHAKTI-Pressure Booster Pump – SH Series), with Po = 60Psi.
5.Mechanical CHAPTER

## Slide 88: 5.Mechanical CHAPTER
Drainage system

## Slide 89: 5.Mechanical CHAPTER
Drainage system

## Slide 90: Drainage system
5.Mechanical CHAPTER

## Slide 91: 5.Mechanical CHAPTER
Rain Water Drainage
Slope= 1%

## Slide 92: Building management system (BMS):
BMS: intelligent microprocessor to monitor and control a building systems.
  .
Benefits of BMS:
1- Energy saving.
2- comfort and healthy environment.
3- efficient maintenance.
4- work effectively with other building systems.
5.Mechanical CHAPTER

## Slide 93: Mechanical sensors
1- ADT water leak detector
5.Mechanical CHAPTER

## Slide 94: 5.Mechanical CHAPTER
2- leak smart valve:
3- water level sensor:

## Slide 95: 5.Mechanical CHAPTER
4- Faucet with motion sense:

## Slide 96: 5.Mechanical CHAPTER
Variable Refrigerant Flow (VRF) system was chosen for the hostel
VRF system consists of:
Outdoor unit
Collectors
indoor unit
HVAC System

## Slide 97: 5.Mechanical CHAPTER
Cassette unit
Wall mounted split unit

## Slide 98: Cassette units in the bedrooms:
5.Mechanical CHAPTER

## Slide 99: Wall mounted units in the offices:
5.Mechanical CHAPTER

## Slide 100: 5.Mechanical CHAPTER
Using Design Builder Software:
Inputs: Internal Temperature in the summer = 22 °C
Internal Temperature in the summer = 24 °C
Relative Humidity = 50%
Outputs: Heating load capacity =109.8KW
Cooling load capacity=254.83KW

## Slide 101: 5.Mechanical CHAPTER
Room description | Cooling load (TR) | Q (KW) | ύ
Dining Area | 22 | 6.2 | 0.41
GYM | 4 | 1.12 | 0.075
Kitchen | 1.5 | 0.43 | 0.028
Waiting Area | 3 | 0.85 | 0.056
Office 1 | 1 | 0.28 | 0.018
Office 2 | 2 | 0.57 | 0.038
Office 3 | 1 | 0.28 | 0.018
Office 4 | 1 | 0.28 | 0.018
Entrance area | 4.5 | 1.27 | 0.084
Study room 1 | 1 | 0.28 | 0.018
Study room 2 | 1 | 0.28 | 0.018
Study room 3 | 1 | 0.28 | 0.018
Study room 4 | 2 | 0.57 | 0.038
Study room 5 | 1 | 0.28 | 0.018
Total | 46 | 12.9 | 0.86
Q= ύ*ρ*Cp*(Ti-Ts)

## Slide 102: 5.Mechanical CHAPTER
Room description | Cooling load (TR) | Q (KW) | ύ
All Bed room have two person Hint: number of room = 12 | 2 Total = 24 TR | 6.7 | 0.45
All Bed room have one person Hint: number of room = 2 | 1 Total = 2 | 0.56 | 0.038
Kitchen1 | 3 | 0.84 | 0.056
Kitchen 2 | 3 | 0.84 | 0.056
Waiting room 1 | 4 | 1.12 | 0.075
Waiting room 2 | 4 | 1.12 | 0.075
Total | 40 | 11.23 | 0.75

## Slide 103: Ventilation
Ventilation has been done for bathrooms, kitchens and laundry rooms.
The following equation used to calculate the air ventilated in every space:
5.Mechanical CHAPTER

## Slide 104: ACH for each spaces
Application | ACH
Bathroom | 10
Kitchen | 20
Coffey bar | 12
Laundry room | 5
Room description | ACH (CFM)
Eating Hole | 6375
Kitchen 1 | 850
Kitchen 2 | 850
Bathroom 1 | 700
Bathroom 2 | 260
Bathroom 3 | 190
Total | 46
5.Mechanical CHAPTER

## Slide 105: ELICTRICAL CHAPTER

## Slide 106: Electrical System Design
Power sockets design and distribution
Low voltage
Occupancy sensors
Lighting design and distribution

## Slide 107: End – User Accessories
Switches
Power sockets
Fused connection units
Distribution box

## Slide 108: Power distribution
Power Sockets Distribution
C.B. for lighting = 10 Amp.
C.B. for sockets = 16 Amp.

## Slide 109: Power distribution
Distribution Box

## Slide 110: Power distribution
Main Distribution Box

## Slide 111: Power distribution
Main Distribution Box

## Slide 112: Power consumption from sockets usage

## Slide 113: Power distribution
Low voltage

## Slide 114: Power distribution
Occupancy sensors:
Passive infrared ( RIP)
Ultrasonic technology
Duel technology

## Slide 115: Artificial lighting
DIALux evo 8.0 software was used to design lighting
Bedroom in 4th Floor
Sleeping Area

## Slide 116: Artificial lighting
DIALux evo 8.0 software was used to design lighting
Bedroom in 4th Floor
Reading Area

## Slide 117: Artificial lighting
DIALux evo 8.0 software was used to design lighting
Bedroom in 4th Floor
      Cocking Area:

## Slide 118: Artificial lighting
DIALux evo 8.0 software was used to design lighting
      Study Room:

## Slide 119: Artificial lighting
DIALux evo 8.0 software was used to design lighting
      Main Lobby:

## Slide 120: Artificial lighting
DIALux evo 8.0 software was used to design lighting
      approximate amount of annual energy consumption for lighting :
Room | Power (KWh/Year) | Number of rooms | Total Power(KWh/Y)
Bedroom | 800 | 54 | 43200
Study Room | 1000 | 5 | 5000
Main Lobby | 5100 | 1 | 5100
Corridors | 1700 | 9 | 15300
Cafeteria | 3200 | 1 | 3200
GYM | 2500 | 1 | 2500
others | 500 |  | 500
Total consumption |  |  | 74,800 KWh/Y

## Slide 121: FIREFIGHTING CHAPTER

## Slide 122: Fire alarm system

## Slide 123
Fire extinguishing System

## Slide 124: Means of escape

## Slide 125
Escape plan
Escape Plan for fourth Floor

## Slide 126
Escape plan
Escape Plan for Ground Floor

## Slide 127: BELL OF QUANTITY ”BOQ”

## Slide 128
Building Cost
Total Building Cost = 7,987,188 NIS
Unit Building Cost = 985.8 NIS