## Slide 1
“Energy efficiency improvement for university college building: lighting system ”
Graduation Project 2 (2019-2020)
Prepared by:
Aya Salman
Tasneem Shabaro
Razan Jawabreh
Introduce to:
Dr. Mohammad Alsayed
Dr.Tamer Hadad
26/12/2019

## Slide 2
Contents
Introduction
Problem statement and scope of work
Objectives of the Work
Methodology
Discussion and Results
Conclusions and Recommendations
1
2
4
3
5
6

## Slide 3
Introduction
Roughly 30-70 per cent of electric energy used in commercial buildings is consumed by the lighting systems.
The study of energy savings from all types of lighting controls used in commercial buildings found that simulations appear to overestimate savings achievable in the field, especially for day lighting.
The various strategies adopted are:
1- Day lighting.
2- Integration of lighting control systems.

## Slide 4
Global Energy Consumption
Energy is essential for economic and social development and improved quality of life in all countries .
Global energy consumption in Buildings sector (residential and commercial) energy consumption
The global contribution from buildings towards energy consumption, both residential and commercial, has steadily increased reaching figures between 20% and 40% in developed countries, and has exceeded the other major sectors: industrial and transportation.

## Slide 5
The project site

## Slide 6
Problem statement and scope of work
Lighting consumes about 20 to 40% of total electricity use in large buildings Like Al-Najah National University . Especially, the Faculty of Engineering.
In this part of the project we calculated the amount of solar radiation average reaching the building and accordingly selected the types of lighting that will be replaced And calculate the savings rate during the year.

## Slide 7
Objectives of the Work
The aim of the project is to provide comfortable lighting for the eye so that we can see those around us comfortably and unobstructed and also reduce energy costs consumed by the use of types of appropriate lighting with good quality and cost. And make the best use of the solar radiation we have to reduce costs.

## Slide 8
The control system that it contains is designed following components: occupancy sensors, lux sensors and dimming actuators and dimmers.
Available daylight during the year was calculated using the program VELUX Daylight Visualize 2 .
A comparison has been made between two types of lighting lamps by excel and Minitab programs.
Methodology

## Slide 9
Discussion and Results
Discussion and Results

## Slide 10
The alternatives to lighting(400lux) and the number of lamp required
Number of Lamp Required | Life Time | Lumens | NIS | CODE | Color | Watt | Type
11 | 50000 | 2000 | 6 | T8 | 6500 | 24 | LED/MAS
12 | 1500 | 1800 | 30 | T8 | 6500 | 18 | LED/Sylvania
10 | 1500 | 2400 | 8 | T8 | 6500 | 24 | LED/ros
10 | 8000 | 2400 | 8 | E27 | 6400 | 26 | PL/sun light

## Slide 11
The alternatives to lighting and the number of bulbs They are replaced annually
Annual lamp replace ment cost (nis/yr) | Annual lamp replace (lamp/yr) | Energy demand cost in one life(NIS/YR) | Energy use (kwh/yr) | Demand (kw) | Type
2.304 | 0.384 | 17.28 | 28.8 | 0.024 | LED/MAS
384 | 12.8 | 12.96 | 21.6 | 0.018 | LED/Sylvania
102.4 | 12.8 | 17.28 | 28.8 | 0.024 | LED/ros
19.2 | 2.4 | 18.72 | 31.2 | 0.026 | PL/sun light
- | 18 | 12.69 | 21.6 | 0.018 | Current Bulb

## Slide 12
Annual saving of energy
The energy saving (kwh/yr) | Alternative
137.4 | The first alternative
190.1 | The second alternative
190.1 | the third alternative
168.1 | the fourth alternative

## Slide 13
type | color | watt | NIS | CODE | lux | life time | lumens | number of lamp required
SUPER | 6500 | 23 | 20 | E27 | 432 | 30000 | 2700 | 6
LED/luxten | 6500 | 36 | 30 | E27 | 432 | 50000 | 2700 | 6
Alternatives to lighting(500lux) and the number of lamp required.

## Slide 14
Annual saving of energy
The first alternative= 6 lamp *23 watt *4 hr/day* 300 day /yr =165.5 kwh/yr
The second alternative= 6 lamp *36 watt *4 hr/day * 300 day /yr =259.2kwh/yr
New system 500 lux with dimmer and lighting sensor
Saving ratio using dimmer and lighting sensor = 20%
The first alternative= 165.5 +33.1=198.6 kwh/yr
The second alternative= 259.2+51.84=311.04 kwh/yr

## Slide 15
In this project, linear relationships were found between two different variables for each of two different types of lamps
Our study was based on the analysis of the data of the two types of lamps are LED and fluorescent lamps
Factor Relations Analysis

## Slide 17
The confidence interval for each of the factors (lumen, cost and watt) of LED and fluorescent lamp was calculated using the T-test by the Minitab program .
- tS/+tS/
𝐘 = 𝐛𝐗 + 𝐜
Mean = ∑ 𝑋𝑖 𝑛 𝑖=1 / n
Standard deviation =
Analysis of confidence intervals

## Slide 18
Type of lamb |  | N | Mean | St dev. | SE mean | 95% CI
Florescent | Cost | 22 | 10.70 | 9.62 | 2.05 | (6.43 , 14.97)
 | Watt | 22 | 20.45 | 15.29 | 3.26 | (13.67 , 27.23)
 | Lumen | 22 | 743 | 570 | 121 | (490 , 995)
Led | Cost | 15 | 9 | 6.10 | 1.58 | (5.62 , 12.38)
 | Watt | 15 | 18.20 | 38.19 | 9.86 | (-2.95,39.35)
 | Lumen | 15 | 802 | 457 | 118 | (549 , 1055)

## Slide 19
Conclusions and Recommendations
Linear relationships between lumen and cost, lumen and watt , and watt and cost were found as the data of two types of Led and fluorescent lamps, linear equations were also found so that linear but weak relationships were obtained using the regression coefficient.
MiniTab was used to calculate Confident Interval using T-test showing that LED Lamps are better than Fluorescent Lamps in terms of cost, lumens and watt.
Dimmer is designed to measure the Lux value every time and sensor to detect the presence of people to light the lamps or extinguish them.
When calculating the energy saving without Deming and sensors LED/MAS saves 137.4 kwh/yr , LED/Sylvania 190.1 kwh/yr , LED/ros 190.1 kwh/yr and PL/sun light saves 168.1 kwh/yr . New system 500 lux with dimmer and lighting sensor , saving ratio using dimmer and lighting sensor = 20% . SUPER saves 198.6 kwh/yr and LED/lux ten saves 311.04 kwh/yr