## Slide 1
New Layout and Operations
Improvement for
Al-Karawan Factory
Student’s Names:
Noor Zedan
Rawan Abu Alhijaa
Masa Tammam
Ahmad Adnan
Supervised by:
Eng. Suleiman Daifi

## Slide 2: Outline
Results
Introduction
Conclusion
Problem Statement
01
02
03
05
06
04
Objectives
Literature Review
07
Recommendation

## Slide 3: Introduction
The second branch is located in Hwarah and produces only Tahina.
The production capacity of this factory is approximately 4 tons per day of tahini
Al-Karawan Factory for Tahina and Halawa was established in 1980.
The main factory has three production lines:
1- Tahina production line
2- Halawa production line
3- Nigella production line.

## Slide 4: Problem Statement
The need to better organizational structure.
Increasing demand
Old random layout
High operational cost
Safety problems related to the old layout
The need for a better Inventory management system

## Slide 5: Objectives
02
01
Developing New effective layout
Developing Safety plan
Developing New Organizational Structure
Developing Inventory management system
03
04

## Slide 6: Literature Review
Layout in food industry
The diamond model elements is a layout model for food processing which was formed by progressively placing the five fundamental.
Based on the activities and amount of risk involve in food processing, primary, secondary, utility, warehousing, and administrative are used.
Secondary
Utility
Primary
Administrative
Stores A
Stores B

## Slide 7: New effective Layout for Al-karawan Factory
Design New Layout
Design New Rack system
Comparing between Flow Processes Charts
Design Silo System

## Slide 8
After analyzing the current layout and discussing the problems associated with it while considering the managerial requirements a new layout was developed.
The layout is based on the diamond model which divides the layout into five main areas:
Primary
Secondary
Utility
Stores
Administration

## Slide 11
Design New Rack system
A rack system will be designed for storing sesame bags.
The bags are arranged in pallets,
Each pallet contain one ton.
The rack system must allow for a total capacity of 400 tons.
The height of the system should not exceed 7m.
There will be an extra 0.25m above the floor.

## Slide 12
Rack System design for alternative 1
Rack System design for alternative 2
The dimensions of the rack system will be calculated Based on the following formulas:

## Slide 13
Design Silo System
The silo system will be designed holed a total amount of 600 ton of sesame this amount will be held in three silos each one of them will have a capacity of 200 ton.
The Silos Design:
Diameter = 4.35 m
Height = 10.5 m
Hopper = 4 m
Total height = 14.5 m
Capacity: 200 ton
Volume = 328,6 m3

## Slide 14
Store design using 4 aisles
Store design using 2 aisles

## Slide 15
3D store design

## Slide 16
Comparing between Flow Processes Charts
Flow Process Chart for the Old Factory
Flow Process Chart for the New Factory

## Slide 17
The number of operations decrease in the new layout to nine operations, while the transportation increased to five, the inspection increased to two inspections during the production, the delay was eliminated and the inventory was reduced to two.

## Slide 18
Space Requirement
The space required for each department of the previous five area is shown in the following table and that’s suitable for the available area:
Total Area =1560 m2

## Slide 19: Organizational Structure
In order to develop the organizational structure a list of all the required departments was established based on the managerial requirements.

## Slide 23: Safety Management
Electric shock
Slipping floor
Vibration
01
02
03
Boiler Hazards
04
The physical and ergonomic part to ensure a safe work place for the workers this category will include five elements.
Loud noise
05

## Slide 26: Safety Management
Each element represent a step in the manufacturing process of tahini.
This category includes 21 elements.
The hazards that could happen in each step were identified and a control measures established.
01
02
03
04
Considering each step in the production process of tahini

## Slide 27: Hazard Analysis for Tahina

## Slide 29: Inventory Management
Determining the Holding Cost
EOQ and Re-order point
MPS and MRP
Forecasting

## Slide 30: Determining the Holding Cost
Holding cost for items stored in the rack system.
Holding cost for items stored in the silos.
Operation cost for storing in silos.
The warehouse labor salaries.

## Slide 31: Rack System Holding Cost
01
03
02
04
The useful life
Annual holding cost
The capacity
Initial Cost
48,800 JD
416 Ton
30 Years
3.9 JD/ton

## Slide 32: Silo System Holding Cost
01
03
02
04
The useful life
Annual holding cost
The capacity
Initial Cost
85,500 JD
600 Ton
25 Years
5.7 JD/ton

## Slide 33: Holding Cost
01
The annual operational cost for the silos=5 JD/ton.
02
Holding Cost from warehouse labor salaries =10 JD/ton
03
The total annual holding cost = 24.6 JD/Ton

## Slide 34: Economic Order Quantity(EOQ)

## Slide 35
Reorder point (ROP)
The reorder point amount is determined by four factors:
The average demand.
The duration of the lead time.
The degree to which demand and/or lead times are variable.
The level of stock out risk that management is willing to take.

## Slide 36: Forecasting
The data in the years from 2018-2021 were used in this project.
The data of years 2018-2020 will be used to develop the model.
The data of the year 2021 as a
hold set.
Graphical representation of the data.
Several models were compared based on MSE and MAPE.
01
02
03
04
05

## Slide 37: Tahina Sales in 2018-2021

## Slide 39: Forecasting Models
Holt’s winter method (triple exponential smoothing)
Holt’s linear method (double exponential smoothing)
Linear Trend model
01
02
03
Holt’s linear method (double exponential smoothing)
02
Holt’s winter method (triple exponential smoothing)
03

## Slide 40
01
Fitted Trend Equation
Yt = 56.74 - 0.108×t
MSD = 70.3677
02
MAPE = 10.6245
03
04
MAD = 6.1204

## Slide 41
Smoothing Constants
α (level) 1.73635
γ (trend) 0.01440
MSD
95.3176
MAPE
11.4033
MAD
6.2994
Holt’s linear method (double exponential smoothing)
02

## Slide 43
Smoothing Constants
α (level) 0.970
γ (trend) 0.018
δ (seasonal) 0.080
MSD
1.21483
MAPE
1.27532
MAD
0.668294

## Slide 45: Testing The Model Adequacy

## Slide 46: Master Production scheduling (MPS)

## Slide 47: Material Requirements Planning (MRP)

## Slide 48: Conclusion
Inventory management system was developed
A clear organization structure was established
Safety plan was developed
A new layout that facilitated the flow of operations was developed
01
02
03
04

## Slide 49: Main Recommendations
Applying the proposed layout in this project which will increase the efficiency of the factory.
Implementing the inventory management system discuss previously in this project.
Investing in an inventory management software.
The forecasting method should be chosen as suggested according to the calculations of each item.

## Slide 50: Main Recommendations
Developing maintenance scheduling and planning for the factory periodically.
Establishing the organizational structure proposed in this project with the established job
description.
Applying the safety plan.

## Slide 51: Thank You