## Slide 1: Design and Simulation of an Extractive Distillation Process to Dehydrate Ethanol Using Aspen Plus
Done by Mohammad Debes under supervision of Dr. Abdelrahim Abusafa

## Slide 2: Introduction
Background, Objectives and Constraints
1

## Slide 3: Bioethanol
Extremely useful compound
Readily available from nature
But must be purified!

## Slide 4: Distillation
Without azeotrope
Straightforward, any purity can be reached.
With azeotrope
Challenging, alternative distillations are required.

## Slide 5: Extractive Distillation
Breaks azeotrope
Achieving higher purity
Efficient
Saving power and materials
Environmentally Friendly
Can be kept green

## Slide 6: Objectives
Design an extractive distillation process, taking ethanol from high-concentration to anhydrous (99.2%+)

## Slide 7: Constraints
Solvent to use, its availability
Feed concentration
Fluctuations
Scale

## Slide 8: Design Process
Choices, Testing and Simulation
2

## Slide 9: Starting Choices
Software
Aspen Plus V14
Solvent
99.5% Glycerol
Feed concentration
92% by mass

## Slide 10: Extraction Column
Arbitrary initial values for ethanol and glycerol feed
Unsatisfactory result, changes made
Hundreds of values tested for many parameters
The resulting column was insensitive and optimized.

## Slide 11: Solvent Recycling Column
Takes its feed from bottoms of extraction column
Optimized for maximum glycerol recovery
Output was not fed back into process
The resulting column was small and effective.

## Slide 12: Complete Process
Recycled solvent was fed back into system
Further optimization was made
System was tested for sensitivity to fluctuations
The system proved to be quite resistant and efficient.

## Slide 13: Results and Discussion
Performance, Specifications and Reliability
3

## Slide 14: Stream Summary
Ethanol Feed
92% ethanol, room temperature
2000 kg/hr
Enters extraction column
Fresh glycerol
99.5% glycerol, room temperature
5 kg/hr at equilibrium
Enters extraction column
Recycled glycerol
Essentially pure
1455 kg/hr at equilibrium
Enters extraction column
Ethanol out
99.7% ethanol
1840 kg/hr
Leaves extraction column
Wastewater
94.1% water, minor ethanol and glycerol content
165 kg/hr
Leaves recycling column

## Slide 15: Column Specifications
Extraction column
20 total stages, 60 cm apart
60 cm diameter
Condenser duty ≈ -890 kW
Reboiler duty ≈ 830 kW
Recycling column
5 total stages, 60 cm apart
35 cm diameter
Condenser duty ≈ -115 kW
Reboiler duty ≈ 260 kW

## Slide 16: Sensitivity and Reliability
Ambient temperature
18 – 30 ℃, no problems
Startup
High, but decreasing flow of fresh glycerol
Shutdown
No fresh glycerol, decreasing flow of ethanol
Divert recycled glycerol to tank
Glycerol purity
Down to 94% allowed in equilibrium
Startup may be problematic
Losses
The process loses:
5.5 kg/hr (0.30%) ethanol in WW
5 kg/hr (0.35%) glycerol in WW

## Slide 17: Process layout

## Slide 18: Conclusions
Closing Thoughts
4

## Slide 19: Extraction Column
The objectives were exceeded
Minimal loss and sensitivity
Power of simulation
Further adjustments may be needed for safety.

## Slide 20: THANKS!
I am open to questions.