## Slide 1
1
A MOBILE CNC MACHINE DESIGNED FOR ENGRAVING WOOD PANELS
Goliath CNC Machine.
GRADUATION PROJECT 2
SUPERVISED BY: DR. BASHEER NOURI
By:
  YAZAN JABER
  Maen shalabi
  WALAA SADEQ

## Slide 2
01
  Table of content:
02
03
04
Robot Control Design
Motivation & Problem statement
CNC Milling Machine Mobile Robot Design
05
Conclusion
2
Proposed Solutions
06
Limitations and Future Work

## Slide 3
3
01
Wood CNC Machines
A wood CNC machine is a specialized tool used for cutting, carving, and shaping wood. These machines are equipped with a spindle motor that holds cutting tools, allowing for intricate designs and accurate woodwork.
  Motivation & Problem statement

## Slide 4
4
01
Wood CNC Machines
  Motivation & Problem statement
Wood CNC machines offer several advantages in woodworking and related industries:
  High precision in design
2. Versatility in Design
3. Reduced Labor Intensity

## Slide 5
5
Wood CNC machines Limitation
01
However, wood CNC machines come with certain problems and limitations. The size of the workpiece that a CNC milling machine can accommodate is restricted by the machine's dimensions. Larger workpieces may require specialized, and potentially more expensive, equipment.
Furthermore, the initial cost and maintenance of CNC machines can be high, making them less accessible for smaller woodworking businesses.
  Motivation & Problem statement

## Slide 6
6
  Motivation
01
  Motivation & Problem statement
2. Autonomous Operation
1. Portability
3. Low power consumption
4. Save time
5. Versatility
6. User-Friendly Interface

## Slide 7
7
2. Proposed Solutions
  Proposed Solutions
02
Goliath CNC Machine

## Slide 8
8
A
Goliath CNC Machine
Goliath represents a paradigm shift in CNC milling, seamlessly integrating autonomous capabilities that redefine the way we approach machining processes.
2. Proposed Solutions : Goliath CNC Machine

## Slide 9
9
02
With Goliath, we are redefining the possibilities of CNC milling, paving the way for a more efficient, productive, and autonomous future in the world of machining technology.
The calculations of equations allow the robot to interpret G-code and convert it into motor movements based on distance and angle, ensuring precise path control using two stepper motors in coordination. The robot uses both motors together to generate X-Y movements rather than controlling X and Y independently.
Goliath CNC Machine
2. Proposed Solutions : Goliath CNC Machine

## Slide 10
10
A. Mechanical design: Goliath CNC Machine
B. Electrical/Electronics System
C. Control System
    CNC Milling Machine Mobile Robot Design
03
3. CNC Milling Machine Mobile Robot Design:

## Slide 11
11
    Mechanical Design
A
The mechanical design plays a crucial role in advanced manufacturing and automation, serving as a foundation for precision, efficiency, and versatility. These robots, guided by Computer Numerical Control, seamlessly integrate intricate mechanical components with cutting-edge technologies to achieve precise and automated motion. The design encompasses various elements, including robust frames, precise actuators, and sophisticated end-effectors that define the robots' operational capabilities.
3. CNC Milling Machine Mobile Robot Design: A. Mechanical Design

## Slide 12
12
  Mechanical Design: Goliath CNC Machine
03
3. CNC Milling Machine Mobile Robot Design: A. Mechanical Design
We used SolidWorks to design the robot in the one project. In the second project we implemented it:

## Slide 13
13
  Electrical/Electronics System
B
3. CNC Milling Machine Mobile Robot Design: B. Electrical Design

## Slide 14
14
  Electrical/Electronics System
03
3. CNC Milling Machine Mobile Robot Design B. Electrical Design

## Slide 15
15
  Robot Control Design
04
1. Reference Generation: Gcode
2. Robot Movement Mechanism
4. Robot Control Design

## Slide 16
16
A
Inkscape
Various software tools can facilitate this conversion. Notable examples like Inkscape with Gcodetools extension. These tools enable the translation of graphical designs into the G-Code instructions needed for the CNC robot to execute the specified movements.
4. Robot Control Design: A. Reference Generation
Reference Generation

## Slide 17
17
  Custom Interface
A
G.Code
The G-Code instructions contain information about the desired movements, speeds, and tool actions. The mobile robot's processor translates these commands into specific voltages to drive the motors and the spindle. This translation process is critical for accurately reproducing the graphical design on the wood.
4. Robot Control Design: A. Reference Generation

## Slide 18
18
  Robot Movement Mechanism
B
4. Robot Control Design: B. Robot Movement Mechanism
The robot has two stepper motors: These motors operate independently, allowing for motion in 2D space. This setup enables diagonal, horizontal, and vertical movements, effectively controlling the robot's position across both X and Y coordinates.
The movement depends on:
  Pulse Input
2. Step Angle
3. Feedback Systems

## Slide 19
19
    Conclusion
05
Built upon a robust modular chassis, Goliath is designed for easy customization and scalability, ensuring it can adapt to evolving industry demands. Its autonomous features are complemented by an array of safety measures, guaranteeing secure and reliable operation in diverse environments.
5. Conclusion

## Slide 20
20
5. Conclusion

## Slide 21
21
  Limitation
A
6. Limitations and Future Work
Based on the result, we noticed some bumps on the wood due to the wheels being exposed to high force during operation.

## Slide 22
22
  Future Work
B
6. Limitations and Future Work
In the future, the wheels should be changed to get the best result and for the robot to operate flexibly and smoothly. In addition, we suggest adding a dust extraction pump.

## Slide 23
THANK YOU!
23