## Slide 1
An-Najah National University
Facility of Engineering and Information Technology
Civil Engineering department
Structural Analysis and Design of Clock tower in Jenin
By: Mohammad Hijjawi, Nour Abu Hantash, Omar Yasin, Mohammad Bzoor

## Slide 2
Content
1 – Introduction:
  Project description
  Codes used
  Material
  Seismicity of Site and Structure
  Loads and Load Combinations
2 – Preliminary design:
  Beam preliminary design
  Slab preliminary design
  Column preliminary design
  Walls preliminary design

## Slide 3
Content
3 – Modeling and Analysis:
  Introduction
  Definition of materials and sections
  Definition of response spectrum
4 – Modeling and Analysis:
  Checks
  Compatibility check
  Equilibrium check
  Internal force check
  Irregularities check
  Drift check
  P-delta check

## Slide 4
Content
5 – Design and Detailing:
    Programs and sheets used
  Beam design
  Column design
  Walls design
  Slab design
  Mat foundation design
  Folded shell design

## Slide 5
PART 1: INTRODUCTION
Located in Jenin, West Bank.
It consists of ten stories.
Two basement stories
Seven stories and auditorium above
Whole area of the structure is 7,605

## Slide 6
3D VIEW

## Slide 7
3D VIEW

## Slide 8
3D VIEW

## Slide 9
PLAN VIEW (Basement)

## Slide 10
CODES AND STANDARDS
ACI 318-14
IBC 2015
ASCE 7-10

## Slide 11
MATERIALS
28 MPa concrete
Property | Value
Compressive strength (Mpa) | 28
Modulus of Elasticity E (Mpa) | 24870
Unit Weight (Kn/m) | 25
Table 1: Concrete 28 properties

## Slide 12
MATERIALS
35 Mpa concrete
Property | Value
Compressive strength (Mpa) | 35
Modulus of Elasticity E (Mpa) | 27800
Unit Weight (Kn/m) | 25
Table 2: Concrete 35 properties

## Slide 13
MATERIALS
Steel Grade 60
Property | Value
Yielding Strength (Mpa) | 420
Modulus of Elasticity E (Gpa) | 200
Table 3: Steel grade 60 properties

## Slide 14
MATERIALS
Non-structural materials
Table 4: Non structural materials properties
Material | Ɣ in kN/m³
Blocks | 12
Filling Materials | 18
Tiles | 26
Plaster | 23
Aggregate | 13
Concrete Mortar | 23
Masonry Stone | 26

## Slide 15
SEISMICITY OF SITE AND STRUCTURE

## Slide 16
SEISMICITY OF SITE AND STRUCTURE
SS = 2.5Z
S1 = 1.25Z
Z for Jenin = 0.2
SS= 0.5, S1 = 0.25
SS(2%) = 0.75, S1(2%) = 0.375

## Slide 17
SEISMICITY OF SITE AND STRUCTURE
Site class  Stiff Soil (D)

## Slide 18
SEISMICITY OF SITE AND STRUCTURE
Site Coefficient Fa = 1.2

## Slide 19
SEISMICITY OF SITE AND STRUCTURE
Site Coefficient Fv (by interpolation) = 1.65

## Slide 20
SEISMICITY OF SITE AND STRUCTURE
SMS = Fa × SS = 0.9
SM1 = Fv × S1 = 0.61875
SDS = × SS = 0.6
SD1 = × S1 = 0.4125

## Slide 21
SEISMICITY OF SITE AND STRUCTURE
Risk Category = III
Determination of risk category

## Slide 22
SEISMICITY OF SITE AND STRUCTURE
Seismic design category =D
Determination of seismic design category

## Slide 23
Structural system used
Structural system Special reinforced concrete shear walls

## Slide 24
Loads and Load Combinations
Gravity Loads
  Dead Load: Weight of structural members.
  Live Load: 3.5 KN/(basement), 5 KN/ (rest stories). (ASCE 7-10)
  SD Load: 5 KN/d and 2 kN/

## Slide 25
Loads and Load Combinations
Lateral Load
The method used in determination the effect of earthquake load is modal response method.
Verified by ELF

## Slide 26
Loads and Load Combinations
Ultimate Load Combinations:
1.4 D
1.2D +1.6L
1.32D +L +1.3EQx +0.39EQy
1.32D +L +1.3EQy +0.39EQx
0.78D +1.3EQx +0.39EQy
0.78D +1.3EQy +0.39EQx

## Slide 27
Loads and Load Combinations
Service Load Combinations:
D+L
1.084 D+0.91EQx+0.273EQy
1.084 D+0.91EQy+0.273EQx
1.063D +0.75L +0.683EQx +0.205EQy
1.063D +0.75L +0.683EQy +0.205EQx
0.516D+0.91EQx+0.273EQy
0.516D+0.91EQy+0.273EQx

## Slide 28
End of Part 1
 Part 2: Preliminary design

## Slide 29
Part 2: Preliminary design
Beam preliminary design
h = Use 0.5m.
b = 0.4m.
depth for some beams in cinema and roof = 0.8m

## Slide 30
Part 2: Preliminary design
Columns preliminary design
Circular columns with diameter of 1000 mm.
Rectangular columns of 800X400, 700x400.

## Slide 31
Part 2: Preliminary design
Walls preliminary design
350 mm
250 mm
Based on architectural drawings

## Slide 32
Thickness 
Depth 
= 17.4m
H = 15cm
Depth = 1.5m
Part 2: Preliminary design
Folded shell preliminary design

## Slide 33
Part 2: Preliminary design
Slab preliminary design
Two way solid slab

## Slide 34
Part 2: Preliminary design
Slab preliminary design
where Ln = 6.5 m, Fy = 420 Mpa and β = 1.4
h = 15.5 cm but we will use 17 cm for all floors for first iteration

## Slide 35
Part 2: Preliminary design
, where Fc=24 MPa, b=1000 mm, and d = 170 – 30(cover) = 140 mm.
∅Vc = 92 kN
Check shear

## Slide 36
Part 2: Final dimension
Walls:
  Wall 300mm
  Wall 400 mm
  Wall 250 mm

## Slide 37
Part 2: Final dimension
Beams:
  Beam 400X500
  Beam 500X600

## Slide 38
Part 2: Final dimension
Columns:
    Column 700X400
    Column 800X400
    Column 900X500
    Column D = 1000 mm
    Column D = 800mm

## Slide 39
PLAN VIEW (Basement - Columns)

## Slide 40
End of Part 2
 Part 3: Modeling

## Slide 41
Part 3: Modeling
Modeling and analysis are performed by using ETABS 18 program.
All supports are modeled as Fixed support.
Ultimate strength method (LRFD) is used.
Exterior partition as linear load and interior partition as distributed load.

## Slide 42
Steel material

## Slide 43
Concrete material

## Slide 44
Slab section

## Slide 45
Column section

## Slide 46
Wall section

## Slide 47
Beam (500x400) Section

## Slide 48
Load patterns

## Slide 49
Load combinations

## Slide 50
Mass Source definition

## Slide 51
Response spectrum definition

## Slide 52
ELF – EQX Defintion

## Slide 53
Modal EQX Defintion (Load Case)

## Slide 54
End of Part 3
 Part 4: Checks

## Slide 55
Part 4: Checks
Compatibility check
Equilibrium check
Stress-Strain (Internal force) check
Base shear check
Modal mass participation ratio check
Irregularities check
Drift check
P-delta check

## Slide 56
Compatibility check

## Slide 57
Equilibrium check

## Slide 58
Stress – Strain Check
Column C1, 400X700 mm at Basement 2

## Slide 59
- Atributary = 4.465 × 5.5 = 24.6m2 - Weight of column = 0.4 × 0.7 × 25 × 30 = 210 kN. - Weight of slab = 0.17 × 25 × 24.6 × 8 = 836.4kN. - Weight of live loads = 8 × 24.6 × 5 = 984 kN. - Weight of superimposed loads = 8*24.6*5 = 984kN - Weight of beams = 0.5 × 0.4 × (4.465+5.5) × 25 × 8 = 298.95kN.  Axial load = 1.2 (210+836.4+984+298.95) + 1.6 (984)
= 4369.62kN.

## Slide 60
ETABS result, C1, 400x700 (B2)
%Error = x 100% = 7.6% < 10% .OK

## Slide 61
Column C9 at Basement 2

## Slide 62
- Atributary = 5×3.725 = 18.625m2 - Weight of circular columns = /4×1×1×6×25= 117.857 kN.
- Weight of rectangular columns = 0.4×0.8×25×((5×3)+(3×5)) = 160 kN. - Weight of slab = 0.17×25×18.625×10 = 791.5625kN. - Weight of live loads = 10×18.625×5 = 931.25kN. - Weight of superimposed loads = 10×18.625×5 = 931.25kN - Weight of beams = 0.5×0.3×(5+3.725)×25×10 = 436.25kN.  Axial load = 1.2 (117.857+160+791.57+93.25+436.25) + 1.6 (931.25)
= 4414.3kN.

## Slide 63
ETABS result, Column C9 at Basement 2
%Error = x 100% = 3.35% < 10% .OK

## Slide 64
Stress-strain check (Beam)

## Slide 65
Stress-strain check (Beam) – Section 1

## Slide 66
Stress-strain check (Beam) – Section 2

## Slide 67
Stress-strain check (Beam) – Section 3

## Slide 68
Moment based on section cuts:
+ 24.87= 44.93 KN.m
Moment by hand calculation:
Beam length = 4.6m
Frame width = 5m
Live load = 5m
= 40.5 KN.m
Error = = 1%

## Slide 69
Base shear check
Manually  V= CsW = 0.09 × 141218.3 = 12409.7 kN.
ETABS 

## Slide 70
Base shear check

## Slide 71
Base shear check
Result from ETABS, Modal resposne

## Slide 72
Modal Mass Participation Ratio

## Slide 73
Modal Mass Particpation Ratio

## Slide 74
All supports are assumed to be pinned
Service (Allowable) load combinations are used
Drift Check

## Slide 75
Drift Check

## Slide 76
Floor |  |  | Elastic drift / Story height | Inelastic drift / Story height | Max drift / story height
F7 | Max | X | 0.001977 | 0.007908 | 0.015
F7 | Max | Y | 0.001903 | 0.007612 | 0.015
F6 | Max | X | 0.001371 | 0.005484 | 0.015
F6 | Max | Y | 0.001685 | 0.00674 | 0.015
F5 | Max | X | 0.001335 | 0.00534 | 0.015
F5 | Max | Y | 0.001902 | 0.007608 | 0.015
F4 | Max | X | 0.001363 | 0.005452 | 0.015
F4 | Max | Y | 0.001942 | 0.007768 | 0.015
F3 | Max | X | 0.00135 | 0.0054 | 0.015
F3 | Max | Y | 0.00191 | 0.00764 | 0.015
F2 | Max | X | 0.001315 | 0.00526 | 0.015
F2 | Max | Y | 0.001838 | 0.007352 | 0.015
F1 | Max | X | 0.001142 | 0.004568 | 0.015
F1 | Max | Y | 0.001564 | 0.006256 | 0.015
GF | Max | X | 0.000832 | 0.003328 | 0.015
GF | Max | Y | 0.001117 | 0.004468 | 0.015
B1 | Max | X | 0.00047 | 0.00188 | 0.015
B1 | Max | Y | 0.000551 | 0.002204 | 0.015
B2 | Max | X | 0.000231 | 0.000924 | 0.015
B2 | Max | Y | 0.000253 | 0.001012 | 0.015
Drift Check

## Slide 77
Torsional Irregularity check (X-direction)
Story | Max drift (mm) | Average (mm) | ratio
B2 | 0.65 | 0.641 | 1.014041
B1 | 2.03 | 2.02 | 1.00495
GF | 6.19 | 6.125 | 1.010612
F1 | 11.665 | 11.712 | 0.995987
F2 | 18.196 | 18.1185 | 1.004277
F3 | 22.345 | 22.2155 | 1.005829
F4 | 22.441 | 24.257 | 0.925135
F5 | 29.77 | 29.97 | 0.993327
F6 | 33.876 | 33.9035 | 0.999189

## Slide 78
Torsional Irregularity check (Y-direction)
Story | Max drift (mm) | Average (mm) | ratio
B2 | 0.765 | 0.6915 | 1.106291
B1 | 2.469 | 2.206 | 1.11922
GF | 7.574 | 6.762 | 1.120083
F1 | 14.51 | 12.905 | 1.12437
F2 | 24.558 | 21.7 | 1.131705
F3 | 30.1 | 26.4 | 1.140152
F4 | 35.6 | 31 | 1.148387
F5 | 41.4 | 35.9 | 1.153203
F6 | 42.5 | 35.7 | 1.167147

## Slide 79
Vertical geometry irregularity

## Slide 80
Vertical geometry irregularity

## Slide 81
Permitted analytical procedures

## Slide 82
P-Delta check
Floor | P | Vx | Vy | Height | THETA X | Theta Y
B2 | 170964.6 | 12407 | 12403 | 3 | 0.005002 | 0.005004
B1 | 155982.9 | 12287 | 12283 | 6 | 0.007731 | 0.007734
GF | 138458.5 | 11959 | 11948 | 11 | 0.010744 | 0.010754
F1 | 117300.6 | 11200 | 11195 | 16 | 0.012484 | 0.01249
F2 | 96142.6 | 10054 | 10001 | 21 | 0.012766 | 0.012834
F3 | 74984.64 | 8478 | 8436 | 24 | 0.012064 | 0.012124
F4 | 56136.24 | 6827 | 6793 | 27 | 0.011347 | 0.011404
F5 | 37442.91 | 4882 | 4855 | 30 | 0.010362 | 0.010419
F6 | 18751.4 | 2717 | 2703 | 33 | 0.009814 | 0.009865
Cinema | 6893.258 | 1118 | 1101 | 38 | 0.011616 | 0.011796

## Slide 83
End of Part 4
 Part 5: Design

## Slide 84
Special Reinforced Concrete Shear Walls
Design and Detailing

## Slide 85
Section Cut 1

## Slide 86
Section Cut 2

## Slide 87
Walls are designed to resist 100% of seismic force
Frames are designed only for gravity loads
Frames are designed as sway special
Model with 0.7 modifier
Model with 0.001 modifier
Mat Model
Design and Detailing

## Slide 88
All members are designed using ETABS 18 software.
Verified Manually
CSI detailing 18
Design and Detailing

## Slide 89
Design check - Beam

## Slide 90
Design check - Beam

## Slide 91
Design check - Beam

## Slide 92
Design check - Beam

## Slide 93
Design check - Beam
Excel show

## Slide 94
Stirrups design - Beam
s2 = d/2 = 420/2 = 210

## Slide 95
Design check - Column

## Slide 96
Design check - Column

## Slide 97
Design check - Column

## Slide 98
Design check - Column

## Slide 99
Design check - Column

## Slide 100
Design check - Column

## Slide 101
Design check - Column

## Slide 102
Design check - Wall

## Slide 103
Design check - Wall

## Slide 104
Design check - Wall
Check shear in X direction
Vux = 41.64 Kn
Vc=
kN > Vux OK
Thickness = 400mm
Length = 3m.
Vuy = 368kN
Vc
=846 kN
use ρ=0.0025  As shear = 0.0025×3000× 400 = 3000 mm2  1000mm2/m

## Slide 105
Design check - Wall
0.0025 × 3000 × 400 = 3000 mm2 (Total)
Thickness = 400mm
Length = 3m.
Check shear in X direction
Mx = 2446
Pz = 5479

## Slide 106
Design check - Wall

## Slide 107
Slab, Mat design
How?

## Slide 108
Slab, Mat design

## Slide 109
Slab, Mat design

## Slide 110
Folded shell design
How?
0.45 × 28 = 12.6 (Allowable compressive stress)

## Slide 111
S11 - TOP

## Slide 112
S22 - TOP

## Slide 113
S11 - BOTTOM

## Slide 114
S22 - BOTTOM

## Slide 115
Tension check

## Slide 116
Folded shell design
Maximum tensile load = 853 kN
As = = = 5077 mm2

## Slide 117
Folded shell design
3D Video

## Slide 118
THE END

Thank you for being here

## Slide 119
THE END

Thank you for being here

## Slide 120
 fr = 3.28 Mpa

## Slide 121
Wall section