## Slide 1: WATER FILTRATION DEVICE IMPROVING AND REDESIGN
Graduation Project II
Students Names:
Qais Nafiz Abu Shaqdam
Omar Najm Aldien Breik
Supervised by:
Dr. Falah Mohammad

## Slide 2: Introduction
In this project we aimed to fix and improved a water filtration device that has been out of work over one year. Our purpose in this project is to developed water filtration device that could help people in many ways, especially those who live in poor and developing countries.
The device we are going to fix and improve is a filtration device for moderately salty water. With the presence of the electrical power, water passes through special membranes that passes anions and cations through these membranes. The process of filtration continues until water have a specific salt concentration and usable for the purpose needed, whether it is going to be used for drinking, crops irrigation or any other purpose.

## Slide 3: Theoretical Background
CED : Capacitance Electrodialysis
Reverse osmosis (RO)
The ultraviolet (UV)

## Slide 4: Reverse osmosis (RO) The Ultraviolet (UV)

## Slide 5: CED : Capacitance Electrodialysis
Capacitance electrodialysis It is a set of stacks made of special membranes (AEM and CEM) between two electrodes of carbon graphite. Water passes through these electrodes and ionized with the presence of electrical voltage between the poles. Ionic move through these membranes and water separates into regions that have a high ions concentration and other regions with moderate ion concentration. This process continues until a specific an ionization level of water is obtained for a specific type of use. For example, it may be used for drinking, crops irrigation or any other purpose.

## Slide 6: CED equivalent circuit :

## Slide 7
voltages VS time

## Slide 8: Parameter VS concentration

## Slide 9: Device Programs of filtration
The device goes through these three programs for the filtration process:
Drinking Program
Irrigation Program
Device self-cleaning Program

## Slide 10: Drinking Water Program
The main purpose of this program is to produce water with a low concentration of salt. The EC value is less than 300 micro Siemens (μS).
This program goes through the following filtration stages:
Tanks filling stage: at this stage the device is fed with salty water from the feed in opening, salty water is pumped from the main pump (P-1). Water then turns to micro filter (F-1), part of the water passes through two-way valve (SV-3) and then water goes to the waste tank (T-2). The other part of water passes through two-way valve (SV-2) and then it moves to the carbon active filter (F-3). This process continues until both tanks are filled to a specific volume defined in the code.

## Slide 11: Drinking Water Program
Charging stage: this stage continues for 10 minutes so that the device does half a turn of the CED stack (F-4). The stage begins by taking water from both tanks (P-2) and (P-3) through two paths:
  Water is pumped by pump (P-2) from tank (T-1). Water then passes through the three-way valve (BV-5), after that it goes through the three-way valve (BV-7) that passes the water CED stack (F-4). Water after that passes through the three-way valve (BV-10) returning to the waste tank (T-2).
  Water is pumped by pump (P-3) from tank (T-2). Water then passes through the three-way valve (BV-6), after that it goes through the three-way valve (BV-8) that passes the water CED stack (F-4). Water after that passes through the three-way valve (BV-9) then the water passes through the uv lamp returning to the drank tank (T-1).

## Slide 12: Drinking Water Program
Charging Stage in Drinking Program:

## Slide 13: Drinking Water Program
Discharging stage: this stage continues up to 10 minutes as the charging stage before, and the device completes a turn of the CED stack (F-4). As in the charging process water is taken from both tanks through these two paths:
  Water is pumped by pump (P-2) from tank (T-1). Water then passes through the three-way valve (BV-5), after that it goes through the three-way valve (BV-8) that passes the water CED stack (F-4). Water after that passes through the three-way valve (BV-9) returning to the waste tank (T-2).
  Water is pumped by pump (P-3) from tank (T-2). Water then passes through the three-way valve (BV-6), after that it goes through the three-way valve (BV-7) that passes the water CED stack (F-4). Water after that passes through the three-way valve (BV-10) then the water passes through the uv lamp returning to the drank tank (T-1).

## Slide 14: Drinking Water Program
Discharging Stage in Drinking Program:

## Slide 15: Irrigation Program
The main purpose of this program is to produce water with moderate concentration of salt. The EC value at this program is 700 micro Siemens (μS).
This program goes through the following filtration stages:
Tanks filling stage: at this stage the device is fed with salty water from the feed in opening, salty water is pumped from the main pump (P-1). Water then turns to micro filter (F-1), part of the water passes through two-way valve (SV-3) and then water goes to the waste tank (T-2). The other part of water passes through two-way valve (SV-1) process continues until both tanks are filled to a specific volume defined in the code.

## Slide 16: Irrigation Program
Charging stage: this stage continues for 10 minutes so that the device does half a turn of the CED stack (F-4). The stage begins by taking water from both tanks (P-2 and P-3) through two paths:
  Water is pumped by pump (P-2) from tank (T-1). Water then passes through the three-way valve (BV-5), after that it goes through the three-way valve (BV-7) that passes the water CED stack (F-4). Water after that passes through the three-way valve (BV-10) returning to the waste tank (T-2).
  Water is pumped by pump (P-3) from tank (T-2). Water then passes through the three-way valve (BV-6), after that it goes through the three-way valve (BV-8) that passes the water CED stack (F-4). Water after that passes through the three-way valve (BV-9) then the water passes returning to the drank tank (T-1).

## Slide 17: Irrigation Program
Charging Stage in Irrigation Program:

## Slide 18: Irrigation Program
Discharging stage: this stage continues up to 10 minutes as the charging stage before, and the device completes a turn of the CED stack (F-4). As in the charging process water is taken from both tanks through these two paths:
  Water is pumped by pump (P-2) from tank (T-1). Water then passes through the three-way valve (BV-5), after that it goes through the three-way valve (BV-8) that passes the water CED stack (F-4). Water after that passes through the three-way valve (BV-9) returning to the waste tank (T-2).
  Water is pumped by pump (P-3) from tank (T-2). Water then passes through the three-way valve (BV-6), after that it goes through the three-way valve (BV-7) that passes the water CED stack (F-4). Water after that passes through the three-way valve (BV-10) then the water passes returning to the drank tank (T-1).

## Slide 19: Irrigation Program
Discharging Stage in Irrigation Program:

## Slide 20: Device Self-Cleaning Program
The main purpose of this program is to keep the device from calcification, especially the CED stack (F-4). This process begins by opening the two-way valve (SV-4) and then Citric acid pumped from tank (T-3) and it mixes with the water that comes from pump (P-3), the mixed water then goes to the three-way valve (BV-6) and the n it goes through the two way valves (BV-7 and BV-8). Water then moves to CED stack (F-4) so that it is being cleaned. After that the mixed water goes through the two-way valves (BV-9 and BV-10) and it returns back the waste tank [2].

## Slide 21: Tools
Pumps
Valves
Sensors
Controller
Tanks
Pipes

## Slide 22: Pumps Used in the filtration Device Main Pump Secondary Pump

## Slide 23: Valves Used In The Filtration Device Three-way ball valve Two-way Solenoid valve

## Slide 24: Types of Sensors Used in The Filtration Device
Current Sensor
Level Sensor
PH Sensor
Temperature Sensor
Level Sensor

## Slide 25: Types of Sensors Used in The Filtration Device (cont’d)
Flow Sensor
Pressure Measurement Device
Electrical Conductivity Sensor
Over and under flow sensor

## Slide 26: Buck and Boost Converter.

## Slide 27: MOSFET

## Slide 28: Relay and Solid-State Relay

## Slide 29: Tanks and Pipes Tanks Pipes
we used to tank with 50 litter volume and one tank with 5 litter volumes
The pipes used in this project is a plastic pipes of 0.5 inches diameter.

## Slide 30: Controller
This is the controller used in this filtration device.
1. Power supply 24v
2. Power supply 5v
3. Fuses
4. Main controller
5. Buck converter 6. Boost converter
7. Relays and solid state relays. 8. Power measurements
9. Circuit breaker

## Slide 31: Experimental Setup
The following Slides explains the problems we have ran into while trying to fix and develop the device.

## Slide 32: Sensors study
We have examined the parts used in reading the sensors, and we found that the ph, ec, flow, and temperature and humidity sensors give the correct results, but there was a defect in the code and also there was a defect in the reading of the level sensor, due to the use of the voltage divider method

## Slide 33
2- Ball and Solenoid Valve Control
the bv and how to control the reversal of its movement and it has become clear to us that the way in which the movement is reversed is by using a signal from the Arduino that enters the mosfet which work as switch.
With regard to the sv, controlling it is similar to bv, and we only need one MOSFET in order to disconnect or connect the voltage source.

## Slide 34
3- Pump and Stack Control
A- The method used to control the pumps is the same as previously used.
B- The speed of the two secondary pumps was controlled by using the buck converter.
C-The required power was connected to the main pump by taking the signal from the MOSFET to the Solid State Relay.
D- we use the previous method to turn on and off the stack and we use relay to change the polarity.

## Slide 35
4- The UV Control
This has been done by using the MOSFET and transmitting the signal to the relay and thus connecting the voltage source to it.

## Slide 36: Results
After completing all the previous steps and checking all the existing equipment, the machine was successfully operated and we took the readings and then we got the following results.

## Slide 37: Result before improvement
This device consumes 4.3 kilo watts per day of electrical energy to produce either 1600 liters of potable water or 1,800 liters of potable water for irrigation of crops.
System performance |  |  |  |  |  |  |  | 
 | conductivity | Capacity |  | Energy consumption |  |  | Water recovery | Purification
 | ms/cm | L/h | Day | Total | Pumps&valves | Stack |  | 
 |  |  |  | Kwh/m3 | Kwh/m3 | Kwh/m3 |  | 
feed | 5.9 |  |  |  |  |  |  | 
Drinking water | 07 | 67 | 1600 | 2,65 | 2,15 | 0,5 | 84% | 95%
Irrigation | 1.2 | 75 | 1800 | 2,36 | 1,92 | 0,45 | 84% | 85%
Waste water | 21 | 15 | 360 |  |  |  |  | 

## Slide 38: Result after improvement
This device consumes 4 kilo watts per day of electrical energy to produce either 1150 liters of potable water or 1,350 liters of potable water for irrigation of crops.
System performance |  |  |  |  |  |  |  | 
 | conductivity | Capacity |  | Energy consumption |  |  | Water recovery | Purification
 | ms/cm | L/h | Day | Total | Pumps&valves | Stack |  | 
 |  |  |  | Kwh/m3 | Kwh/m3 | Kwh/m3 |  | 
feed | 15.5 |  |  |  |  |  |  | 
Drinking water | 0.7 | 48 | 1150 | 3.45 | 1,95 | 1,5 | 84% | 95%
Irrigation | 1.2 | 56.2 | 1350 | 2.94 | 1,72 | 1,22 | 84% | 85%
Waste water | 35 | 15 | 300 |  |  |  |  | 

## Slide 39: Capacity of the device (Cont’d)
Comparison between running cost of this technique and others:
so as the table show previously the devise consumed 2,65 kwh/m3 for drinking and 2,36 kwh/m3 for irrigation so the cost of either as below:
for drinking = total kwh/m3 consumption * tariff ($)
=2,65*0,17$= 0,45 $
for irrigation = total kwh/m3 consumption * tariff ($)
=2,36×0,17$= 0,40 t6$
Total fixed cost for the Filtration device is approximately 2500$.
Technique | Cost ($)
CED stack | 0.4-0.45
Reverse osmosis | 0.8-2.4
Thermal | 0.8-1.1

## Slide 40: Thanks!
Does anyone have any questions?