## Slide 1
Faculty of Engineering & Information Technology Department of Civil Engineer
Graduation Project II
Design & Analysis for AL-Sha`ar Building in Nabluse City
Prepared By:
Ammar Khader Amr
Linda Fares Bsharat
Qusai Khaled Khalifa
Rami Omar Daraghmeh
Under supervision of: Dr. Mohammad Samaaneh

## Slide 2
Contents
1
2
3
4
5
6
Introduction
Preliminary Dimensions
Modeling Using ETABs
Seismic Force Analysis
Design for Structural Elements
Design of Footing
7
Shear Wall

## Slide 3
Side View
Front View

## Slide 4
1
Introduction
1.1: Project Description
The project is a residential and commercial building, located in the city of Nablus in Palestine, and consists of 6 floors, ground floor and basement level and enchanted floor and three floors of a total area of 2636 square meters.
Consistence and use of floor | Area (m2) | Floor
commercial | 401 | Ground floor
Residential and commercial | 397.3 | First floor
Residential | 3*436.17 | Residential floors 2-4

## Slide 5
1
Introduction
1.2: Codes & Materials
Codes:
ACI318-14
ASCE7-10
IBC-2015
Materials:
Concrete
Reinforcing Steel Fy = 420 MPa

## Slide 6
1
Introduction
1.3: Loads
1.3.1: Load Types
(1)Dead Load:
consist of the own weight of the structure.
•Main Beams(450*300) weight = 4045kN
•Columns weight = 3410 kN
•Shear wall weight = 8919kN
•Slab weight = 14619kN
Total weight due to dead loads = 30994 kN

## Slide 7
1
Introduction
1.3: Loads
1.3.1: Load Types
(2)Live Load: include any temporary or transient forces . Total live load =12594.4 KN
Usage | Live Load (KN/m2)
Residential buildings | 2
Commercial | 4
Roof | 10
Parking | 10

## Slide 8
1
Introduction
1.3: Loads
1.3.1: Load Types
(3)Superimposed Load: come from the weight of all non-structural elements.
Item | Unit weight Ɣ (KN/m3) | Thickness (cm) | Calculations | Weight per m2 (KN/m2)
Mortar | 23 | 3 | 0.03*23 | 0.69
Tiles | 26 | 1 | 0.01*26 | 0.26
Filling | 18 | 5 | 0.05*18 | 0.90
Plastering | 23 | 1 | 0.01*23 | 0.23
Total Super Dead Load |  |  |  | 2.08

## Slide 9
1
Introduction
1.3: Loads
1.3.2: Load Combinations
ULTIMATE:
1.4 D.L.
1.2 D.L. + 1.6 L.L.

## Slide 10
1
Introduction
1.3: Loads
1.3.2: Load Combinations
SEISMIC:
1.2 D + 1L +EX+EV
1.2 D + 1L - EX+EV
0.9 D + EX + EV
0.9 D - EX + EV
1.2D+L-Ey+Ev
1.2D+L+Ey+Ev
0.9+L+Ey+Ev
0.9+L-Ey+Ev

## Slide 11
1
Introduction
1.3: Loads
1.3.2: Load Combinations
SERVICE:
1D + 1L
1D+0.7Ev+0.7Eh
1D+(0.75(.0.7Ev+0.7Eh))+0.25L
0.6D-0.7Ev+0.7Eh
Also the same of this load combinations in other direction.

## Slide 12
Beams
Columns
Main Beams
Square
Circular
Slab
Preliminary Dimensions
Secondary Beam

## Slide 13
Preliminary Dimensions
2
2.1: Slab
After comparing between two systems (Two-Way Ribbed Slab and Two-Way Solid Slab)_as table bellow_
We decide to use Two-Way Solid Slab.
System type | Thickness | Shear ( | Deflection
Ribbed | 30 cm | 26 KN | 
Solid | 20 cm | 112 KN | 
System type | Thickness |  | Deflection
Ribbed | 30 cm | 26 KN | 
Solid | 20 cm | 112 KN | 

## Slide 14
Preliminary Dimensions
2
2.1: Slab
Two-Way Solid Slab we took critical panel
Slab thickness h = 20 cm
h = ; β=
h =

## Slide 15
Preliminary Dimensions
2
2.2: Beams
Main Beams(drop)
= 450 * 300 mm
Secondary Beam(drop)
(around the structure)

## Slide 16
Preliminary Dimensions
2
2.2: Columns
Rectangular Column Dimensions
We used three dimensions for columns:
600*300 mm
600*250 mm
650*400 mm

## Slide 17
Preliminary Dimensions
2
2.2: Columns
Tributary area for the column = 3.44*5.79 = 19.92
Wu =1.2WD+1.6WL
=1.2(0.22*25+2.08) + 1.6*4=15.5 kN
Load on the column = Wu * tributary area
= 15.5* 19.92 = 308.76 KN= Pu
∅Pn = 1371 KN
∅Pn > Pu  OK

## Slide 18
Preliminary Dimensions
2
2.2: Columns
Circular Columns Dimensions D = 500 mm
Area of circular column = mm2
Circular Column

## Slide 19
Modeling Using ETABs
3
3.1: Model Checks
Compatibility check
Equilibrium check
Internal force check ( stress – srain check )
Deflection check

## Slide 20
Modeling Using ETABs
3
3.2: Element modifiers

## Slide 21
Modeling Using ETABs
3
3.1: Model Checks
3.1.1: Compatibility Check
As picture show
There is large
compatibility

## Slide 22
Modeling Using ETABs
3
3.1: Model Checks
3.1.2: Equilibrium check
 | Manual | From ETAB’s | %Error
LIVE LOAD | 13272.2 | 13278 | 0.04%
DEAD LOAD | 30994 | 30080 | 2.9%
SD LOAD | 13215.375 | 13222 | 0.05%
All values less than 5 %, So it`s OK

## Slide 23
Modeling Using ETABs
3
3.1: Model Checks
3.1.3: Internal force check
From combination →

## Slide 24
Modeling Using ETABs
3
3.1: Model Checks
3.1.3: Internal force check

## Slide 25
Modeling Using ETABs
3
3.1: Model Checks
3.1.3: Internal force check
Ln = 4.8 m
Q = 5kN/m2
M = Ln2 * L2 * Q/ 8
= 56.52 kN.m
From ETABs = 54.1 kN.m
% diff. = 3.7 % < 25%
It`s OK

## Slide 26
Modeling Using ETABs
3
3.1: Model Checks
3.1.4: Deflection check
Live: =4.03mm

## Slide 27
Modeling Using ETABs
3
3.1: Model Checks
3.1.4: Deflection check
=1.617mm

## Slide 28
Modeling Using ETABs
3
3.1: Model Checks
3.1.4: Deflection check
=2.827mm

## Slide 29
Modeling Using ETABs
3
3.1: Model Checks
3.1.4: Deflection check
=16.3mm
< (OK)

## Slide 30
Seismic Force Analysis
4
4.1: seismic zone factor ‘Z’
The building is in Nablus City, Palestine. So according to figure 5-1, seismic zone factor ‘Z’ equals to 0.2g
Z value is used to calculate mapped acceleration parameters.

## Slide 31
Seismic Force Analysis
4

## Slide 32
Seismic Force Analysis
4

## Slide 33
Seismic Force Analysis
4

## Slide 34
Seismic Force Analysis
4

## Slide 35
Seismic Force Analysis
4

## Slide 36
Seismic Force Analysis
4

## Slide 37
Seismic Force Analysis
4

## Slide 38
Seismic Force Analysis
4
Period Check
This picture shows stories that been considered

## Slide 39
Seismic Force Analysis
4
T = Cu * Ta
Ta = Ct *
Ct= 0.0488 , x = 0.75 , h = 20.04 m
Ta = 0.0488 *63 sec.
Cu = 1.4 (from table)
T = Cu * Ta = 1.4 * 0.463 = 0.651 sec.
Period Check

## Slide 40
Seismic Force Analysis
4
Period Check
Fundamental mode period from ETABS ( T= 0.593 Sec.)
Manual ( T= 0.651 Sec.)
T= 0.651 Sec. > ETABS Period
It`s OK

## Slide 41
Seismic Force Analysis
4
W = 56362.71 kN
V = Cs * W = 56362.71 * 0.114 = 6425.35 kN
From ETABs = 6309.45 kN
%diff. = 1.8% < 5%

## Slide 42
Seismic Force Analysis
4
4.2: After running the model

## Slide 43
Seismic Force Analysis
4
4.3: Check moment on beams:
Weight of drop beam per meter length= 0.25*0.30*25*1= 1.875 kN/m
Tributary area = 12 m2
Wu = 36.7 kN/m
Moment for both fixed ends = WL2/12 = 79.55 kN.m
Total moment = Wl2/8 = 79.55 kN.m
Moment from ETABs:
Negative one = 62 kN.m
Negative two = 71 kN.m
Positive = 45 kN.m
So total value = 111.5 kN.m
% difference = 6.4 %

## Slide 44
Seismic Force Analysis
4
4.3: Check story drift:
Story | H (m) | Delta (mm) | Displacement | Story drift | Allowable | Check
1 | 4.94 | 1.842 | 7.368 | 7.368 | 34.58 | Ok
2 | 7.54 | 4.084 | 16.336 | 8.968 | 52.78 | Ok
3 | 10.44 | 7.117 | 28.468 | 12.132 | 73.08 | Ok
4 | 13.64 | 10.735 | 42.94 | 14.472 | 95.48 | Ok
5 | 16.84 | 14.460 | 57.84 | 14.9 | 118 | Ok
6 | 20.04 | 17.998 | 71.992 | 14.152 | 143 | Ok
X- Direction:

## Slide 45
Seismic Force Analysis
4
4.3: Check story drift:
Y- Direction:
Story | Height | Delta (mm) | Displacement | Story drift | Allowable | Check
1 | 4.94 | 2.157 | 8.628 | 8.628 | 34.58 | Ok
2 | 7.54 | 3.687 | 14.748 | 6.12 | 52.78 | Ok
3 | 10.44 | 6.119 | 24.476 | 9.728 | 73.08 | Ok
4 | 13.64 | 9.149 | 36.596 | 12.12 | 95.48 | Ok
5 | 16.84 | 12.278 | 49.112 | 12.52 | 118 | Ok
6 | 20.04 | 15.181 | 60.724 | 11.62 | 143 | Ok

## Slide 46
Seismic Force Analysis
4
4.4: Check torsional irregularly:
X – Direction:
Story | Load Case/Combo | Item | Max Drift | Avg Drift | Ratio
Story10 | EQx Max | Diaph project X | 0.000242 | 0.000152 | 1.599
Story9 | EQx Max | Diaph project X | 0.000521 | 0.000346 | 1.506
Story8 | EQx Max | Diaph project X | 0.000578 | 0.000408 | 1.416
Story7 | EQx Max | Diaph project X | 0.000578 | 0.000419 | 1.379
Story6 | EQx Max | Diaph project X | 0.000565 | 0.00037 | 1.527
Story5 | EQx Max | Diaph project X | 0.000603 | 0.000432 | 1.395
Story4 | EQx Max | Diaph project X | 0.000509 | 0.00036 | 1.413
Story3 | EQx Max | Diaph project X | 0.000152 | 0.000106 | 1.436
Story2 | EQx Max | Diaph project X | 8E-05 | 6.5E-05 | 1.234
Story1 | EQx Max | Diaph project X | 6.7E-05 | 5.1E-05 | 1.314

## Slide 47
Seismic Force Analysis
4
4.4: Check torsional irregularly:
Story | Load Case/Combo | Item | Max Drift | Avg Drift | Ratio
Story10 | EQy Max | Diaph project Y | 0.000192 | 0.000125 | 1.542
Story9 | EQy Max | Diaph project Y | 0.000497 | 0.000322 | 1.541
Story8 | EQy Max | Diaph project Y | 0.000551 | 0.000369 | 1.492
Story7 | EQy Max | Diaph project Y | 0.000565 | 0.000394 | 1.436
Story6 | EQy Max | Diaph project Y | 0.000587 | 0.000393 | 1.494
Story5 | EQy Max | Diaph project Y | 0.000534 | 0.000402 | 1.33
Story4 | EQy Max | Diaph project Y | 0.00038 | 0.000281 | 1.351
Story3 | EQy Max | Diaph project Y | 0.000189 | 0.000138 | 1.371
Story2 | EQy Max | Diaph project Y | 0.000131 | 0.000114 | 1.147
Story1 | EQy Max | Diaph project Y | 0.000132 | 9.5E-05 | 1.391
Y – Direction:
As we see almost all values more than the ratio 1.2 so there is Irregularity and must be taken in the design.

## Slide 48
Seismic Force Analysis
4
4.5: Check P-delta
X – Direction:
Story | h | Delta | p | V | Ø
1 | 4.9 | 1.842 | 46003.3219 | 6224.1291 | 0.000695
2 | 2.6 | 4.084 | 37768.6034 | 5752.7372 | 0.002578
3 | 2.9 | 7.117 | 29075.0635 | 4959 | 0.003597
4 | 3.2 | 10.735 | 20431.5021 | 3899.1568 | 0.004395
5 | 3.2 | 14.460 | 11825.182 | 2416.4529 | 0.005528
6 | 3.2 | 17.998 | 517.7992 | 226.5714 | 0.003213
Story | h |  | p | V | Ø
1 | 4.9 | 1.842 | 46003.3219 | 6224.1291 | 0.000695
2 | 2.6 | 4.084 | 37768.6034 | 5752.7372 | 0.002578
3 | 2.9 | 7.117 | 29075.0635 | 4959 | 0.003597
4 | 3.2 | 10.735 | 20431.5021 | 3899.1568 | 0.004395
5 | 3.2 | 14.460 | 11825.182 | 2416.4529 | 0.005528
6 | 3.2 | 17.998 | 517.7992 | 226.5714 | 0.003213

## Slide 49
Seismic Force Analysis
4
Y- Direction:
4.5: Check P-delta
Story | h | delta | p | v | Ø
1 | 4.9 | 1.675 | 46003.3219 | 4346.7907 | 0.000904
2 | 2.6 | 2.865 | 37768.6034 | 4023.4958 | 0.002586
3 | 2.9 | 4.320 | 29075.0635 | 3474.2099 | 0.003117
4 | 3.2 | 5.870 | 20431.5021 | 2703.9146 | 0.003465
5 | 3.2 | 7.480 | 11825.182 | 1672.3407 | 0.004132
6 | 3.2 | 8.976 | 517.7992 | 151.35 | 0.002399
All values less than 0.1, so it’s ok

## Slide 50
Design of Beams
Design of Slabs
Design of Columns
Design for Structural Elements

## Slide 51
Design for Structural Elements
5
5.1: Design of Beams
5.1.1: Flexural
For
Assume
n = with Ast = 10*254 = 2540

## Slide 52
Design for Structural Elements
5
5.1: Design of Beams
5.1.2: Shear
V =
V = (1.2+0.4
V = 1.2D+1.6L
FOR As = 2111 & As = 1137
a =

## Slide 53
Design for Structural Elements
5
5.1: Design of Beams
5.1.2: Shear
=
Dead = 62.2 kN
Sd = 42.35 kN
Sd ring beam = 120 kN
Live = 37.6 kN

## Slide 54
Design for Structural Elements
5
5.1: Design of Beams
5.1.2: Shear
V = =
V = (1.2+0.4= 356.461 +2*(12.4) = 381.261 kN
3. V = 1.2D+1.6L = 281.72 kN
=
= V = (1.2+0.4

## Slide 55
Design for Structural Elements
5
5.1: Design of Beams
5.1.3: Torsion
Calculate the ultimate torsion =
From ETABs

## Slide 56
Design for Structural Elements
5
5.1: Design of Beams
5.1.3: Torsion
Calculate threshold torsion = 0.75*1* = 3.7 kN
& y = depth -2cover –ds = 318 mm so
Which is equal = x*y = 308 * 358 = 85224 381.261 kN
  2.8 mPa , so dimensions are ok

## Slide 57
Design for Structural Elements
5
5.1: Design of Beams
5.1.3: Torsion
= 2.70 + (2*0.325) = 3.35

## Slide 58
Design for Structural Elements
5
5.1: Design of Beams
5.1.3: Torsion
Assume stirrups with so Ab = 113
Check spacing:

## Slide 59
Design for Structural Elements
5
5.1: Design of Beams
5.1.3: Torsion
Calculate the longitudinal torsion reinforcement:
= * = 381
= SO use
Use

## Slide 60
Design for Structural Elements
5
5.1: Design of Beams
5.1.4: Example of Beam Reinforcement

## Slide 61
Design for Structural Elements
5
5.2: Design of Columns
5.2.1: Flexural
Pu = 2748.62 kN
0.1Ag fc = 0.1*28*600*250 = 420 kN
So 0.1Ag fc < Pu so design it Sa column

## Slide 62
Design for Structural Elements
5
5.2: Design of Columns
5.2.1: Flexural
So the value of K =1.72

## Slide 63
Design for Structural Elements
5
5.2: Design of Columns
5.2.1: Flexural

## Slide 64
Design for Structural Elements
5
5.2: Design of Columns
5.2.1: Flexural
Calculate M2:
Compare this value with the value of moment from top steel of Beams:

## Slide 65
Design for Structural Elements
5
5.2: Design of Columns
5.2.1: Flexural
So As = 497
a =
1.2* = 170.77 kN.m, So 1.2* > so take 1.2*

## Slide 66
Design for Structural Elements
5
5.2: Design of Columns
5.2.1: Flexural
Calculate MIII:
= 1.4(5.6+4.3+0.7) + 2.11 + 1.1*41.23 = 62.3 kN.m
Now check the dimensions according to the Bresler equation:

## Slide 67
Design for Structural Elements
5
5.2: Design of Columns
5.2.1: Flexural

## Slide 68
Design for Structural Elements
5
5.2: Design of Columns
5.2.1: Flexural
Assume so As = = 0.01 Ag
= 0.65*0.8 (0.85*28(Ag-0.01Ag) +420*0.01*Ag = 3284.245 kn
From interaction diagram determine the value of the px & py from M3, M2 respectively so
Px = 1852.2 kN Py = 1981.4 kN
= 1076.2 kN so its ok

## Slide 69
Design for Structural Elements
5
5.2: Design of Columns
5.2.2: Shear
Moment of As= 5 = 5*
V = compare this value with the value from ultimate and take the large value so take the 61 kN

## Slide 70
Design for Structural Elements
5
5.2: Design of Columns
5.2.2: Shear
=

## Slide 71
Design for Structural Elements
5
5.2: Design of Columns
5.2.3: Sample of rectangular column reinforcement

## Slide 72
Design for Structural Elements
5
5.3: Design of Slabs
5.3.1: Design of flexure
Section in Slab
We check slab in story @ elevation = 16.84 m
Assume shrinkage steel ratio (
so Ast = 0.0018 * 1000 * 200 = 360
Assume , n = use 4
So Ast = 4*113 = 452

## Slide 73
Design for Structural Elements
5
5.3: Design of Slabs
5.3.1: Design of flexure
= 0.9*452*420 ( 160 -

## Slide 74
Design for Structural Elements
5
5.3: Design of Slabs
5.3.1: Design of flexure
The regions in the dark color exceed the minimum steel ratio (

## Slide 75
Design for Structural Elements
5
5.3: Design of Slabs
5.3.1: Design of flexure
So we display the moment ( range from ( -40 – 40 kn.m ) :

## Slide 76
Design for Structural Elements
5
5.3: Design of Slabs
5.3.1: Design of flexure
= 0.0043
Ast = 0.0043 b*d = 0.0043 *1000*160 = 688 , assume
so number of bars n = use 7
with area of steel = 7 * 113 = 791

## Slide 77
Design for Structural Elements
5
5.3: Design of Slabs
5.3.1: Design of flexure
= 0.0043
Ast = 0.0043 b*d = 0.0043 *1000*160 = 688 ,
assume so number of bars n = use
7 with area of steel = 7 * 113 = 791 .

## Slide 78
Design for Structural Elements
5
5.3: Design of Slabs
5.3.2: Example of slab reinforcement

## Slide 79
Design of Footing
6
6.1: Introduction
Foundation is the element of a structure which connects it to the ground, and transfers loads from the structure to the ground. Foundations are generally considered either shallow or deep.

## Slide 80
Design of Footing
6
6.1: Introduction

## Slide 81
Design of Footing
6
6.2: Design
Depending on the calculation that will be shown later we saw that mat foundation is the appropriate type of footing to be used.

## Slide 82
Design of Footing
6
6.2: Design
Distribution of columns and load value on each

## Slide 83
Design of Footing
6
6.2: Design
Based on the ultimate loads on the columns from the whole structure we calculated the area of the foundation.
Total area of mat foundation = 749.23

## Slide 84
Design of Footing
6
6.2: Design
Screenshots from ETABs for the building showing the foundation

## Slide 85
Design of Footing
6
6.2: Design
6.2.1: Check if there is tensions under mat foundation
total service loads = 41852 kN = P
area of mat = 749.23
Find the moment in two directions:
= 41582 * 3.264 = 136604.93 KN.m (with positive direction)
= 33322.562 KN.m (with positive direction)

## Slide 86
Design of Footing
6
6.2: Design
6.2.1: Check if there is tensions under mat foundation
Tension area for the footing

## Slide 87
Design of Footing
6
6.2: Design
6.2.1: Check if there is tensions under mat foundation
Now we find stress @ point A & B to check if there is tension @ foundation.

## Slide 88
Design of Footing
6
6.2: Design
6.2.1: Check if there is tensions under mat foundation
Bearing capacity of the foundation are 3.5 which is equal to 343.35 .
Both values are less than Bearing capacity, so its ok
Select the design strip which is contains the maximum strip load: Total load inside these strip = 11508.03 kN Width of these strip = 6.33 m Length of strip = 39.08 m

## Slide 89
Design of Footing
6
6.2: Design
6.2.2: Select the design strip which is contains the maximum strip load
Total load inside these strip = 11508.03 kN Width of these strip = 6.33 m Length of strip = 39.08 m

## Slide 90
Design of Footing
6
6.2: Design
6.2.2: Select the design strip which is contains the maximum strip load

## Slide 91
Design of Footing
6
6.2: Design
Now we need to calculate the stress @ point (C + D):
Total soil reaction = 59.54 * 6.33 * 39.08 = 14728.791 KN
6.2.2: Select the design strip which is contains the maximum strip load

## Slide 92
Design of Footing
6
6.2: Design
Total load inside these strip = kn
Average pressure in the strip = 59.54 * ( = 53.03
Column loads modification factor =
So line load on the strip = 6.33 * 53.03 = 335.68 kN /m
6.2.2: Select the design strip which is contains the maximum strip load

## Slide 93
Design of Footing
6
6.2: Design
we multiply the reactions on columns by factor = 1.14 and draw Shear Force Diagram ‘SFD’ to calculate preliminary thickness for foundations SFD for the strip:
6.2.2: Select the design strip which is contains the maximum strip load

## Slide 94
Design of Footing
6
6.2: Design
6.2.3: Thickness of footing
The maximum shear force value equal to 2394.91 Kn
Wide Beam shear = = = 4186.9 d
Maximum shear force @ distance d from face of column = 2394.91 – 335.68 ( )
2394.91 – 335.68*( = 2361.342 +335.68 d
So the value of depth (d) = 0.6 m , h = 0.80 m.

## Slide 95
Design of Footing
6
6.2: Design
6.2.4: Punching shear check
Punching shear area:

## Slide 96
Design of Footing
6
6.2: Design
6.2.4: Punching shear check
Ultimate load on column = 3252.96 kN
Minimum value from above = 4729.28 > 3252.96 so its ok (thickness of slab acceptable).
h = 0.80 m (OK)

## Slide 97
Design of Footing
6
6.3: Design Foundation by ETABs
6.3.1: Check pressure under foundation by service loads:
Maximum value of stress under mat nearly equal to 70 << 343.35 so its ok .

## Slide 98
Design of Footing
6
6.3: Design Foundation by ETABs
6.3.2: Punching Shear Check:
As picture shows there is no Punching shear in foundation
so its ok.
Punching Shear vales from ETABs

## Slide 99
Design of Footing
6
6.3: Design Foundation by ETABs
6.3.2: Punching Shear Check:
As picture shows there is no Punching shear in foundation so its ok.
Punching Shear vales from ETABs:
Which the maximum value from circular column equal to 0.542
All of ratios less than one so its ok , which these ratios equal to .

## Slide 100
Design of Footing
6
6.3: Design Foundation by ETABs
6.3.2: Punching Shear Check:
As picture shown maximum shear force in x-direction equal to 1659.741 kN < 2512.14 kN so the capacity of foundation to resist shear force are ok.

## Slide 101
Design of Footing
6
6.3: Design Foundation by ETABs
6.3.2: Punching Shear Check:
Here maximum value equal to 2159.688 kN < 2512.14 kN so its ok, also we over conservative because we take the value @ the center of columns.

## Slide 102
Design of Footing
6
6.4: Foundation Detailing
6.4.1: Rebar in Direction one:
Top Rebar:
As figure shown the top steel is approximately minimum steel and this the general case.
Row Values in direction1

## Slide 103
Design of Footing
6
6.4: Foundation Detailing
6.4.1: Rebar in Direction one:
Bottom Rebar:
Here we note that the steel is too big than previous so its ok.

## Slide 104
Design of Footing
6
6.4: Foundation Detailing
6.4.2: Rebar in Direction Two:
Top Rebar

## Slide 105
Design of Footing
6
6.4: Foundation Detailing
6.4.2: Rebar in Direction Two:
Bottom Rebar:

## Slide 106
Design of Footing
6
6.5: Mat foundation Reinforcement

## Slide 107
Shear Wall
7
7.1: Design of Shear Wall
Location of Shear Wall:

## Slide 108
Shear Wall
7
7.1: Design of Shear Wall
By using section designer program: we got the following results:
ultimate forces in this table:
Required area of steel = 0.015263

## Slide 109
Shear Wall
7
7.1: Design of Shear Wall
From Bresler equation:
From
From
Minimum steel ratio for walls ( = 0.0025) ,
= 0.65*0.80* ( 0.85*28 ( ) + 420 *
= 12.89 * 5750 * 200 = 14823.50 KN >>> 1519.2739KN so its ok

## Slide 110
Shear Wall
7
7.1: Design of Shear Wall
Also ()more than ultimate load from envelope of all combinations so its OK.
Axial & Torsion values from ETABs:

## Slide 111
Shear Wall
7
7.1: Design of Shear Wall
In our design we use Uniform Reinforcing method: (
According to the figure above shown the values of design loads:
ultimate load which is equal to 1519.3
ultimate moment equal to 9642.2 .

## Slide 112
Shear Wall
7
7.1: Design of Shear Wall
Now we need to calculate the tension and compression acting of the boundary element of the wall
Compression force (C):
2. Tension force (T):

## Slide 113
Shear Wall
7
7.1: Design of Shear Wall
calculate area of steel for both compression and tension and take maximum value from both.
For compression calculate area of steel from capacity of column in axial.
2665.1 * = 0.65 * 0.80 ( 0.85*28 ( 1500*200 - ) + 420 * )
2665.1 * = 3712800 + 206.024
,So no need to Reinforcement

## Slide 114
Shear Wall
7
7.1: Design of Shear Wall
2. For tension side:
So the value we take 4953.5 , 25
3. For the critical section in middle we calculate area of steel for it from the remaining of
Where the value of the moment in second direction is equal to as shown from the previous figure.
So we represent the inner zone in SAP to get interaction diagram for it.

## Slide 115
Shear Wall
7
7.1: Design of Shear Wall
So from the values in previous we note that the ratio of axial load to the second bending moment are huge, so we can calculate the area of steel from axial compression load only from capacity of column in axial.
, (41

## Slide 116
Shear Wall
7
7.2: Shear Reinforcement
For wall
Transverse Reinforcement for Boundary element:
max of these values
So take maximum ratio from above 0.0077113
so

## Slide 117
Shear Wall
7
7.3: Shear wall layout
7.3.1:Shear wall layout for stories 6, 7 & 8

## Slide 118
Shear Wall
7
7.3: Shear wall layout
7.3.2: Shear wall layout for story 5

## Slide 119
Shear Wall
7
7.3: Shear wall layout
7.3.3: Shear wall layout for story 4

## Slide 120
Shear Wall
7
7.3: Shear wall layout
7.3.4: Shear wall layout for story 3

## Slide 121
Shear Wall
7
7.3: Shear wall layout
7.3.5: Shear wall layout for story 2

## Slide 122
Shear Wall
7
7.3: Shear wall layout
7.3.6: Shear wall layout for story 1

## Slide 123
Shear Wall
7
7.4: Detailing of Shear wall

## Slide 124
Shear Wall
7
7.4: Detailing of Shear wall

## Slide 125
Shear Wall
7