## Slide 1: بسم الله الرحمن الرحيم
An-Najah National University
Faculty of Engineering and Information Technology
Department of Mechanical and Mechatronics Engineering

## Slide 2: FAMO A 3-Axis Multi Tool CNC Machine
Supervised by :
Dr. Salameh Abdul Fattah
Fahid Yaseen
Omar Moumar
Mahmoud Diab

## Slide 3: Contents
Introduction
Mechanical Design
Motors
Control
Results & Analysis
Discussion
Conclusions and Recommendations

## Slide 4: Introduction
Overview of CNC machine
  What do we mean by CNC ? CNC stands for Computer Numerically Controlled machine
Basic Components
  Machine
  Control System
    Open loop
    Close loop

## Slide 5: Objectives & Motivations
To achieve very high accuracy
To reduce time and effort needed.
To design a more flexible production system
Reducing error probabilities in a way devolves to zero error.
Able to perform many shapes.

## Slide 6: Mechanical Design
The Mechanical design consists of two main parts:
The Frame
The Transmission System

## Slide 7: Frame
The frame of the machine is made of HDF wood.
  We designed the frame using AutoCAD.
  We cut the frame pieces using a CNC milling machine.
  We assembled the pieces together.

## Slide 8: 3D Drawing by AutoCAD

## Slide 9: Transmission System
We will talk about :
  Sliders and bearings
  Rails
  Pulley and Belt

## Slide 10: Sliders and Bearings
Sliders and Bearings
  Constrain motion to one degree of freedom motion only
  Greatly reduces friction between moving parts
  We used linear ball bearing sliders

## Slide 11: Sliders
  In our project we used the following ball bearing sliders.
LMK8 flange ball bearing slider
SC8UU ball bearing slider.

## Slide 12: Rails
Rails are the part that the slider moves along.
  Rails provide free linear motion in one direction
  Frictionless to make motion very smooth
Chrome-plated steel shaft

## Slide 13: Pulley and Belt
Belts
  Transmit motion from motor pulley to the counter pulley.
  Provide constant tension

## Slide 14: Pulley and Belt
GT2 20 teeth timing pulley
GT2 timing belt

## Slide 15: Motors
What is a Stepper Motor ?
  DC motors that move in discrete steps
  Multiple coils (phases)
  By energizing each phase in sequence, the motor will rotate, one step at a time

## Slide 16: Motors
What are stepper motors good for ?
  Precise positioning
  Speed Control
  Low speed – High torque

## Slide 17: Motors
Advantages
  High torque at startup
  Easy to control
  Easy to implement
  Can be used for both open-loop and closed-loop systems
  High precision and Reliability
  Excellent response time

## Slide 18: Motors
Disadvantages
  Requires a dedicated control circuit
  High current consumption
  Torque reduced at high speed
  Hard to control at high speeds

## Slide 19: Control
Hardware
  Arduino Uno
  GRBL Shield
  Stepper motor drivers ( A4988)
  Computer
Software
  GRBL and XLoader
  Universal Gcode Sender
  MakerCAM

## Slide 20: Control
What is GRBL ?
  Open source software
  Runs on Arduino
  Takes Gcode and turns it to motor signals
What is Gcode ?
  The most widely used numerical control (NC) programming language.
  It is a way for you to tell the machine to move to various points at a desired speed.

## Slide 21: The Arduino and the shield.
The Arduino, the shield and the drivers

## Slide 22: Control
How get this to work ?
  Upload GRBL software to Arduino Using XLoader

## Slide 23: Streaming G-Code
  There are many programs that can be used one of which is Universal G-Code sender.

## Slide 24: Advantages
Universal Gcode Sender
  User friendly interface
  Sending Gcode Commands
  Sending Gcode Files
  Visualizing
  Micro Steps Control
  Speed Control

## Slide 25: G-Code
CAD to Gcode
  CAD models can be created using many programs. These drawings can later be turned to G-Codes.

## Slide 26: Discussion
Problems
Changing the primary idea of the project
Material of the frame of the machine.
Final processing of wood
Cutting the wood into the frame
Wrong dimensions
The Corners
Accuracy of the Y-axis

## Slide 27: Changing the primary idea of the project
The first idea was to create a 2-axis hot wire
the idea was changed to make a 3-axis multi tool CNC machine

## Slide 28: Material of the frame of the machine
Stainless steel, Aluminum, Acrylic plastic and wood
We chose processed wood

## Slide 29: Final processing of wood
Although the wood used is already processed but after being subjected to humidity or liquids for extended periods of time
painting the wood with car paint that works as an insulator

## Slide 30: Cutting the wood into the frame
cuting the wood with primitive tools
Afterwards, we redesigned the project for better balance and cut the parts of the frame at a CNC workshop to get maximum accuracy

## Slide 31: Wrong dimensions
After cutting the wood into shape, we realized that the thickness of the wood was not as ordered (16mm) but it was (17mm). This lead to some problems in fitting the pieces together.
To solve the problem we had to use a file to smoothen the edges and curves of the pieces

## Slide 32: Accuracy of the Y-axis
At first we had one motor running each axis
We solved this problem by adding another motor to the other side of the y-axis

## Slide 33: How to Improve In the future
To make the machine as industrial as possible we are going to replace the wood frame with a stainless steel or Aluminum frame. The z-axis links will be higher so that there will be more space for the z-axis to travel.
Better motors and control system will be used for a larger scale machine.
The transmission system will be replaced with screw and gears mechanism.

## Slide 34: Conclusion
The round cross-sectional rails are not the best choice to go with accurate industrial machines, but we had to go with what was available and affordable. But on the other hand, the linear rails aren’t too bad to be used because they linear smooth and frictionless motion.
A better alternative would be to use the rack and pinion mechanism or the gear and screw type of mechanisms.
The stepper motor is the best choice for automated and computerized motion due to its ease of use and high accuracy and reliability. It’s very easy to control and install into automated systems.

## Slide 35: Conclusion
The Arduino is the best attractive choice of a controller, because it’s very cheap and easy to deal with. Sensors can be connected to Arduino directly and also it’s very basic programs and simple algorithms.
We found out for the first time that the Arduino can host a CNC GRBL shield to receive G-Codes and send pulses to control steppers very accurately using micro-stepping motor driver.

## Slide 36: Recommendations
For industrial purposes a better controller must be used, because the Arduino isn’t designed to be put in an industrial environment. Mach3 Interface board or PLC are recommended.
An industrial machine should be made of better materials than wood such as Aluminum and Stainless steel.
A screw and gear mechanism is the best choice for both accuracy and endurance.
Larger and stronger motors must be used to handle the high torques and bending forces.
A set of industrial motor drivers must be used to handle the high currents the motors will draw.

## Slide 37: Thank you