## Slide 1
Done by :Ayed Hamad ,Izzat Omran and Meera Mustafa
Military Helmet Design
Supervised by : Dr.Iyad Assaf

## Slide 2
Introduction
01
03
05
02
04
Material selection
ABAQUS/CAE
Theoretical
Conclusion

## Slide 3
Introduction
History of military helmets
Helmets evolves with the evolution of firearms and the newer the helmets the lighter and more protective they are.
Composite materials
Definition, advantages, Fiber reinforced composites, Aramid Fibers.
Kevlar 129
Kevlar types, comparison between Kevlar 29 and 129.
Manufacturing
Preheating oven, thermoforming, and trimming.
Hashin damage
Explanation of the symbols and the meanings.

## Slide 4
Introduction
History of military helmets
Composite materials
Kevlar 129
Manufacturing
Hashin damage

## Slide 5
History of military helmets
Composite materials
Kevlar 129
Manufacturing
Hashin damage
The development and diversity of weapons drew attention to the military protective helmet, to reduce serious injuries and to protect the soldier's head from fragmentation and the ballistic impact caused by these weapons, and to prevent bullet penetration. There was a need to develop the old helmet and reduce its heavy weight and high cost. Moreover, the use of available materials to achieve this purpose.

## Slide 6
History of military helmets
Composite materials
Kevlar 129
Manufacturing
Hashin damage
'Composite material' is defined as a combination of (usually) two different materials, each with its own mechanical and chemical properties, that work together after being judiciously embedded, either physically or chemically, to produce a new material with unique properties that are better than the sum of those of the constituent components.
Fiber-reinforced composites (FRC) are the most common composites employed in today's technological applications. The major objectives to be met while creating these materials are great strength and stiffness while keeping the weight to a minimum.
Aramid fiber is organic fiber which is defined as a manufactured fiber in which fiber forming substance is a long chain synthetic polyamide. Fibers such as Kevlar, Nomex, Technora, and Twaron will be included in the Aramid family.

## Slide 7
History of military helmets
Composite materials
Kevlar 129
Manufacturing
Hashin damage
Kevlar Types
Kevlar 29
Kevlar 49
Kevlar 100
Kevlar 119
Kevlar 129
Kevlar 149
Kevlar29 VS Kevlar 129

## Slide 8
History of military helmets
Composite materials
Kevlar 129
Manufacturing
Hashin damage

## Slide 9
History of military helmets
Composite materials
Kevlar 129
Manufacturing
Hashin damage
Tensile strength
Shear strength

## Slide 10
ABAQUS/CAE
Bullet shape comparison
1
Angle comparison
2
Material comparison
3
Layers comparison
4
Helmet Full Model
5

## Slide 11
ABAQUS/CAE
Bullet shape selection
Angle comparison
Material comparison
Layers comparison

## Slide 12
Bullet shape selection
Angle comparison
Material comparison
Layers comparison
Conical shape
Hemispherical shape
Chart: time (ms)
Bullet shape | Kinetic energy before (J) | Kinetic energy after (J) | Energy absorbed by the plate (J)
Hemispherical | 3200 | 2886.4 | 313.6
Coincal | 3200 | 3002.9 | 197.1

## Slide 13
Bullet shape selection
Angle comparison
Material comparison
Layers comparison
Chart: time (ms)
Angles | Kinetic energy before (J) | Kinetic energy after (J) | Energy absorbed by the plate (J)
90/0 | 3200 | 2879.6 | 320.4
0/90 | 3200 | 2880.2 | 319.8
90/45 | 3200 | 2846.5 | 353.5
45/-45 | 3200 | 2833.3 | 366.7
0/45 | 3200 | 2861.2 | 338.8
45/0 | 3200 | 2869.4 | 330.6
45/90 | 3200 | 2851.35 | 348.6

## Slide 14
Bullet shape selection
Angle comparison
Material comparison
Layers comparison
Chart: time (ms)
Material | Kinetic energy before (J) | Kinetic energy after (J) | Energy absorbed by the plate (J)
Glass fiber reinforced polymer | 3200 | 2732.5 | 467.5
Carbon fiber reinforced polymer | 3200 | 2768.4 | 431.6
E glass epoxy | 3200 | 2412.8 | 787.2
kevlar 129 | 3200 | 1860.7 | 1339.3
Carbon fiber toray T800 | 3200 | 2472.5 | 727.5

## Slide 15
Bullet shape selection
Angle comparison
Material comparison
Layers comparison
Chart: time (ms)
the more layers added the less ballistic velocity outcome and noticed that the positive ballistic velocity means that the projectile has fully penetrated the target plate, while the negative represents partial penetration and rebounding. It can be observed that for the case of 4.5mm, its ballistic velocity is -325.4m/s. It means that the most kinetic energy of the projectile has been absorbed by the target; negative ballistic velocity means that rebounding has emerged.

## Slide 16
Helmet Full Model
Modeling on the ABAQUS
Modeling the parts, Material definition and assembly, Boundary conditions and meshing and finally the model results.
Effect of impact angle on helmet thickness
Different models were carried out to investigate the effect of the impact contact angle.
2
1
Theoretical
The results of the theoretical calculation and comparison with the analytical results.
4
3
Conclusion
The summary of the study and the results.

## Slide 17
Modeling on the ABAQUS
Modeling the parts
Material definition and model assembly
Boundary conditions parts meshing
Model Results

## Slide 18
Modeling the parts
Material definition and model assembly
Material comparison
Model Results
Half helmet dimensions
rigid bullet dimensions

## Slide 19
Modeling the parts
Material definition and model assembly
Boundary conditions parts meshing
Layers comparison
The material of the military helmet was made of Kevlar 129 since it absorbs more energy than other composite materials. The helmet consists of different plies with different direction. As indicated in the investigation chapter, the best orientation of plies angle was selected as (45/-45).
A reference point (RP) was assigned to the rigid bullet.

## Slide 20
Modeling the parts
Material definition and model assembly
Boundary conditions parts meshing
Model Results
the element type for the helmet was S3R (shell element, three nodes, reduce integration). In addition, the rigid bullet was meshed using R3D3 (rigid element, three dimensions, three node)
the bottom surface of the helmet was fully clamped as shown in figure (6.4). Also, the bullet was not allowed to move in all direction except in z-direction (where the bullet will move 800m/s)

## Slide 21
Modeling the parts
Material definition and model assembly
Boundary conditions parts meshing
Model Results
the more layers added the less ballistic velocity outcome and noticed that the positive ballistic velocity means that the projectile has fully penetrated the Helmet, while the negative represents partial penetration and rebounding. It can be observed that for the case of 10mm, the bullet rebounded at time 0.075ms and returned back
Chart: Velocity against time

## Slide 22
Effect of impact angle on helmet thickness
At the angle 0°
At the angle 30°
At the angle 45°
At the angle 60°
At the angle 90°

## Slide 23
At the angle 0°
the helmet thickness needed
To stop the bullet is 10 mm
At the angle 30°
the helmet thickness needed
To stop the bullet is 8.25 mm
At the angle 45°
the helmet thickness needed
To stop the bullet is
8 mm
At the angle 60°
the helmet thickness needed
To stop the bullet is 8.75 mm
At the angle 90°
the helmet thickness needed
To stop the bullet is 10.25 mm

## Slide 24
Theoretical
Initial velocity
for the projectile
Which is kept unknown.
The cone angle
The angle of the nose of bullet = 112.3°
The projectile diameter
Which equals 7.6mm
The projectile mass
Which is 10 g
Pi symbol
Which equals 3.1415
Constant beta
Equals 2sin (θ/2)=1.66
Yield strength of Kevlar 129
Which equals 3620MPa
The helmet thickness
Which varied between
1 mm and 15 mm
Which equals 1230Kg/m^3
Kevlar 129 density

## Slide 25
Theoretical results
289.89 m/s
431.34 m/s
549.12 m/s
197.71 m/s
364.98 m/s
492.17 m/s
603.17 m/s
1mm
2mm
4mm
6mm
3mm
5mm
7mm
704.88 m/s
800.42 m/s
891.51 m/s
654.95 m/s
753.29 m/s
846.44 m/s
935.73 m/s
8mm
9mm
11mm
13mm
10mm
12mm
14mm

## Slide 26
Theoretical VS ABAQUS/CAE
Chart: velocity m/s
| 198 | 290 | 365 | 431 | 492 | 549 | 603 | 655 | 705 | 753 | 800 | 846 | 892 | 936 | 979
Theorital thickness | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15

FEA thickness | 2 | 3 | 4.5 | 5.75 | 6.5 | 7 | 8 | 8.5 | 8.75 | 9.25 | 10 | 9.5 | 10.25 | 10 | 11

## Slide 27
Conclusion
The hazardous
bullet shape
The most hazardous bullet shape was the conical shape.
The best layers
Layup angles
The best angles were
(45/-45)
Which absorbs more energy than the other angles.
The best composite
Material for the helmet
Kevlar 129 is the best of 5 materials were tested in Abaqus/cae
Theoretical
After comparing the theoretical and analytical results for velocity 800 m/s there was a good agreement
Effect of impact
Angle
After comparing the results of different impact angles the most hazardous impact angle was 90°

## Slide 28
Thank Y u
1