## Slide 1: Spare Parts inventory Management system
Academic Year: 2016
Department Name: Industrial Engineering
Group Members:
Barehan Qishawi
Dua'a Hammad
Ruba Radi
Rula Aqel
Supervisor Name: Eng. Tamer Haddad
An-Najah National University
Faculty of Engineering and IT

## Slide 2: List of content
Overview
Problem statement
Objectives
Comparison of current and new situation
Methodology
Recommendations
Inventory Model
The limitations
Forecast Model

## Slide 3: Overview
The company was established in 1950
Their products
Their progress.
Notes: In 2007, Al Arz started the first step towards exporting, where Jordan was the first station,
two years later, Al Arz acquired the global food safety certificate HACCP. This
achievement was a Palestinian industrial pride, since Al Arz was the first company that
acquired this certificate among the ice cream and dairy manufacturers in Palestine and
Jordan.
With state of the art facilities and equipment along with a production capacity reaching up
to 8 million liters of ice cream per month, offering more than 65 SKUs, we aim to create a
smile for our clients who enjoy the experience of different tastes of life

## Slide 4: Problem statement
Notes: Al-Arzcompany is suffering from lack of excellent spare parts inventory management
systems. These lead to increase the required efforts, time and money. It also leads to
production break down in certain cases due to the lack of spare parts, or delays in
receiving required parts and resulted in back orders. Such issue causes less productivity,
profitability, efficiency, and quality.Therefore, the company performance in the
competitive environment will be affected.
After visiting the factory, looking into the current available systems and having
discussions with the factory management these problems were noticed.This project aims
to solve the above mentioned problems and arrange the inventory management system.

## Slide 5: objectives
To establish spare parts management system.
      Save time
      Reduce the number of break downs
      Provide high productivity ,efficiency and quality.
      Reduce cost.
      Identify which item to be stock, quantity to stock and other parameters.
Notes: The project aims to provide establish spare parts inventory management system that
will save time, reduce the number of break downs and provide high productivity,
efficiency ,effectiveness , quality, reduce cost, and increase confidence. Also, that will
help the company to identify which item to be stock, quantity to stock ,lead time and
other parameters.

## Slide 6: Methodology
Data Collections
Aggregation
Building
Forecasting
model
Building
Inventory
model
ABC Analyses
Comparison

## Slide 7: Data Collections
There are many types of data that was collected from Al-Arz Company:
Company departments
Machines in each department
List of spare parts, spare parts price, lead time and the current inventory level.
Maintenance orders

## Slide 8: Aggregation
By clustering several similar services or products.
565 Maintenances orders
215 Spare parts
110
groups

## Slide 9: Aggregation
According to
    Type
    price
    lead time.
    Group 19(لبادة 12)
Notes: Benefit from aggregation is more accurate forecast and less error

## Slide 10: ABC Classification
A-items have highest demand and C-items have lowest demand.
Notes: انو ركزنا على مجوعه A فقط لانو باقي المجموعات مالها معلومات كافيه وليش عملنا هاد التحليل

## Slide 11: A-items
Notes: هاي القائمه بتمثل عناصر المجموعه A والي ركزنا عليها وعددهم35 ... العناصر الملونه هيك الجروب زي متلا بيل 8 اما الي مو ملونه بتمثل قطعه وحده زي طقم سكاكين

## Slide 12: Forecasting model
Measurable forecast
    Naïve method
Ft = yt-1
yt-1: actual value in period t-1 Ft: forecast for period t
    Simple moving average:
Ft= (At-1+At-2+At-3+…+At-n)/n
Ft: forecast for the coming period. n:number of periods to be averaged
At-1: actual occurrence in the past period for up to "n" periods.
    Exponential Smoothing:
Ft =α *At-1+(1- α)*Ft
α: smoothing constant. Ft: forecast for period t A: actual value in period t.
    Trend Adjusted Exponential Smoothing:
Ft+1 = At + Tt At = αDt+ (1- α)( At-1 + Tt-1) Tt= β(At - At-1) + (1 - β)Tt-1
Tt: smoothed trend for time period t.
α:smoothing constant for forecast.
β:smoothing constant for trend.
Notes: انو طبقنا اربع طرق الفوركاست على كل قطع A

## Slide 13: Spare part 22
Notes: انو هاد مثال لقطعت غيار معمولها فوركاست والي هي سكاكين على شكل في وهاي الجداول موجوده بالابندك

## Slide 14
Chart: 
| 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27
Actual Quantity | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 2 | 0 | 3 | 3 | 2 | 0 | 1 | 0 | 0 | 0 | 6 | 0 | 1 | 1
Forecast | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 2 | 0 | 3 | 3 | 2 | 0 | 1 | 0 | 0 | 0 | 6 | 0 | 1
Chart: 
| 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27
Actual Quantity | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 2 | 0 | 3 | 3 | 2 | 0 | 1 | 0 | 0 | 0 | 6 | 0 | 1 | 1
Forecast | 5 | 3 | 0 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 2 | 2 | 3 | 2 | 1 | 1 | 1 | 0 | 2 | 2 | 3
Chart: 
| 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27
Actual Quantity | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 2 | 0 | 3 | 3 | 2 | 0 | 1 | 0 | 0 | 0 | 6 | 0 | 1 | 1
Forecast | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 2 | 0 | 3 | 3 | 2 | 0 | 1 | 0 | 0 | 0 | 6 | 0 | 1
Chart: 
| 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27
Actual Quantity | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 2 | 0 | 3 | 3 | 2 | 0 | 1 | 0 | 0 | 0 | 6 | 0 | 1 | 1
Forecast | -1 | -1 | 2 | 1 | -1 | -1 | -1 | -1 | 1 | 1 | 3 | 1 | 4 | 4 | 3 | -2 | 1 | -1 | -1 | -1 | 9 | 1 | 1 | 1
Naïve
Simple Moving Averages
Exponential Smoothing
Trend Adjusted Exponential Smoothing

## Slide 15: Forecasting Errors
Forecast errors can be classified as
    Biased errors.
    Random errors.
Type of errors :
    The cumulative sum of forecast errors (CEF)
    Average forecast error (mean bias)
    The mean squared error (MSE)
    Mean absolute deviation

## Slide 16
Type of errors
  Stander deviation
  The mean absolute percent error

## Slide 17: selection Criteria
Forecast method has been selected by using these criteria.
Minimizing bias
Minimizing MAD or MSE.
Meeting managerial expectations of changes in the components of demand.
Minimizing the forecast error last period.
For Spare parts 22

## Slide 18
Select The pest methods
Notes: بنوضح انو بناء على اقل خطء لتنبء للقطعه بنختاره وبنضرب النسبه المئويه بالكميه المتوقعه

## Slide 19
The model used is the fixed order quantity.
    Total Inventory Monthly Cost.
Q: lot size in a unit
H: cost of holding one unit in inventory for one month (percentage)
D: monthly demand
S: cost of ordering or setup one lot (NIS per lot)
    Safety stock.
Inventory Model
Z: the number of standard deviation to the right of the average demand during the lead
time that places 90% of the standard deviation curve.
σl :Stander Deviation for lead time
σt : standard deviation of monthly demand
L: lead time
Notes: When the inventory position reaches a predetermined minimum level, called reorder point (R),a fixed order (Q) is ordered depends on the item. In a continuous review system, although the order quantity Q is fixed, the time between orders can vary. Hence Q can be based on the EOQ, a price break quantity (the minimum lot size that qualifies for a quantity, discount), a container size, or some other parameters can be selected by the manager.

## Slide 20
    Economic Order Quantity EOQ
    D: monthly demand
    Time between orders TBO
Inventory Model

## Slide 21
Assumptions:
Demands are known and vary with the spare parts
Lead time is known and constant for each spare part
Only variable costs are setup and holding
Receipt of inventory is instantaneous and complete
Quantity discounts not possible
H = 20% of the spare part price ,S = 5% of spare part price and the level of confidence = 90% (Z=1.28).
Inventory Model

## Slide 22
Inventory monthly Cost

## Slide 23
Inventory Parameters

## Slide 24
Comparison of current and new situation

## Slide 25
Inventory monthly cost was 646 NIS then become 548 NIS.
So it decreased by 15%.
Comparison of current and new situation
Chart: 
| 2 | 1 | 2 | 2 | 3 | 0 | 0 | 2 | 3 | 1 | 3 | 2 | 3 | 2 | 2 | 3 | 2 | 3 | 3 | 1 | 0 | 0 | 1 | 1 | 2 | 1 | 1 | 1
EOQ | 15.75 | 29 | 7.2 | 9.5 | 40 | 55 | 66 | 4.5 | 20 | 17.5 | 21.375 | 74 | 2.85 | 2.25 | 1.75 | 11.25 | 3.45 | 3 | 22.5 | 13 | 7.5 | 1.5 | 1.5 | 9 | 9 | 6 | 94 | 0.45
Old Q | 15.75 | 30 | 7.2 | 9 | 40 | 62.5 | 75 | 4.5 | 20 | 17.5 | 20.25 | 76 | 2.85 | 2.25 | 1.75 | 11.25 | 3.45 | 3 | 22.5 | 13 | 7.5 | 1.5 | 1.5 | 9 | 9 | 6 | 114 | 60.0008

## Slide 26: The limitations
There is not enough data; the data used are from 2011-2014, the only available data.
Poor data collection, missing data in some dates, incorrect naming for the spare parts, etc…
There is no tracking system for the inventory, so the data were not accurate and it has been estimated.
They have added new production lines so these don't have enough data.

## Slide 27: Recommendation
There is need for supervisor on the workers to fill the required data in maintenance orders.
More attention needed to document data because having a high quality data will lead to a better result.
Build a historical data for new production line.
Summarize and document accurate information about amounts such as inventory quantity, lead time, and price.
The spare parts need to have coding system that will reduce the time and the effort to identify them.
Using of computerize maintenance order or fill paper maintenance order on computer in order to benefit from computer programs.