## Slide 1: Design of OFFICE OF EXCHANGE “Palestinian Post \ Jericho”
Prepared by:
Khawla Salameh
Noor Barbour
Rema’ Alawneh
Supervisor:
Dr. Riyad Awad

## Slide 2: Outlines
Project objective.
Project description.
Preliminary Design of slabs, beams & columns.
Three dimensional structural analysis and design.
Seismic loads analysis.

## Slide 3: Project Objective
To design the building of Office of Exchange \ Palestinian Post in Jericho using the primary principles of structures by using one dimensional analysis and three dimensional structural analysis and then design it for seismic loads analysis.

## Slide 4: Plan of Ground Floor

## Slide 5: Project Description
The building is used for commercial purposes.
The building consists of one floor with an area of 349.7 m²
The floor assumed to be two blocks, block 1is used for Customer Services and block 2 for offices.
The elevation of the floor is 7.05 m in block 1 and 4.45 m in block 2.

## Slide 6: Materials
Reinforced concrete:
  Concrete compressive strength fc = 24 MPa for slabs, beams and columns.
  Concrete compressive strength fc = 28 MPa for footings.
  Modulus of elasticity Ec = 23 GPa
Steel:
  Yield stress in steel bars and stirrups = 420 MPa

## Slide 7: Design Codes
ACI 318-08: American concrete institute provisions for reinforced concrete structure design.
UBC-97: Universal Building Code used for seismic loads calculations.
IBC 2009:International Building Code used for live load determination.
Notes: The following codes and standards are used in this study:

## Slide 8: Preliminary Design of slabs

## Slide 9: One way Solid slab: (Block 1)
Thickness = 20 cm
Dead load = 5 KN/m²
Live load = 0.5 KN/m²
Superimposed dead load = 2 KN/m²
Notes: I will begin with the type of slabs that we used in block 1 , that is one way solid slab
thickness of the slab is determined based on the longest span and it 20cm Since the slabs are inclined , they are not accessible , so live load is
Dead load is calculated using the thickness of the slab, and it..
Superimposed dead load is assumed to be 2 KN/m2 , we took into consideration the weight of solar pools In it.

## Slide 10: Solid slab reinforcement distribution
Notes: Using the principles of simple beam , we determine the reinforcement in the solid slab

## Slide 11: One way ribbed slab:(Block 2)
Thickness = 30 cm
Dead load = 5.1 KN/m²
Live load = 2.5 KN/m²
Superimposed dead load = 4.1 KN/m²

## Slide 12: Superimposed dead load details:
Super imposed load = Wtiles + Wmortar + Wsand + Wplaster +0.104 (partition)
= (0.03)(27) + (0.03)(23) + (0.1)(20) + (0.02)(23) + 0.104
= 4.1 KN/m²

## Slide 13: Ribbed slab reinforcement distribution

## Slide 14: Preliminary Design of beams

## Slide 15: Beam distribution in block 1
B1
B2

## Slide 16: Beams in block 1

## Slide 17: Moment diagram for frame 2

## Slide 18: Reinforcement distribution for B1 & B2:
B1
B2

## Slide 19: Beams details in block 1

## Slide 20: Beams of block 2:
Notes: We consider the main beams as simple beams , and the secondary beams as continuous beams , and here we have a girder

## Slide 21: Beams details in block 2

## Slide 22: Preliminary Design of columns

## Slide 23: Columns distribution:

## Slide 24: Design requirements According to (ACI318-08) code: Ф Pn= Фλ (0.85 f'c (Ag-As) +As fy) Buckling will not occur if : Pu < Ф Pcr. Where: Ф reduction factor = 0.7

## Slide 25: Column 1
Column 2
Columns details:

## Slide 26: Three Dimensional Structural Analysis and Design

## Slide 27: Material Property for concrete

## Slide 28: Shell Data
Ribbed slab definition

## Slide 29: Modification Factors
A1= (0.06×0.52) + (0.12×0.24) =0.06 m2
A2= (0.06×0.52) = 0.0312 m2
A3= (0.224×0.52) = 0.1165 m2
I1= (0.52×0.063/12) + (0.06×0.52) × (0.08162) + (0.12×0.243/12) + (0.12×0.24) × (0.06842) =4.87 e-4 m4
I2 = (0.52×0.063/12) = 9.36 e-4 m4
I3 = (0.52×0.2243/12) = 4.87e-4 m4

## Slide 30: Modifiers equations
whe
Modifiers for ribbed slab
Membrane f11modifier =(A2/A3) = 0.27
Membrane f22 modifier = (A1/A3)=0.515
Membrane f12 modifier = (A2/A3) = 0.27
Bending m11 modifier = 0.25×( I2/ I3) = 0.004805
Bending m22 modifier = 0.25×( I1/ I3) = 0.25
Bending m12 modifier = 0.25×( I2/ I3) =0.004805
Shear v13 modifier = (A2/A3)= 0.27
Shear v23 modifier = (A1/A3)= 0.515
Mass m modifier = (M 1 way rib / M solid) = 0.91
Weight w modifier = (9.81×M 1 way rib/ 9.81×M solid)= 0.91

## Slide 31: Modifiers
One way solid slab
solid slab section data

## Slide 32: Modifiers
For columns
For Beams

## Slide 33: Compatibility Check

## Slide 34: Check equilibrium
Description | Block 1 | Block 2
Slabs | 960 | 645.66
Columns | 206.85 | 112.5
Beams | T-section = 375 Rec. = 500 | 388.665
Total | 2041.85 | 1146.825
Total dead load =3188.675 KN
Total live load= 427.925 KN
Total Superimposed load = 965.18 KN
Dead load results:

## Slide 35: Dead, live and superimposed results from SAP
Error % in dead load = 4.4 % < 5% OK
Error % in live load = 3 % < 5% OK
Error % in superimposed = 2.25% < 5% OK

## Slide 36: Slabs Design

## Slide 37: Bending moment for block1 in y-direction

## Slide 38: Solid slab reinforcement distribution
Notes: Using the principles of simple beam , we determine the reinforcement in the solid slab

## Slide 39: Solid slab reinforcement distribution

## Slide 40: Bending moment for block2 in y-direction

## Slide 41: Ribbed slab reinforcement distribution

## Slide 42: Ribbed slab reinforcement distribution

## Slide 43: Beams Design

## Slide 44: Beams layout in block 1

## Slide 45: Reinforcement for all beams in block 1
Beams of Block 1 |  |  |  |  |  |  |  |  |  |  |  |  | 
Frame | Beam |  | station | Area of steel due to moment and torsion |  |  |  |  |  |  |  |  | 
 |  | Dimension of beam (cm) |  | Moment |  |  |  |  |  |  |  | Shear | 
 |  |  |  | Area of steel(mm²) +ve |  |  |  | Area of steel(cm²) -ve |  |  |  | Av/s (mm²/mm) | # of bars
 |  |  |  | Bottom | As min | As provided | # of bars | Top | As min | As provided | # of bars |  | 
1 | 1 |  | Left | 238 | 544.5 | 544.5 | 3Φ16 | 482 | 544.5 | 544.5 | 3Φ16 | 0 | 2Φ10/15
 |  | 30×60 | Middle | 215 | 544.5 | 544.5 | 3Φ16 | 118 | 544.5 | 544.5 | 3Φ16 | 0 | 2Φ10/15
 |  |  | Right | 184 | 544.5 | 544.5 | 3Φ16 | 370 | 544.5 | 544.5 | 3Φ16 | 0 | 2Φ10/15
2 | 1 |  | Left | 227 | 544.5 | 544.5 | 3Φ16 | 459 | 544.5 | 544.5 | 3Φ16 | 0 | 2Φ10/15
 |  | 30×60 | Middle | 153 | 544.5 | 544.5 | 3Φ16 | 153 | 544.5 | 544.5 | 3Φ16 | 0 | 2Φ10/15
 |  |  | Right | 241 | 544.5 | 544.5 | 3Φ16 | 241 | 544.5 | 544.5 | 3Φ16 | 0 | 2Φ10/15
 | 2 | Outside stem = 0.7 Outside flange = 1.0 Flange thickness = 0.2 Stem thickness = 0.4 | Left | 695 | 2178 | 2178 | 7Φ20 | 1080 | 871.2 | 1080 | 4Φ20 | 0.333 | 2Φ10/30
 |  |  | Middle | 853 | 2178 | 2178 | 7Φ20 | 348 | 871.2 | 871.2 | 3Φ20 | 0 | 2Φ10/30
 |  |  | Right | 498 | 2178 | 2178 | 7Φ20 | 853 | 871.2 | 871.2 | 3Φ20 | 0.333 | 2Φ10/30
3 | 1 |  | Left | 343 | 544.5 | 544.5 | 3Φ16 | 540 | 544.5 | 544.5 | 3Φ16 | 0.05 | 2Φ10/15
 |  | 30×60 | Middle | 187 | 544.5 | 544.5 | 3Φ16 | 187 | 544.5 | 544.5 | 3Φ16 | 0.016 | 2Φ10/25
 |  |  | Right | 263 | 544.5 | 544.5 | 3Φ16 | 263 | 544.5 | 544.5 | 3Φ16 | 0 | 2Φ10/15
 | 2 | Outside stem = 0.7 Outside flange = 1.0 Flange thickness = 0.2 Stem thickness = 0.4 | Left | 608 | 2178 | 2178 | 7Φ20 | 940 | 871.2 | 940 | 3Φ20 | 0.333 | 2Φ10/30
 |  |  | Middle | 716 | 2178 | 2178 | 7Φ20 | 304 | 871.2 | 871.2 | 3Φ20 | 0 | 2Φ10/30
 |  |  | Right | 454 | 2178 | 2178 | 7Φ20 | 853 | 871.2 | 871.2 | 3Φ20 | 0.333 | 2Φ10/30

## Slide 46: Checking deflection requirements for serviceability in block 1:
Deflection type | Deflection value (mm)
∆ Dead | 3.8
∆ Live | 0.19
∆ Sustain load | 0.097
The critical beam was taken to check in block 1 (Beam 1 in Frame 2) and the results were as follows:
∆ LT = ∆L + λ ∆D + λ T∆LS
= 0.19 + (1.4×3.8) + (1.4×0.097) = 5.64 mm
∆ L ≤ = = 26.04 mm  Ok
All the results were acceptable

## Slide 47
Longitudinal section in Beam 1
Sections in Beam 1

## Slide 48
Longitudinal section in Beam 2
Sections in Beam 2

## Slide 49: Beams layout in block 2

## Slide 50
Beams of Block2 |  |  |  |  |  |  |  |  |  |  |  |  | 
Beam | Dimension of beam (cm) |  | station | Area of steel due to moment and torsion |  |  |  |  |  |  |  |  | 
 |  | span |  | Moment |  |  |  |  |  |  |  | Shear | 
 |  |  |  | Area of steel(mm²) +ve |  |  |  | Area of steel(mm²) -ve |  |  |  | Av/s (mm²/mm) | # of bars
 |  |  |  | Bottom | As min | As provided | # of bars | Top | As min | As provided | # of bars |  | 
1 | 40X30 |  | Left | 109 | 330 | 330 | 2Φ16 | 220 | 330 | 330 | 2Φ16 | 0.101 | 2Φ10/15
 |  | 1 | Middle | 181 | 330 | 330 | 2Φ16 | 63 | 330 | 330 | 2Φ16 | 0.188 | 2Φ10/15
 |  |  | Right | 126 | 330 | 330 | 2Φ16 | 254 | 330 | 330 | 2Φ16 | 0.188 | 2Φ10/15
2 | 40X30 |  | Left | 104 | 330 | 330 | 2Φ16 | 210 | 330 | 330 | 2Φ16 | 0.186 | 2Φ10/10
 |  | 2 | Middle | 146 | 330 | 330 | 2Φ16 | 54 | 330 | 330 | 2Φ16 | 0 | 2Φ10/20
 |  |  | Right | 109 | 330 | 330 | 2Φ16 | 220 | 330 | 330 | 2Φ16 | 0 | 2Φ10/10
3 | 40X30 |  | Left | 103 | 330 | 330 | 2Φ16 | 208 | 330 | 330 | 2Φ16 | 0 | 2Φ10/15
 |  | 3 | Middle | 124 | 330 | 330 | 2Φ16 | 52 | 330 | 330 | 2Φ16 | 0 | 2Φ10/20
 |  |  | Right | 104 | 330 | 330 | 2Φ16 | 209 | 330 | 330 | 2Φ16 | 0 | 2Φ10/15
4 | 40X30 |  | Left | 138 | 330 | 330 | 2Φ16 | 279 | 330 | 330 | 2Φ16 | 0 | 2Φ10/15
 |  | 4 | Middle | 182 | 330 | 330 | 2Φ16 | 69 | 330 | 330 | 2Φ16 | 0 | 2Φ10/25
 |  |  | Right | 127 | 330 | 330 | 2Φ16 | 257 | 330 | 330 | 2Φ16 | 0.186 | 2Φ10/15
5 | 40X30 |  | Left | 184 | 330 | 330 | 2Φ16 | 360 | 330 | 360 | 2Φ16 | 0.19 | 2Φ10/15
 |  | 5 | Middle | 238 | 330 | 330 | 2Φ16 | 92 | 330 | 330 | 2Φ16 | 0.102 | 2Φ10/20
 |  |  | Right | 93 | 330 | 330 | 2Φ16 | 188 | 330 | 330 | 2Φ16 | 0.005 | 2Φ10/15
Reinforcement for all beams in block 2

## Slide 51: Checking deflection requirements for serviceability in block 2:
The critical beam in block 2 is beam 2 and it was taken to check.
The results were as follows:
∆ LT = ∆L + λ ∆D + λ T∆LS
∆ LT = 2.56 + (1.15×6.83) + (1.15×1.28) = 11.89 mm
∆ L T≤ = = 12.08mm  Ok
all the results were acceptable
Deflection type | Beam (mm)
∆ Dead | 6.83
∆ Live | 2.56
∆ Sustain load | 1.28

## Slide 52: Cross section in beam 1

## Slide 53: Columns Design

## Slide 54: Columns are designed to carry one floor at block 1 and three floors at block 2.

## Slide 55: Design Requirements:
Using this equation Ψ=( 4EI/L)C/(4EI/L)b and by using Nomograms the value of K was obtained.
All Columns were short because Kl/r ≤ 34 – 12( )
Each column is designed
using interaction diagram

## Slide 56: Reinforcement for all columns in block 1
No. of column | Section (cm×cm) | rebar percentage | AS (mm2) | # of bars | Ties
C1 | 45×45 | 1% | 2025 | 10Ø16 | 1Ø10/10cm
C2 | 45×45 | 1.49% | 2066 | 11Ø16 | 1Ø10/10cm
C3 | 45×45 | 1% | 2025 | 10Ø16 | 1Ø10/10cm
C4 | 45×45 | 1.12% | 2343 | 12Ø16 | 1Ø10/10cm
C5 | 45×45 | 1% | 2025 | 10Ø16 | 1Ø10/10cm
C6 | 45×45 | 1% | 2025 | 10Ø16 | 1Ø10/10cm
C7 | 45×45 | 1% | 2025 | 10Ø16 | 1Ø10/10cm
C8 | 45×45 | 1% | 2025 | 10Ø16 | 1Ø10/10cm
C9 | 45×45 | 1% | 2025 | 10Ø16 | 1Ø10/10cm
C10 | 45×45 | 1% | 2025 | 10Ø16 | 1Ø10/10cm
Section in column 1

## Slide 57: Reinforcement for all columns in block 2
Section in column 2
No. of column | Section (cm×cm) | rebar percentage | AS (mm2) | # of bars | Ties
C11 | 25×50 | 1% | 1250 | 6Ø16 | 1Ø10/10cm
C12 | 25×50 | 1.02% | 1274 | 6Ø16 | 1Ø10/10cm
C13 | 25×50 | 1.23% | 1537 | 8Ø16 | 1Ø10/10cm
C14 | 25×50 | 1.12% | 1250 | 6Ø16 | 1Ø10/10cm
C15 | 25×50 | 1% | 1250 | 6Ø16 | 1Ø10/10cm
C16 | 25×50 | 1% | 1250 | 6Ø16 | 1Ø10/10cm
C17 | 25×50 | 1% | 1250 | 6Ø16 | 1Ø10/10cm
C18 | 25×50 | 2.69% | 3369 | 8Ø25 | 1Ø10/10cm

## Slide 58: Footings Design

## Slide 59: Design requirements
The selected footings in this project are pile footings since the project is located in Jericho, where the soil is very poor.
Piles is designed to carry one floor at block 1 and three floors at block 2.
Based on the soil type in Jericho , the following assumptions are used:
Ø = 21˚
γ = 17 KN/m²
C = 12

## Slide 60: Design requirements
The following equations are used for designing the piles:
Qp = (C×Nc* + qNq*) Ap
Qs = ∑ DL × ρ × f
Q ultimate = Qp + Qs
ØPn = 0.65×0.8 (0.85×f'c (Ag-As) +As×Fy)
As = ρmin×Area the cross section of the pile
s = 0.45

## Slide 61: Selection of pile length & diameter
Results of Bearing capacity at different lengths and diameters
Design Chart for selecting piles

## Slide 62: Piles Groups and design
Diameter (m) | Length (m) | No. of piles | Q allowable | Pu | Group No.
0.6 | 4 | 1 | 490 | 400 | 1
0.8 | 6 | 1 | 900 | 700 | 2
0.7 | 6 | 2 | 700 | 1250 | 3
Piles grouping and characteristics:
Piles groups design:

## Slide 63: Design of the pile cap
Cap reinforcement | Cap depth (m) | Cap Dimensions ( m × m) | Group Number
3Ø20 | 0.6 | 0.9 × 0.9 | Group 1
4Ø20 | 0.6 | 1.1 × 1.1 | Group 2
6Ø20 | 1.2 | 1 × 3.1 | Group 3
Group 3
Group 1

## Slide 64
Vertical section in Pile 1 / column 1
Horizontal section in Pile 1 / column 1

## Slide 65: Seismic Load analysis

## Slide 66: The structure is located in Jericho area which is classified as zone 3 according to Palestine seismic zones, in Palestine seismic zones map

## Slide 67: The UBC97 code seismic parameters are as follows:
The seismic zone factor, Z= 0.3 (Table16-I)
The soil is stiff soil profile, so the soil type is SD.(Table16-j)
The importance factor, I= 1.0 (Table16-k).
The ductility factor, R= 5.6 (Table16-n).
The seismic coefficient, Ca=0.36 (Table16- Q).
The seismic coefficient, Cv=0.54 (Table16-R)

## Slide 68: Define response spectrum function

## Slide 69: Define load cases

## Slide 70: Define load case data

## Slide 71: Design of Slabs for seismic load
Bending resistance: (Block.1)
Mu-ve = 12.5 KN.m
As =360 mm²
Use 3 Ф 14/m
Mu+ve = 13.6 KN.m
As =360 mm²
Use 3 Ф 14/m

## Slide 72: Design of Slabs for seismic load
Bending resistance: (Block.2)
Mu-ve = 30.5 KN.m
As =369 mm²
Use 2 Ф 16
Mu+ve = 16.5 KN.m
As = 64.8 mm²
Use 2 Ф 10

## Slide 73: Design of Beams for seismic load
Block 2 : (Beam2)
Mu-ve = 187.25 KN.m
As = 2088.3 mm²
Use 11Ø16
Mu+ve = 117.1 KN.m
As = 1266 mm²
Use 7Ø16
Shear diagram
Use 1 Ф10/10 cm

## Slide 74: Design of Beams for seismic load
Block 1 : (Frame2/Beam1)
Mu-ve = 72.5 KN.m
As = 554.4 mm²
Use 4Ø16
Mu+ve = 26 KN.m
As = 554.4 mm²
Use 3Ø16
Shear diagram
Use 1 Ф10/25 cm

## Slide 75
We are glad
to hear
your comments
& questions
about the
presentation
Khawla
Noor
Rema’ 