## Slide 1
An-Najah National University
Faculty of Engineering
Civil Engineering Department
Graduation Project
Submitted To:- En. Imad Al-Qasem.
Prepared By: - Omar Mohammed.
Nabeeh Isleem.
Nadeem Al-Jallad.

## Slide 2: Overview
  Mecca Mall.
  Under Construction.
  Twelve Story and Roof.

## Slide 3
Total Area is 6500 m2 .
ACI 318-08 .
LRFD 2005 .

## Slide 4
f 'c = 28 Mpa for columns and footing.
f 'c = 24 Mpa for slabs.
Fy = 420 Mpa.
Bearing Capacity Of Soil = 2.5kg/cm2.

## Slide 5
Story Number | Own weight (kN/m2) | Super imposed (kN/m2) | Live load office (kN/m2) | Live load storage (kN/m2) | Live load corridors (kN/m2)
Roof | 6.8 | 0 | 10 |  | 
2-8 | 6.8 | 4.1 | 2.5 | 0 | 4
1 | 6.8 | 4.1 | 4 | 0 | 5
GF | 6.8 | 4.1 | 4 | 5.25 | 5
B1 | 6.8 | 4.1 | 0 | 5.25 | 0

## Slide 6: Load factors (Combination)
Wu = 1.4DL
Wu = 1.2DL + 1.6LL
Wu = 0.9DL + EL
Wu = 1.2DL + LL + EL

## Slide 7: Slabs Thickness
From Architectural plans the cantilever = 3m .
h min = 3000/8 = 375 mm ……. Take the thickness equal to 40cm .

## Slide 8: Reinforcing Direction

## Slide 13
Cross Section in Rib

## Slide 14
Cross Section in Slab

## Slide 15
Cross Section in Wall

## Slide 16: Check Slabs for Shear
ØVc =0 .75*( bd√f 'c) /1000
ØVc = 0.75*120*350*5.3/6000 = 28 Kn
Max shear less than concrete capacity.

## Slide 17: Shrinkage Steel
As = 0.0018*b*d
As = 0.0018*1000*60 = 141mm2
Use 3 Ø 8 /m

## Slide 18: Distribution of Beams

## Slide 25: Columns Design

## Slide 26
Tied Columns will be used.
Dimensions are selected by architect.
Area of steel is minimum.
According to Buckling Check the columns are short.

## Slide 27
Group Number | Dimension (m) | Load (Kn) | Column in the Group
1 | 1.65*0.45 | 5365 | C1, C4, C7, C19, C20,C25
2 | 1.0*1.0 | 6663 | C2,C5,C21,C24
3 | 0.5*0.5 | 3188 | C3,C6,C16,C13,C22,C23
4 | 0.9*0.9 | 7288 | C8
5 | 1.5*0.45 | 4832 | C9,C10
6 | 3.0*0.45 | 8377 | C11,C12, C15
7 | 0.6*0.3 | 2458 | C14,C17
8 | 2.3*0.45 | 8386 | C18
9 | 0.8*0.3 | 567 | C26
10 | 0.7*0.3 | 435 | C27

## Slide 28
 | G1 | G2 | G3 | G4 | G5
Ultimate load kN | 5400 | 6700 | 3200 | 7300 | 4900
Dimensions m | 1.65*0.45 | 1.0*1.0 | 0.5*0.5 | 0.9*0.9 | 1.5*0.45
Reinforcement | 30Ø18 | 32Ø20 | 14Ø16 | 26Ø20 | 28Ø18
Stirrups mm | Ø10 | Ø10 | Ø10 | Ø10 | Ø10
Spacing cm | 20 | 20 | 20 | 20 | 20
 | G6 | G7 | G8 | G9 | G10
Ultimate load kN | 8400 | 2500 | 8400 | 600 | 500
Dimensions m | 3.0*0.45 | 0.6*0.3 | 2.3*0.45 | 0.8*0.3 | 0.7*0.3
Reinforcement | 54Ø18 | 10Ø16 | 42Ø18 | 12Ø16 | 12Ø16
Stirrups mm | Ø10 | Ø10 | Ø10 | Ø10 | Ø10
Spacing cm | 20 | 20 | 20 | 20 | 20

## Slide 29
Three Dimensional Modeling
1.Compatibility.
2.Equilibrium .
3.Stress – Strain relationship .

## Slide 30
Compatibility.

## Slide 31: Equilibrium Check

## Slide 32
Error | Sap | Hand | 
2.6 %. | 21667.3 kN | 22244.5 kN | Live
4.3% | 21459.7 kN | 22429.46 kN | Super
3.9 % | 257724.53 | 247644.89 | Dead
Note: all Equilibrium Load check's are OK

## Slide 33
Stress – Strain relationship .
Figure (5.14): Bending moment diagram for beam10(1D) kN.m.

## Slide 34
Figure (5.15): Left Bending moment diagram for beam10(3D) kN.m.

## Slide 35
Figure (5.16): Right Bending moment diagram for beam10(3D) kN.m

## Slide 36
Figure (5.17):Middle Bending moment diagram for beam10(3D) kN.m

## Slide 37
Mu+ from 3D = (48.2+ 65.3)/2 + 24.5 = 81.3 kN.m
Error = (81.3 – 76.7 ) / 81.3 = 5.0%
Note: all Stress-Strain Relationship check's OK

## Slide 38
Footing Design
460 (560*0.5) = 280 m2
Mat Foundation should be used in the Project.

## Slide 39: Check Punching Shear:
*Vu=Pu=8400 kN.
*When d equal 1.2
*ϬVc=9392 kN>8400 kN
OK

## Slide 40
Check for Deflection
Δ = 10mm.is the maximum deflection.
Figure (6.1): Deflection Shape value for footing under surface load(m)

## Slide 42
Dynamic Analysis
Earthquake analysis procedure :
Model/Ritz Vectors Analysis.
Equivalent Lateral Load.
Response Spectrum.
Linear Time History.
Response Spectrum had been used to design and analysis .

## Slide 44
Figure(7.1): Periods and frequencies for modes.
T = 1.72 second.

## Slide 45
Figure(7.2): Modal Participating Mass Ratios.

## Slide 46
Story Number | Displacement x | Displacement y | Displacement z
B2 | 0 | 0 | .6
B1 | .01 | .24 | .43
GF | .1 | .5 | .6
1 | .02 | 2 | 1
2 | .05 | 4 | 1.1
3 | .08 | 6 | 1.2
4 | .1 | 8 | 1.3
5 | .1 | 10 | 1.3
6 | .1 | 12 | 1.35
7 | .1 | 13.7 | 1.35
8 | .07 | 15.4 | 1.32
9 | .05 | 16.8 | 1.3
Roof | .6 | 17 | .82
Displacement in all stories from first mode.

## Slide 47
Story Number | Displacement X | Displacement Y | Displacement Z
B2 | 0 | 0 | 3.3
B1 | .5 | .7 | 3
GF | 3.1 | 1.6 | 3.1
1 | 6.5 | 7 | 5.5
2 | 12.9 | 15.4 | 7.4
3 | 20.2 | 25.1 | 8
4 | 27.7 | 35.1 | 8.2
5 | 34.8 | 44.6 | 8.3
6 | 41.1 | 53.2 | 8.2
7 | 47.4 | 60.8 | 8
8 | 52.6 | 67.3 | 7.8
9 | 56.86 | 72.4 | 7.3
Roof | 57.99 | 65.4 | 4.7
Displacement in(mm) in all stories from Response Spectrum Method hitting X direction:

## Slide 48
Response Spectrum Method Procedure
Ca
Cv
I
R
Ca = 0.28 and Cv = 0.4 according to UBC code .
I = 1 and R = 3

## Slide 49
Thank you for your Attention
Thank you for your Attention
Thank you for your Attention