## Slide 1: IMPLEMENTATION OF A DIGITAL COMMUNUCATION SYSTEM
Data File
Source Coder
Encryption System
Channel FEC coder
AWGN Channel
Steganography System
Murad S. Qasim & Mohammad Hamid
Dr. Allam Mousa

## Slide 2: Introduction
The implementation of the digital communication system is important for the study, analysis, test and development of the performance of the system.
The topics that are considered
Source coding
FECC
AES
Data File
Source Coder
Encryption System
AWGN Channel
Steganography System
Channel FEC coder

## Slide 3: Source Coding
Burrows–Wheeler Compressor
1

## Slide 4: Source Coding
Lossless Source Coding Algorithms
Entropy Encoding
Huffman Coding
Shannon-Fano
Dictionary coders
Lempel-Ziv Algorithms
Arithmetic coding
Golomb coding
Other Encoding Algorithms
Data deduplication
Run-length encoding
Context mixing
Dynamic Markov Compression
Burrows–Wheeler Algorithm
The data compression or source coding is the process of encoding information using fewer bits (or other information-bearing units) than a non-encoded representation
It Aims at removing the redundancy until limit defined as entropy through the using of specific encoding schemes that are shown below

## Slide 5: Information & Entropy
# | size Bytes | Entropy
1 | 1.14 k | 4.1486
2 | 30.5k | 4.179
3 | 56.9k | 4.155
4 | 79.6k | 4.157
5 | 183k | 4.1626
Text Files
# | Size Bytes | Entropy
1 | 2.25M | 6.555
2 | 2.26M | 7.74
3 | 28.8M | 7.85
4 | 264K | 7.57
5 | 510K | 6.63
TIF Images (Tagged Image File)
# | Image size Mb | Entropy
1 | 4.82 | 7.9177
2 | 3.41 | 7.7087
3 | 0.091 | 7.6722
4 | 0.838 | 7.311
JPG Images
# | File size bytes | Entropy
1 | 286K | 13.0752
2 | 160.6K | 13.1137
3 | 59K | 13.24
4 | 78.7K | 14.11
5 | 61K | 12.8
9 | 23K | 12.56
Speech Files
Average information of a source is measured in bits per Symbol and defined as the source ENTROPY denoted as (H)
In order to implement source coding techniques, the files have to be analyzed by measuring its Size & Entropy in bits per symbol , the results are obtained for different samples of :

## Slide 6: The Burrows-Wheeler Algorithm
The Burrows-Wheeler transform, also called “block-sorting” does not process the input sequentially, but instead it processes a block of text as a single unit.
Has a
high code efficiency
And high compression ratio
so it reduces the file’s bits per symbol and so the bit rate and the bandwidth required for transmitting the data
but it has a High memory utilization
It is done in three main steps
BWT
MTF
Entropy Coding
Source Coding Example

## Slide 7: The Burrows-Wheeler Transform
Starting with input data as a one block S of N=14
m | o | h | a | m | m | a | d | & | m | u | r | a | d
d | m | o | h | a | m | m | a | d | & | m | u | r | a
One cycle shift at the step
This string has an Entropy of 2.753 bit/symbol
The input text, which is treated as a string S of N characters
first step is to create an N x N matrix M by using the input string S as the first row and rotating (cyclic shifting) the string N-1 times
second step is to sort the Matrix M lexicographically by rows. At least one of the rows of the newly created M’
m | o | h | a | m | m | a | d | & | m | u | r | a | d
d | m | o | h | a | m | m | a | d | & | m | u | r | a
a | d | m | o | h | a | m | m | a | d | & | m | u | r
r | a | d | m | o | h | a | m | m | a | d | & | m | u
S =
.
.
.
.
.
.
.
.

## Slide 8
lexically ordered rows
The Output
of the
transform
&muradmohammad
ad&muradmohamm
admohammad&mur
ammad&muradmoh
d&muradmohamma
dmohammad&mura
hammad&muradmo
mad&muradmoham
mmad&muradmoha
mohammad&murad
muradmohammad&
ohammad&muradm
radmohammad&mu
uradmohammad&m
The Primary Index is 10
last step is to take the last characters of each row (from top to bottom) and write it in a separate string L.
This transform produces a short distance text that is suitable for MTF according to Burrows & Wheeler
L

## Slide 9: Move-To-Front Transform Global Structure Transform
Move-to-Front encoding, is a scheme that makes a list of all possible symbols and modifies it at every cycle (moving one symbol, the last one used).
The advantages are that allows fast encoding and decoding, and requires only one pass over the data to be compressed
The combination of BWT & MTF reduces the file Entropy to approx. 20% for large files
The transform starts by initializing the dictionary of the source symbols and starts the process of search and move to front
The local BW- transformed file is Globalized by MTF to be Huffman Encoded

## Slide 10
BWT Output
dmrhaaomad&mum
& | a | d | h | m | o | r | u
MTF Dynamic Dictionary
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
output
dmrhaaomad&mum
d | & | a | h | m | o | r | u
dmrhaaomad&mum
m | d | & | a | h | o | r | u
Find the symbol location
Move to front
dmrhaaomad&mum
r | m | d | & | a | h | o | u
2
4
6
5
dmrhaaomad&mum
h | r | m | d | & | a | o | u
5
0
dmrhaaomad&mum
a | h | r | m | d | & | o | u
Take the index
.
.
.
.
.
.
.
.
.
.
.
.
.
.

## Slide 11
The process continues for all symbols (14 steps ) and the output is
24655064256371
& | a | d | h | m | o | r | u
Final dictionary arrangement that is needed to decoding
To Huffman coding
To store as MTF Dic.
This code has av. Code len. of 2.857 bit/symbol
And a size of 5 bytes
The a compression ratio of 2.8 i.e. the output size is 35% of the original
After applying the Huffman coding (Basic Entropy Encoder )
The final code is the Huffman coder output

## Slide 12: Source Coding Comparison for Real Data Files
File name | Size Before [Bytes] | BWT [Bytes] | Huffman [Bytes] | Run- Length [Bytes] | RAR [Bytes] | Average code Length for Huffman [Bits/symbol] | Average code Length for BWT [Bits/symbol] | Entropy Of the source [Bits/symbol]
File 1 | 1k | 0.532k | 0.664 k | 1.53 k | 0.47 k | 4.40 | 2.94 | 4.38
File 2 | 1.36 k | 0.787k | 0.874 k | 2.67 k | 0.77 k | 4.40 | 3.59 | 4.38
File 3 | 3.66 k | 1.96 k | 2.40 k | 7.16 k | 1.88 k | 4.89 | 3.74 | 4.85
File 4 | 4.12k | 1.95 k | 2.62 k | 7.72 k | 1.82 k | 4.75 | 3.27 | 4.72
File 5 | 6.08 k | 2.92 k | 4.05 k | 11.9 k | 2.82 k | 5.09 | 3.5 | 5.05
File 6 | 12.7 k | 5.02 k | 7.21 k | 25 k | 4.87 k | 4.41 | 2.97 | 4.39
File 7 | 16.0 k | 6.02 k | 9.14 k | 31.5 k | 5.85 k | 4.46 | 2.85 | 4.44
File 8 | 18.1 k | 6.75 k | 10.2 k | 35.6 k | 6.72 k | 4.45 | 2.85 | 4.43
Reference
Limited by
Entropy Reduction is obvious

## Slide 13: Data security
Encryption
Embedding
2

## Slide 14: Rijndael algorithm
RIJNDAEL(Joan Daemen and Vincent Rijmen) design in 1998.
It’s type of AES(Advanced encryption standard) is applied in 2001 by government of USA.
Symmetric block cipher
The available keys 128,192 and 256 bits.
Features of Rijndael: flexibility , security and does not require a lot of memory to operate
The attackers need 150 trillion years to crack the algorithm.
Rijndael algorithm based on Galois field generated by the primitive polynomial

## Slide 15: Flow chart of Rijndael encryption
*

## Slide 16: Key schedule
2B | 28 | AB | 09 | A0 | 88 | 23 | 2A
7E | AE | F7 | CF | FA | 54 | A3 | 6C
15 | D2 | 15 | 4F | FE | 2C | 39 | 76
16 | A6 | 88 | 3C | 17 | B1 | 39 | 05
01 | 02 | 04 | 08 | 10 | 20 | 40 | 80 | 1B | 36
00 | 00 | 00 | 00 | 00 | 00 | 00 | 00 | 00 | 00
00 | 00 | 00 | 00 | 00 | 00 | 00 | 00 | 00 | 00
00 | 00 | 00 | 00 | 00 | 00 | 00 | 00 | 00 | 00
D0 | C9 | E1 | B6
14 | EE | 3F | 63
F9 | 25 | 0C | 0C
A8 | 89 | C8 | A6
For first column in each round key
For the others

## Slide 17: SUB BYTES
19 | A0 | 9A | E9
3D | F4 | C6 | F8
E3 | E2 | 8D | 48
BE | 2B | 2A | 08
D4 | E0 | B8 | 1E
27 | BF | B4 | 41
11 | 98 | 5D | 52
AE | F1 | EF | 30
where
Encryption process

## Slide 18: Shift Rows
1 | 2 |  | 
1 | 2 |  | 
Mix columns

## Slide 19: Add round key
The most important process in the Advanced Encryption Standard (AES).Its take one by one column form one block and form the desired round key.

## Slide 20: Embedding
Its optional second layer of security.
It makes an effort to hide the fact that the encrypted data even exists, so not drawing attention to it.
In our implementation we embedded the encrypted data (from Rijndael) in a RGB bitmap indexed image (carrier source ) which is a high security level.
Each symbol in the carrier source represented by a set of 8 binary digits , the least significant digit (bit) is replaced with the encrypted data without obvious distortion to the source due to its nature (the effect of the LSB is neglected)

## Slide 21: Implemented Embedding System
Carrier Source
Encrypted Data
Embedding Algorithm
LSBE
Carrier source
+
Secret information
Decoding Key

## Slide 22: Embedding System Application with AES
To increase the data security and protection steganography is used to conceal the encrypted data within another carrier data file
AES cipher key 2B 7E 15 16 28 AE D2 A6 AB F7 15 88 09 CF 4F 3C HEX
Input Data Implementation of a digital communication System
Encrypted Data §¦<]­C£SøfsÕúeíþGØÇD¢)VsÌ ×ÔºÉõu}÷k¸³>BðG¹To
The steganography generated key 200 HEX
Original source file
The Embedded source

## Slide 23: Channel coding
FEC BCH(15,5,7)
3

## Slide 24: Forward Error Correction Block BCH Encoder
Channel coding or error control coding is a part of a Digital communication system used to detect the errors in the data and correct it using redundant bits added to the original data
The added redundancy should be acceptable in terms of the Channel Capacity
This class of codes is highly flexible, allowing control over block length and acceptable error thresholds, it can be designed to a given specification and mathematical constrains
The primary advantage of BCH codes is the ease of decoding, by algebraic method known as syndrome decoding which Allows Faster error detection and correction.
A block FEC codes which are extensively used in communication systems and computer storage devices (Reed-Solomon)

## Slide 25: Channel Capacity
the channel capacity “ C ” is the maximum average information that can be transmitted over the channel per each channel use
For BSC the capacity is obtained form
Where is the entropy of the transmitted source of data and the joint entropy between the transmitted data X and data Y
is the probability of receiving Y given X is transmitted and it could be obtained from .
For AWGN channel
Shannon-Hartly theorem stats that
)

## Slide 26: Block coding BCH code
The Bose , Chaudhuri and Hocquenghem codes is a powerful random multiple error correcting cyclic codes.
Even be found bch & :
Block length :
Number of parity-check digits:
Minimum distance :
Where:
n: output codeword length
k:input bits
m:the order of primitive polynomial
t: number of errors that can be correct
dmin: the minimum distance

## Slide 27: BCH(15,5,7) Generation matrix & data Encoding
Primitive polynomial & t=3 , ,
; C : code words , d: message

## Slide 28: Decoding BCH (syndrome decoding)
For any BCH code word
if the input of the BCH decoder is the code word r which contains errors so that
The definition states that the Syndrome S is the multiplication of the output code word by the parity check matrix H
So the error could be corrected according to look up table generated for all possible error patterns so the correct code word is obtained by

## Slide 29: Performance of BCH(15,5,7)
Theoretical and practical
Performance over AWGN
channel for BCH(15,5,7)
The comparison between coded
and non-coded signal is shown
it shows better performance for
the coded signal at the higher
Eb/N0 levels