## Slide 1
An-Najah National University
Faculty of Engineering and Information Technology
Civil Engineering department
Structural Design Of Rawabi Town Centre Building.
Prepared by: Waseem Fouad Alomari
Mo’men Na’el Alqub
Ahmad Barham
Supervised by: Dr. Mahmoud Dwekat

## Slide 2
Content:-
Introduction
01
Preliminary Design
02
Three dimensional analysis and design
03

## Slide 3
The building consist of 9 floors, with total area of building= with area as shown in the table.
01 Introduction
Project description:-
Rawabi Town Centre building Phase 06, part 1.
located in Q-centre in Rawabi city .
Floor | Area
GF | 1840
S1 | 1840
S2 | 1840
S3 | 1840
S4 | 1840
S5 | 1840
S6 | 1840
S7 S8 | 1840 1840
Floor | 
GF | 1840
S1 | 1840
S2 | 1840
S3 | 1840
S4 | 1840
S5 | 1840
S6 | 1840
S7 S8 | 1840 1840
Table-1: Floors Area.
Soil bearing capacity= 400KN/

## Slide 4
Rawabi town center building
Figure-1:Top view show the place of the building in Rawabi city.

## Slide 5
Changes in original plans
1- Because of lack of architectural information and in agreement with our supervisor we have considered that the building consists of 9 floors and all the 9 floors has the same architectural design.
2 - There is a water tank underneath the building which we cancelled because of lake of architectural drawing for the tank.
3 - We have done some structural changes in the building . We add some shear walls because the first mode was torsion .and we made some changes on the original shear wall such that , We made all of them starts from the ground .

## Slide 6
Project description:-
Figure-2: Architectural plan for the story's.

## Slide 7
Project description:-
Figure-3: south side view.

## Slide 8
Project description:-
Figure-4: North side view.

## Slide 9
Project description:-
Figure-5: West side view

## Slide 10
IBC 2015.
01 Introduction
Codes and Standard:-
ACI318-11.
ASCE 7-16.

## Slide 11
01 Introduction
Material:-
Material used in the project divide into two type:-
Structural material: Material which used in structural element, with properties as shown in the below table.
Table-2: Structural materials properties.
Material | Compressive strength | Modules of elasticity | Unit weight
Concrete | 28 Mpa for slab and beam 32 Mpa for columns and shear wall | 24870 Mpa 26587 Mpa | 25 KN/
 | Yield strength | Modules of elasticity | Unit weight
Steel Gr (60)A615 | 420 MPa | 200 GPa | 78 KN/
Material | Compressive strength | Modules of elasticity | Unit weight
Concrete | 28 Mpa for slab and beam 32 Mpa for columns and shear wall | 24870 Mpa 26587 Mpa | 
 | Yield strength | Modules of elasticity | Unit weight
Steel Gr (60)A615 | 420 MPa | 200 GPa | 

## Slide 12
Material:-
Non-structural material: Material which form non-structural element, with properties as shown in the below table.
Materials | Unit Weight (KN/)
Tiles | 23
Blocks | 12
Masonry Stones | 27
Filling Materials | 16
Concrete Mortar | 23
Materials | 
Tiles | 23
Blocks | 12
Masonry Stones | 27
Filling Materials | 16
Concrete Mortar | 23
Table-3: Non-Structural materials properties.

## Slide 13
01 Introduction
Loads and load combinations:-
Gravity loads: live and dead loads.
Live loads with value =2.5 KN/for offices, 5 KN/ for corridors, stairs and restaurant.
Dead load composed of own weight of structure with value 7.5 KN/for slabs
Super dead from tiles, mortar , partions and plaster equal 3.6 KN/
And distributed super-imposed dead load 16.3 KN/m as linear load Represent weight of exterior wall

## Slide 14
01 Introduction
Loads and load combinations:-
Seismic loads:
There are many areas that are exposed to earthquake. Palestine is considered one of these areas. Therefore, buildings and other structure are constructed and designed to resist the ground motions caused by earthquakes because if there is a failure occur that will lead to risk at human life and to structure itself. The structure must be designed according to the codes requirements that related to mainly by ASCE7-16, UBC-97, Israeli code 413.

## Slide 15
seismic parameters
Risk category.
The codes classified the building according the risk to four categories as shown in (ASCE 7-16 Table 1.5-1).

## Slide 16
seismic parameters
Importance factor.
A- Seismic zone factor.
Seismic zone factor, Z = 0.15

## Slide 17
seismic parameters
Importance factor.
B- Site class.
The site class shall be assigned according to the type of soil present and its properties. The type of the soil in the site is rock and the soil site class is assumed to be B

## Slide 18
seismic parameters
Importance factor.
Importance factor is defined as a factor that accounts for the degree of risk, based on the risk category which is III in this project.
So, the value of seismic importance factor (Ie) is equal to 1.25 as shown in (ASCE 7-16 Table 1.5-2)

## Slide 19
seismic parameters
Design spectral acceleration parameters, Sds and Sd1
Find the values of Ss and S1:-
Ss = 2.5*1.5*Z  2.5*1.5*0.15 = 0.5625
S1 = 1.25*1.5*Z  1.25*1.5*0.15 = 0.28125
Find the value of Fa

## Slide 20
seismic parameters
Design spectral acceleration parameters, Sds and Sd1
Find the value of Fv
 Fa = 0.9 & Fv = 0.8

## Slide 21
seismic parameters
Design spectral acceleration parameters, Sds and Sd1
Find the values of Sms and Sm1:-
SMS = Fa * SS = 0.9*0.5625=0.5
SM1 = Fv * S1 = 0.8*0.28125 = 0.225
-Find the value of Sds and Sd1:-
SDS = (2/3) SMS = 2/3* 0.506 = 0.337
SD1 = (2/3) SM1 = 2/3* 0.225 = 0.15

## Slide 22
seismic parameters
Seismic design category.
According to the values of Sds, Sd1 and risk category, the seismic design category is C

## Slide 23
seismic parameters
Type of lateral force resisting systems:-.
The structural system that will be used:-
Dual systems with intermediate moment frames capable of resisting at least 25% of prescribed seismic force ( Ordinary reinforced concrete shear wall ).

## Slide 24
Loads and load combinations:-
Load combination used with according to ASCE7-16 :
The service loads combinations that will be used in the model is the following:-
1-D+SD+L
2-1.04725D + 1.04725SD + Ex
3-1.04725D + 1.04725SD + Ey
4-1.0379D + 1.0379 SD + 0.75L + 0.525Ex
5-1.0379D + 1.0379 SD + 0.75L + 0.525Ey
6-0.5527D + 0.5527SD + 0.7Ex
7-0.5527D + 0.5527SD + 0.7Ey

## Slide 25
Loads and load combinations:-
Load combination used with according to ASCE7-16 :
The ultimate loads combinations that will be used in the model is the following :-
1-1.2D + 1.6L
2-1.2675D + 1.2675SD + L +Ex
3-1.2675D + 1.2675SD + L +Ey
4-0.83325D + 0.83325 SD + Ex
5-0.83325D + 0.83325 SD + Ey

## Slide 26
02 Preliminary Dimensions
preliminary dimensions for Beam and slab :-
System of slab used is tow way solid slab with 300 mm thickness.
Figure-6: Load distribution in tow way slab.

## Slide 27
02 Preliminary Dimensions
preliminary dimensions for Beam and slab :-
Dimension of beam will be determine as the following:
Table-1: Minimum depth of non-prestressed beams.
h = Use 0.50m.
h = Use 0.55m.
b = 0.80m.
System of beam used is drop beams between all columns.

## Slide 28
Preliminary Dimensions
Slab thickness
Assume that solid slab, hslab = 30cm
Check shear:
LL = 2.5 kN/m2
SD = 3.6 kN/m2
Wu = 1.2(0.3*25 + 3.6) + 1.6(2.5) = 17.32 kN/m2
X-direction:
Vu = Wu*(L/2 -b1/2- d) = 17.32(8/2 -0.8/2- 0.26) = 57.84 kN/m
Where:
Wu: ultimate load in slab.
L: short panel dimension.
b1: width of beam.
d: effective depth of slab.

## Slide 29
Preliminary Dimensions
ØVc =Ø𝛾√𝑓𝑐 bw d/6
Where:
Ø: Shear reduction factor = 0.75
𝛾 = 1 for normal weight concrete
𝑓𝑐 = concrete compressive strength for slab = 28 Mpa
bw = Web width of the slab section = 1 m
ØVc = (0.75*1)/6 √28 *1000*260/1000 = 172 kN/m > Vu
Ok for shear.

## Slide 30
Preliminary Dimensions
The following figure show the distribution and the dimensions of beams
Beams :.
Figure-1: Layout and dimensions for beams.

## Slide 31
Preliminary Dimensions
Beams dimensions:.
Table-2: Dimensions of beams

## Slide 32
Preliminary Dimensions
Columns layout:
Figure-2: Layout of columns.

## Slide 33
Preliminary Dimensions
*Interior rectangular column:
Loads: -
slab = 0.3*25*1= 7.5 KN/𝑚2
The column C7 carried slab with dimensions = 8*8.2
ws=7.5*8*8.2=492 KN
wbeam= 0.8*0.5*25*8+0.8*0.55*25*8.2
= 170.2 KN
wcolumn = 0.8*1*3.64*25 =72.8 KN
wsD= 3.6*8*8.2 = 236.16 KN
LL = 2.5*8*8.2 = 164 KN
DL = 492+170.2+72.8+236.16 = 971.16 KN
P (one story) = 1.2D+1.6L = 1.2*971.16+1.6*164 = 1428 KN
PU = 1428*9 = 12852 KN
ΦPn = Φ λ (0.85*fc'(Ag – AS) + Fy* AS)
12852* 103 = 0.65*0.8(0.85*32(Ag – 0.01Ag) +420*0.01* Ag)
Ag = 794*103 𝑚𝑚2
(800*1000) mm
Preliminary dimensions for columns:

## Slide 34
Preliminary Dimensions
*Interior circular column:
Loads: -
slab = 0.3*25*1=7.5 KN/𝑚2
The column C8 carried slab with dimensions = 8.2*5.1
ws=7.5*8.2*5.1=313.65 KN
wbeam= 0.8*0.55*25*8.2+0.8*0.50*25*5.1
= 141.2 KN
wcolumn = 0.42*𝜋 ∗3.64*25 =45.74 KN
WsD= 3.6*8.2*5.1 = 150.6 KN
LL = 2.5*8.2*5.1 = 104.6 KN
DL = 313.65+141.2+45.74+150.6= 651.2 KN
P (one story) = 1.2D+1.6L = 1.2*651.2+1.6*104.6 = 948.8 KN
PU = 948.8*9 = 8539.2 KN
ΦPn = Φ λ (0.85*fc'(Ag – AS) + Fy* AS)
8539.2* 103 = 0.75*0.85(0.85*32(Ag – 0.01Ag)+420*0.01* Ag)
Ag = 430.3 *103 𝑚𝑚2
Diameter = (740) 𝑚𝑚2

## Slide 35
Preliminary Dimensions
*Exterior rectangular column:
Loads: -
slab = 0.3*25*1=7.5 KN/𝑚2
The column C11 carried slab with dimensions = 8.2*1.1
ws=7.5*8.2*1.1=67.65 KN
wbeam= 0.8*0.55*25*8.2+0.8*0.5*25*1.1
= 67.37 KN
wcolumn = 0.5 ∗ 0.3 *25*3.64=13.65 KN
WsD= 3.6*1.1*8.2 = 32.472 KN
LL = 2.5*1.1*8.2 = 22.55 KN
DL = 67.65+67.37+13.65+32.472= 181.15 KN
P (one story) = 1.2D+1.6L = 1.2*181.15+1.6*22.55 = 253.46 KN
PU = 253.46*9 = 2281.14 KN
ΦPn = Φ λ (0.85*fc'(Ag – AS) + Fy* AS)
2281.14* 103 = 0.65*0.8(0.85*32(Ag – 0.01Ag) +420*0.01* Ag)
Ag = 140.9 *103 𝑚𝑚2
(300*500) mm

## Slide 36
Preliminary Dimensions
*Exterior rectangular column:
Loads: -
slab = 0.3*25*1=7.5 KN/𝑚2
The column C1 carried slab with dimensions = 8.2*4
ws=7.5*8.2*4=246 KN
wbeam= 0.8*0.5*25*4+0.8*0.5*25*8.2
= 122 KN
wcolumn = 0.8 ∗ 0.5 *25*3.64=36.4 KN
WsD= 3.6*4*8.2 = 118.1 KN
LL = 2.5*4*8.2 = 82 KN
DL = 246+122+36.4+118.1= 522.5 KN
P (one story) = 1.2D+1.6L = 1.2*522.5+1.6*82 = 758.2 KN
PU = 758.2*9 = 6823.8 KN
ΦPn = Φ λ (0.85*fc'(Ag – AS) + Fy* AS)
6823.8* 103 = 0.65*0.8(0.85*32(Ag – 0.01Ag)+420*0.01* Ag)
Ag = 422 *103 𝑚𝑚2
(850*500) mm

## Slide 37
Preliminary Dimensions
Column dimensions:.
Table-3: Dimensions of columns.

## Slide 38
Preliminary Dimensions
Preliminary dimensions and distribution of walls of walls:.
All walls has 25cm depth
Figure-34 : Layout of shear walls.

## Slide 39
All supports will be model as fixed support.
Exterior partition as linear load and interior partition as distributed load.
03 Three dimensional analysis
Introduction:-
Modeling and analysis will performed by using ETABS 18 program.

## Slide 40
The units that will be used is according to SI units:-
-for dimensions- meter (m).
-for forces- kilo newton (KN).
-for temperature –Celsius (C)
Units

## Slide 41
Define material and sections and loads:-
Figure-1: Steel properties definition.
Define material , sections and loads:-

## Slide 42
Define material , sections and loads:-
Figure-2: Concrete for beam and slab properties definition.

## Slide 43
Define material , sections and loads:-
Figure-3: Concrete for column and shear wall properties definition.

## Slide 44
Define material , sections and loads:-
Figure-4: Slab properties definition.

## Slide 45
Define material , sections and loads:-
Figure-5: Beam properties definition.

## Slide 46
Define material , sections and loads:-
Figure-6: Shear wall properties definitions.

## Slide 47
Define material , sections and loads:-
Figure-7: Column properties definitions.

## Slide 48
Define material , sections and loads:-
Figure-9: Define load patterns.

## Slide 49
Define material , sections and loads:-
Figure-9: Seismic loading for both directions.

## Slide 50
Define material , sections and loads:-
Figure-10: Define load combinations.
We added service and ultimate loads that mentioned previously as shown in the following figure.

## Slide 51
Define material , sections and loads:-
Figure-10: Define load case.

## Slide 52
Define material , sections and loads:-
Figure-10: Define EQx.
After modified the scale factor and Eqst.in x-direction Be equal to RSx the scale factor will be as shown in the following figure.

## Slide 53
Define material , sections and loads:-
Figure-10: Define EQy.
After modified the scale factor and Eqst.in y-direction Be equal to RSy the scale factor will be as shown in the following figure.

## Slide 54
Define material , sections and loads:-
Figure-10: Define response spectrum.
Definition of response spectrum function

## Slide 55
Define material , sections and loads:-
Figure-10: Define mass source.
Definition of mass source.

## Slide 56
Checks
The Checks which will be discussed in this section divided into two main Type as the following:
1- Model checks: checks perform to verify from all input the structure are ok and program transfer the load in right way.
Checks are, compatibility check, equilibrium check, and internal force check.
2- Design checks: checks perform to verifying if the structure satisfy the needed requirement of not with accordance to design specifications.
Checks are, Period check , deflection check ,P-Delta ,Drift and slenderness check.
Introduction:-

## Slide 57
Model checks:-
1-compatibility check:
Figure‑1: compatibility animation 1.
Figure-2: compatibility animation 2.

## Slide 58
Model checks:-
2-Equilibrium check:
Live load:
From program = 38503.7 KN
Manually =
Then, Error 1.4% <5% ok.
Dead load:
From program = 176332KN
Manually = 178345
Then, Error 1.1% < 5% OK
Super dead load:
From program = 73205 KN
Manually =
Then, Error 3.6% < 5% OK

## Slide 59
Model checks:-
3- Internal force check:
Slab: ( At story 1)
From program M = 20.4 KN.m
Manually M = 21 .m
Then, Error 3% <10% ok.
Beam : ( At story 1)
From program M =225.5
Manually M =
Then, Error 9.5% < 10% ok
Figure-4: Beam location.
Figure-3: Slab location.
Note: Internal force check will be done on live load only.

## Slide 60
Design checks:-
1-Deflection check:
From ACI code allowable deflection equal L/360
Maximum deflection in all structure 3.4 mm from live load in panel equal 10  8.
Allowable deflection = L/360 =8000/360 = 22.2 mm
Then, the deflection ok.
1) Immediate deflection check
Figure-5: Deflection from live load.

## Slide 61
Design checks:-
2- :long term deflection
By use combination U = 2*(D+SD)+0.5L According the ACI code the allowable deflection = 8000/240 = 34 mm
Maximum deflection in all structure from D , SD and L = 30.25 mm in panel equal 10 x 8.
Then, the deflection ok.

## Slide 62
Design checks:-
2- :Period check.
The period from the model = 1.041 sec.
 Hand calculation of period using method A
Ta = Ct
Where : : height of structure in meters. Ct : 0.0488 (for all other building).
X : 0.75
Figure-6: Period check. Ta = 0.0488* = 0.668 *1.6 = 1.07 sec > 1.041 sec (the period of the building).

## Slide 63
Design checks:-
3- :The number of mods and percent of participation.
Table-1 : sum. Of UX , UY and RZ

## Slide 64
Design checks:-
4- Drift check.
F∆ = (Cd × δ)/Ie , Cd = 5.5 , I = 1.25
Allowable value = 0.015 h = 0.015 x 3640 = 54.6 mm
Table-2 :Drift in x-direction for model 1.
Table-3:Drift in y-direction for model 1.
**As shown in the following figure all values is less than 54.6 mm

## Slide 65
Design checks:-
5- P-Delta check.
Table-4: P-Delta in x-direction for model 1.
Table-5 : P-Delta in y-direction for model 1.

## Slide 66
Design checks:-
6- Irregularity check.
We have done the irregularity check in both direction horizontal and vertical , So we fined that there is no horizontal or vertical irregularity in this structure.

## Slide 67
Design
Introduction:-
Preliminary dimensions of the different structural members were found. Now, after finishing the model, these members will be tested and evaluated to see if they are adequate or not.
After finish all definitions , Three dimensional model and checks. it’s the time to design the structural elements that we have

## Slide 68
Design
The area of steel that needed for the slab will be obtained from the program.
Figure-1: Slab reinforcement

## Slide 69
Design
Slab design :-
As = 540
Asmin. = 0.0018*1000*300 = 540 = As
 Use area of steel minimum = 540  1 Φ12/200mm
The needed top bars = As(sh.)
As(sh.) = Asmin. = 540
 Top bars = 540 1 Φ12/200mm
The same reinforcement in both directions X & Y.

## Slide 70
Design
Slab design :-
Figure-2: Section in slab

## Slide 71
Design
Beam design :-
*We will get the value of negative reinforcement for the beams at right and left from the model 2 .
*We will get the value of positive reinforcement for the beams at the mid. from the model 2 .
*We will get the value of negative reinforcement for the beams at the mid. from the model 1 .

## Slide 72
Design
Beam design :-
The following table show the flexural design for a span at each beam .
The total reinforcement for the beams are located in the detailed drawing for the beams in AutoCAD file.
Table-1 : Beams Reinforcement for flexural.

## Slide 73
Design
Beam design :-
Reinforcement of beam 1
Figure-3: Beam 1 reinforcement for flexure

## Slide 74
Design
Beam design :-
The following table show the shear design for the beam
.
Table-2 : Beams Reinforcement for shear.

## Slide 75
Design
Beam design :-
The following figure show the dimension of needed stirrups for beam1 and the dimensions of needed stirrups for each beam show in the AutoCAD drawings
Figure-3: Beam 1 reinforcement for shear

## Slide 76
Design
Column design.
Table-3 : Column Reinforcement for flexural.
The following table show the value of flexural reinforcement for columns

## Slide 77
Design
Column design.
The following table show the value of shear reinforcement for columns
Table-4: Column Reinforcement for shear.

## Slide 78
Design
Column design.
Figure-4: Section and needed reinforcement for column.
The following figures show the longitudinal reinforcement for column1 and the dimension of needed stirrups for column 1

## Slide 79
Design
 Shear wall
The following table show the need reinforcement for shear wall in the structure.
Table-5 : Walls Reinforcement.

## Slide 80
Design
 Shear wall
The following figures show the reinforcement for wall 1.
Figure-5: Section in wall 1.

## Slide 81
Design
 Ground beam
The following figure show cross section in the ground beam.
Figure-6: Section in Ground beam.

## Slide 82
Design
 Footings
The following figures show the layout of footings
Figure-7: Footing layout

## Slide 83
Design
Footings
The following table show the needed reinforcement for the footings
Table-6:Footing reinforcement

## Slide 84
Design
Footings
The following figure show the reinforcement for single footing.
Figure-8: Section in single footing
Figure-8: Section in Wall footing

## Slide 85
Design
Design of stairs
Figure-9: Dimension of stairs
Dimensions :-
Landing width = 1.25m
Landing length = 2.50 m
Step width = 2.5 m
Going = 0.3 m
Rise = 0.175 m

## Slide 86
Design
Design of stairs
Figure-10: Load transfers in the flight.
Load transfers:-
Figure-11: Load transfers in the landing.

## Slide 87
Design
Design of stairs
We design the landing and flight by hand and assuming them as simply supported beam and we get the following value of reinforcement but the value of steel that we use is the quantity recognized in the market .
For flight
As, shrinkage = 0.0018 b d = 0.0018 x 1000 x 170 = 306 mm2. ,1Ø12/250 mm.
Mu- = 16.67 kN.m, ρ = (0.85 f’c)/fy (1-√(1-(2.61 Mu)/(b d^2 f^' c))) = 0.0017,
As,min = ρbd = 306 mm2, use 1Ø12/250 mm.
Mu+ = 28 kN.m, ρ = 0.00262,
As = ρbd = 524 mm2, use 1Ø14/250 mm.

## Slide 88
Design
Design of stairs
We design the landing and flight by hand and assuming them as simply supported beam and we get the following value of reinforcement but the value of steel that we use is the quantity recognized in the market .
For landing
As, shrinkage = 0.0018 b d = 0.0018 x 1000 x 170 = 306 mm2, 1Ø12/250 mm.
Mu+ = 47 kN.m, ρ = (0.85 f’c)/fy (1-√(1-(2.61 Mu)/(b d^2 f^' c))) = 0.0036,
As = ρbd = 720 mm2, use 1Ø14/200 mm.

## Slide 89
References
•ACI Committee 318, “Building Code Requirements for Structural Concrete (ACI 318M-11)”, American Concrete Institute, Michigan, 2011.
•ASCE Committee, “American Society of Civil Engineers, Minimum Design Loads for Buildings and Other Structures” Edition 7-16.
•'' International Building Code 2015'' (IBC 2015 )

## Slide 90
Thank you