## Slide 1
Integrating Flood Risk Management and Sponge City Concept within the Palestinian Context, Case Study: Nablus City
An-Najah National University
Faculty of Engineering
Planning and City Technology Department
Prepared By: Muath Owda
Supervised By: Dr. Ali Abdulhameed, Dr. Zahraa Zawawi,

## Slide 2
1
2
3
TABLE OF CONTENTS
General Introduction
City Selection & Analysis
Results & Interventions
4
Conclusion & Recommendations

## Slide 3
General Introduction
Project Idea, Project Objectives, Methodology

## Slide 4
General Introduction
City Selection & Analysis
Conclusion & Recommendations
Results & Interventions
Project Idea
A sponge city is a new urban construction model started in China. It can alleviate urban flooding, water resources shortage, and the urban heat island effect by absorbing and capturing rain water and utilizing it to reduce floods. Rain water harvested can be repurposed for irrigation and home use. It is a sustainable drainage system on an urban scale and beyond.
Source: Wikipedia
Source: China-Britain Business FOCUS, May 2016

## Slide 5
General Introduction
City Selection & Analysis
Conclusion & Recommendations
Results & Interventions
Project Objectives
Main Objective: Localizing the sponge city factors to the Palestinian context, and analyzing the current situation of Nablus city as a case study to find the exposure situation of the city and its affection on the social economical aspects, along with finding the capacity of the city due to its “sponginess” in order to come up with interventions on the land use, and recommending some policies for the city.

## Slide 6
General Introduction
City Selection & Analysis
Conclusion & Recommendations
Results & Interventions
Methodology
The model here represents the methodology that the project has been through.
It’s divided into 3 steps:
Data Collection
City Analysis
Interventions

## Slide 7
City Selection & Analysis
City Selection, Exposure Analysis, Capacity Analysis

## Slide 8
General Introduction
City Selection & Analysis
Conclusion & Recommendations
Results & Interventions
City Selection
The selection process went through multiple levels, National and Regional levels.
National Level: There is 11 Palestinian cities distributed along the West Bank contain 3 geographical regions.

## Slide 9
General Introduction
City Selection & Analysis
Conclusion & Recommendations
Results & Interventions
City Selection
Regional Level: As the researcher is a resident at the northern area of the West Bank, the city will be selected from the cities in the north side of the West Bank for the ease of mobility, which they area Jenin, Tubas, Tulkarm, Qalqiliya, Nablus, and Salfit.

## Slide 10
General Introduction
City Selection & Analysis
Conclusion & Recommendations
Results & Interventions
City Selection
Regional Level
In the table, the main criteria for the selection process are shown with a classification for each one, with specifying data score and weight:

## Slide 11
General Introduction
City Selection & Analysis
Conclusion & Recommendations
Results & Interventions
City Selection
Regional Level
In the table, the main criteria for the selection process are shown with a classification for each one, with specifying data score and weight:

## Slide 12
General Introduction
City Selection & Analysis
Conclusion & Recommendations
Results & Interventions
City Selection
(GIS Model)
The next figure present a reality assessment form (Model) to determine the most suitable city for the study.

## Slide 13
General Introduction
City Selection & Analysis
Conclusion & Recommendations
Results & Interventions
City Selection
Suitability analysis result
Nablus, Jenin, and Tulkarm seem to be the most suitable cities for the project.

## Slide 14
General Introduction
City Selection & Analysis
Conclusion & Recommendations
Results & Interventions
City Selection
Final City Selection
As shown in the next table, Nablus is the most suitable city for the project.

## Slide 15
General Introduction
City Selection & Analysis
Conclusion & Recommendations
Results & Interventions
City Selection
Selected City
As explained in the previous slides, the selected city is Nablus.

## Slide 16
General Introduction
City Selection & Analysis
Conclusion & Recommendations
Results & Interventions
Analysis is divided into two sections:
Exposure Analysis
Capacity Analysis
City Analysis

## Slide 17
General Introduction
City Selection & Analysis
Conclusion & Recommendations
Results & Interventions
Risk Map
The next table represent the spatial criteria of the vulnerability analysis
Exposure Analysis

## Slide 18
General Introduction
City Selection & Analysis
Conclusion & Recommendations
Results & Interventions
(GIS Model)
The next figure present a reality assessment form (Model) to determine the vulnerability of the city.
Exposure Analysis

## Slide 19
General Introduction
City Selection & Analysis
Conclusion & Recommendations
Results & Interventions
Risk analysis process maps
Exposure Analysis

## Slide 20
General Introduction
City Selection & Analysis
Conclusion & Recommendations
Results & Interventions
Risk analysis process maps
Exposure Analysis

## Slide 21
General Introduction
City Selection & Analysis
Conclusion & Recommendations
Results & Interventions
Risk analysis process maps
Exposure Analysis

## Slide 22
General Introduction
City Selection & Analysis
Conclusion & Recommendations
Results & Interventions
Risk analysis process maps
Exposure Analysis

## Slide 23
General Introduction
City Selection & Analysis
Conclusion & Recommendations
Results & Interventions
Hydrological model to determine the streams paths and the flow length in Nablus
Exposure Analysis

## Slide 24
General Introduction
City Selection & Analysis
Conclusion & Recommendations
Results & Interventions
Risk analysis process maps
Exposure Analysis

## Slide 25
General Introduction
City Selection & Analysis
Conclusion & Recommendations
Results & Interventions
Risk analysis process maps
Exposure Analysis

## Slide 26
General Introduction
City Selection & Analysis
Conclusion & Recommendations
Results & Interventions
Risk analysis process maps
Exposure Analysis

## Slide 27
General Introduction
City Selection & Analysis
Conclusion & Recommendations
Results & Interventions
Flood risk map (final results)
Exposure Analysis

## Slide 28
General Introduction
City Selection & Analysis
Conclusion & Recommendations
Results & Interventions
Flood risk map (final results)
Exposure Analysis

## Slide 29
General Introduction
City Selection & Analysis
Conclusion & Recommendations
Results & Interventions
Flood risk map (final results)
Exposure Analysis

## Slide 30
General Introduction
City Selection & Analysis
Conclusion & Recommendations
Results & Interventions
Area of focus for the social economical factors
Exposure Analysis

## Slide 31
General Introduction
City Selection & Analysis
Conclusion & Recommendations
Results & Interventions
Exposure Analysis
Social Economical Factors:
Buildings (within high flood risk areas) (15%)
Streets/Accessibility (within high flood risk areas) (20%)
Industrial Areas (within high flood risk areas) (10%)
Poverty areas (within high flood risk areas) (25%)
Camps (within high flood risk areas) (12%)
Emergency Facilities (Fire Station, Police, Hospitals) (within high flood risk areas) (18%)

## Slide 32
General Introduction
City Selection & Analysis
Conclusion & Recommendations
Results & Interventions
Exposure Analysis
Buildings (within high flood risk areas) (15%)
There are (3,965.5 dunum) of buildings area in the city, and (19,032.4 dunum) of them are within the high-risk area which means 47% of the buildings in Nablus are high-risk buildings, this means that the buildings in Nablus score 5.85% out of 15% in exposure to vulnerability.

## Slide 33
General Introduction
City Selection & Analysis
Conclusion & Recommendations
Results & Interventions
Exposure Analysis
Buildings (within high flood risk areas) (15%)
5.85%

## Slide 34
General Introduction
City Selection & Analysis
Conclusion & Recommendations
Results & Interventions
Exposure Analysis
Streets/Accessibility (within high flood risk areas) (20%)
There is (383,823.2 m) length of streets in the city, and (94,906.8 m) of it is within high-risk area which means 25% of the streets length in Nablus are high-risk streets, and most of them are very important streets that connect the east side of Nablus to the west side through the city center, this means that the streets in Nablus score 5% out of 20% in exposure to vulnerability.

## Slide 35
General Introduction
City Selection & Analysis
Conclusion & Recommendations
Results & Interventions
Exposure Analysis
Streets/Accessibility (within high flood risk areas) (20%)
5%

## Slide 36
General Introduction
City Selection & Analysis
Conclusion & Recommendations
Results & Interventions
Exposure Analysis
Industrial Areas (within high flood risk areas) (10%)
There are (1,550.25 dunum) of industrial land use in the city, and (970.2 dunum) of it are within the high-risk area which means 62.5% of the industrial zone in Nablus is high-risk lands, this means that the industrial zone in Nablus score 6.25% out of 10% in exposure to vulnerability.

## Slide 37
General Introduction
City Selection & Analysis
Conclusion & Recommendations
Results & Interventions
Exposure Analysis
Industrial Areas (within high flood risk areas) (10%)
6.25%

## Slide 38
General Introduction
City Selection & Analysis
Conclusion & Recommendations
Results & Interventions
Exposure Analysis
Poverty areas (within high flood risk areas) (25%)
According the poverty map below, there is (9,556.7 dunum) between high and very high poverty areas in the city, and (3,515.86 dunum) of it are within the high-risk area which means 36.8% of the poverty areas in Nablus is high-risk areas, also as the high-risk area is (6,282.1 donum) and as mentioned (3515.86 dunum) of it is poverty areas with 56%, this means that the poverty areas in Nablus score 14% out of 25% in exposure to vulnerability.

## Slide 39
General Introduction
City Selection & Analysis
Conclusion & Recommendations
Results & Interventions
Exposure Analysis
Poverty areas (within high flood risk areas) (25%)

## Slide 40
General Introduction
City Selection & Analysis
Conclusion & Recommendations
Results & Interventions
Exposure Analysis
Poverty areas (within high flood risk areas) (25%)
14%

## Slide 41
General Introduction
City Selection & Analysis
Conclusion & Recommendations
Results & Interventions
Exposure Analysis
Camps (within high flood risk areas) (12%)
There are (543.4 dunum) of camps area in the city, and (485.8 dunum) of it are within the high-risk area which means 89.4% of the camps in Nablus is high-risk lands, this means that the camps areas in Nablus score 10.73% out of 12% in exposure to vulnerability.

## Slide 42
General Introduction
City Selection & Analysis
Conclusion & Recommendations
Results & Interventions
Exposure Analysis
Camps (within high flood risk areas) (12%)
10.73%

## Slide 43
General Introduction
City Selection & Analysis
Conclusion & Recommendations
Results & Interventions
Exposure Analysis
Emergency Facilities (Fire Station, Police, Hospitals) (within high flood risk areas) (18%)
There are 11 emergency facilities in the city, and they area divided into 1 police station, 2 fire stations, and 8 hospitals, all of the police station, the 2 fire stations, and 6 out of 8 hospitals area within the high-risk area, and as the fire station represent 7% of the 18%, and the police is 3%, and the hospitals are 8%, this means that the emergency facilities in Nablus score 3% in police exposure, and 7% in fire stations, and 6% in hospitals with total of 16% out of 18% in exposure to vulnerability.

## Slide 44
General Introduction
City Selection & Analysis
Conclusion & Recommendations
Results & Interventions
Exposure Analysis
Emergency Facilities (18%)
16%

## Slide 45
General Introduction
City Selection & Analysis
Conclusion & Recommendations
Results & Interventions
Exposure Analysis
Final Exposure of Nablus
The risk area of interest is the very high-risk area, which is covering 16% of Nablus new master plan and all the other social economical factors are evaluated within this area of interest.
Factor |  | Percentage from risk area | Score |  | Weight | Standard
Buildings |  | 47% | 5.85% |  | 15% | 0%
Streets |  | 25% | 5% |  | 20% | 0%
Industrial Zone |  | 62.5% | 6.25% |  | 10% | 0%
Poverty |  | 56% | 14% |  | 25% | 0%
Camps |  | 89.4% | 10.73% |  | 12% | 0%
Emergency Facilities | Police Station | 100% | 3% | 16% | 18% | 0%
 | Fire Station | 100% | 7% |  |  | 
 | Hospital | 75% | 6% |  |  | 
Total |  | - | 57.83% |  | 100% | 0%

## Slide 46
General Introduction
City Selection & Analysis
Conclusion & Recommendations
Results & Interventions
Capacity Analysis
Assessment Factors (Sponginess measure)
In this section, an analysis to the assessment factors to measure the sponginess of the city are being applied and evaluated. And the factors are as below.
Urban development rate (15%)
Per capita green areas (18%)
Permeate pavement rate (14%)
Total annual runoff control rate (14%)
Urban heat island value (15%)
Rainwater utilization rate (14%)
Sewage treatment rate (10%)

## Slide 47
General Introduction
City Selection & Analysis
Conclusion & Recommendations
Results & Interventions
Capacity Analysis
Urban development rate (15%)
The urban development rate has been divided into:
Population Density (7%)
Buildings Density (8%)

## Slide 48
General Introduction
City Selection & Analysis
Conclusion & Recommendations
Results & Interventions
Capacity Analysis
Population Density (7%)
A predict of the population increase based on the population growth rate for the years 2030, and 2038, to get the ratio of area per person.
Year | Population | Population Growth
1997 | 126,472 | -
2007 | 155,283 | 28,811
2017 | 184,816 | 29,533
2022 | 203,358 | 18,542
Year | Population
2022 | 203,358
2030 | 237,458
2038 | 277,276

## Slide 49
General Introduction
City Selection & Analysis
Conclusion & Recommendations
Results & Interventions
Capacity Analysis
Population Density (7%)
New master plan area = 40,421.8 dunum
Standard area/person = 115 Sqm / Person (According to the National Spatial Plan)
Year Factor | 2022 | 2030 | 2038
Population | 203,358 | 237,458 | 277,276
Area / Person | 200 Sqm | 170 Sqm | 145 Sqm
Ratio of Standard | 174% | 148% | 126%

## Slide 50
General Introduction
City Selection & Analysis
Conclusion & Recommendations
Results & Interventions
Capacity Analysis
Population Density (7%)
Score 7%
As shown in the map, there is a concentration in city center and east side.

## Slide 51
General Introduction
City Selection & Analysis
Conclusion & Recommendations
Results & Interventions
Capacity Analysis
Buildings Density (8%)
An evaluation of the building’s density in the new master plan in Nablus after 16 years in 2038.
New master plan area = 40,421.8 dunum
Standard Maximum Area = 12,030 dunum (30%)
Average Buildings Area Growth / Year = 324 dunum / year
Year Factor | 2022 | 2030 | 2038
Buildings Area | 4,289 dunum | 6,881 dunum | 9,473 dunum
Buildings Density | 10.6% | 17% | 23.5%
Buildings Area / Standard Maximum Area | 35.65% | 57.2% | 78.7%

## Slide 52
General Introduction
City Selection & Analysis
Conclusion & Recommendations
Results & Interventions
Capacity Analysis
Buildings Density (8%)
8%

## Slide 53
General Introduction
City Selection & Analysis
Conclusion & Recommendations
Results & Interventions
Capacity Analysis
Urban development rate (15%)
The urban development rate has been divided into:
Population Density (7%) >>> Score (7%)
Buildings Density (8%) >>> Score (8%)
The total Score is 15%

## Slide 54
General Introduction
City Selection & Analysis
Conclusion & Recommendations
Results & Interventions
Capacity Analysis
Per capita green areas (18%)
The Per capita green areas has been divided into:
Green area to master plan area (9%)
Green area per person (9%)

## Slide 55
General Introduction
City Selection & Analysis
Conclusion & Recommendations
Results & Interventions
Capacity Analysis
Green area to master plan area (9%)
Master Plan Factor | Old Master Plan | New Master Plan
Master Plan Area | 29,453.5 dunum | 40,421.8 dunum
Green Area | 507.5 dunum | 554.5 dunum
Ratio | 1.7% | 1.37%
Evaluation | 31% | 25%
Calculations have been done to determine the ratio of the green areas to the city master plan, then an evaluation is applied to determine the capacity of the green area city-wise.
Standard proportion = 4% - 7% >>> (5.5%)
2.25%

## Slide 56
General Introduction
City Selection & Analysis
Conclusion & Recommendations
Results & Interventions
Capacity Analysis
Green area to master plan area (9%)
Calculations have been done to determine the ratio of green area per each person, then an evaluation is applied to determine the capacity of the green area for each person in the city.
The standard proportion = 5 sqm/person
Master Plan Factor | 2022 (Old Master Plan) | 2038 (New Master Plan)
Population | 203,358 | 277,276
Green Area | 507.5 dunum | 554.5 dunum
Green area per person | 2.5 Sqm | 2 Sqm
Evaluation | 50% | 40%
Score = 3.6%

## Slide 57
General Introduction
City Selection & Analysis
Conclusion & Recommendations
Results & Interventions
Capacity Analysis
Per capita green areas (18%)
5.85%

## Slide 58
General Introduction
City Selection & Analysis
Conclusion & Recommendations
Results & Interventions
Capacity Analysis
Per capita green areas (18%)
The Per capita green areas has been divided into:
Green area to master plan area (9%) >>> Score (2.25%)
Green area per person (9%) >>> Score (3.6%)
Total Score = 5.85%

## Slide 59
General Introduction
City Selection & Analysis
Conclusion & Recommendations
Results & Interventions
Capacity Analysis
Permeate pavement rate (14%)
an evaluation of the permeate pavement rate has been done to determine the percentage of the permeate streets in Nablus.
Standard Ratio = 100%
0.60%
Type Factor | Rainfall Drainage | Permeate Roads | Nablus Streets
Length | 12,173.45 m | 4,239.55 m | 383,823 m
Ratio | 3.17% | 1.1% | 100%
Total Length | 16,413 m |  | 383,823 m
Total Ratio | 4.27% |  | 100%

## Slide 60
General Introduction
City Selection & Analysis
Conclusion & Recommendations
Results & Interventions
Capacity Analysis
Permeate pavement rate (14%)
0.60%

## Slide 61
General Introduction
City Selection & Analysis
Conclusion & Recommendations
Results & Interventions
Capacity Analysis
Total annual runoff control rate (14%)
The average annual precipitation rate is 660 mm, and from this rate there is at least 60% as runoff water, with 0% control, this means the score of this factor is 0% out of 14%.
Standard Ratio = 100%

## Slide 62
General Introduction
City Selection & Analysis
Conclusion & Recommendations
Results & Interventions
Capacity Analysis
Total annual runoff control rate (14%)

## Slide 63
General Introduction
City Selection & Analysis
Conclusion & Recommendations
Results & Interventions
Capacity Analysis
Urban heat island value (15%)
the urban heat island value is above the average with 4.7 °C and since the standard acceptable increase is 3 °C the UHI value is 1.7 °C and this represent 56.7% increase above the average increase, this means the urban heat island rate factor scored 8.5% out of 15%.
Standard (Accepted) Increase Rate = 3
 | Value | Average Range
LST (Summer) | 28.6 – 39.2 °C | 23 – 32 °C
UHI (Summer) | 5.6 – 7.2 °C | -
UHI rate (Summer) | 6.4 °C (23.4%) | -
LST (Winter) | 10 – 24 °C | 8 – 20 °C
UHI (Winter) | 2 – 4 °C | -
UHI rate (Winter) | 3 °C (22.5%) | -
Average UHI | 4.7 °C (23%) | -
UHI value | 1.7 °C | -
Equation = k2/(log((k1/(((( LMAX - LMIN)/ (CALMAX - CALMIN))*(b-1))+ LMIN))+1))

## Slide 64
General Introduction
City Selection & Analysis
Conclusion & Recommendations
Results & Interventions

## Slide 65
General Introduction
City Selection & Analysis
Conclusion & Recommendations
Results & Interventions
Capacity Analysis
Urban heat island value (15%)
Average Land surface temperature during summer

## Slide 66
General Introduction
City Selection & Analysis
Conclusion & Recommendations
Results & Interventions
Capacity Analysis
Urban heat island value (15%)
Average Land surface temperature during winter

## Slide 67
General Introduction
City Selection & Analysis
Conclusion & Recommendations
Results & Interventions
Capacity Analysis
Urban heat island value (15%)
Average annual Land surface temperature
Score = 8.5%

## Slide 68
General Introduction
City Selection & Analysis
Conclusion & Recommendations
Results & Interventions
Capacity Analysis
Rainwater utilization rate (14%)
The annual average rainy days in Nablus is 60 – 70 days.
Nablus average precipitation rate is 660 mm.
As the utilization of the rainwater in Nablus is close to 0%, this factor scored 0% out of 14%.
Standard utilization rate = 100%
Year | Precipitation Rate | Percentage
2010 | 508.6 | 77%
2011 | 612.9 | 92.9%
2012 | 547.8 | 83%
2013 | 806.5 | 122%
2014 | 360.8 | 55%
2015 | 595.4 | 90%
2016 | 681.2 | 103%
2017 | 291 | 44%
2018 | 873.3 | 132%
2019 | 779.6 | 118%
2020 | 849 | 129%
2022/2023 | 561.9 | 85%

## Slide 69
General Introduction
City Selection & Analysis
Conclusion & Recommendations
Results & Interventions

## Slide 70
General Introduction
City Selection & Analysis
Conclusion & Recommendations
Results & Interventions
Capacity Analysis
Sewage treatment rate (10%)
The sewage treatment rate in Nablus is 55%, therefore, the sewage treatment rate factor scores 5.5% out of 10%, with the ability to raise it whenever the east station is created.
Standard Ratio = 100%
Quantity Factor | Amount | Percentage
Average Wastewater Produced Yearly | 7,883,336 | 100%
Average Wastewater Not Treated Yearly | 3,547,501 | 45%
Average Wastewater Treated Yearly | 4,335,835 | 55%
Quantity Factor | Amount | Percentage
Average Wastewater Produced Yearly |  | 100%
Average Wastewater Not Treated Yearly |  | 45%
Average Wastewater Treated Yearly |  | 55%

## Slide 71
General Introduction
City Selection & Analysis
Conclusion & Recommendations
Results & Interventions
Capacity Analysis
Sewage treatment rate (10%)
5.5%

## Slide 72
General Introduction
City Selection & Analysis
Conclusion & Recommendations
Results & Interventions
Capacity Analysis
Final Sponginess of Nablus
After analyzing the assessment factors to measure the sponginess of Nablus, this section shows the final evaluation of the whole stage to come up with the sponginess rate in Nablus.
Factor | Weight | Score
Urban Development rate | 15% | 15%
Per capita green areas | 18% | 5.85%
Permeate pavement rate | 14% | 0.60%
Total annual runoff control rate | 14% | 0%
Urban heat island value | 15% | 8.5%
Rainwater utilization rate | 14% | 0%
Sewage treatment rate | 10% | 5.5%
Total | 100% | 35.45%
35.45%

## Slide 73
Results & Interventions
Analysis Results, Projects, Policies

## Slide 74
General Introduction
City Selection & Analysis
Conclusion & Recommendations
Results & Interventions
Analysis Results
Capacity =
35.54%
Exposure =
57.83%
Within the very high risk area that covers 16% of the city
Within the whole city of Nablus

## Slide 75
General Introduction
City Selection & Analysis
Conclusion & Recommendations
Results & Interventions
Interventions
Industrial lands within risk area

## Slide 76
General Introduction
City Selection & Analysis
Conclusion & Recommendations
Results & Interventions
Projects
There is two projects proposed:
Modification of land uses in the industrial zone
Proposed rainwater drainage network in the industrial zone
Outputs
Spongier Master Plan
Physical Permeability
New land use plan
Rainwater drainage Network

## Slide 77
General Introduction
City Selection & Analysis
Conclusion & Recommendations
Results & Interventions
Projects
Modification of land uses in the industrial zone
Existing Land Use
There is a lack of green space, lack of emergency facilities, and lack of physical flood defenses barriers to defend the buildings from damage.

## Slide 78
General Introduction
City Selection & Analysis
Conclusion & Recommendations
Results & Interventions
Land Use | Old Land Use Plan
Open Green Areas | 3,800 Sqm
Public Garden | 18,238 Sqm
Emergency Center | 0 Sqm
Open Green Areas ratio | 0.17%
Public Garden ratio | 0.82%
Emergency Facilities ratio | 0%
Projects
Modification of land uses in the industrial zone
Industrial Zone = 2,209,242 Sqm

## Slide 79
General Introduction
City Selection & Analysis
Conclusion & Recommendations
Results & Interventions
Projects
Modification of land uses in the industrial zone
Proposed Land Use
More green spaces, proposed emergency center, and more green belts that work as barriers to protect buildings within their blocks

## Slide 80
General Introduction
City Selection & Analysis
Conclusion & Recommendations
Results & Interventions
Projects
Modification of land uses in the industrial zone
Industrial Zone = 2,209,242 Sqm
Land Use | New Land Use Plan | Old Land Use Plan
Open Green Areas | 20,126 Sqm | 3,800 Sqm
Public Garden | 46,651 Sqm | 18,238 Sqm
Emergency Center | 2,078 Sqm | 0 Sqm
Open Green Areas ratio | 0.91% | 0.17%
Public Garden ratio | 2.1% | 0.82%
Emergency Facilities ratio | 0.09% | 0%

## Slide 81
General Introduction
City Selection & Analysis
Conclusion & Recommendations
Results & Interventions
Projects
Modification of land uses in the industrial zone
Proposed Land Use
More green spaces, proposed emergency center, and more green belts that work as barriers to protect buildings within their blocks

## Slide 82
General Introduction
City Selection & Analysis
Conclusion & Recommendations
Results & Interventions
Projects
Open green areas
It work like a green belt around the block to prevent water to enter the buildings space and damage the building.

## Slide 83
General Introduction
City Selection & Analysis
Conclusion & Recommendations
Results & Interventions
Projects
Modification of land uses in the industrial zone
Industrial Zone = 2,209,242 Sqm
Land Use | New Land Use Plan | Old Land Use Plan
Open Green Areas | 20,126 Sqm | 3,800 Sqm
Public Garden | 46,651 Sqm | 18,238 Sqm
Emergency Center | 2,078 Sqm | 0 Sqm
Open Green Areas ratio | 0.91% | 0.17%
Public Garden ratio | 2.1% | 0.82%
Emergency Facilities ratio | 0.09% | 0%

## Slide 84
General Introduction
City Selection & Analysis
Conclusion & Recommendations
Results & Interventions
Projects
Proposed drainage network in the industrial zone
Analysis
Water flow is affected by the topography

## Slide 85
General Introduction
City Selection & Analysis
Conclusion & Recommendations
Results & Interventions
Projects
Proposed drainage network in the industrial zone
Analysis
Industrial zone suffer from high flood risk and streams, and the current drainage network doesn’t cover much

## Slide 86
General Introduction
City Selection & Analysis
Conclusion & Recommendations
Results & Interventions
Projects
Proposed drainage network in the industrial zone
Analysis
The old drainage network only covers 13% of the industrial zone, while the proposed network covers 100% of it.

## Slide 87
General Introduction
City Selection & Analysis
Conclusion & Recommendations
Results & Interventions
Projects
Proposed drainage network in the industrial zone
Analysis
The old drainage network only covers 13% of the industrial zone, while the proposed network covers 100% of it.

## Slide 88
General Introduction
City Selection & Analysis
Conclusion & Recommendations
Results & Interventions
Projects
Proposed drainage network in the industrial zone
Analysis
The network is connected to 5 water collecting underground tanks, to utilize it in agricultural and industrial usage.

## Slide 89
General Introduction
City Selection & Analysis
Conclusion & Recommendations
Results & Interventions
Projects
Proposed drainage network in the industrial zone
the area that the new network cover is 100% of the industrial zone, while the existing network covers only 13% of the industrial area without any form of water collection or utilization of the rainwater, while the proposed network has it.
Network Factor | Existing drainage network | Proposed drainage network
Length of the network | 3,375.5 m | 27,576.2 m
Percentage cover of the industrial area | 13% | 100%
Existence of water collection | No | Yes
Volume of water collection | 0 | 10,602.5
Existence of rainwater utilization | No | Yes
Network Factor | Existing drainage network | Proposed drainage network
Length of the network | 3,375.5 m | 27,576.2 m
Percentage cover of the industrial area | 13% | 100%
Existence of water collection | No | Yes
Volume of water collection | 0 | 
Existence of rainwater utilization | No | Yes

## Slide 90
General Introduction
City Selection & Analysis
Conclusion & Recommendations
Results & Interventions
Policies
The policies are for the owners to make them contribute in the solution:
Orienting buildings to operate a rainwater harvesting system.
Orienting buildings to create rooftop gardens.
Strategies
Rainwater utilization
Reduce runoff water
RWH
Green Roofs

## Slide 91
General Introduction
City Selection & Analysis
Conclusion & Recommendations
Results & Interventions
Policies
Rain water harvesting system (RWH)

## Slide 92
General Introduction
City Selection & Analysis
Conclusion & Recommendations
Results & Interventions
Policies
Rooftop gardens
Source: City of Melbourne website

## Slide 93
Conclusion & Recommendations

## Slide 94
General Introduction
City Selection & Analysis
Conclusion & Recommendations
Results & Interventions
Conclusion
Exposure = 57.83% Within risk area 16% of the city
Capacity = 35.54%
Projects:
Drainage Network
New Land Use Plan
Policies:
Rain Water Harvesting (RWH)
Rooftop Gardens (Green Roofs)

## Slide 95
General Introduction
City Selection & Analysis
Conclusion & Recommendations
Results & Interventions
Recommendations
For the city of Nablus:
A detailed studies for the rest of city areas like (Residential neighborhoods, Commercial centers, Public areas) to make them spongier.
Creating detailed data for the water related studies, like run-off water ratio, rainfall ratio by neighborhood.
Managing the density of the city by distributing the buildings in the new areas in the master plan without crowding them up.
Making plans for flood emergency situations.

## Slide 96
Thank you for listening
- Mauth Owda
“Let’s build better cities for better future”