## Slide 1
A comprehensive design of a Municipality building in Nablus
An-Najah National University
Faculty of Engineering & Information Technology
Department of Building Engineering
Supervisor: Eng. Amer Al-Shareef
Prepared by:
                Ahmad Nazeeh Nasrallah
                Shadi Zarour
                Ibrahim Hassan

## Slide 2: Outline:
Definition of the Municipality.
Architectural Design.
Environmental Design.
Structural Design.
Electrical design.
Mechanical And Safety Design.
Quantity Survey And Cost Estimation.
1

## Slide 3: What is the Municipality
Municipality : is one of the state departments, And the Municipal building, is the chief administrative building of a city.
Main goal: The city of Nablus was chosen because the existing building of the municipality of Nablus is now an old building, and is no longer adequate.

## Slide 4
Architectural Aspects

## Slide 5
2.3 km from the city center( 4 minutes by car)
Site description :

## Slide 6
Total Land Area ( 6552 m2 )
Annual average of humidity (61%).
Maximum temperature in August = 38 ºC.
Wind speed 5 Km/hr.
Noise level in the site. 38dB
Site Analysis

## Slide 7: Sun path Winter:

## Slide 8: Summer:

## Slide 9
Municipality departments
Administration department
Parking
Investment
Technical Section
Finance Department
Department of Land Control and Infringement
Department of Environmental Health

## Slide 11: Basement Floor plan

## Slide 12: ground floor plan

## Slide 13: First Floor plan

## Slide 14: Second Floor plan

## Slide 15: General view of the Municipality :

## Slide 16: Some views from the Municipality

## Slide 17: Some views from the Municipality

## Slide 18: Some views from the Municipality

## Slide 19: Some views from the Municipality

## Slide 20: Environmental Aspects

## Slide 21
Environmental Aspects
Thermal and energy simulation.
Acoustical Analysis.
Natural lighting analysis.
Environmental Aspects

## Slide 22: Acoustical analysis
Reverberation time (RT60):
Mayor room
RT60 range ( 0.4 - 0.6 )

## Slide 23: Acoustical analysis
Meeting room :
RT60 range (0.65 - 1.25)

## Slide 24: Acoustical analysis
Public service zone:
RT60 range (1.4 - 2)

## Slide 25
External wall (30cm)
Thermal Analysis
Limestone (50 mm)
Concrete (100 mm)
Polystyrene (50 mm)
Block (100 mm)
Plaster (13 mm)
U-Value = 0.5 W/m2.k
Roof:
Asphalt (10 mm)
Concrete foam (50 mm)
Polyurethane (50 mm)
Concrete and block (250 mm)
Plaster (10 mm)
U-Value = 0.45 W/m2.k
Floor:
Tiles (10 mm)
Mortar (30 mm)
Sand (150 mm)
Polystyrene (50 mm)
Concrete and block (250 mm)
U-Value = 0.9 W/m2.k

## Slide 26
Energy simulation
Maximum Cooling = 578 kW
Maximum Heating = 479 kW

## Slide 27
  Natural Lighting:
  Avg. DF for the building
  Daylight factor for some of the main spaces: 4.6
Room | DF %
F.F Electrical Room | 3.9
G.F Archive Room | 5.2
F.F Licenses Room | 2.8
F.F Bath Room | 0.4
F.F Surviving Room | 2.1
F.F Tenders Room | 15.3
Court of Law Room 2nd.F | 3.5
cafeteria G.F | 5.7
Multi-purpose room 2nd.F | 3
Natural Lighting

## Slide 28
Structural Design

## Slide 29: Design Data:
Concrete Fʹc = 24 MPa for slabs, and beams.
Concrete Fʹc = 28 MPa for columns, and footings.
Allowable Bearing Capacity of Soil = 300 kN/m²
Loads:
Super imposed load = 4.5 kN/m²
Live load = 4.5 kN/m²

## Slide 30: Seismic Design Data
Standard Occupancy, I = 1.0
Soil Profile Type is Sc
R = 5.5
Ca = 0.24
Cv= 0.32
Location → Nablus
Zone =2B → Z=0.20

## Slide 31: Structural plan

## Slide 32: Plan of structural designed block
Model from ETABS
1400m2@4floors

## Slide 33
Deformed shape of the building:
The model is valid for:
1- Compatibility.
2- Equilibrium.
3- Stress & Strain relationship.

## Slide 34
Period check:
 T standard =0.47sec
 From ETAB 0.464 sec
Dynamic checks:

## Slide 35
Maximum drift available = 29 mm
∆ limit of the story = 0.02 * height of story = 0.02 *1450 = 29 cm (manual check).
∆ inelastic =0.7*R*∆elastic (ETABS check).
Drift check:
→∆inelastic for moment in x- direction =0.7*5.5* -4.158 = 16.0083 mm
→∆inelastic for moment in y- direction =0.7*5.5* 3.13 = 12.0505 mm
Since ∆inelastic (for delta Mx and delta My) < ∆ limit story then check drift is ok.

## Slide 36: Results:
1) Slab design:
Reinforcement:
Thickness= 320mm
2∅14 mm/rib
As shrinkage 4∅8 mm/m

## Slide 37: layout

## Slide 38: 2)Beam design details:

## Slide 39
3) Column 1 design details:

## Slide 40
Column 2 design details:

## Slide 41
Column 3 design details:

## Slide 42
4) Footings
Distribution layout

## Slide 43
Footing 3 design details:

## Slide 44
→ Take As,min = 450mm2 → 4Φ12/m
Stairs design details

## Slide 45
Artificial Lighting

## Slide 46
1) offices
E(avg) = 418 Lux
U = 0.57 UGR = 15.7
Walls’ reflection factor = 50 %.
Ceiling’s reflection factor = 70.5 %.
Floor reflection factor = 44.2 %.

## Slide 47
Offices luminaire

## Slide 48
2) multi-purpose
Walls’ reflection factor = 50 %.
Ceiling’s reflection factor = 70.5 %.
Floor reflection factor = 44.2 %.
E avg = 586 Lux
U = 0.52 UGR = 16.2

## Slide 49
multi-purpose room luminaire

## Slide 50
Connect the bulbs :

## Slide 51
Connect the Sockets :

## Slide 52
Mechanical Aspects

## Slide 53
Mechanical Aspects
HVAC system.
Water supply.
Drainage system.
Mechanical Aspects

## Slide 54
1) Water supply system

## Slide 55
1) Types of water supply system
Cold water
Hot water
Filtered water
Is used only in WC

## Slide 56
Ground floor:
Floor/Pipe | Vertical | Horizontal | Branch
Ground floor | 2.5in | 2 in | 1.5in
Floor/Pipe | Vertical | Horizontal | Branch
First floor | 2.5 in | 2 in | 1.5 in
First floor:
Dimensions of pipes in water supply system

## Slide 57
2) Drainage system
Each W.C represents 6Dfu…………. pipe 4".
Each Lavatory represent 1Dfu…………… pipe 2".
Each kitchen sinks Represent 2Dfu………… pipe 2".
Main stack 4". Use ventilation stack 4''.

## Slide 58
Types of drainage system
Black water
Gray water

## Slide 59: Drainage system on the site plane

## Slide 60: Rain water drainage

## Slide 61
3) HVAC system design
The method of the HVAC system is VRF system, which allow for cooling and heating at the same time.
The internal unit that is used is suspended on false ceiling .

## Slide 62
HVAC Units distribution for the ground floor.

## Slide 63
Safety Design
Standpipes and hose station
Automatic fire Sprinkler

## Slide 64: Safety Design
Fire alarm system used heat detectors in office building.

## Slide 65
Escape route

## Slide 66
Quantity survey & cost estimation

## Slide 67
Excavation :
Quantity survey & Cost estimation
Total cost of excavation= NIS 50,000
Cost (Nis) | 
50,000 | excavation

## Slide 68
Cost of concrete and steel:
Quantity survey & Cost estimation
Total cost of
concrete
And steel =
NIS 1,233,270
total cost | cost steel | cost concrete | steel (ton) | Concrete (CM) | 
124070 | 35100 | 88970 | 13 | 287 | footing
64340 | 30240 | 34100 | 11.2 | 110 | tie beam
92770 | 24570 | 68200 | 9.1 | 220 | ground slab
94710 | 57510 | 37200 | 21.3 | 120 | column
695300 | 307800 | 387500 | 114 | 1250 | slabs
87680 | 44280 | 43400 | 16.4 | 140 | shear wall
74400 | 0 | 74400 | 0 | 240 | plain concrete
1233270 |  |  |  |  | total

## Slide 69
Quantity survey & Cost estimation
Total cost of stone, tiles, plaster and ..its
= NIS 3,731,525
cost | meter square | 
840000 | 5600 | Porcelain tiles
390000 | 2600 | stone
66000 | 3520 | blocks 10 cm
78750 | 2100 | blocks ribbed
6875 | 220 | blocks 20 cm
120000 | 600 | Satires marble
16500 | 30 | granite
716400 | 11940 | plaster
597000 | 11940 | painting
300000 | 500 | glass wall + window
100000 | 200 | door
500000 | 1000 | Marble tile
3731525 |  | total

## Slide 70
Finishes of
cost
Quantity survey & Cost estimation
Total cost
of finishes = NIS 3,726,650
cost | 
200000 | electricity
280000 | elevators
80000 | plumping
1237600 | laborer construction
42500 | cement
30000 | sand & gravel
165000 | Engineering and Licensing
656550 | PR requirements
500000 | HVAC
325000 | fall ceiling
10000 | Clay tile
200000 | furniture
3726650 | total

## Slide 71
Total cost of the building = NIS 8,741,445
Total cost of site plane = NIS 725,000
total cost = NIS 9,466,445
Final cost for the building:
Quantity survey & cost estimation
Unit cost of the building = NIS 1853.2/m2
Unit cost of the building and site = NIS 2007/m2