## Slide 1: High School design
Prepared by: Supervised by:
Aya Al-Taher. Eng. Fadi Fatayer.
Haneen Nassar.
Yara Abu-Baker.

## Slide 2
Quantity surveying
Site analysis
Architectural design
Structural design
Environmental design
Electrical design
Mechanical design
Outline

## Slide 3: Site analysis
Located in the east of Nablus city at Al-Ma’ajeen
Land area = is 5237.3 m2
Building area = 3911 m2
Noise Level
Noise Level (dB) | Direction
68 | East
63 | South
67 | West
64 | North

## Slide 4: Architectural design
School site

## Slide 5: Architectural design
Site plan

## Slide 6: Architectural design
Basement floor plan
Space | Required area | Actual area | Check
General storage | 40 | 42 | Ok
Mechanical room and Electrical room | 15 | 19.60 | Ok

## Slide 7: Architectural design
Ground floor plan
Space | Required area | Actual area | Check
Classroom (40 student) | 48 | 75 | Ok
Head office | 30 | 42 | Ok
First aid | 15 | 20 | Ok
Kitchen | 10 | 20 | Ok
Teachers room | 50 | 50 | Ok
Secretary | 20 | 20 | Ok
Canteen | 16 | 73 | Ok
Archive, Printing | 15 | 18.8 | Ok
Music room | 70 | 75 | Ok

## Slide 8: Architectural design
First floor plan
Space | Required area | Actual area | Check
Classroom (40 student) | 48 | 75 | Ok
Consultant (adviser) | 15 | 37 | Ok
Storage | 15 | 20 | Ok
Chemistry lab | 70 | 71 | Ok
computer lab | 65 | 71 | Ok
Music room | 70 | 75 | Ok

## Slide 9: Architectural design
Second floor plan
Space | Required area | Actual area | Check
Classroom (40 student) | 48 | 75 | Ok
Library | 80 | 180 | Ok
Storage | 15 | 20 | Ok
Chemistry lab | 70 | 71 | Ok

## Slide 10: Architectural design
South Elevation

## Slide 11: Architectural design
East Elevation

## Slide 12: Architectural design
West elevation

## Slide 13: Architectural design
North Elevation

## Slide 14: Architectural design
Section A-A

## Slide 15: Architectural design
Section B-B

## Slide 16: Architectural design
Section C-C

## Slide 17: Architectural design
3D View

## Slide 18: Architectural design
3D View

## Slide 19: Architectural design
3D View

## Slide 20: Architectural design
3D View

## Slide 21: Structural design
Reinforced concrete structure

## Slide 22: Structural design
Steel structure

## Slide 23: Structural design
Codes:
ACI 318-14
UBC – 97 for earthquake design.
ASCE for loads computations.

## Slide 24: Structural design
Designing data and loads:
f’c = 24 Mpa for beams and slabs.
f’c = 28 Mpa for columns.
Fy = 420 Mpa
Bearing capacity of soil at street level = 250 KN/m².
Live loads = 5 KN/m².
Super imposed dead load = 4KN/m².

## Slide 25: Structural design
Lateral loads:
The seismic zone of Nablus is 2B (Z = 0.20)
The soil profile is type Sc.
The acceleration seismic coefficient Ca=0.24
The velocity seismic coefficient Cv=0.32
The Seismic importance factor is 1
The structural design type is building frame R=5.5
(for sway intermediate concrete frame structure).
Response spectrum scale factor= (g×I)/R=1783.63

## Slide 26: Structural design
Manual checks
Compatibility check → ok
Equilibrium check → ok
Internal force check → ok
Deflection check → ok
Period check → ok
Base shear check → ok
Drift check → ok

## Slide 27: Structural design
Compatibility check:
The building Is compatible.

## Slide 28: Structural design
Percentage of difference | From manual (KN) | From ETAB(KN) | Load Case
1.9% | 12980 | 13236.3 | Dead
%0.04 | 5740 | 5742.6 | Live
%0.6 | 12650.4 | 12574.6 | SID
Equilibrium check:
%of error <5% →ok

## Slide 29: Structural design
Internal force check:
For columns:
Manual axial load =300KN
Axial load from ETAB =303KN
The percentage of difference= 1% < 5%
→the check is OK
20 May 2019

## Slide 30: Structural design
Deflection check:
Immediate deflection.
This check from live load for critical slab
Max allowable deflection =25 mm
Max deflection from ETAB = 9.9mm
→the check is ok.

## Slide 31: Structural design
Period check (model1)
T manual=0.676 sec
T Etab=0.607 sec
T etabs < T manual→ So the check is ok.

## Slide 32: Structural design
Base shear check (model1):
Vx = 7672 KN.
Vy = 8731.6 KN.
FZ (KN) | FY (KN) | FX (KN) | Load Case/Combo
28884.0982 | -0.0048 | 0.0317 | Dead
11000.3638 | -0.0014 | 0.0255 | Live
48406.0013 | -0.0059 | 0.05 | SID
7.113E-06 | 3541.5574 | 7672.0103 | EQx Max
2.329E-05 | 8731.7853 | 4608.3174 | EQy Max

## Slide 33: Structural design
Drift check (model1):
story | Height (mm) | Displacment X( mm) | Displacment Y mm | Drift Xmm | Drift Y mm | Delta X | Delta Y | Delta -limit(mm)
1 | 4500 | 1.23 | 0.24 | 1.23 | 0.24 | 4.74 | 0.93 | 90
2 | 3500 | 3.52 | 3.37 | 2.29 | 3.13 | 8.82 | 12.06 | 70
3 | 3500 | 7.13 | 6.8 | 3.61 | 3.43 | 13.9 | 13.21 | 70
4 | 3500 | 11.25 | 9.75 | 4.12 | 2.95 | 15.87 | 11.3575 | 70

## Slide 34: Structural design
Two way ribbed slab
Thickness = 40cm
As shrinkage = 3Ø8/m
As = 2Ø12

## Slide 35: Structural design
Beams reinforcement and details:

## Slide 36
Zone B length 1-8mm/150mm | Zone A length 1-8mm/100mm | F- length(m) 3-16mm | E- length(m) 2-16mm | c-length(m) 2-16mm | A-length(m) 3-16mm | Beam dimension (cm) | beam length(m) | Beam Number
3.4 | 0.8 | 6.6 | 3.7 | 3.9 | 2.3 | 60*40 | 5 | 1
0.6 | 0.8 | 3.8 | 2.5 | 2 | 1.6 | 60*40 | 2.2 | 2
0.4 | 0.8 | 3.6 | 2.4 | 1.9 | 1.5 | 60*40 | 2 | 3
5.9 | 0.8 | 9.1 | 4.7 | 5.6 | 2.9 | 60*40 | 7.5 | 4
0.3 | 0.8 | 3.5 | 2.4 | 1.8 | 1.5 | 60*40 | 1.9 | 5
2.4 | 0.8 | 5.6 | 3.2 | 3.2 | 2 | 60*40 | 4 | 6

## Slide 37: Structural design
Columns reinforcement and details:
20 May 2019

## Slide 38: Structural design

## Slide 39: Structural design
Shear walls reinforcement and Details:

## Slide 40: Structural design
Foundations(model1):

## Slide 41: Structural design
Foundations(model2):

## Slide 42: Structural design
Footing design
Isolated footings are used:

## Slide 43: Structural design
Steel umbrella:
Design assumptions:
The truss section is selected to be tube section (TUBO)
The cover system Louvres
The type of welded connection is E60xx

## Slide 44: Structural design

## Slide 45: Structural design
Load type | value
L.L (kN) | 3.75
W.L (kN) | 1.92
SID (kN) | 3.75
Loads:

## Slide 46: Structural design
Checks:
Compatibility check:

## Slide 47: Structural design
Equilibrium check:
Total truss length was 135.64m
Manual check:
For Live load 1KN/m*135.64m=135.64KN
For SID = 135.64KN
For wind load 0.51*227.3=69.17KN.
From ETABS:
ETAB result | Load type
136.5699 | Live
136.5699 | Sid
69.6506 | Wind

## Slide 48: Environmental DESIGN:
Shading
Acoustics
Thermal
Daylight factor

## Slide 49: Environmental DESIGN:
Used design builder program

## Slide 50: Environmental DESIGN:
Envelope properties
External walls
U-value = 0.432 W/.K

## Slide 51: Environmental DESIGN:
Envelope properties
2) Internal walls
U-value = 1.188 W/.K

## Slide 52: Environmental DESIGN:
Envelope properties
3) Roof
U-value = 0.333 W/.K

## Slide 53: Environmental DESIGN:
Envelope properties
4) Floors
U-value = 0.321 W/.K

## Slide 54: Environmental DESIGN:
Envelope properties
4) Windows material is double glass generic clear 3mm glass
U-value = 1.092 W/.K

## Slide 55: Environmental DESIGN:
Heating load design.
Air temperature = 23 °C
Radiant temperature = 20 °C
Operative temperature =22 °C
Total heating load = 77.75 kW

## Slide 56: Environmental DESIGN:
Comfort curves
RH less 60%
PMV between (-0.5 - 0.5)

## Slide 57: Environmental DESIGN:
Comfort curves
The number of uncomfortable hours equals 1688 hr/year.
Energy consumption = 33.71 kWh/

## Slide 58: Environmental DESIGN:
Daylight factor
Ground floor
Average DF% in first floor equal 0.5% not within the standard (2-5)%

## Slide 59: Environmental DESIGN:
Daylight factor
First floor and second floor
Average DF% in first floor equal 3.9% within the standard (2-5)%

## Slide 60: Environmental DESIGN:
Louver system was used on southern façade 2mm thickness, 30 cm depth and 0.5 m vertical spacing

## Slide 61: Environmental DESIGN:
Acoustics (
Used Ecotect program
and for Classroom
FREQUNECY | ∝ (Walls: Painted Plaster) | ∝ (Floor: Tile) | ∝ (Ceiling: Plaster) | ∝ (Glass) | ∝ (Door) | RT60
63Hz | 0.31 | 0.01 | 0.01 | 0.10 | 0.05 | 0.69
125Hz | 0.31 | 0.01 | 0.01 | 0.10 | 0.05 | 0.69
250Hz | 0.33 | 0.02 | 0.02 | 0.07 | 0.25 | 0.56
500Hz | 0.14 | 0.02 | 0.02 | 0.05 | 0.60 | 0.81
1kHz | 0.10 | 0.02 | 0.02 | 0.03 | 0.15 | 0.80
2kHz | 0.10 | 0.02 | 0.02 | 0.02 | 0.05 | 0.59
4kHz | 0.12 | 0.02 | 0.02 | 0.02 | 0.10 | 0.58
8kHz | 0.12 | 0.02 | 0.02 | 0.02 | 0.10 | 0.42
16kHz | 0.12 | 0.02 | 0.02 | 0.02 | 0.10 | 0.42

## Slide 62: Environmental DESIGN:
Acoustics (
Millington-Sette is selected
for Classroom is in the range (0.5 – 0.9sec.)
the result from different frequencies is within the range

## Slide 63: Environmental DESIGN:
Acoustics ( for other spaces
FREQUNECY | RT60 (art room) | RT60 (computer lab) | RT60 (meeting room) | RT60 (music room) | RT60 (library)
63Hz | 0.63 | 0.73 | 0.85 | 0.68 | 0.66
125Hz | 0.62 | 0.73 | 0.85 | 0.68 | 0.69
250Hz | 0.51 | 0.58 | 0.72 | 0.57 | 0.63
500Hz | 0.74 | 0.77 | 1.15 | 0.90 | 0.88
1kHz | 0.73 | 0.70 | 1.13 | 0.95 | 0.90
2kHz | 0.62 | 0.46 | 0.82 | 0.76 | 0.67
4kHz | 0.59 | 0.53 | 0.72 | 0.66 | 0.76
8kHz | 0.39 | 0.43 | 0.47 | 0.45 | 0.65
16kHz | 0.38 | 0.42 | 0.46 | 0.45 | 0.64
RT60 (standard) | (0.5 – 0.8sec.) | (0.4 – 0.8sec.) | (0.6 – 1.3sec.) | (0.6 – 1.3sec.) | (0.4 – 0.8sec.)

## Slide 64: Environmental DESIGN:
Acoustics (
Millington-Sette is selected
the result from
different frequencies is within the range

## Slide 65: Environmental DESIGN:
STC and IIC:
IIC for floor = 59 > 52 ok
IIC for ceiling = 54 >52 ok
Space | Adjected area | STC required | STC deign | Check
Classroom | Classroom | 42-40 | 43 | Ok
 | Corridor | 40-38 | 43 | Ok
Headteacher room | Corridor | 40-38 | 43 | Ok
Teachers room | Science lab | 45-41 | 43 | Ok
 | Corridor | 40-38 | 43 | Ok
 | Classroom | 40-38 | 43 | Ok
Music room | Corridor | 45-42 | 43 | OK
Library | Corridor | 45-42 | 43 | OK
Internal wall
External wall

## Slide 66: Environmental DESIGN:
Noise reduction:
The background noise for class rooms is from 30-35 dB.
space | Noise | NR | BN | Standard | OK/not ok
classroom | 67 | 39.67 | 27.32 | < 30 | Ok

## Slide 67: PV system design
PV system distribution
Horizontal landscape | PV panel
130 | No. of modules
39.65 | Electricity produced (KW)
82.45% | Performance ratio
88.63 | (MKW/Year)

## Slide 68: Electrical design
Sockets distribution
Artificial lighting design
Sound reinforcement system design
Electrical boards distribution

## Slide 69: Electrical design
Sockets distribution

## Slide 70: Electrical design
Artificial lighting
classroom

## Slide 71: Electrical design
Classroom lighting design
Used luminaires
LED panels  (2550) Lm
LED panels  (4700) Lm
Maximum required | Minimum required | Value
19 | <10 | 15.2
Glare
Ceiling | walls | Floor
45% | 44% | 50%
Surface reflection
plan | Required | Value
classroom | 300 lux | 365
board | 500 | 516
lux

## Slide 72: Electrical design
Lighting distribution

## Slide 73: Electrical design
Artificial lighting
Computer lab

## Slide 74: Electrical design
Computer lab lighting design
Used luminaires
LED panels  (2550) Lm
LED panels  (4700) Lm
Maximum required | Minimum required | Value
19 | <10 | 16.4
Glare
Ceiling | walls | Floor
45% | 45% | 50%
Surface reflection
plan | Required | Value
Lab | 300 lux | 324
board | 500 | 517
lux

## Slide 75: Electrical design
Luminaires distribution

## Slide 76: Electrical design
Sound reinforcement system design
is (H-2/WP) type from TOA Corp company
θ =
Coverage :
Ceiling mounted

## Slide 77: Electrical design
Sound reinforcement system design
Cafeteria
Sport hall

## Slide 78: Electrical design
Sound reinforcement system design
corridors

## Slide 79: Electrical design
Electrical boards distribution
GF
1st
2nd

## Slide 80: Mechanical design
Storm water
HVAC
System
Fire Fighting
Drainage
System
Water Supply
System
Emergency Exits

## Slide 81: Mechanical design
Radial System radiators
HVAC system
Radiator from VIADRUS company.
KALOR :

## Slide 82: Mechanical design
Radial System radiators
Steel pipe sizing
PVC-pipe sizing
Selection of Pump
Number of Section
The volume of boiler
HVAC system
Total heating load in the school = 77.75 kW

## Slide 83: Mechanical design
Steel pipe sizing – D =25 mm
PVC-pipe sizing – D =15 mm
Selection of Pump - Using Barmesa Pump model 24S 051
HVAC system
Ground floor design

## Slide 84: Mechanical design
Number of Section
HVAC system
Ground floor design
Space | Q Heating Load From Design Builder | Qrad | Number of Section | Section Use
Teacher Room | 1.27 | 1.4605 | 12.1 | 13
Meeting Room | 2.15 | 2.4725 | 20.6 | 21
Corridor | 1.4 | 1.61 | 13.4 | 14
Head Office | 1.32 | 1.518 | 12.6 | 13
Secretary | 0.5 | 0.575 | 4.7 | 5
First Aid | 0.58 | 0.667 | 5.5 | 6
Reception 1 | 0.82 | 0.943 | 7.8 | 8
W.C's | 2.31 | 2.6565 | 22.1 | 23
Classroom | 2.44 | 2.806 | 23.3 | 24
Reception 2 | 1.17 | 1.3455 | 11.2 | 12
Multipurpose Room | 1.76 | 2.024 | 16.8 | 17

## Slide 85: Mechanical design
HVAC system
Ground floor design
Distribution of radiators
in ground floor

## Slide 86: Mechanical design
HVAC system
Distribution of radiators
in first floor and
second floor

## Slide 87: Mechanical design
HVAC system
The volume of boiler
for the building equal 2 m3

## Slide 88: Mechanical design
Water supply system
Diameters of water pipes:
Pipe Diameter (in) | Branch | Horizontal | Vertical
Ground Floor | ¾ | 1.25 | 2
First Floor | ¾ | 1.25 | 2
Second Floor | ¾ | 1.25 | 2

## Slide 89: Mechanical design
Water supply system
The total fresh water volume = 97.80 m³/3day.
Distribution of water supply in ground floor

## Slide 90: Mechanical design
Water supply system
Distribution of water supply in first floor and second floor

## Slide 91: Mechanical design
Drainage system
Vertical stack had a 4-inch diameter.
Vertical vent had a 4-inch diameter.
Sewer line for the W.C's had 4-inch diameter. (1% slope)
Sewer line for the lavatories and sink had 2-inch diameter (2% slope)
The pipes between manholes is 6-inch.

## Slide 92: Mechanical design
Drainage system
Distribution of drainage system
in ground floor

## Slide 93: Mechanical design
Drainage system
Distribution of drainage system
in first floor and second floor

## Slide 94: Mechanical design
Storm water
Minimum slope on roofs 0.05%.
The capacity of the underground water tank equal 730 m3

## Slide 95: Mechanical design
Fire fighting system
Fire suppression using:
  Extinguishers
  Hose stations
  Sprinklers
Fire detecting :
  Smoke detectors

## Slide 96: Mechanical design
Distribution of Fire suppression system

## Slide 97: Mechanical design
Distribution of Fire suppression system

## Slide 98: Mechanical design
Distribution of detecting system

## Slide 99: Mechanical design
Safety
Emergency signs
Emergency routes

## Slide 100: Mechanical design
Safety
Emergency signs
Emergency routes

## Slide 101: Quantity surveying
Total school cost
= 6,326,602 NIS
Total unit cost = 1617.6 NIS/ m2

## Slide 102: Conclusion
New Design.
Site analysis
Architectural design
Structural design
Environmental design
Electrical design
Mechanical design