## Slide 1: Evaluation and Analysis of Nablus Entrances

## Slide 2: Objectives
Analyze and evaluate the traffic conditions for Nablus entrances, in order to increase their efficiency at these entrances by checking traffic conditions at the mentioned entrances.
Estimation of future conditions for the entrances .

## Slide 3: Significance of work
The significance of the work is to study the entrances of nablus city. Since it has an importance to facilitate traveling from nablus to other cities and villages, and vice versa.
The volume at these intersections is relatively high, and expected to increase significantly in future, due to the population growth and nablus economical position. This growth will make the movement more complicated.

## Slide 4
Help the municipality of nablus to improve the accessibility and mobility to the city therefore that will lead to improvement the touristic and economic situation for the city.

## Slide 5: Methodology
Counting traffic volume at each intersection.
Data analysis to obtain LOS for current and future conditions.
Check the intersections for warrants.
Signal timing for the warranted intersections.
LOS’s assuming warranted intersections are signalized.

## Slide 6: Site Description
Al-Ghawi intersection

## Slide 7: Al-Ghawi intersection
The intersection carries traffic from the eastern part of Nablus to the center of the city with four approaches,
Al-Hesba street (Approach A),
Balata street (Approach B),
Amman Street (Approach C)
Askar street (Approach D).

## Slide 8: Al-Quds intersection

## Slide 9: Al-Quds intersection
Have two major streets
Al-Quds street (Approach B) that carries traffic from ramallah and many villages around nablus like howara village, etc... ,
Minor road which is carrying traffic from balata refugees’ camp and many villages located in east of nablus like beit-fourik, salem, etc...(Approach D)

## Slide 10: Beit –Wazan intersection

## Slide 11: Beit –Wazan intersection
T intersection that carries the traffic from Qalqilya city and a part of Tulkarm traffic in addition to small traffic volumes from Ramallah and the western villages of Nablus, Qouseen, etc.. .
The other approach connects to the major entrance street that comes from Deir-Sharaf intersection.

## Slide 12: Deir-Sharaf intersection

## Slide 13: Deir-Sharaf intersection
T intersection carries traffic volume from Jenin, Nablus, and Tulkarm cities. As shown in the photo, the western approach comes from Tulkarm and continues to Nablus, while the Eastern-North comes from Jenin.

## Slide 14: Traffic volume
Count the traffic volume for the four intersections
Al-Ghawi intersection
Al-Quds intersection
Beit –Wazan intersection
Deir-Sharaf intersection

## Slide 15
 | AL-Ghawi | Beit-Wazan | Deir-Sharaf | AL-Quds
PH | 7:45 – 8:45 | 7:15 - 8:15 | 7:15 - 8:15 | 7:15 - 8:15
PHV | 2119 | 1385 | 896 | 2937

## Slide 16: Accidents (Crashes)
Safety is an important issue when planning to improve existing facility.
The number of crashes per year is the major indication of the safety on The intersection

## Slide 17
The numbers of crashes occur exactly at Al-Ghawi Intersection at the last 12 months are 19 crashes , regardless of their severity, and for Al-Quds Intersection are 9 crashes.
The average was estimated to be within 15-20 crash per year at Al-Ghawi intersection and about 10 at Al-Quds intersection, in the day and night time, which is considered to be a high value.

## Slide 18
Month / Year | No. of accidents Al-Ghawi Intersection | No. of accidents Al-Quds Intersection
Jan-14 | 3 | 0
Feb-14 | 2 | 4
Mar-14 | 1 | 0
Apr-14 | 2 | 2
May-14 | 2 | 1
Jun-14 | 0 | 1
Jul-14 | 0 | 1
Aug-14 | 3 | 0
Sep-14 | 0 | 1
Oct-14 | 0 | 0
Nov-14 | 1 | 0
Dec-14 | 2 | 0
Jan-15 | 1 | 1
Feb-15 | 1 | 1
Mar-15 | 2 | 0
Apr-15 | 4 | 0
May-15 | 2 | 1
Jun-15 | 0 | 1
Jul-15 | 3 | 2
Aug-15 | 1 | 1
Sep-15 | 1 | 1
Oct-15 | 1 | 0

## Slide 19: Data analysis

## Slide 20: Future Analysis
To calculate the future traffic volume, there is a need to determine the traffic growth rate ( i )
Based on the Palestinian Central Bureau of Statistics related to number of vehicles in Nablus form 2001 to 2014.
i=4 % .

## Slide 21
Level of service (LOS) is a measure used by traffic engineers to determine the effectiveness of elements of transportation infrastructures it is most commonly used to analyze highways, but the concept has also been applied to intersections, transit, and pedestrian facilities. The transportation LOS system uses the letters A through F, with A being the best and F being the worst.

## Slide 22: Level of service
SIDRA , HCS Softwares were used to estimate the level of service’s at the intersection’s while hand caculations according to HCM were also used to determine LOS’s for the links and Deir Sharaf intersection .

## Slide 23: Data Analysis for Intersections (level of service) current
Current LOS for the intersections |  |  |  | 
Intersection | AL-Ghawi | Beit-Wazan | Deir-Sharaf | AL-Quds
Current LOS | F | B | A | F

## Slide 24: Data Analysis for Intersections (level of service) expected
Future LOS for the intersections |  |  |  | 
Intersection | AL-Ghawi | Beit-Wazan | Deir-Sharaf | AL-Quds
Future LOS | F | F | B | F

## Slide 25: Data Analysis for links (Two Lane Rural Highway) current
Where: 1: West approach in Beit-Wazan intersection
2: North approach in Beit-Wazan intersection
3: north approach in Deir-Sharaf intersection.
4: West approach in Deir-Sharaf intersection.
5: Approach C in AL-Ghawi intersection
Current LOS’s for two lane highway links. |  |  |  |  | 
Link # | 1 | 2 | 3 | 4 | 5
LOS | D | A | B | B | C

## Slide 26: Data Analysis for links (Two Lane Highway) Expected
Where: 1: West approach in Beit-Wazan intersection
2: North approach in Beit-Wazan intersection
3: north approach in Deir-Sharaf intersection.
4: West approach in Deir-Sharaf intersection.
5: Approach C in AL-Ghawi intersection.
Future LOS’s for two lane highway links. |  |  |  |  | 
Link # | 1 | 2 | 3 | 4 | 5
LOS | E | B | C | C | E

## Slide 27: Data Analysis for links (MultiLane Rural Highway) current
Where:
1: East approach in Beit-Wazan intersection.
2: East approach in Deir-Sharaf intersection.
3: Approach A in AL-Quds intersection.
4: Approach B in AL-Quds intersection.
5: Approach C in AL-Quds intersection.
6: Approach D in AL-Ghawi intersection.
7: Approach A in AL-Ghawi intersection.
8: Approach B in AL-Ghawi intersection.
LOS’s for the current multilane highway links. |  |  |  |  |  |  |  | 
LINK # | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
LOS | B | A | B | B | C | A | A | B

## Slide 28: Data Analysis for links (MultiLane Rural Highway) current
Where:
1: East approach in Beit-Wazan intersection.
2: East approach in Deir-Sharaf intersection.
3: Approach A in AL-Quds intersection.
4: Approach B in AL-Quds intersection.
5: Approach C in AL-Quds intersection.
6: Approach D in AL-Ghawi intersection.
7: Approach A in AL-Ghawi intersection.
8: Approach B in AL-Ghawi intersection.
LOS’s for the current multilane highway links. |  |  |  |  |  |  |  | 
LINK # | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
LOS | B | A | B | B | C | A | A | B

## Slide 29: TRAFFIC SIGNAL WARRANT
A warrant is a set of criteria which can be used to define the relative need for a particular traffic control device (traffic signal, etc.).
In order to achieve the purpose to check the four intersections for
TRAFFIC SIGNAL WARRANT , PC WARRANT SOFTWARE was used .

## Slide 30
Warrant 1, Eight-Hour Vehicular Volume condition A,
check for Al-Ghawi intersection.obtained using PC WARRANT .

## Slide 31
Deir Sharaf | Beit Wazan | AlQuds | AlGhawi | 
Not | Not | Met | Met | Warrant 1, Eight-Hour Vehicular Volume
Not | Not | Met | Met | Warrant 2, Four-Hour Vehicular Volume
Not | Not | Met | Not | Warrant 3, Peak Hour

## Slide 32: DESIGN OF TRAFFIC SIGNALS

## Slide 33: Al Ghawi Intersection

## Slide 34: Phases for Al-Ghawi

## Slide 35: Phases for Al-Ghawi

## Slide 36: Sample Calculations
This table summarizes the volume, flow, saturation flow and Yi for every approach
Sum (Yi) = 0.53
volume | approach A | approach B | approach C | approach D
 | 517 | 209 | 808 | 141
qi | 575 | 233 | 898 | 157
S | 3700 | 3700 | 3700 | 3700
Yi | 0.1554 | 0.076 | 0.2427 | 0.0554

## Slide 37: calculations
E) Determine the optimum cycle length
Co = (1.5L+5)/(1-sumYi)
Where L is the total lost time in all phases (assume L=3.5sec/approach)
L = 4*3.5=14 sec
Co = (1.5*14+5)/ (1-0.567) = 55.35 sec
Then the optimum cycle length equal (60sec)

## Slide 38: calculations
F) Find yellow interval
Yellow interval = δ + (W+L/Uo) + (Uo/ (2(a+Gg))
Yellow interval =6 sec and take all red 1sec
So,
Total effective green time = Co-{L + R}
= 60-{14+4} = 42sec

## Slide 39: calculations
G) Actual green time for each phase
Actual green time for phase (A) = ((0.164/0.53)*42) + 3.5 -6 = 11 sec
Actual green time for phase (B) = ((0.098/0.53)*42) + 3.5 -6 = 5.6 sec take 6 sec
Actual green time for phase (C) = ((0.237/0.53)*42) + 3.5 -6 = 14 sec
Actual green time for phase (D) = ((0.068/0.53)*42) + 3.5 -6 = 3.1 sec take 6 sec as minimum actual green time equals to yellow time

## Slide 40: calculations
H) Calculations for pedestrian green time:
Gp=3.2+ (L/Sp) + {2.7*(Nped/WE)}…… for WE ≥ 10 ft
L = (4*3.6) +.5 =15m = 49 ft
WE = take 4 m = 13.12 ft
Nped = considered as min. (25)
Gp = 3.2+ (49/4) + {2.7*(25/13.12)}
Gp = 20 sec
So, consider 20 sec all-red interval for pedestrian.

## Slide 41: Results
Hand calculations results
Phase | A | B | C | D
Green Time (sec) | 11 | 6 | 17 | 6
Yellow Time (sec) | 6 | 6 | 6 | 6
All-Red Time (sec) | 1 | 1 | 1 | 1
Phase Time (sec) | 18 | 13 | 24 | 13

## Slide 42: SIDRA Results
The signal timing was designed by SIDRA program and the results were as follow:
Phase | A | B | C | D
Green Time (sec) | 12 | 6 | 18 | 6
Yellow Time (sec) | 6 | 6 | 6 | 6
All-Red Time (sec) | 1 | 1 | 1 | 1
Phase Time (sec) | 19 | 13 | 25 | 13

## Slide 43: Al Quds Intersection
Phase A

## Slide 44: Phases for Al Quds Intersection

## Slide 45: Results
Hand calculations results by applying the same previous equations
Phase | A | B | C
Green Time (sec) | 22 | 21 | 6
Yellow Time (sec) | 6 | 6 | 6
All-Red Time (sec) | 1 | 1 | 1
Phase Time (sec) | 29 | 28 | 13

## Slide 46: SIDRA Results
Phase | A | B | C
Green Time (sec) | 23 | 20 | 6
Yellow Time (sec) | 6 | 6 | 6
All-Red Time (sec) | 1 | 1 | 1
Phase Time (sec) | 30 | 27 | 13

## Slide 47: LOS for Al-Ghawi as signalized intersection.
Al-Ghawi |  |  |  | 
Approach D | Approach C | Approach B | Approach A | 
C | C | C | C | App. LOS
C |  |  |  | Intersection LOS

## Slide 48: LOS for Al-Quds intersection as signalized intersection.
Al-Quds |  |  |  | 
Approach D | Approach C | Approach B | Approach A | 
A | C | C | C | App. LOS
C |  |  |  | Intersection LOS

## Slide 49: CONCLUSIONS AND RECOMMENDATIONS

## Slide 50
The outcomes of this research could be as the followings.
1-Intersection at Deir-Sharaf: The LOS at this intersection is A, which means the high comfort for the users and the free flow speed is applied. This result could be justified since left turns were not exists. Besides, roundabout will eliminate the crossing conflict points.

## Slide 51
2-Intersectionat Al-Ghawi: The LOS at this intersection is B, which means slight decline in the freedom to maneuver with in the traffic stream, this could be justified since the intersection right turns were existed, besides adequate lane widths for all approaches. In addition; this will make crossing points to be eliminated

## Slide 52
3-Intersection at Beit-Wazan. The LOS at this interception B this is justified due to the low traffic volume from the north approach.
4-Al-Quds Intersection. The LOS F. This is due to a high volumes at all approaches. Queues were formed at all approaches. In addition the intersection angle is high. This make the vehicles from east approach to minimize their speed to turn right that decline the performance at that approach.

## Slide 53: Recommendations
A more detailed travel demand study is recommended, taking into account the future demand generation in the study area. The number of crashes mentioned in this study was collected from the surrounding inhabitance since no database for the next generations, in order to save time instead of review a written documents in the police department.

## Slide 54
The interaction between the transportation and environmental is not discussed
Traffic signal management (TSM) actions and measures may be locked for.

## Slide 55
For instance, remedial actions for Beit wazan intersection to enhance the LOS with available ROW and within standard may solve the problem or short-term solution may be considered.
Public involvement for searching a solution is recommended for such projects.

## Slide 56
Thank You