## Slide 1
جامعة النجاح الوطنية
كلية الهندسة
An-Najah National University
Faculty of Engineering
Civil Engineering Department
Graduation Project
Analysis and Design of Al-Assi Mall
Supervisor: Dr. Shaker Bitar.
Prepared by: Hala Bouzia
Mohammed Bayyari
Muzna Masri

## Slide 2: Outline
Introduction.
Preliminary design.
Three Dimensional structural analysis.
ETABS model checks.

## Slide 3: Introduction
Project description :
A commercial building located in Nablus , Palestine.
consist of ten floors with total area of 11313.82 m² .
The building will be assessed as a parking facility at the heart of the commercial center in Nablus.

## Slide 4: Architectural plan for Base Floor

## Slide 5: Architectural plan for Ground Floor

## Slide 6: Architectural plan for First Floor

## Slide 7: Architectural plan for Second to Seventh Floor

## Slide 8: Architectural plan for Eighth Floor

## Slide 9
Codes and Standards:
      ACI 318-14 (American concrete institute )
      ASCE 7-16 (American Society Of Civil Engineers )
      AASHTO (American Association of State Highway and Transportation )
Materials :
  Structural :
        Reinforcement steel
        Concrete
  Non Structural
Material | Density KN/m3
Fill | 16
Mortar | 23
Plaster | 23
Tile | 25

## Slide 10
Gravity loads :
      Live Load :
Parking (2.0 kN/m2) Shopping and restaurants (5.0 kN/m2) Stair(5.0 kN/m2)
      Super Impose Dead Load:
Parking(1.0 kN/m2) Shopping , restaurants & Stair (2.5 kN/m2)
      Slab Own Weight (8.75 kN/m2)

## Slide 11
Geometry design of Parking Garage
In our project we found that the parking doesn’t satisfy AASHTO specifications of :
1) Ramp slope 2) Ramp width 3) Turning circles
Some of criteria we used:
Ramp width
ramp width = 7.0m
Ramp slope
In AASHTO the maximum
allowable slope is about 16%
Ramp | Slope%
From ground | 15.9 & 10
From first (& all other ramps the same) | 15

## Slide 12: Plan before modification Plan after modification

## Slide 13
section for building before modification

## Slide 14
First ramp after modified
second ramp after modification
Computer programs:
ETAPS 2016 is used to analyze and design the structural elements (3D).
spSlab is used to analysis and design the slabs on the project.

## Slide 15: Equivalent frame method
The slab is divided into series of two-dimensional frames in each direction, positive and negative moments are computed by an elastic frame analysis. Then, these moments are divided between middle and column strips.

## Slide 16: To ensure if spSLAB software analyzed correctly we applied example 13.3 (DESIGNE OF CONCRETE STRUCTURES 14th edition in SI UNITS)
The maximum between the Example and spSLAB
=[(423.96-407)/423.96]*100%=4%

## Slide 18: Preliminary design.
Slab System
Two-way solid slab and flat plate
The ratio of the long span to the short span (L/B) =1.39 which is less than 2 so it’s preferable to design the slab as two way solid slab
11m
7.9m

## Slide 19: Slab thickness
In our structure the minimum thickness (t) equal to L/33
t=11/33=0.33m
So we used t=350mm
Preliminary design.

## Slide 20: Check slab for Punching
Slab thickness t=350mm , d=310mm
𝐼 𝑐𝑖𝑟𝑐𝑢𝑙𝑎𝑟 = 𝐼 𝑠𝑞𝑢𝑎𝑟𝑒
Л(𝐷^4)/64=1/12∗ 𝑏 ∗ ℎ
b =h= 1.051 mm
Tributary area=(7.4/2)+(11/2)∗ 7.9 = 72.68𝑚
𝑊𝑢 = (0.35 ∗ 25 + 1) ∗ 1.2 + (2 ∗ 1.6) = 14.9KN/m^2
𝑃𝑢 = (72.68∗14.9)-14.9(1.05+0.31)^2= 1055.3𝐾𝑁
𝑃𝑛 =1055.3/0.75=1407.06𝐾𝑁
𝑏0 = (1051 + 310)∗4=5444𝑚𝑚, 𝑑=310𝑚𝑚, 𝛼=40, 𝐵=1
𝑣𝑐𝑝1=[0.17(1+1/2)∗(28^0.5)∗5444∗310]/1000=2277.18𝐾𝑁
𝑣𝑐𝑝2=[0.083∗({40∗310/5444}+2)∗(28^0.5)∗5444∗310]/1000=3170.66𝐾𝑁
𝑣𝑐𝑝3=[0.33∗(28^0.5)∗5444∗310]/1000=2976.71𝐾𝑁
Minimum 𝑣𝑐𝑝=2277.18𝐾𝑁 > 𝑃𝑛 =1407.06𝐾𝑁 …… OK
Preliminary design.

## Slide 21: Beam dimensions
Beam thickness (h):
We chose the critical beam span length which is 11m
h=11/21=0.52m
We used h=550mm
Beam width:
Minimum allowable width=200mm …. Try 300mm
Preliminary design.

## Slide 22: Columns
The slenderness for columns is calculated as shown below:
Assume Sway …….. KL/R <22
K=1, L= 5.1, r = 0.25D, D=1.2m
KL/R=17 < 22 ……so we have short column
Columns dimensions:
12666.104*10^3=0.75*0.85[0.85*28(Ag-0.02Ag)+420*0.02Ag]
Ag=6262814.05mm…..so Dmin=892.9 mm
So we take in this part of project diameter as it come from architectural drawing=1200 mm
Preliminary design.

## Slide 23
Three Dimensional structural analysis

## Slide 24
Input data of the Models.
  Material:
f′𝑐= 28MPa for columns & shear walls.
f′𝑐= 24MPa for beams & reinforced slabs.
  The modifiers of Columns, Beams, Slab and Shear wall are shown in table:
  But, Torsion modifiers are too small 𝑴𝟏𝟐 = 𝟎. 𝟎𝟎𝟏 No need for torsional reinforcement.
Section | Modifiers
Column | 0.7
Beam | 0.35
Slab | 0.35
Shear wall | 0.7

## Slide 25
Sections on ETABS:

## Slide 27: Loads on ETABS:
Load Cases:
Live load:
-Parking ………… (2.0 kN/m2)
- Shopping and restaurants ………… (5.0 kN/m2)
- Stair………… (5.0 kN/m2)

## Slide 28: Superimposed dead load:
-Parking ………… (1.0 kN/m2)
- Shopping and restaurants ………… (2.5 kN/m2)
- Stair………… (2.5 kN/m2)

## Slide 29: ETABS model checks
Drawing structural model
Compatibility
External equilibrium
Stress Strain Check
Slab deflection

## Slide 30: Drawing structural model

## Slide 31: Compatibility
As shown in period = 0.938 which is Acceptable

## Slide 32: External equilibrium
Hand calculation
Dead loads = 143900.1644 kN
Live loads = 32944.64869 Kn
2. Etabs values:
= Acceptable
= Acceptable

## Slide 33: Stress Strain Check.
For interior span in EF frame in X-direction:
E
F

## Slide 34: For moment values from spSLAB :

## Slide 35: Slab deflection

## Slide 36
max 𝑑𝑒𝑓𝑙𝑒𝑐𝑡𝑖𝑜𝑛 = 7.9 ∗ 1000 /240 = 32.917mm
32.687 < 32.917mm
8.596 < 32.917mm

## Slide 37: CONCLUSION
As a result of this stage of project:
1.we modified this building and make a proper design for its parking garage.
2. make preliminary design for building.
3. prepare this building for second stage.
In the stage #2 of this project we will:
1. Design this building to gravity and seismic loads.
2. design the most suitable footing for this building.

## Slide 38
Thank You All
for your attention