## Slide 1: Integrated Re-design of the Faculty of Economics at Palestine Technical University
An-Najah National university
Faculty Of Engineering
Building Engineering Department
Supervisor :
Dr. Monther Dwaikat
Prepared by :
Nirmeen Mhanna
Nour Salahat
Seema Bolas

## Slide 2: OUTLINES
Introduction
Site description
Architectural design
Environmental design
Structural design
Mechanical design
Electrical design
Cost estimation

## Slide 3: Introduction
Integrated Re-design of the Faculty of Economics at Palestine Technical University.
Statistics at Palestine Technical University indicate that the number of students enrolled in the Faculty of Economics has been increasing in recent years.
Total number of students is 1800 ( 2019/2020).
Total number of employees is 70 .

## Slide 4: Site Description
Located to the west of Tulkarm.
Total area of the site is 5606 m².
It is surrounded by the university’s library and Tulkarm Industrial Secondary School .
The faculty is reached by two roads each has an entrance leading inside, the first road has a width of 12 m, and the second has a width of 9m.

## Slide 5: Architectural Design
The 3rd model for the existed architectural plan.

## Slide 6: Project Description
Five stories with total area of 10130 m² .
First floor
area
1621.5 m²
second floor area
1775.6 m²
Third floor area
1775.6 m²
Ground floor area
2405.3 m²
Basement
2411.7 m²

## Slide 7: Project Description
Area (m²) | Spaces
57.6 | Classroom
20.2 | Office has three employees
11.6 | Office has two employees
61.5 | Computer lab
58.8 | Meeting room
452.4 | Auditorium
120.8 | Cafeteria
Spaces area

## Slide 8: Architectural Modifications
Basement floor
Before
After

## Slide 9: Architectural Modifications
Emergency stairs
Before
After

## Slide 10: Architectural Modifications
Covering area for students
Before
After

## Slide 11: Architectural Modifications
Doors orientation and furniture layout
Before
After

## Slide 12: Architectural Modifications
Shaft dimension
Before
After

## Slide 13: Architectural Plans
Basement floor plan

## Slide 14
Ground floor plan

## Slide 15
First floor plan

## Slide 16
Second floor

## Slide 17
Third floor

## Slide 18: Elevations
South-east
North-east

## Slide 19: Elevations
North-west
South-west

## Slide 20: Sections
Section B-B
Section 1-1

## Slide 21: Environmental design
Material properties
Thermal behavior
Ventilation
Daylighting
shading

## Slide 22
Material properties
U – value for glass equals 1.8 w/m2.k
U – value
0.438 w/m2.k
External wall
Internal wall
U – value
1.61 w/m2.k

## Slide 23
Thermal comfort Analysis
Relative humidity
42 %
Temperature
23 C
Pierce PMV
(-3 to +3)

## Slide 24: Thermal Analysis
Total design heating capacity = 186 kW
Total design cooling capacity = 205 kW
Number of uncomfortable hour = 472.5 hour/year .

## Slide 25
Daylight analysis for the model for the ground floor before and after modification
Before
After

## Slide 26: Ventilation
Natural ventilation is obtained through court yard truss system.

## Slide 27: Shading
Horizontal and vertical louvers were added to windows and curtains of the southeastern and southwestern facades for the decreasing process of solar gain through glass.

## Slide 28: Structural Design
Material properties
Verification checks
Seismic checks
Design and detailing
Codes

## Slide 29: Structural Design
Codes
IBC 2014
ACI 318M-14
AISC-16
Material Properties
Reinforced Concrete
Property | Value
Compressive strength fʹc | 24 MPa
Modulus of elasticity E | 23025
Poisson’s ratio U | 0.2

## Slide 30
Reinforcing Steel
Structural Steel
Property | Value
Grade | Grade 60
Modulus of elasticity | 200 GPa
Yielding strength | 420 MPa
Ultimate strength | 620 MPa
Property | Value
Grade | Grade 50
Modulus of elasticity | 200 GPa
Yielding strength | 340 MPa
Ultimate strength | 450 MPa
Load | Value
Live load 1 | 5 kN/m²
Live load 2 | 3 kN/m²
Live load 3 | 1 kN/m²
Super imposed dead load 1,2 | 5 kN/m²
Super imposed dead load 3 | 0.1 kN/m²
Snow load | 0.15 kN/m²
Wind load | 1 kN/m²
Designed Loads

## Slide 31
Earth quick load
Short period spectral acceleration ( Ss) = 0.45
one second period spectral acceleration ( S1) = 0.09
Soli profile: Stiff soil with site classification D
Site coefficient Fa = 1.44
Site coefficient Fv = 2.4
Structural system block 1 : Special reinforced concrete shear walls (R = 6)
Structural system block 2 : Special reinforced concrete moment frames (R = 8)

## Slide 32
Structural blocks

## Slide 33
Verifications checks
Compatibility check
Equilibrium check
Internal Forces check
Deflection check
Block 2
Block 1

## Slide 34
Seismic load checks
Mass participation ratio for modal analysis check
Base shear for response spectrum analysis check
Load case | EQ res1 | EQ eq 1 | EQ eq /EQ res | New scale factor | EQ res2 | EQ eq 2 | Difference
Vx | 7509.9773 | 8087.1576 | 1.077 | 2736.58 | 7917.4 | 7178.5079 | 0.02
Vy | 8039.4138 | 7908.6191 | 0.984 | 2500.27512 | 8081.8527 | 7178.5096 | 2.00E-07
Load case | EQ res1 | EQ eq 1 | EQ eq /EQ res | New scale factor | EQ res2 | EQ eq 2 | Difference
Vx | 132.9473 | 445.307 | 3.35 | 5134.91 | 445.307 | 445.373 | 0.2
Vy | 563.4189 | 553.795 | 0.983 | 1506.742 | 553.795 | 553.654 | 2.00E-01

## Slide 35
Seismic load checks
Drift check
Story | Direction | Design elastic story drifts | Design inelastic story drifts | Allowable story drift | Check
Story6 | X | 0.000154 | 0.000616 | 0.015 | Ok
Story6 | Y | 0.000818 | 0.003272 | 0.015 | Ok
Story5 | X | 0.000621 | 0.002484 | 0.015 | Ok
Story5 | Y | 0.002541 | 0.010164 | 0.015 | Ok
Story4 | X | 0.000806 | 0.003224 | 0.015 | Ok
Story4 | Y | 0.001842 | 0.007368 | 0.015 | Ok
Story3 | X | 0.00092 | 0.00368 | 0.015 | Ok
Story3 | Y | 0.001481 | 0.005924 | 0.015 | Ok
Story2 | X | 0.00102 | 0.00408 | 0.015 | Ok
Story2 | Y | 0.001506 | 0.006024 | 0.015 | Ok
Story1 | X | 0.0011974 | 0.0047896 | 0.015 | Ok
Story1 | Y | 0.0012445 | 0.004978 | 0.015 | Ok
Story6 | Y | 0.003573 | 0.014292 | 0.015 | Ok
Story5 | X | 0.00057 | 0.00228 | 0.015 | Ok
Story5 | Y | 0.001243 | 0.004972 | 0.015 | Ok
Story4 | X | 0.000746 | 0.002984 | 0.015 | Ok
Story4 | Y | 0.001675 | 0.0067 | 0.015 | Ok
Story3 | X | 0.000847 | 0.003388 | 0.015 | Ok
Story3 | Y | 0.002014 | 0.008056 | 0.015 | Ok
Story2 | X | 0.000863 | 0.003452 | 0.015 | Ok
Story2 | Y | 0.001904 | 0.007616 | 0.015 | Ok
Story1 | X | 0.0012366 | 0.0049464 | 0.015 | Ok
Story1 | Y | 0.0011192 | 0.0044768 | 0.015 | Ok
Story | Direction | Elastic story drifts | Inelastic story drifts | Allowable story drift | Check
Story1 | X | 0.00318 | 0.014 | 0.015 | Ok
Story1 | Y | 0.00034 | 0.0015 | 0.015 | Ok

## Slide 36
Seismic load checks
P- Delta check
Base | Service envelope
Vx | 7084.634
p | 230913.7
Δ elastic | 9.145
Δ Inelastic | 36.58
h | 4000
cd | 5
I | 1.25
θ | 0.0745 < 0.1
 | 1
θmax | 0.1
Base | Service envelope
Vx | 7084.634
p | 230913.7
Δ elastic | 9.145
Δ Inelastic | 36.58
h | 4000
cd | 5
I | 1.25
θ | 0.0745 < 0.1
 | 1
θmax | 0.1
Base | Service envelope
Vx | 312.34
p | 10898.59
Δ elastic | 19.75
Δ Inelastic | 86.89
h | 8230
cd | 5.5
I | 1.25
θ | 0.090 < 0.1
 | 1
θmax | 0.091
Base | Service envelope
Vx | 312.34
p | 10898.59
Δ elastic | 19.75
Δ Inelastic | 86.89
h | 8230
cd | 5.5
I | 1.25
θ | 0.090 < 0.1
 | 1
θmax | 0.091
Block 1
Block 2
Story | Direction | Delta-Max | Delta-Min | Max/Avg
1 | x | 0.836 | 0.795 | 1.025
2 | x | 3.089 | 3.08 | 1.001
3 | x | 6.09 | 6.06 | 1.002
4 | x | 9.571 | 9.491 | 1.004
5 | x | 13.105 | 13.041 | 1.002
6 | x | 10.779 | 10.646 | 1.006
1 | y | 0.904 | 0.647 | 1.166
2 | y | 4.831 | 3.489 | 1.161
3 | y | 10.105 | 7.343 | 1.158
4 | y | 15.985 | 11.492 | 1.164
5 | y | 21.773 | 16.245 | 1.145
6 | y | 33.427 | 19.34 | 1.267

## Slide 37
Slabs systems
Block 2 – Solid slab 20 cm – Drop beams
Block 1 – Two-way ribbed slab 40 cm – Drop beams

## Slide 38
Two-way ribbed slab section
Solid slab section

## Slide 39
Beams Design

## Slide 40
Columns Design
Column | Rebar % | Width | Depth | As used | Middle | Corner | S1 | S2
 |  | mm | mm | mm² | bars | bars | cm | cm
C1 | 1.66% | 400 | 800 | 5316 | 18Ø18 | 4Ø18 | 9 | 7
C2 | 1.00% | 400 | 800 | 3200 | 18Ø14 | 4Ø14 | 14 | 10
C3 | 3.85% | 400 | 1000 | 15412 | 18Ø32 | 4Ø25 | 12 | 6
C4 | 2.25% | 400 | 1000 | 9017 | 22Ø20 | 4Ø32 | 8 | 10
C5 | 1.00% | 400 | 1000 | 4000 | 22Ø14 | 4Ø14 | 9 | 7
C6 | 2.15% | 400 | 800 | 6892 | 18Ø20 | 4Ø20 | 8 | 7
C7 | 1.75% | 300 | 800 | 4196 | 18Ø16 | 4Ø16 | 19 | 5
C8 | 2.62% | 500 | 1000 | 13117 | 24Ø25 | 4Ø25 | 8 | 7
Column | Rebar % | Width | Depth | As used | Middle | Corner | S1 | S2
 |  | mm | mm | mm² | bars | bars | cm | cm
C9 | 1.00% | 400 | 1500 | 6000 | 26Ø16 | 4Ø16 | 9 | 9
C10 | 1.26% | 400 | 1500 | 6367 | 24Ø18 | 4Ø18 | 14 | 9
C11 | 1.06% | 400 | 1500 | 7554 | 28Ø18 | 4Ø18 | 14 | 9
Longitudinal reinforcement steel design

## Slide 41
Columns Design
Column | Width | Depth | bc1 | bc2 | Ash1 | Ø used | No. | Ash2 | Ø used | No. | So | S1 | Lo
 | mm | mm | mm | mm | mm² | mm | bars | mm² | mm | bars | mm | mm | mm
C1 | 400 | 800 | 320 | 720 | 213.3 | 12 | 2 | 480 | 12 | 5 | 100 | 100 | 800
C2 | 400 | 800 | 320 | 720 | 213.3 | 12 | 2 | 480 | 12 | 5 | 100 | 100 | 800
C3 | 400 | 1000 | 320 | 920 | 196.8 | 12 | 2 | 565.7 | 12 | 6 | 100 | 150 | 1000
C4 | 400 | 1000 | 320 | 920 | 196.8 | 12 | 2 | 565.7 | 12 | 6 | 100 | 120 | 1000
C5 | 400 | 1000 | 320 | 920 | 196.8 | 12 | 2 | 565.7 | 12 | 6 | 100 | 100 | 1000
C6 | 400 | 800 | 320 | 720 | 213.3 | 12 | 2 | 480 | 12 | 5 | 100 | 120 | 800
C7 | 300 | 800 | 220 | 720 | 194.3 | 12 | 2 | 635.8 | 12 | 6 | 100 | 100 | 800
C8 | 500 | 1000 | 420 | 920 | 216 | 12 | 2 | 473.1 | 12 | 5 | 100 | 150 | 1000
Column | Width | Depth | bc1 | bc2 | Ash1 | Ø used | No. | Ash2 | Ø used | No. | So | S1 | Lo
 | mm | mm | mm | mm | mm² | mm | bars | mm² | mm | bars | mm | mm | mm
C9 | 400 | 1500 | 320 | 1420 | 175.8 | 12 | 2 | 780 | 12 | 7 | 100 | 100 | 1500
C10 | 400 | 1500 | 320 | 1420 | 175.8 | 12 | 2 | 780 | 12 | 7 | 100 | 100 | 1500
C11 | 400 | 1500 | 320 | 1420 | 176 | 12 | 2 | 780 | 12 | 7 | 100 | 100 | 1500
Transverse reinforcement steel design

## Slide 42
Shear wall Design
S.W | Length mm | Thickness mm | Reinforcement | S mm
SW1 | 2000 | 300 | 2Ø10/200mm | 200
SW2 | 2900 | 300 | 2Ø10/200mm | 200
SW3 | 3500 | 300 | 2Ø10/200mm | 200
SW4 | 5900 | 300 | 2Ø10/200mm | 200
SW5 | 2880 | 300 | 2Ø10/200mm | 200
SW6 | 4820 | 310 | 2Ø10/200mm | 200
SW7 | 1280 | 150 | 2Ø10/400mm | 400
SW8 | 4300 | 300 | 2Ø10/200mm | 200
SW9 | 6900 | 300 | 2Ø10/200mm | 200
SW10 | 2850 | 300 | 2Ø10/200mm | 200
SW11 | 4250 | 300 | 2Ø10/200mm | 200
S.W | Length mm | Thickness mm | Ø used mm | No.bars each side | S mm
SW1 | 2000 | 300 | 14 | 11 | 180
SW2 | 2900 | 300 | 16 | 15 | 190
SW3 | 3500 | 300 | 12 | 20 | 150
SW4 | 5900 | 300 | 14 | 30 | 190
SW5 | 2880 | 300 | 14 | 15 | 190
SW6 | 4820 | 310 | 14 | 25 | 190
SW7 | 1280 | 150 | 12 | 11 | 190
SW8 | 4300 | 300 | 14 | 18 | 200
SW9 | 6900 | 300 | 14 | 30 | 200
SW10 | 2850 | 300 | 14 | 16 | 200
SW11 | 4250 | 300 | 10 | 21 | 200
B.E | Width mm | Depth mm | Ash1 | Ash2
BE1 | 300 | 280 | 3Ø12 | 2Ø12
BE2 | 300 | 460 | 2Ø12 | 3Ø12
BE3 | 300 | 390 | 2Ø12 | 3Ø12
BE4 | 300 | 760 | 2Ø12 | 4Ø12
BE5 | 300 | 382 | 2Ø12 | 3Ø12
BE6 | 310 | 618 | 2Ø12 | 4Ø12
BE7 | 150 | 292 | 2Ø12 | 4Ø12
BE8 | 300 | 470 | 2Ø12 | 3Ø12
BE9 | 300 | 790 | 2Ø12 | 4Ø12
BE10 | 300 | 395 | 2Ø12 | 3Ø12
BE11 | 250 | 390 | 2Ø12 | 3Ø12
Transverse reinforcement
Longitudinal reinforcement
Boundary Element T. reinforcement

## Slide 43
Footing Design
50 cm matt foundation
100 cm matt foundation

## Slide 44
Steel Design
Group | Section (mm)
Top cord | TUBO 80×80×8
Bottom cord | TUBO 80×80×8
Vertical | TUBO 80×80×8
Diagonal | TUBO 80×80×8
Lateral | TUBO 80×80×8
Bracing | UPN-80
Purlin | UPN-80

## Slide 45
Connection Design

## Slide 46
Top chord – Bracing Connection
Connection 5 detailing
Connection Design

## Slide 47
Splice connection
Connection Design

## Slide 48
Connection Design
Connection between Bracings

## Slide 49
Retaining wall Design
Side | Moment | Rebar | As | 0.5 As min | As used | Ø | No. bars
 | kN.m | percentage | mm²/m | mm²/m | mm²/m | mm | 
Vertical left | 58 | 0.000958 | 393 | 375 | 393 | 12 | 4
Vertical right | 60.4 | 0.001 | 410 | 375 | 410 | 12 | 4
Side | Moment | Rebar | As | As min | As used | Ø | No. bars
 | kN.m | percentage | mm²/m | mm²/m | mm²/m | mm | 
Top | 69.73 | 0.001956 | 606.3 | 720 | 720 | 14 | 5
Bottom | 40.3 | 0.00113 | 350.41 | 375 | 720 | 14 | 5
Retaining wall’s base steel reinforcement for top and bottom
Vertical reinforcement for basement retaining wall

## Slide 50
Stairs Design
External stair detailing

## Slide 51: Mechanical design
Water system
Drainage system
HVAC system
Fire Fighting

## Slide 52: Water system
Roof water tank capacity =170 m3.
Diameter Of Pipes
Vertical | Horizontal | Branch
2.5 '' | 2'' | 0.75''

## Slide 53: Drainage system

## Slide 54: Drainage system
Rain water drainage

## Slide 55
Out door unit
Samsung VRF DVM S
Daikin FIXN_K (E) VJU - Wall mounted split unit
Daikin FCQ PVJU - Cassette unit
Total cooling load = 205.72 kW
Three out door units with a capacity of 72.8 kW for each unit
Indoor unit – wall mounted with air flow of 473 CFM
Indoor unit – cassette unit with air flow of 390 CFM
HVAC system ( VRF )

## Slide 56: Distribution of exhaust ducts for the ground floor

## Slide 57: Distribution of exhaust ducts for the first floor

## Slide 58: Distribution of indoor supply and piping system for the first floor

## Slide 59: Fire Fighting

## Slide 60: Emergency Exits

## Slide 61: Electrical design
Socket distribution
Artificial lighting
Load speakers

## Slide 62: Electrical design Socket distribution

## Slide 63: Electrical design Artificial lighting
Class room
Computer lap
Lux | Required Lux | UGR | Required UGR | Uniformity | Required uniformity
508 | 500 | 16.8 | 19 | 0.62 | 0.6
Lux | Required Lux | UGR | Required UGR | Uniformity | Required uniformity
508 | 500 | 17.9 | 19 | 0.61 | 0.6

## Slide 64: Light and switch distribution

## Slide 65: Main distribution board

## Slide 66: Acoustical Design
Auditorium
Cafeteria
Classroom
Corridor
Designed spaces:
Massing, shape and arrangement of seating
Assumptions

## Slide 67
RT 60 (s) | SPL (dB) | STI | Alcons | NC (dB) | STC (dB) | C50
1.4-1.8 | > 85 | >= 0.6 | < 10% | 35-40 | 42-45 | >-5
RT -60 Results
H 1315 WP
Reinforcement system
Design standards

## Slide 68
Distribution of values for articulation loss
Distribution of values for STI
Total STC
Distribution of values for direct SPL
Distribution of values for C50

## Slide 69: Reflected ceiling for ground floor

## Slide 70: Quantity surveying and cost estimation
1. Total project cost is ILS 18,294,150
2. Unit cost for project ILS 1810 per m²
3. Unit cost for structural work ILS 1660 per m²
4. Unit cost for mechanical work ILS 77 per m²
5. Unit cost for electrical work ILS 72 per m²

## Slide 71
Chart: Percentage of works cost from total cost
| Sub-Structure | Super-Structure | Finishes | Mechanical work | Electrical work
Sales | 16 | 30 | 46 | 4 | 4