## Slide 1: Redesign of Residential and Commercial building
Graduation Project 2
Prepared By:
Ali Mahamdeh
Amr Sama’neh
Anas Suheil
Mohammad Kharouf
Supervised by: Eng. Fadi Fatayer
Building Engineering Department

## Slide 2: Outline:
Introduction
Structural Design
Quantity Surveying and Cost Estimation
Environmental Design
Mechanical Design
Electrical Design
Architectural Redesign
Safety Design

## Slide 3: Introduction:
Multi-functional building in general ( commercial and residential) is an example of the integrated design that use different functions to achieve the economic benefits in its own region as well as to exploit the street categories in the right case as mentioned by the local municipality .
However, multi-functional buildings are considered to be one of the vast and vital projects that spread worldwide in globe in general and in Palestine in particular since human beings need that type to express their needs and to provide a safe place where inhabitants can exercise their socio-cultural activities.

## Slide 4: Site location:
Location: Nablus City, Rafidya street behind of Amaken Restaurant

## Slide 5: Site location:
The slope of land can be handled.
Has a quiet surrounding environment.
Site Advantages :

## Slide 6: Architectural Re-Design

## Slide 7: Architectural Redesign:
Old design layout:

## Slide 8: Architectural Redesign:
Old design elevation:

## Slide 9: Architectural Redesign:
Modifications:
Rearranging the locations of kitchens, living room, dinning, and guest rooms in compatible of ventilation, lighting, and the ease of access.
Making architectural changes in the shape of building to obtain the privacy between the three apartments.

## Slide 10: Architectural Redesign:
Modifications:
Changing the locations of bathrooms in order to decrease the amount of ventilation-voids
Removing the backfill soil, thus allowing for more space for cars.
Enlarge sizes for certain stores

## Slide 11: Architectural Redesign:
Site plan:

## Slide 12: Architectural Redesign:
Ground Floor Area = 480 m2.

## Slide 13: Architectural Redesign:
First Floor Area = 520 m2.

## Slide 14: Architectural Redesign:
Basement Floor Area = 500 m2.

## Slide 15: Architectural Redesign:
Elevation:

## Slide 16: Architectural Redesign:
Elevation:

## Slide 17: Architectural Redesign:
Section:

## Slide 18: Architectural Redesign:
Final design photos:

## Slide 19: Architectural Redesign:
Final design photos:

## Slide 20: Architectural Redesign:
Final design photos:

## Slide 21: Architectural Redesign:
Video

## Slide 22: Architectural Redesign:
Video:

## Slide 23: Structural Design

## Slide 24: Structural Design:
Design Codes:
ACI -318-08 (American Concrete Institution) for reinforced concrete structural design.
UBC-97 (Uniform Building Code) for earthquake load computations.
ASCE (American Society Of Civil Engineers) for design loads.

## Slide 25: Structural Design:
Materials:
Material | Density KN/m3
Reinforced concrete | 25
Concrete Hollow Block | 12
Masonry stones | 27
Polystyrene | 0.3
Mortar | 26
Glass | 2.3

## Slide 26: Structural Design:
Types of loads:
Type of load | Load KN/m2
Live load For Apartments Live load For Storages | 3 KN/m2 5 KN/m2
Super imposed dead load | 4 KN/m2
Exterior walls | 21 KN/m
Combined Glazed walls with stone | 7 KN/m

## Slide 27: Structural Design:
Structural System:
Ribbed slab system.
The system of the slab is one way ribbed slab(30 cm thickness) with Hidden beams.

## Slide 28: Structural Design:
Sap model:

## Slide 29: Structural Design:
Model validation:
Compatibility check

## Slide 30: Structural Design:
Deflection check:

## Slide 31: Structural Design:
Equilibrium check:
Load | Manual | Sap | Error
Dead load | 25238.8 KN | 25613 KN | 1.46 %
Live load | 3710 KN | 3820.2 KN | 2.88 %
Internal forces check
Element | Manual | Sap | Error
Slab | 35.4 KN.m/m | 36.65 KN.m/m | 3.41 %
Beam | 157.16 KN.m | 163.10 KN.m | 3.64 %
Column 7 | 2058 KN | 2176.959 KN | 5.00 %

## Slide 32: Structural Design:
Dynamic Analysis
Weight of the building = dead load + 0.25 live load = 65106.55+ 0.25 *9960.6 = 67596.7 KN.
Base shear (V)=

## Slide 33: Structural Design:
Slab Reinforcement

## Slide 34: Structural Design:
Beam Layout

## Slide 35: Structural Design:
Beam Reinforcement

## Slide 36: Structural Design:
Bracket Beam Reinforcement

## Slide 37: Structural Design:
Column Reinforcement

## Slide 38: Structural Design:
Shear wall Reinforcement

## Slide 39: Structural Design:
Stairs Reinforcement

## Slide 40: Structural Design:
Footing layout

## Slide 41: Structural Design:
Footing Reinforcement

## Slide 42: Structural Design:
Earthquake Requirements
Angel Shear wall at the corner of building.
Bracket beam at cantilever to reduce potential risk for cantilever

## Slide 43: Structural Design:
Bracket Beam Reinforcement

## Slide 44: Structural Design:
Reinforcement around window

## Slide 45
Environmental Design

## Slide 46: Environmental Design:
Wind analysis:

## Slide 47: Environmental Design:
Solar analysis:
Summer day

## Slide 48: Environmental Design:
Solar analysis:
Winter day

## Slide 49: Environmental Design:
Solar Shading:
The southern elevation was considered to be the most critical one because it is fully exposed to solar with large glassing windows which affected the results of solar gaining along the whole .

## Slide 50: Environmental Design:
Solar Shading:
As shown in the last figure, the sun is concentrated on the southern elevation at the afternoon hours where is the highest peak for sun at summer. So the heating gain is huge.
Solution:
Using vertical louvers with depth 1m to block sun exposure, in order to reduce heat gain and side fines with depth 1m
Used material:
Windows are double glassing with 20% e and 6mm argon gas
Glassing doors with 70% visibility

## Slide 51: Environmental Design:
Solar Shading:

## Slide 52: Environmental Design:
Thermal Insulation:
The goal: The achieved thermal coefficient U for all new and air-conditioned buildings should be not more than the U-value of the specified code
 | Highest Value for U | Outer structural elements of the building |  | Number | 
 | 0.5 | The External wall |  | I-1 | 
 | 0.39 | Exposed horizontal roof |  | I-2 | 
 | 0.39 | Exposed leaning roof |  | I-3 | 

## Slide 53: Environmental Design:
Thermal Insulation:
Exterior wall
 |  | R | K | Thickness (m) | Material Name |  | 
 |  | 0.31 |  |  | Inside |  | 
 |  | 0.019 | 2.6 | 0.05 | Stone |  | 
 |  | 0.054 | 1.85 | 0.1 | concrete |  | 
 |  | 2.27 | 0.022 | 0.05 | insulation |  | 
 |  | 0.24 | --- | 0.1 | Block |  | 
 |  | 0.014 | 1.4 | 0.02 | Plaster |  | 
 |  | 0.05 |  |  | External |  | 
 |  | 2.957 | Total |  |  |  | 
U = = 0.338 (W/(m.))< 0.50

## Slide 54: Environmental Design:
Thermal Insulation:
Ceiling
U = = 0.32 (W/(m.))< 0.390

## Slide 55: Environmental Design:
Acoustical Design:
One goal of acoustical engineering can be the reduction of unwanted noise, which is referred to as noise control. Unwanted noise cane have significant impacts on human health and well-being
According to specifications of residential apartments the required RT60 is ( 0.6 – 0.8 ) sec
The calculation was taken for the bed room:
RT60=0.61 sec

## Slide 56: Environmental Design:
Acoustical Design:
STC Calculations:
For inner wall ( between the kitchen and bedroom ):
Required STC 55
Final STC after modification 58
Previous design: 100mm lightweight hollow block + plaster on both sides = 36+4 = 40dB
Current design: 150mm dense hollow block + plaster resilient on both sides = 43+15 = 58dB

## Slide 57: Environmental Design:
Heating and cooling:
The results of total zone heating and total cooling loads for the five- story building were 65KW/m2 which is between 30-80KW/m2 as shown below.

## Slide 58: Environmental Design:
Daylight factor:
For example the average daylight for the living room and kitchen was 2.59% with uniformity 0.6 and 233 Lux

## Slide 59
Mechanical Design

## Slide 60: Mechanical Design:
HVAC system
VRF : variable refrigerator flow
Design capacity Cooling (KW) | Design capacity Heating (KW) | Floor
25.91 | 15.28 | 1

## Slide 61: Mechanical Design:
HVAC system
Duct sizing

## Slide 62: Mechanical Design:
Water supply

## Slide 63: Mechanical Design:
Water drainage

## Slide 64: Mechanical Design:
Basement Floor drainage system

## Slide 65: Mechanical Design:
Tank installation with Solar Panel

## Slide 66: Mechanical Design:
Roof Slope:

## Slide 67
Electrical Design

## Slide 68: Electrical Design:
Artificial lighting for bedroom
Lamp used: PHILIPS 332TSW 2*TL-5 24W
Power: 2*24 watt
Luminous flux: 3045 lm
Correction factor: 0.58
Lighting level: 300 lux
Suspension Height: 0 m

## Slide 69: Electrical Design:
Artificial lighting for bedroom
Fixtures distribution & results:
Number of units: 2
Center distance: 1.9 m
Side Distance: 0.86 m

## Slide 70: Electrical Design:
Artificial lighting for bedroom

## Slide 71: Electrical Design:
Artificial lighting for kitchen and living room
Fixtures distribution & results:
Number of units: 4
Center distance: 1.5 m
Side Distance: 1.46 m

## Slide 72: Electrical Design:
Artificial lighting for Guest room
Fixtures distribution & results:
Number of units: 2
Center distance: 1.5 m
Side Distance: 1.2 m

## Slide 73
Safety Design

## Slide 74: Safety Design:
Fire system
Hose station Fire system

## Slide 75: Safety Design:
Flame detector
Flame detector in the Kitchen

## Slide 76: Safety Design:
Fire System at parking

## Slide 77
Quantity surveying and cost estimation:
The total cost of Project is about 3851046 NIS .
The total cost per meter square of project is about 270 JD / m2