## Slide 1
BRAILLE PRINTER
SUPERVISOR Dr.
Nidal Farahat

## Slide 2: Outline…
Introduction
Objectives
Mechanical & Electrical components
Control system
Protection
Methodology
Cost
Future work
Conclusion

## Slide 3: Introduction
In our project we look at the reality of life and search for the most marginalized groups which need serious attitudes to help them .
We found that the more groups that deserve assistance are a class of blindness

## Slide 4: So we worked hard to develop a printer which prints braille alphabets with High-tech and low cost than those in the world market.

## Slide 5: Overview of Braille language
Each character is presents by six points, three on the right and three on the left

## Slide 6: OBJECTIVES
Help blind people to learn by offering enough amounts of Braille books.
Reduce time and cost for blind people to get a book written in Braille language.
Increase the efficiency of performance in blind’s schools.
Make printing very effective process using computer and flash memory.

## Slide 7: MECHANICAL & ELECTRICAL COMPONENTS
Housing and paper feeder
The cover of our project is
designed to like the modern
printer.
Housing contains USB ports
,screen, paper feeder

## Slide 8
RODS
Four rods are used two to support the solenoid, and the other to connected with rollers to allow passing paper through printing.

## Slide 9
GEARS
Five spur gears are used to transfer the motion of DC motor to rod that used for pull the paper.

## Slide 10
BELTS
One toothed belt is used to move the solenoid left and right (in the horizontal direction) when receives data from stepper motor.

## Slide 11
Universal Serial Bus (USB)
In this project any USB can be used, because Raspberry Pi contains a USB hub which make it easy to recognize the files inserted by user.

## Slide 12
SENSORS
We used the sender and receiver sensor (TCRT 5000) that will give an output when there is no paper in the feeder.

## Slide 13: One stepper motor of type (Bipolar) is used to move the solenoid horizontally while printing, and one DC motor is used to passing the paper.
DC MOTOR
STEPPER MOTOR
STEPPER AND DC MOTORS

## Slide 14
SOLENOID
In our project we used a Solenoid with relay carried by a stainless steel rods.
We choose the electrical Solenoid with the needle that make the required hole in the paper

## Slide 15: CONTROL SYSTEM

## Slide 16
CONTROLLING DEVICE
In project1 we discussed to use Arduino Due in controlling the printer but after constructing the printer we decided to use Raspberry pi.

## Slide 17
Raspberry Pi is the main part in our project that connects all the electrical and mechanical components with each other.
operates in the same way as a standard PC, requiring a keyboard for command entry, a display unit and a power supply.

## Slide 18
FLASH MEMORY & SD CARD
Importing data and files from flash memory or SD cards will be the main source from printing.
The user can print any document (PDF, txt, word)

## Slide 19
SERIAL CONNECTIONS
The other source of data that the printer will receive is the computer.
Serial connections includes any interfacing device such as mouse, keyboard, … etc

## Slide 20
SCREEN
The screen is used in our project that will act as an output and Input device, it is display the data coming from flash memory and computer in icons, and controlled by a remote.

## Slide 21: protection
In designing Braille printer we considered the protection sources, these are:
Fuses: we use fuses to overall protection
H-Bridge: Used to protect DC motor

## Slide 22
ULN2003: it is stepper motor driver module used to protect and controlling the movement of the stepper motor
Raspberry Pi Cooler: required to remove the waste heat produced by printer components, to keep them within permissible operating temperature limits
Relay: is used to protect the solenoid and passes power

## Slide 23: methodology
Insert Flash Memory
Read The File
Print ”NO PAPER”
Read The Matrix
Convert To Matrix (0,1)
Pull The Next Paper
DC Will Pull The Paper
The Solenoid Will Strike
START
END
end Line
(1)
Sensor ON
End Paper
IF
NO
YES
IF
NO
YES
IF
NO
YES
NO
YES

## Slide 24: Video….

## Slide 25: cost
In project1 we put a plan explained the cost to about 600 JD, but actually it costs 2000 JD, Due to the prices of the components available in the market.

## Slide 26: Future work
In the future, we will work to make different sizes of braille printer to enable printing on the various paper sizes (A3,A5,..)
We can also make the printing process more fast that will print a whole document such as the ordinary printer prints.

## Slide 27
In this project we made a plan of Braille printer that does not need any extra program that will be installed in computer and receive data from flash memories and computers .
The printer enable receiving files (Pdf ,text, and document) and convert it to Braille language by convert each letter or character to a specific movement of stepper motor that hold needle carried by solenoid the printing will be effective and fast depending on the speed of solenoid and stepper motors.
conclusion

## Slide 28
THANK YOU
FOR LISTENEING