## Slide 2: Content
Introduction
Data collection
Data analysis and discussion
Database and webpage
Oscillator design
SWOT analysis
Future Work

## Slide 3: Introduction
Data traffic exchanged over the Internet is increasing rapidly.
New services are released everyday.
Demands are rising to provide high bitrates everywhere.

## Slide 4: IOTV
It is a project that aims to transmit Internet wirelessly over TV band using Cognitive Radio technique, and utilizing the white space. In order to cover rural and remote areas.

## Slide 5: Definitions
Licensed band :
  no one can transmit over this band but the authorized one.
Unlicensed band :
  anyone can transmit over this band under strict specifications.
White spaces :
  frequencies allocated to broadcast services but are not used.

## Slide 6: Cognitive radio
Smart way of accessing the spectrum

## Slide 7: Our work!!
Developing the real field TV spectrum usage database and provide it as online service for public access and analyze the data.
Design and simulation of a 2-GigaByte microwave oscillator which represents a key function in the final hardware design

## Slide 8
Data Collection
We Chose Nablus as our target.
we have divided it into two main parts:
the villages surrounding the city, which were divided into four categories according to location from Nablus city, South, West, North, and East.
the city itself and within existing neighborhoods.

## Slide 9
To locate points of measurement we took into account:
Size of the area
Distribution of population
Diversity of terrain
Data Collection

## Slide 10
For Example:
Beit Furik:
The village of Bet Forik 7 kilometers east of the city of Nablus, with a residential area of ​​18 KM2 ,reaching a population of 11740 people in 2013.
Data Collection
Height541 m
Height602 m

## Slide 11
Data Collection
After we choose the appropriate measurement sites:
Nablus
Divided To
38
Measurement
points
We measured In
In
N
E
S
W
28
Regions
Vertical
Polarization
Horizontal
Polarization
We now have 304 readings
In each reading we measured the power of 50 channels distributed over a 400-800 MHz Spectrum.

## Slide 12
For this phase of the project we have used spectrum analyzer and a Yagi Uda Antenna .
Equipment

## Slide 13: Data Analysis

## Slide 15
Nablus Spectrum measurement, averaged over all the directions

## Slide 16: Data discussion
We can classified all result into three main categories :
Band width less than 8MHz.
Band width equal 8MHz.
Band width 100KH.

## Slide 17: Our designed Data Base
Contains:
1- login table
2- users table
3- locations table
4- power table

## Slide 18: Oscillator

## Slide 19: Design

## Slide 20: SWOT Analysis
S
TRENGTHS
W
EAKNESSES
O
PPORTUNITIES
T
HREATS
Professional well-trained team.
The results of this phase are valuable resource for researchers, companies...etc
The real TV spectrum usage database is the first of its type in Palestine
Well equipped.
Competitive.
Political and occupational restrictions
It is difficult to determine the origin and the type of signals we have detected.
Existence of free spectrum for utilization.
The absence of broadband internet services in rural areas.
Switching to digital TV, this will free up more spectrum to be used.
Absence of rules and regulations about channels allocation.
Occupation.
Negative
Internal
factors
External
factors
Positive

## Slide 21: Future work
Complete the Database.
Build the complete system.

## Slide 22
Thank you