## Slide 2: Outlines:-
  Environmental Design.
Architectural Design Modifications.
  Structural Design
  Quantity compare
  Lighting and Mechanical Design.

## Slide 3: Objective:
The principal objectives of this project are to reduce the construction cost of residential buildings, through proposing material alternative for floor tiles, door, window and walls.

## Slide 4: Objective:

## Slide 5: Site plan :

## Slide 6: Wind direction :

## Slide 7: Old design :

## Slide 8: Old design :

## Slide 9: New design :

## Slide 10: 2nd floor:

## Slide 11: Elevation :

## Slide 12: Elevation :

## Slide 13: Elevation :

## Slide 14: Elevation :

## Slide 15: Section :

## Slide 16: Section :

## Slide 17: 3d :

## Slide 20: Passive solar
At the south we decide to make solar window…..Why??
* Because solar chimney is not effected as shown in calculation

## Slide 21: Passive solar
Solar chimney calculated:
A = 4 ft2
T1-T2 = 30 F in winter
H = 18 ft.
Q= 540*A*√h (T1-T2)
= 540*4*√18 (30)
= 50193.86 ft3/ hr.
Volume of space = 9486 ft3
Number of change = Q/ V
=50193.86/9486 = 5.2 change/hour and that less than 6 so the chimney not efficacy in the house ,

## Slide 22: Shading :
Sample calculation:
Design the horizontal lover in the 21/5 at 12 pm
X = h/ (tan (Alt))
X= horizontal length of lover
H = glass height
Alt =Altitude at 21/5 at 12 pm and equal 78
So the first design for h = 40 cm and y = 0
X = 0.4/ (tan (78)) = 9 cm
And anther design for h = 120cm and y = 0
X = 1.2/ (tan (78)) = 25cm

## Slide 26: Environmental :
Artificial lighting
Emergency lighting
Natural lighting

## Slide 27: Environmental :
        Natural lighting
compute the D.F by ECOTECT program
Function | D.F% | Standard value | Accept
Guest room | 3.1 | 2.5-4 | √
Living 1st floor | 3 | 2.5-4 | √
Kitchen | 2.9 | 2.5-4 | √
Bath | 1.5 | 1.5-2.5 | √
Corridor | 1.9 | 1.5-2.5 | √
Master bed room | 2.6 | 2.5-4 | √
Room 3 | 2.7 | 2.5-4 | √
Living 2nd floor | 3 | 2.5-4 | √
Bed room 1 | 2.6 | 2.5-4 | √
Bed room 2 | 2.4 | 2.5-4 | √
Bed room 3 | 2.8 | 2.5-4 | √

## Slide 28: Environmental :

## Slide 29: Environmental :

## Slide 30: Environmental :
DIALUX software was used to design the Artificial lighting system
B-Artificial lighting

## Slide 31: Environmental :
Technical values for design
Function | Eavg | Work plan
Gust room | 250-300 | 0.75m
Kitchen room | 350-500 | 1m
Living room | 300-500 | 0.75m
Corridor | 150 | 1-1.5m
Bath | 150 | 0.75m

## Slide 32: Environmental :
SAMPLE:.
Guest room
Laminar distributed
Illumenance =250 lux
Work plane =75cm
uniformity= 0.66
#of lamps=2 lamps
12Led

## Slide 33: Environmental :

## Slide 34: Environmental :
SAMPLE:.
Bed room
Laminar distributed
Illumenance =340lux
Work plane =75cm
uniformity= 0.66
#of lamps=7 lamps
18Led

## Slide 35: Environmental :

## Slide 36
Structural

## Slide 37: Construction material properties:
Concrete, f’c= 24MPa
steel, fy= 420MPa

## Slide 38
super impose dead Load=2.5KN/M2
building parameter wall load =21KN/M
loads
Live load =4KN/M2

## Slide 39: COLUMNS

## Slide 40: SOME CHECK On RESULT from SAP
40
  DEAD LOAD from = 6446 kN/m2 calculation=6446KN/M2 KNkN/m2
  DEAD LOAD from Sap =6234 kN/m2

## Slide 41: CHECK On deflection
41
Max deflection=7mm
∆max= 19.7mm
19.7≻7 ok
∆max= 19.7mm
19.7≻7 ok

## Slide 42: Design beam
42
Main beam(60*25)
Asmin=440mm2
Secondary beam(40*25)
Asmin=295mm2

## Slide 45: Design slab

## Slide 46: Design slab

## Slide 47: Design column
47

## Slide 48: Footing Design
48

## Slide 49: Design Tie beam
49
Tie beam(50*30 cm)

## Slide 50: HVAC System
The former design did not design for HVAC system.
Element of the wall and slab

## Slide 51: External Wall

## Slide 52: Internal wall Ceiling

## Slide 53: Ground

## Slide 54: Heating Load
Heat transfer through wall and slab.
Infiltration through window and door.
Out side temperature = 8C
Inside temperature =20C
Total heating load = 10 KW

## Slide 55: Heating Load
# of zone | Q Total | Q total kw | Q TR
1 | 1227.03 | 1.23 | 0.35
2 | 1173.60 | 1.17 | 0.33
3 | 310.36 | 0.31 | 0.09
4 | 748.74 | 0.75 | 0.21
5 | 210.88 | 0.21 | 0.06
6 | 638.26 | 0.64 | 0.18
7 | 1946.52 | 1.95 | 0.55
8 | 917.16 | 0.92 | 0.26
9 | 423.55 | 0.42 | 0.12
10 | 444.15 | 0.44 | 0.13
11 | 859.10 | 0.86 | 0.24
12 | 342.84 | 0.34 | 0.10
13 | 1109.74 | 1.11 | 0.32
Total | 10351.95 | 10.35 | 2.94

## Slide 56: Cooling Load
Heat transfer through wall and slab.
Infiltration through window and door.
due to equipment
Outside temperature = 35C
Total cooling load = 9 KW

## Slide 57: Cooling Load
# Zone | Q Totlal | Qtotal kw | Q TR
1 | 2682.83 | 2.68 | 0.76
2 | 42.03 | 0.04 | 0.01
3 | 90.21 | 0.09 | 0.03
4 | 603.04 | 0.60 | 0.17
5 | 53.76 | 0.05 | 0.02
6 | 655.74 | 0.66 | 0.19
7 | 1406.38 | 1.41 | 0.40
8 | 911.51 | 0.91 | 0.26
9 | 142.55 | 0.14 | 0.04
10 | 171.06 | 0.17 | 0.05
11 | 1097.41 | 1.10 | 0.31
12 | 193.73 | 0.19 | 0.06
13 | 1123.31 | 1.12 | 0.32
 | 9173.56 | 9.17 | 2.61

## Slide 58: Average heating and cooling load in building.

## Slide 59: Use split unit
total | price | Number | Type
27000 | 3000 | 9 | 9000 Btu
252 | 14 | 18 | Pipe 1.5”
27252 |  |  | total

## Slide 60: Installation of split unit

## Slide 61: Electrical design

## Slide 62: Circuit breaker board

## Slide 63: Earth system

## Slide 64: Lighting distribution in ground floor

## Slide 65: Lighting distribution in first floor

## Slide 66: Socket distribution in ground floor

## Slide 67: Socket distribution in first floor

## Slide 68: Protection system :
Fire extinguisher (two class)
1-Class K Fire Extinguisher
2-Class C Fire Extinguisher

## Slide 69: Water Systems design ( plumping system) :
Diameter used:
Vertical feeder = 1.25 inch
Horizontal feeder = 1 inch
Branch = ¾ inch

## Slide 70: Water Systems design:

## Slide 71: The collector location:

## Slide 72: Drainage Systems design:
Black water :W.CS & kitchen sink
Grey water : Laundries & shower head

## Slide 73: Black water:

## Slide 74: Grey water :

## Slide 75: Quantity and comparison:
Divide into two types :
1- cost without using alternative materials with area equal 350 m 2 (former design)
2- cost after revised and using alternative materials with area equal 354 m 2 (revised design)

## Slide 83: Conclusion:
Using the alternative materials, external stone, PVC windows, doors, fiber hollow block in the internal wall and PVC floors tiles, reducing the total cost about 21%, with the same or best efficiency than the local material.

## Slide 84
Thanks
For Your Attention