## Slide 1: Comparison Between Different Slab Systems (Structural and Economical)
Prepared by :
Abdullah Shehab
Jihad Zakarnah
Mohammed Al-Qasim

## Slide 2: In this project
3D model had been designed with different slab systems
Quantity survey and cost estimate has been done for each system.
Bill of quantity was constructed for each of them.
The most economical system was selected.

## Slide 3
We used four slab systems:
1- Two-way Flat Plate
2- Two-way Solid Slab
3- Two-Way Ribbed Slab
4- One-Way Ribbed Slab

## Slide 4
The project is about a residential building
Salfit City - Palestine
Floor | Area (m2) | Consistence and use of floor
Ground floor | 182.5 | consists a three bed rooms, kitchen, three bath rooms, entrance and living room
First floor | 182.5 | is the same as the ground floor
Staircase | 14.3 | 
Total | 379.3 | 

## Slide 5
Centre Line Plan

## Slide 6: Flat plate slab system

## Slide 7: THREE-DIMENSIONAL STRUCTURAL ANALYSIS

## Slide 8: Slab and beams
Thickness of Slab = 200 mm
For Beams we used Edge beams:
Width of Beam1 (B1) = 300 mm
Depth of Beam1 (B1) = 200 mm
Width of Beam2 (B2) = 450 mm
Depth of Beam2 (B2) = 200 mm

## Slide 9: Columns
Column Group | Column Dimensions (mm) | Longitudinal Steel | Stirrups
C1 | 700 X 200 | 10 ∅ 14 mm | 1 ∅10 @ 200 mm
C2 | 400 X 200 | 8 ∅ 12 mm | 1 ∅10 @ 190 mm
C3 | 300 X 200 | 6 ∅ 12 mm | 1 ∅10 @ 190 mm

## Slide 10: Footings
Type of footing | Dimension ( m ) | Bottom steel |  | Top steel | 
 |  | Long Direction | Short Direction | Long Direction | Short Direction
Single footings | 1.4 X 1.4 X 0.35 | 8 ∅12 | 8 ∅12 | 4 ∅12 | 4 ∅12
Single footings | 1.6 X 1.6 X 0.35 | 9 ∅12 | 9 ∅12 | 5 ∅12 | 5 ∅12
Single footings | 1.85 X 1.85 X 0.35 | 11 ∅12 | 11 ∅12 | 6 ∅12 | 6 ∅12

## Slide 11: Two way solid slab system

## Slide 12: Three-Dimensional Structural Analysis

## Slide 13: Slab and beams
Thickness of Slab = 150 mm
Width of beams = 300 mm
Depth of beams = 300 mm

## Slide 14: Columns
Column Group | Column Dimensions (mm) | Longitudinal Steel | Stirrups
C1 | 550 X 200 | 10 ∅ 12 mm | 1 ∅10 @ 190 mm
C2 | 400 X 200 | 8 ∅ 12 mm | 1 ∅10 @ 190 mm
C3 | 300 X 200 | 6 ∅ 12 mm | 1 ∅10 @ 190 mm

## Slide 15: Footings
Type of footing | Dimension ( m ) | Bottom steel |  | Top steel | 
 |  | Long Direction | Short Direction | Long Direction | Short Direction
Single footings | 1.4 X 1.4 X0.35 | 8 ∅12 | 8 ∅12 | 4 ∅12 | 4 ∅12
Single footings | 1.6 X 1.6 X 0.35 | 9 ∅12 | 9 ∅12 | 5 ∅12 | 5 ∅12
Single footings | 1.85 X 1.85 X 0.4 | 12 ∅12 | 12 ∅12 | 6 ∅12 | 6 ∅12

## Slide 16: Two way ribbed slab system (Waffle slab)

## Slide 17
THREE-DIMENSIONAL STRUCTURAL ANALYSIS

## Slide 18: Slab
Total Thickness of Slab = 250 mm
Width of Rib bw = 120 mm
Flange Width = 520 mm
Block Dimensions = 40 X 25 X 17 cm Height

## Slide 19: Beams
We used two types of beams and they are hidden beams:
B1 with width = 450 mm
B1 with depth = 250 mm
B2 with width = 300 mm
B2 with depth = 250 mm

## Slide 20: Columns
Column Group | Column Dimensions (mm) | Longitudinal Steel | Stirrups
C1 | 550 X 200 | 10 ∅ 12 mm | 1 ∅10 @ 190 mm
C2 | 400 X 200 | 8 ∅ 12 mm | 1 ∅10 @ 190 mm
C3 | 250 X 200 | 6 ∅ 12 mm | 1 ∅10 @ 190 mm

## Slide 21: Footings
Type of footing | Dimension ( m ) | Bottom steel |  | Top steel | 
 |  | Long Direction | Short Direction | Long Direction | Short Direction
Single footings | 1.2 X 1.2 X 0.3 | 6 ∅12 | 6 ∅12 | 3 ∅12 | 3 ∅12
Single footings | 1.5 X 1.5 X 0.35 | 9 ∅12 | 9 ∅12 | 5 ∅12 | 5 ∅12
Single footings | 1.8 X 1.8 X 0.4 | 12 ∅12 | 12 ∅12 | 6 ∅12 | 6 ∅12

## Slide 22: ONE way ribbed slab system

## Slide 23
THREE-DIMENSIONAL STRUCTURAL ANALYSIS

## Slide 24: Slab
Total Thickness of Slab = 300 mm
Width of Rib bw = 120 mm
Flange Width = 520 mm
Block Dimensions = 40 X 25 X 24 cm Height

## Slide 25: Beams
We used two types of beams and they are hidden beams:
B1 with width = 700 mm
B1 with depth = 300 mm
B2 with width = 400 mm
B2 with depth = 300 mm

## Slide 26: Columns
Column Group | Column Dimensions (mm) | Longitudinal Steel | Stirrups
C1 | 550 X 200 | 10 ∅ 12 mm | 1 ∅10 @ 190 mm
C2 | 400 X 200 | 8 ∅ 12 mm | 1 ∅10 @ 190 mm
C3 | 250 X 200 | 6 ∅ 12 mm | 1 ∅10 @ 190 mm

## Slide 27: Footings
Type of footing | Dimension ( m ) | Bottom steel |  | Top steel | 
 |  | Long Direction | Short Direction | Long Direction | Short Direction
Single footings | 1.3 X 1.3 X 0.35 | 8 ∅12 | 8 ∅12 | 4 ∅12 | 4 ∅12
Single footings | 1.55 X 1.55 X 0.35 | 9 ∅12 | 9 ∅12 | 5 ∅12 | 5 ∅12
Single footings | 1.75 X 1.75 X 0.4 | 12 ∅12 | 12 ∅12 | 5 ∅12 | 5 ∅12

## Slide 28: Quantity surveying & Cost estimate

## Slide 29: Quantity And Material Takeoff
Quantity takeoff : is a process of measuring the work of the project in the form of a series of quantified work items.
Material takeoff : is used to compute the quantity of materials that need to be purchased in order to construct a particular item of the project.

## Slide 30: Quantity Surveying (QS)
Consultant QS
Contractor QS

## Slide 31: Estimation
Estimating is an approximation that defines the Cost of construction Activity or activities prior to commencement of work V.S the cost of work during and after construction, which is the Actual cost.
Activity Cost in general is basically the cost of material, labor and equipment.
Conceptual Estimate & Detailed Estimate

## Slide 32: Work Breakdown Structure (WBS)
A hierarchical system which sub-divides larger elements of the project to smaller elements.
The smallest unit of the WBS is the work package.
work packages should be manageable, independent and Measurable

## Slide 33: Work Breakdown Structure (WBS)

## Slide 34: Bill Of Quantity ( BOQ)
The Bill of Quantities (sometimes referred to as ‘BOQ' or 'BQ') is a document prepared by the cost consultant (often a Quantity Surveyor) that provides project specific measured quantities of the items of work identified by the drawings and specifications in the tender documentation.
The quantities may be measured in number, length, area, volume, weight or time Preparing a bill of quantities requires that the design is complete and a specification has been prepared.

## Slide 35: Project Quantities
Quantities were made for two major elements:
Structural elements: including Footings, Column necks, Columns, Beams and Slabs.
Nonstructural elements: mainly the interior finishing works.
Nonstructural elements had calculated for one time since it had never changed for different slab systems.

## Slide 36: Tow-way Flat Plate
Excavation For Footing |  |  |  |  |  |  | 
Type of Footing | No. of Footing | Length(m) | Width (m) | Depth(m) | Volume of Bank(m^3) | Swell Factor | Volume of Loose(m^3)
F1 | 9 | 2.4 | 2.4 | 1.5 | 77.76 | 1.5 | 116.64
F2 | 8 | 2.6 | 2.6 | 1.5 | 81.12 | 1.5 | 121.68
F3 | 5 | 2.85 | 2.85 | 1.5 | 60.91875 | 1.5 | 91.378125
Total |  |  |  |  | 219.79875 |  | 329.698125
Excavation For Footings
Assume allowance from each side = 0.5 m

## Slide 37: Tow-way Flat Plate
Footings: Blinding & main Concrete
Type of Footing | N | L(m) | W(m) | D(m) | Volume (m3)
F1 | 9 | 1.4 | 1.4 | 0.35 | 6.17
F2 | 8 | 1.6 | 1.6 | 0.35 | 7.17
F3 | 5 | 1.85 | 1.85 | 0.4 | 6.85
Total |  |  |  |  | 20.19
Type of Footing | N | L(m) | W(m) | D(m) | Volume(m3)
F1 | 9 | 1.60 | 1.60 | 0.10 | 2.30
F2 | 8 | 1.80 | 1.80 | 0.10 | 2.60
F3 | 5 | 2.05 | 2.05 | 0.10 | 2.10
Total |  |  |  |  | 7.00
Volume of Blinding Concrete
Volume of Main Concrete

## Slide 38: Tow-way Flat Plate
Footings: Formwork & Reinforcement
Type of Footing | N | Bar Size (mm) | Weight (Kg) | L(m) | No. of Bar | Total Weight (Ton)
F1 | 9 | 12 | 0.888 | 1.25 | 24 | 0.24
F2 | 8 | 12 | 0.888 | 1.45 | 28 | 0.29
F3 | 5 | 12 | 0.888 | 1.7 | 34 | 0.26
Total |  |  |  |  |  | 0.79
Type of Footing | N | L (m) | W (m) | D (m) | Thickness (m) | Volume (m3)
F1 | 9 | 1.4 | 1.4 | 0.4 | 0.025 | 0.504
F2 | 8 | 1.6 | 1.6 | 0.4 | 0.025 | 0.512
F3 | 5 | 1.85 | 1.85 | 0.4 | 0.025 | 0.37
Total |  |  |  |  |  | 1.386

## Slide 39: Tow-way Flat Plate
Column necks: Concrete & Formwork Volumes
Group of Column | N | L(m) | W (m) | D(m) | Volume (m3)
C1 | 9 | 0.3 | 0.2 | 1.15 | 0.62
C2 | 8 | 0.4 | 0.2 | 1.15 | 0.74
C3 | 5 | 0.7 | 0.2 | 1.1 | 0.77
Total |  |  |  |  | 2.13
Type of Column | N | L(m) | W(m) | D(m) | Thickness(m) | Volume (m3)
C1 | 9 | 0.3 | 0.2 | 1.2 | 0.025 | 0.27
C2 | 8 | 0.4 | 0.2 | 1.2 | 0.025 | 0.29
C3 | 5 | 0.7 | 0.2 | 1.1 | 0.025 | 0.25
Total |  |  |  |  |  | 0.81
Volume of Concrete
Volume of Formwork

## Slide 40: Tow-way Flat Plate
Column necks: Longitudinal & Transverse Reinforcement
Group of Column | N | Bar Size(mm) | Weight (Kg) | L(m) | No. of Bar | Total Weight (Ton)
C1 | 9 | 12 | 0.889 | 2.4 | 6 | 0.1152
C2 | 8 | 12 | 0.889 | 2.4 | 8 | 0.136533
C3 | 4 | 14 | 1.21 | 2.4 | 10 | 0.116148
 | 1 | 14 | 1.21 | 2.4 | 18 | 0.052267
Total |  |  |  |  |  | 0.42
Longitudinal Reinforcement
Group of Column | N | Size (mm) | Weight (Kg) | No. of Stirrup | Width stirrup(m) | Depth stirrup(m) | Peri. Of ST(m) | Total Weight (Ton)
C1 | 9 | 10 | 0.617 | 8 | 0.25 | 0.15 | 0.8 | 0.03555556
C2 | 8 | 10 | 0.617 | 8 | 0.35 | 0.15 | 1 | 0.03950617
C3 | 4 | 10 | 0.617 | 8 | 0.73 | 0.3 | 2.1 | 0.04069136
 | 1 | 10 | 0.617 | 8 | 1.27 | 0.45 | 3.4 | 0.01698765
Total |  |  |  |  |  |  |  | 0.13274074
Transverse Reinforcement

## Slide 41: Tow-way Flat Plate
Ground Beams: Blinding, main Concrete & Formwork volumes
Volume of Blinding Concrete
Volume of Formwork
Type of Tie Beams | L(m) | W(m) | D(m) | Volume(m3)
T1 | 131 | 0.3 | 0.1 | 3.93
Total |  |  |  | 3.93
Type of Tie Beams | L(m) | W(m) | D(m) | Volume(m3)
T1 | 131 | 0.2 | 0.5 | 13.1
Total |  |  |  | 13.1
Lengths of tie beams are found using AutoCAD.
Type of Tie Beams | L(m) | W(m) | D(m) | Thickness(m) | Volume (m3)
T1 | 131 | 0.2 | 0.6 | 0.025 | 3.93
Total |  |  |  |  | 3.93
Volume of Main Concrete

## Slide 42: Tow-way Flat Plate
Ground Beams: Longitudinal & Transverse Reinforcement
Longitudinal Reinforcement
Transverse Reinforcement
Type of TB | L(m) | Bar Size(mm) | Weight (Kg) | No. of Bar | Total Weight (Ton)
TB | 151 | 14 | 1.20988 | 4 | 0.730765432
Total |  |  |  |  | 0.730765432
Size (mm) | Weight (Kg) | Spacing (m) | L (m) | N | W (m) | D (m) | Perimeter | Total Weight (Ton)
10 | 0.61728 | 0.2 | 131 | 655 | 0.15 | 0.45 | 1.2 | 0.485

## Slide 43: Tow-way Flat Plate
Ground Slab: Concrete & Formwork Volumes
Volume of Concrete
Volume of Formwork
Elevation | Area(m3) | t(m) | V(m3)
0.00 | 182.5 | 0.1 | 18.25
Total Concrete V(m3) |  |  | 18.25
Ground Slab | Perimeter (m) | Depth(m) | Thickness(m) | Volume (m3)
 | 65 | 0.1 | 0.025 | 0.1625

## Slide 44: Tow-way Flat Plate
Ground Slab: Longitudinal Reinforcement
Longitudinal Reinforcement
No. of Bars | length of Bar (m) | Total Length (m) | Bar Size (mm) | Weight (Kg) | Total Weight (Ton)
40 | 11.1 | 444 | 8 | 0.395061728 | 0.175407407
10 | 17.4 | 174 | 8 | 0.395061728 | 0.068740741
20 | 13.2 | 264 | 8 | 0.395061728 | 0.104296296
30 | 12.3 | 369 | 8 | 0.395061728 | 0.145777778
10 | 7 | 70 | 8 | 0.395061728 | 0.027654321
25 | 14.32 | 358 | 8 | 0.395061728 | 0.141432099
Total |  |  |  |  | 0.663308642

## Slide 45: Tow-way Flat Plate
Floor Slab: Concrete Volumes
Volume of Concrete
Floor | Area (m2) | Thickness(m) | Volume(m3)
First | 182.5 | 0.2 | 36.5
Second | 182.5 | 0.2 | 36.5
Third | 14.3 | 0.2 | 2.86
Total |  |  | 75.86

## Slide 46: Tow-way Flat Plate
Floor Slab: Formwork Volumes
Total Area of Sheating (m2) | 379
Total Volume of Sheating (m3) | 9.475
Total Volume of Formwork (m3) | 16.555
Total No. of Shores | 843
Volume of Formwork
Assumptions for Formwork
Assume distance between Shores = 0.5 m in direction1 and 0.9 m in direction 2
Assume distance between Stringer = 0.9 m in each direction
Assume distance between Joist = 0.4 m in each direction
Stringer 0.05 X 0.1 X Length
Joist 0.05 X 0.1 X Length
Sheeting 0.025 X 0.1 X Length

## Slide 47: Tow-way Flat Plate
Floor Slab: Slab Reinforcement
Top Reinforcement For Slab in direction 1
Floors | Top Bar |  |  |  | 
 | No. of Bars | φ(mm) | Weight (Ton) | Length (m) | Total Weight
Direction1 | 36 | 12 | 0.00089 | 8.7 | 0.2784
 | 20 | 12 | 0.00089 | 2.8 | 0.049777778
 | 10 | 14 | 0.00121 | 9.7 | 0.117358025
 | 8 | 12 | 0.00089 | 9.3 | 0.066133333
 | 10 | 14 | 0.00121 | 9.3 | 0.112518519
 | 15 | 12 | 0.00089 | 5.6 | 0.074666667
 | 20 | 12 | 0.00089 | 3 | 0.053333333
Total Reinforcement For Slab = 6.362 Tons

## Slide 48: Tow-way Flat Plate
Frames: Longitudinal Reinforcement For Frames
Top Reinforcement For First Four frames
Total Longitudinal Reinforcement For Frames = 1.432 Tons
Frame Type | Top Bar |  |  |  | 
 | No. of Bars | φ(mm) | Weight (Ton) | Length (m) | Total Weight (Ton)
Frame1 | 6 | 12 | 0.00088889 | 3.4 | 0.018133333
 | 4 | 12 | 0.00088889 | 2.3 | 0.008177778
Frame2 | 8 | 12 | 0.00088889 | 8.8 | 0.062577778
 | 4 | 12 | 0.00088889 | 6.7 | 0.023822222
Frame3 | 10 | 12 | 0.00088889 | 4.3 | 0.038222222
Frame4 | 8 | 12 | 0.00088889 | 4.5 | 0.032
 | 4 | 12 | 0.00088889 | 4.4 | 0.015644444

## Slide 49: Tow-way Flat Plate
Frames: Transverse Reinforcement For Frames
Transverse Reinforcement For First Four frames
Total Transverse Reinforcement For Frames = 0.87 Tons
Stirrup |  |  |  |  | 
Frame Type | No.of ST. | φ(mm) | Perimeter(m) | Weight (Ton) | Total Weight (Ton)
Frame1 | 90 | 10 | 1.04 | 0.0006173 | 0.057777778
Frame2 | 200 | 10 | 1.54 | 0.0006173 | 0.190123457
Frame3 | 40 | 10 | 1.04 | 0.0006173 | 0.025679012
Frame4 | 52 | 10 | 1.54 | 0.0006173 | 0.049432099

## Slide 50: Tow-way Flat Plate
Columns:
Columns are divided into three groups according to their elevations,
these groups are:
columns from 0.78-4.16 m
columns from 4.16-7.54 m
columns from 7.54 – 9.97 m
We will show the calculations for columns form 0.78-4.16 m

## Slide 51: Tow-way Flat Plate
Columns: Concrete, Formwork & Joists Volumes
Group of Column | N | L(m) | W(m) | D(m) | Volume (m3)
C1 | 9 | 0.3 | 0.2 | 3.38 | 1.8252
C2 | 8 | 0.4 | 0.2 | 3.38 | 2.1632
C3 | 5 | 0.7 | 0.2 | 3.38 | 2.366
Total |  |  |  |  | 6.3544
Volume of Formwork
Type of column | N | L (m) | Width (m) | D(m) | Thickness(m) | Volume (m3)
C1 | 9 | 0.3 | 0.2 | 3.38 | 0.025 | 0.7605
C2 | 8 | 0.4 | 0.2 | 3.38 | 0.025 | 0.8112
C3 | 5 | 0.7 | 0.2 | 3.38 | 0.025 | 0.7605
Total |  |  |  |  |  | 2.3322
Volume of Concrete
No. of Joist | Volume of one Joist (m3) | Volume of Joist (m3)
10 | 0.005 | 0.045
10 | 0.006 | 0.048
10 | 0.009 | 0.045
Total |  | 0.138
Volume of Joists

## Slide 52: Tow-way Flat Plate
Columns: Longitudinal & Transverse Reinforcement
Longitudinal Reinforcement
Transverse Reinforcement
Group of Column | N | Bar Size(mm) | Weight (Kg) | L(m) | No. of Bar | Total Weight (Ton)
C1 | 9 | 12 | 0.888889 | 4.7 | 6 | 0.2256
C2 | 8 | 12 | 0.888889 | 4.7 | 8 | 0.2673778
C3 | 4 | 14 | 1.209877 | 4.7 | 10 | 0.2274568
 | 1 | 14 | 1.209877 | 4.7 | 18 | 0.1023556
Total |  |  |  |  |  | 0.8227901
Group of Column | N | Size (mm) | Weight (Kg) | No. of Stirrup | W(m) | D(m) | P(m) | Total Weight(Ton)
C1 | 9 | 10 | 0.617284 | 18 | 0.25 | 0.15 | 0.8 | 0.08
C2 | 8 | 10 | 0.617284 | 18 | 0.35 | 0.15 | 1 | 0.088889
C3 | 4 | 10 | 0.617284 | 17 | 0.73 | 0.3 | 2.06 | 0.086469
 | 1 | 10 | 0.617284 | 17 | 1.27 | 0.45 | 3.44 | 0.036099
Total |  |  |  |  |  |  |  | 0.291457

## Slide 53: Tow-way Flat Plate
Stairs:
The stairs are divided into areas to calculate their volume, as shown in figure.

## Slide 54: Tow-way Flat Plate
Stairs: Concrete & Formwork Volumes
Level | A | B | t | L | # Stairs | l | h | Triangles Area | Concrete Volume Vc (m3) | Formwork Volume Vw(m3)
00-0.78 | 1.3 | 1.13 | 0.3 | 1.379 | 4 | 0.3 | 0.17 | 0.102 | 0.805 | 0.192
0.78-2.47 | 1.3 | 1.13 | 0.2 | 3.448 | 10 | 0.3 | 0.17 | 0.255 | 1.314 | 0.342
2.47-4.16 | 1.3 | 1.13 | 0.3 | 3.448 | 10 | 0.3 | 0.17 | 0.255 | 1.461 | 0.351
4.16-5.85 | 1.3 | 1.13 | 0.2 | 3.448 | 10 | 0.3 | 0.17 | 0.255 | 1.314 | 0.342
5.85-7.54 | 1.3 | 1.13 | 0.3 | 3.448 | 10 | 0.3 | 0.17 | 0.255 | 1.461 | 0.351
Total |  |  |  |  |  |  |  |  | 6.354 | 1.577
Detailing’s For Stairs

## Slide 55: Tow-way Flat Plate
Stairs: Longitudinal Reinforcement
Longitudinal Reinforcement For stairs
Level | φ | ΣL | Linear Density | W(ton)
00-0.78 | 12 | 37.52440406 | 0.000888889 | 0.033355026
 | 14 | 26.73440406 | 0.001209877 | 0.032345328
0.78-2.47 | 12 | 58.56151016 | 0.000888889 | 0.052054676
 | 14 | 45.56151016 | 0.001209877 | 0.055123802
2.47-4.16 | 12 | 58.56151016 | 0.000888889 | 0.052054676
 | 14 | 45.56151016 | 0.001209877 | 0.055123802
4.16-5.85 | 12 | 58.56151016 | 0.000888889 | 0.052054676
 | 14 | 45.56151016 | 0.001209877 | 0.055123802
5.85-7.54 | 12 | 58.56151016 | 0.000888889 | 0.052054676
 | 14 | 45.56151016 | 0.001209877 | 0.055123802
Total |  |  |  | 0.439290464

## Slide 56: Tow-way Flat Plate
Plastering & Painting
Assumptions:
Plaster thickness is 2 cm.
Paint thickness is 0.6 cm.
Results:
Area of Plastering For Walls = 1123.48 m2
Area of Plastering For Floors = 304.5 m2
Area of Painting For Walls = 1123.48 m2
Area of Painting For Floors = 304.5 m2

## Slide 57: Tow-way Flat Plate
Tiles
Results:
 For Ground Tiles:
Area of Ground Tile = 274.02 m2
Total area of bathroom tiles = 194.68 m2
For Skirting Tiles (Panel):
Area of ground tile = 251.34 m
 Total Filling Volume = 30.45 m3
 Total Mortar Volume = 5.496 m3

## Slide 58: Tow-way Flat Plate
Wall Partitions
Results:
Area for external partitions = 437.24 m2
Area for internal partitions = 35 m2
Area for Parapet Partitions = 65 m2
Wall partitions divided into external and internal walls.
We used Blocks 40 X 20 X 25 cm Height
Number of Blocks needed =
Total no. of boxes of block 10 needed | 23
Total no. of boxes of block 20 needed | 89
Total volume of mortar needed (CM) | 5.80

## Slide 59: Tow-way Flat Plate
Natural Stone
Natural stone used as a cover for the villa, we used natural stone with 4 cm thickness
Area Of Stone | Area Of Opening | Total Area(m2)
119.7 | 36.67 | 83.03
120 | 13 | 107
126.98 | 14 | 112.98
126.98 | 29.28 | 97.7
39 | 2.47 | 36.53
Total |  | 437.24
From the factory, factor of area = 1.5
Total Area of natural stone needed = 437.24 * 1.5 = 655.86 m²

## Slide 60: Tow-way Flat Plate
Doors & Windows
Material Type | Shape | Height | Width | No. | Surface area (m2)
Aluminum | Flat | 130 | 160 | 14 | 29.12
Aluminum | Flat | 104 | 160 | 2 | 3.328
Aluminum | Flat | 130 | 120 | 2 | 3.12
Aluminum | Flat | 78 | 60 | 8 | 3.744
Aluminum | Slider | 234 | 168 | 4 | 15.7248
Aluminum | Slider | 624 | 104 | 2 | 12.9792

## Slide 61: Tow-way Flat Plate
Waste Factors
The physical waste includes loss of materials and damages while cost and time overrun refers to non-physical waste. In building material, waste can be described as the difference between total quantity of material brought on site and actual quantity used.
So, according to be conservative in calculating quantities the contractor QS should take in considerations materials that will be lost during construction process by multiply each material quantity to its waste factor.
Waste factors different for contractor to other according to the historical database.

## Slide 62: Tow-way Flat Plate
Waste Factors
The waste factors used in this project:

## Slide 63: Tow-way Flat Plate
Summery Quantities
Structural Elements | Material | Waste Factor | Calculated Value | Total Value
Footings | Con. B300 | 7.30% | 20.187 | 21.66
 | Con. B150 | 7.30% | 7 | 7.51
 | Wood | 25% | 1.386 | 1.73
 | Steel | 5.70% | 0.7856 | 0.83
Column Necks | Con. B300 | 7.30% | 2.127 | 2.28
 | Wood | 25% | 0.8055 | 1.01
 | Steel | 5.70% | 0.552888889 | 0.58
Tie Beams | Con. B300 | 7.30% | 13.1 | 14.06
 | Con. B150 | 7.30% | 3.93 | 4.22
 | Wood | 25% | 3.93 | 4.91
 | Steel | 5.70% | 1.215950617 | 1.29
Ground Slab | Con. B300 | 7.30% | 18.25 | 19.58
 | Wood | 25% | 0.1625 | 0.20
 | Steel | 5.70% | 0.663308642 | 0.70

## Slide 64: Tow-way Flat Plate
Summery Quantities
Structural Elements | Material | Waste Factor | Calculated Value | Total Value
columns (0.78 - 4.16 ) | Con. B300 | 7.30% | 6.3544 | 6.82
 | Wood | 25% | 2.4702 | 3.09
 | Steel | 5.70% | 1.114246914 | 1.18
columns ( 4.16-7.54) | Con. B300 | 7.30% | 6.3544 | 6.82
 | Wood | 25% | 2.4702 | 3.09
 | Steel | 5.70% | 1.114246914 | 1.18
columns (7.54-9.97) | Con. B300 | 7.30% | 0.729 | 0.78
 | Wood | 25% | 0.30245 | 0.38
 | Steel | 5.70% | 0.113160494 | 0.12
Floors Slab | Con. B300 | 7.30% | 75.86 | 81.40
 | Wood | 25% | 16.555 | 20.69
 | Steel | 5.70% | 6.596622222 | 6.97
Frames | Steel | 5.70% | 2.308696296 | 2.44

## Slide 65: Tow-way Flat Plate
Summery Quantities
Structural Elements | Material | Waste Factor | Calculated Value | Total Value
Stairs | Con. B300 | 7.30% | 6.354067943 | 6.82
 | Wood | 25% | 1.577140874 | 1.97
 | Steel | 5.70% | 0.439290464 | 0.46
Sloping Screed | Con. B150 | 7.30% | 5.046 | 5.41
plastering Floors | mortar | 13% | 1427.4 | 1612.96
painting Floors (Ceiling) | - | 10% | 304.5 | 334.95
Walls |  | 10% | 1124.545455 | 1237.00
Tiles | Ground | 6% | 274.02 | 290.46
 | Wall | 6% | 194.68 | 206.36
 | Skriting | 6% | 17.92 | 19.00
 | mortar | 13% | 456.64 | 516.00
 | Filling |  | 340 | 

## Slide 66: Tow-way Flat Plate
Summery Quantities
Structural Elements | Material | Waste Factor | Calculated Value | Total Value
Wall Partitions | External (20) | 5.60% | 4712 | 4975.87
 | Internal (20) | 5.60% | 346 | 365.38
 | Internal (10) | 5.60% | 2696 | 2846.98
 | mortar | 13% | 5.1784 | 5.85
Concrete over Parapet | Con. B300 | 7% | 0.52 | 0.56
Beams | Con. B300 | 7% | 6.26 | 6.72
 | Wood | 25% | 1.83 | 2.29
 | Steel | 6% | 0.615111111 | 0.65
Natural Stone | Stone | 5.70% | 655.86 | 693.24
Concrete Between Stone and Block | Con. B300 | 7% | 17.4896 | 18.77

## Slide 67: Tow-way Flat Plate
Summery Costs
Name | Cost | Unit Cost | Unit
Excavation for Footing | 4442.8 | 13.48 | $/CM
Footing | 3697.45 | 170.7 | $/CM
Column Neck | 989.22 | 433.87 | $/CM
Tie Beams | 3583.27 | 254.86 | $/CM
Ground Slab | 2420.1 | 123.6 | $/CM
Columns | 5248.16 | 363.95 | $/CM
Floors Slab | 18680.43 | 49.25 | $/SM
Frames | 2035.2 | 834.1 | $/Ton
Stairs | 1137.61 | 166.8 | $/CM
Sloping Screed | 465.64 | 86.07 | $/CM
Plastering Floors | 9677.78 | 6 | $/SM
Painting Floors | 4808.71 | 3.06 | $/SM

## Slide 68: Tow-way Flat Plate
Summery Costs
Name | Cost | Unit Cost | Unit
Tiles | 12310.86 | 23.87 | $/SM
Blocks | 10054.07 | 88.97 | $/Box
Stone | 38599.8 | 55.68 | $/SM
Beam | 2581.18 | 384.1 | $/CM
Doors | 5322.36 | 134.17 | $/SM
Windows | 5441.6 | 80 | $/SM
Staircase Rail | 606.8 | 40 | $/SM
Staircase Tile | 1021.44 | 38 | $/SM
Window stone | 2057.6 | 40 | $/SM
Granite Stone | 800 | 100 | $/SM
Total Direct Cost | 135982.07 |  | 

## Slide 69: Tow-way Flat Plate
BOQ
Assumptions:
%JO = 10%
%OO = 3%
%P = 5%
Bill of Quantity |  |  |  |  |  | 
Item | Description | Quantity |  | Unit Price |  | Total Price $
 |  | Value | Unit | Value | Unit | 
1 | Excavation for Footing | 329.70 | CM | 16.04 | $/CM | 5288.78
2 | Footing | 21.66 | CM | 203.13 | $/CM | 4399.86
3 | Column Neck | 2.28 | CM | 516.31 | $/CM | 1177.18
4 | Tie Beams | 14.06 | CM | 303.28 | $/CM | 4264.16
5 | Ground Slab | 19.58 | CM | 147.08 | $/CM | 2879.90
6 | Columns | 14.42 | CM | 433.10 | $/CM | 6245.31
7 | Floors Slab | 379.30 | SM | 58.61 | $/SM | 22229.82
8 | Frames | 2.44 | Ton | 992.58 | $/Ton | 2421.89
9 | Stairs | 6.82 | CM | 198.49 | $/CM | 1353.72
10 | Sloping Screed | 5.41 | CM | 102.42 | $/CM | 554.11
11 | Plastering Floors | 1612.96 | SM | 7.14 | $/SM | 11516.53

## Slide 70: Tow-way Flat Plate
BOQ
Bill of Quantity |  |  |  |  |  | 
Item | Description | Quantity |  | Unit Price |  | Total Price $
 |  | Value | Unit | Value | Unit | 
12 | Paintening Floors | 1571.95 | SM | 3.64 | $/SM | 5724.10
13 | Tiles | 515.82 | SM | 28.41 | $/SM | 14652.02
14 | Blocks | 113.00 | Box | 105.87 | $/Box | 11963.80
15 | Stone | 693.24 | SM | 66.26 | $/SM | 45933.53
16 | Beam | 6.72 | CM | 457.08 | $/CM | 3071.57
17 | Doors | 41.75 | SM | 159.66 | $/SM | 6665.90
18 | Windows | 68.02 | SM | 95.20 | $/SM | 6475.50
19 | Staircase rail | 15.17 | SM | 47.60 | $/SM | 722.09
20 | Staircase Tile | 26.88 | SM | 45.22 | $/SM | 1215.51
21 | Window Stone | 51.44 | SM | 47.60 | $/SM | 2448.54
22 | Granite Stone | 8.00 | SM | 119.00 | $/SM | 952.00
Total Bid Price |  |  |  |  |  | 162155.82

## Slide 71: Two-way Solid Slab
Summery Quantities
Structural Elements | Material | Waste Factor | Calculated Value | Total Value
Footings | Con. B300 | 7.30% | 19.714 | 21.15
 | Con. B150 | 7.30% | 6.901 | 7.40
 | Wood | 25% | 1.376 | 1.72
 | Steel | 5.70% | 0.7824 | 0.83
Column Necks | Con. B300 | 7.30% | 1.933 | 2.07
 | Wood | 25% | 0.759 | 0.95
 | Steel | 5.70% | 0.483377778 | 0.51
Tie Beams | Con. B300 | 7.30% | 13.1 | 14.06
 | Con. B150 | 7.30% | 3.93 | 4.22
 | Wood | 25% | 3.93 | 4.91
 | Steel | 5.70% | 1.215950617 | 1.29
Ground Slab | Con. B300 | 7.30% | 18.25 | 19.58
 | Wood | 25% | 0.1625 | 0.20
 | Steel | 5.70% | 0.663308642 | 0.70

## Slide 72: Two-way Solid Slab
Summery Quantities
Structural Elements | Material | Waste Factor | Calculated Value | Total Value
columns (0.78 - 4.16 ) | Con. B300 | 7.30% | 5.746 | 6.17
 | Wood | 25% | 2.3091 | 2.89
 | Steel | 5.70% | 0.976022222 | 1.03
columns ( 4.16-7.54) | Con. B300 | 7.30% | 5.746 | 6.17
 | Wood | 25% | 2.3091 | 2.89
 | Steel | 5.70% | 0.976022222 | 1.03
columns (7.54-9.97) | Con. B300 | 7.30% | 0.729 | 0.78
 | Wood | 25% | 0.30245 | 0.38
 | Steel | 5.70% | 0.113160494 | 0.12
Floors Slab | Con. B300 | 7.30% | 56.895 | 61.05
 | Wood | 25% | 16.555 | 20.69
 | Steel | 5.70% | 5.873422222 | 6.21

## Slide 73: Two-way Solid Slab
Summery Quantities
Structural Elements | Material | Waste Factor | Calculated Value | Total Value
Stairs | Con. B300 | 7.30% | 6.354067943 | 6.82
 | Wood | 25% | 1.577140874 | 1.97
 | Steel | 5.70% | 0.439290464 | 0.46
Sloping Screed | Con. B150 | 7.30% | 5.046 | 5.41
plastering Floors | mortar | 13% | 1427.4 | 1612.96
painting Floors (Ceiling) | - | 10% | 304.5 | 334.95
Walls |  | 10% | 1124.545455 | 1237.00
Tiles | Ground | 6% | 274.02 | 290.46
 | Wall | 6% | 194.68 | 206.36
 | Skriting | 6% | 17.92 | 19.00
 | mortar | 13% | 456.64 | 516.00
 | Filling |  | 340 | 
Stairs | Con. B300 | 7.30% | 6.354067943 | 6.82

## Slide 74: Two-way Solid Slab
Summery Quantities
Structural Elements | Material | Waste Factor | Calculated Value | Total Value
Frames (Drop) | B300 | 7.30% | 13.1 | 14.06
 | Wood | 25.00% | 2.91 | 3.64
 | Steel | 5.70% | 3.436641975 | 3.63
Wall Partitions | External (20) | 5.60% | 4712 | 4975.87
 | Internal (20) | 5.60% | 346 | 365.38
 | Internal (10) | 5.60% | 2696 | 2846.98
 | mortar | 13% | 5.1784 | 5.85
Concrete over Parapet | Con. B300 | 7% | 0.52 | 0.56
Beams | Con. B300 | 7% | 6.26 | 6.72
 | Wood | 25% | 1.83 | 2.29
 | Steel | 6% | 0.615111111 | 0.65
Natural Stone | Stone | 5.70% | 655.86 | 693.24
Concrete Between Stone and Block | Con. B300 | 7% | 17.4896 | 18.77

## Slide 75: Two-way Solid Slab
Summery Costs
Name | Cost | Unit Cost | Unit
Name | Cost | Unit Cost | Unit
Excavation for Footing | 4384.11 | 13.42 | $/CM
Footing | 3632.040951 | 171.7 | $/CM
Column Neck | 884.5349805 | 426.47 | $/CM
Tie Beams | 3583.27 | 254.86 | $/CM
Ground Slab | 2420.1 | 123.6 | $/CM
Columns | 4729.495643 | 360.67 | $/CM
Floors Slab | 27231.24669 | 71.79 | $/SM
Frames | 4235.759407 | 1232.53 | $/Ton
Stairs | 1137.61 | 166.8 | $/CM
Sloping Screed | 465.64 | 86.07 | $/CM
Plastering Floors | 9677.78 | 6 | $/SM

## Slide 76: Two-way Solid Slab
Summery Costs
Name | Cost | Unit Cost | Unit
Tiles | 12310.86 | 23.87 | $/SM
Blocks | 10054.07 | 88.97 | $/Box
Stone | 38599.8 | 55.68 | $/SM
Beam | 2581.18 | 384.1 | $/CM
Doors | 5322.36 | 134.17 | $/SM
Windows | 5441.6 | 80 | $/SM
Staircase rail | 606.8 | 40 | $/SM
Staircase Tile | 1021.44 | 38 | $/SM
Window Stone | 2057.6 | 40 | $/SM
Granite Stone | 800 | 100 | $/SM
Total Direct Cost | 145986.0077 |  | 

## Slide 77: Two-way Solid Slab
BOQ
Bill of Quantity |  |  |  |  |  | 
Item | Description | Quantity |  | Unit Price |  | Total Price $
 |  | Value | Unit | Value | Unit | 
1 | Excavation for Footing | 326.63 | CM | 15.97 | $/CM | 5216.26
2 | Footing | 21.15 | CM | 204.32 | $/CM | 4322.07
3 | Column Neck | 2.07 | CM | 507.50 | $/CM | 1052.61
4 | Tie Beams | 14.06 | CM | 303.28 | $/CM | 4264.16
5 | Ground Slab | 19.58 | CM | 147.08 | $/CM | 2879.90
6 | Columns | 13.11 | CM | 429.20 | $/CM | 5628.12
7 | Floors Slab | 379.30 | SM | 85.43 | $/SM | 32403.64
8 | Frames | 3.44 | Ton | 1466.71 | $/Ton | 5040.56
9 | Stairs | 6.82 | CM | 198.49 | $/CM | 1353.72
10 | Sloping Screed | 5.41 | CM | 102.42 | $/CM | 554.11
11 | Plastering Floors | 1612.96 | SM | 7.14 | $/SM | 11516.53

## Slide 78: Two-way Solid Slab
BOQ
Bill of Quantity |  |  |  |  |  | 
Item | Description | Quantity |  | Unit Price |  | Total Price $
 |  | Value | Unit | Value | Unit | 
12 | Painting Floors | 1571.95 | SM | 3.64 | $/SM | 5724.10
13 | Tiles | 515.82 | SM | 28.41 | $/SM | 14652.02
14 | Blocks | 113.00 | Box | 105.87 | $/Box | 11963.80
15 | Stone | 693.24 | SM | 66.26 | $/SM | 45933.53
16 | Beam | 6.72 | CM | 457.08 | $/CM | 3071.57
17 | Doors | 41.75 | SM | 159.66 | $/SM | 6665.90
18 | Windows | 68.02 | SM | 95.20 | $/SM | 6475.50
19 | Staircase rail | 15.17 | SM | 47.60 | $/SM | 722.09
20 | Staircase Tile | 26.88 | SM | 45.22 | $/SM | 1215.51
21 | Window Stone | 51.44 | SM | 47.60 | $/SM | 2448.54
22 | Granite Stone | 8.00 | SM | 119.00 | $/SM | 952.00
Total Bid Price |  |  |  |  |  | 174056.25

## Slide 79: Two-way Ribbed Slab (Waffle)
Summery Quantities
Structural Elements | Material | Waste Factor | Calculated Value | Total Value
Footings | Con. B300 | 7.30% | 16.8705 | 18.10
 | Con. B150 | 7.30% | 6.151 | 6.60
 | Wood | 25% | 1.221 | 1.53
 | Steel | 5.70% | 0.7096 | 0.75
Column Necks | Con. B300 | 7.30% | 1.916 | 2.06
 | Wood | 25% | 0.79075 | 0.99
 | Steel | 5.70% | 0.40 | 0.42
Tie Beams | Con. B300 | 7.30% | 13.1 | 14.06
 | Con. B150 | 7.30% | 3.93 | 4.22
 | Wood | 25% | 3.93 | 4.91
 | Steel | 5.70% | 1.215950617 | 1.29
Ground Slab | Con. B300 | 7.30% | 18.25 | 19.58
 | Wood | 25% | 0.1625 | 0.20
 | Steel | 5.70% | 0.663308642 | 0.70

## Slide 80: Two-way Ribbed Slab (Waffle)
Summery Quantities
Structural Elements | Material | Waste Factor | Calculated Value | Total Value
columns (0.78 - 4.16) | Con. B300 | 7.30% | 5.6446 | 6.06
 | Wood | 25% | 2.2477 | 2.81
 | Steel | 5.70% | 1.036748148 | 1.10
columns (4.16-7.54) | Con. B300 | 7.30% | 5.6446 | 6.06
 | Wood | 25% | 2.2477 | 2.81
 | Steel | 5.70% | 0.981190123 | 1.04
columns (7.54-9.97) | Con. B300 | 7.30% | 0.6318 | 0.68
 | Wood | 25% | 0.2673 | 0.33
 | Steel | 5.70% | 0.104439506 | 0.11
Floors Slab | Con. B300 | 7.30% | 65.7854 | 70.59
 | Wood | 25% | 16.555 | 20.69
 | Steel | 5.70% | 6.744 | 7.13
 | Blocks | 5.00% | 2129.75 | 2236.24
Frames | Steel | 5.70% | 4.461520988 | 4.72

## Slide 81: Two-way Ribbed Slab (Waffle)
Summery Quantities
Structural Elements | Material | Waste Factor | Calculated Value | Total Value
Stairs | Con. B300 | 7.30% | 6.354067943 | 6.82
 | Wood | 25% | 1.577140874 | 1.97
 | Steel | 5.70% | 0.439290464 | 0.46
Sloping Screed | Con. B150 | 7.30% | 5.046 | 5.41
plastering Floors | mortar | 13% | 1427.4 | 1612.96
painting Floors (Ceiling) | - | 10% | 304.5 | 334.95
Walls |  | 10% | 1124.545455 | 1237.00
Tiles | Ground | 6% | 274.02 | 290.46
 | Wall | 6% | 194.68 | 206.36
 | Skriting | 6% | 17.92 | 19.00
 | mortar | 13% | 456.64 | 516.00
 | Filling |  | 340 | 

## Slide 82: Two-way Ribbed Slab (Waffle)
Summery Quantities
Structural Elements | Material | Waste Factor | Calculated Value | Total Value
Wall Partitions | External (20) | 5.60% | 4712 | 4975.87
 | Internal (20) | 5.60% | 346 | 365.38
 | Internal (10) | 5.60% | 2696 | 2846.98
 | mortar | 13% | 5.1784 | 5.85
Concrete over Parapet | Con. B300 | 7% | 0.52 | 0.56
Beams | Con. B300 | 7% | 6.26 | 6.72
 | Wood | 25% | 1.83 | 2.29
 | Steel | 6% | 0.615111111 | 0.65
Natural Stone | Stone | 5.70% | 655.86 | 693.24
Concrete Between Stone and Block | Con. B300 | 7% | 17.4896 | 18.77

## Slide 83: Two-way Ribbed Slab (Waffle)
Summery Costs
Name | Cost | Unit Cost | Unit
Excavation for Footing | 4192.897514 | 13.91 | $/CM
Footing | 3169.391633 | 175.0847139 | $/CM
Column Neck | 810.0514413 | 394.0191886 | $/CM
Tie Beams | 3587.78 | 255.18 | $/CM
Ground Slab | 2418.74 | 123.53 | $/CM
Columns | 4705.235948 | 367.848506 | $/CM
Floors Slab | 22857.96312 | 60.26354631 | $/SM
Frames | 3933.000288 | 834 | $/Ton
Stairs | 1137.61 | 166.8 | $/CM
Sloping Screed | 465.64 | 86.07 | $/CM
Plastering Floors | 9677.78 | 6 | $/SM

## Slide 84: Two-way Ribbed Slab (Waffle)
Summery Costs
Name | Cost | Unit Cost | Unit
Tiles | 12310.86 | 23.87 | $/SM
Blocks | 10054.07 | 88.97 | $/Box
Stone | 38599.8 | 55.68 | $/SM
Beam | 2581.18 | 384.1 | $/CM
Doors | 5322.36 | 134.17 | $/SM
Windows | 5441.6 | 80 | $/SM
Staircase rail | 606.8 | 40 | $/SM
Staircase Tile | 1021.44 | 38 | $/SM
Window Stone | 2057.6 | 40 | $/SM
Granite Stone | 800 | 100 | $/SM
Total Direct Cost | 140560.51 |  | 

## Slide 85: Two-way Ribbed Slab (Waffle)
BOQ
Bill of Quantity |  |  |  |  |  | 
Item | Description | Quantity |  | Unit Price |  | Total Price $
 |  | Value | Unit | Value | Unit | 
1 | Excavation for Footing | 301.48 | CM | 16.55 | $/CM | 4989.55
2 | Footing | 18.10 | CM | 208.35 | $/CM | 3771.58
3 | Column Neck | 2.06 | CM | 468.88 | $/CM | 963.96
4 | Tie Beams | 14.06 | CM | 303.66 | $/CM | 4268.40
5 | Ground Slab | 19.58 | CM | 147.08 | $/CM | 2879.90
6 | Columns | 12.79 | CM | 437.74 | $/CM | 5599.23
7 | Floors Slab | 379.30 | SM | 71.71 | $/SM | 27200.98
8 | Frames | 4.72 | Ton | 992.46 | $/Ton | 4680.27
9 | Stairs | 6.82 | CM | 198.49 | $/CM | 1353.72
10 | Sloping Screed | 5.41 | CM | 102.42 | $/CM | 554.11
11 | Plastering Floors | 1612.96 | SM | 7.14 | $/SM | 11516.53

## Slide 86: Two-way Ribbed Slab (Waffle)
BOQ
Bill of Quantity |  |  |  |  |  | 
Item | Description | Quantity |  | Unit Price |  | Total Price $
 |  | Value | Unit | Value | Unit | 
12 | Painting Floors | 1571.95 | SM | 3.64 | $/SM | 5724.10
13 | Tiles | 515.82 | SM | 28.41 | $/SM | 14652.02
14 | Blocks | 113.00 | Box | 105.87 | $/Box | 11963.80
15 | Stone | 693.24 | SM | 66.26 | $/SM | 45933.53
16 | Beam | 6.72 | CM | 457.08 | $/CM | 3071.57
17 | Doors | 41.75 | SM | 159.66 | $/SM | 6665.90
18 | Windows | 68.02 | SM | 95.20 | $/SM | 6475.50
19 | Staircase rail | 15.17 | SM | 47.60 | $/SM | 722.09
20 | Staircase Tile | 26.88 | SM | 45.22 | $/SM | 1215.51
21 | Window Stone | 51.44 | SM | 47.60 | $/SM | 2448.54
22 | Granite Stone | 8.00 | SM | 119.00 | $/SM | 952.00
Total Bid Price |  |  |  |  |  | 167602.79

## Slide 87: One-way Ribbed Slab
Summery Quantities
Structural Elements | Material | Waste Factor | Calculated Value | Total Value
Footings | Con. B300 | 7.30% | 18.67 | 20.04
 | Con. B150 | 7.30% | 6.538 | 7.02
 | Wood | 25% | 1.334 | 1.67
 | Steel | 5.70% | 0.762 | 0.81
Column Necks | Con. B300 | 7.30% | 1.962 | 2.11
 | Wood | 25% | 0.76425 | 0.96
 | Steel | 5.70% | 0.528 | 0.56
Tie Beams | Con. B300 | 7.30% | 13.1 | 14.06
 | Con. B150 | 7.30% | 3.93 | 4.22
 | Wood | 25% | 3.93 | 4.91
 | Steel | 5.70% | 1.215950617 | 1.29
Ground Slab | Con. B300 | 7.30% | 18.25 | 19.58
 | Wood | 25% | 0.1625 | 0.20
 | Steel | 5.70% | 0.663308642 | 0.70

## Slide 88: One-way Ribbed Slab
Summery Quantities
Structural Elements | Material | Waste Factor | Calculated Value | Total Value
columns (0.78 - 4.16 ) | Con. B300 | 7.30% | 5.8474 | 6.27
 | Wood | 25% | 2.336 | 2.92
 | Steel | 5.70% | 0.9936 | 1.05
columns ( 4.16-7.54) | Con. B300 | 7.30% | 5.8474 | 6.27
 | Wood | 25% | 2.336 | 2.92
 | Steel | 5.70% | 0.9936 | 1.05
columns (7.54-9.97) | Con. B300 | 7.30% | 0.7047 | 0.76
 | Wood | 25% | 0.289875 | 0.36
 | Steel | 5.70% | 0.116 | 0.12
Floors Slab | Con. B300 | 7.30% | 79 | 84.77
 | Wood | 25% | 16.555 | 20.69
 | Steel | 5.70% | 6.078410746 | 6.42
 | Blocks | 5.00% | 1832 | 1923.60
Frames | Steel | 5.70% | 4.7577 | 5.03

## Slide 89: One-way Ribbed Slab
Summery Quantities
Structural Elements | Material | Waste Factor | Calculated Value | Total Value
Stairs | Con. B300 | 7.30% | 6.354067943 | 6.82
 | Wood | 25% | 1.577140874 | 1.97
 | Steel | 5.70% | 0.439290464 | 0.46
Sloping Screed | Con. B150 | 7.30% | 5.046 | 5.41
plastering Floors | mortar | 13% | 1427.4 | 1612.96
painting Floors (Ceiling) | - | 10% | 304.5 | 334.95
Walls |  | 10% | 1124.545455 | 1237.00
Tiles | Ground | 6% | 274.02 | 290.46
 | Wall | 6% | 194.68 | 206.36
 | Skriting | 6% | 17.92 | 19.00
 | mortar | 13% | 456.64 | 516.00
 | Filling |  | 340 | 

## Slide 90: One-way Ribbed Slab
Summery Quantities
Structural Elements | Material | Waste Factor | Calculated Value | Total Value
Wall Partitions | External (20) | 5.60% | 4712 | 4975.87
 | Internal (20) | 5.60% | 346 | 365.38
 | Internal (10) | 5.60% | 2696 | 2846.98
 | mortar | 13% | 5.1784 | 5.85
Concrete over Parapet | Con. B300 | 7% | 0.52 | 0.56
Beams | Con. B300 | 7% | 6.26 | 6.72
 | Wood | 25% | 1.83 | 2.29
 | Steel | 6% | 0.615111111 | 0.65
Natural Stone | Stone | 5.70% | 655.86 | 693.24
Concrete Between Stone and Block | Con. B300 | 7% | 17.4896 | 18.77

## Slide 91: One-way Ribbed Slab
Summery Costs
Name | Cost | Unit Cost | Unit
Excavation for Footing | 4311.3 | 13.7 | $/CM
Footing | 3461.665298 | 172.76 | $/CM
Column Neck | 930.4206102 | 441.96 | $/CM
Tie Beams | 3583.27 | 254.86 | $/CM
Ground Slab | 2420.1 | 123.6 | $/CM
Columns | 4802.830968 | 360.99 | $/CM
Floors Slab | 22779.01305 | 60.06 | $/SM
Frames | 4194.106185 | 834 | $/Ton
Stairs | 1137.61 | 166.8 | $/CM
Sloping Screed | 465.64 | 86.07 | $/CM
Plastering Floors | 9677.78 | 6 | $/SM
Painting Floors | 4808.71 | 3.06 | $/SM

## Slide 92: One-way Ribbed Slab
Summery Costs
Name | Cost | Unit Cost | Unit
Tiles | 12310.86 | 23.87 | $/SM
Blocks | 10054.07 | 88.97 | $/Box
Stone | 38599.8 | 55.68 | $/SM
Beam | 2581.18 | 384.1 | $/CM
Doors | 5322.36 | 134.17 | $/SM
Windows | 5441.6 | 80 | $/SM
Staircase rail | 606.8 | 40 | $/SM
Staircase Tile | 1021.44 | 38 | $/SM
Window Stone | 2057.6 | 40 | $/SM
Granite Stone | 800 | 100 | $/SM
Total Direct Cost | 141368.1561 |  | 

## Slide 93: One-way Ribbed Slab
BOQ
Bill of Quantity |  |  |  |  |  | 
Item | Description | Quantity |  | Unit Price |  | Total Price $
 |  | Value | Unit | Value | Unit | 
1 | Excavation for Footing | 314.70 | CM | 16.30 | $/CM | 5130.45
2 | Footing | 20.04 | CM | 205.58 | $/CM | 4119.39
3 | Column Neck | 2.11 | CM | 525.93 | $/CM | 1107.21
4 | Tie Beams | 14.06 | CM | 303.28 | $/CM | 4264.16
5 | Ground Slab | 19.58 | CM | 147.08 | $/CM | 2879.90
6 | Columns | 13.30 | CM | 429.58 | $/CM | 5715.39
7 | Floors Slab | 379.30 | SM | 71.47 | $/SM | 27109.10
8 | Frames | 5.03 | Ton | 992.46 | $/Ton | 4990.99
9 | Stairs | 6.82 | CM | 198.49 | $/CM | 1353.72
10 | Slooping Screed | 5.41 | CM | 102.42 | $/CM | 554.11
11 | Plastering Floors | 1612.96 | SM | 7.14 | $/SM | 11516.53

## Slide 94: One-way Ribbed Slab
BOQ
Bill of Quantity |  |  |  |  |  | 
Item | Description | Quantity |  | Unit Price |  | Total Price $
 |  | Value | Unit | Value | Unit | 
12 | Paintening Floors | 1571.95 | SM | 3.64 | $/SM | 5724.10
13 | Tiles | 515.82 | SM | 28.41 | $/SM | 14652.02
14 | Blocks | 113.00 | Box | 105.87 | $/Box | 11963.80
15 | Stone | 693.24 | SM | 66.26 | $/SM | 45933.53
16 | Beam | 6.72 | CM | 457.08 | $/CM | 3071.57
17 | Doors | 41.75 | SM | 159.66 | $/SM | 6665.90
18 | Windows | 68.02 | SM | 95.20 | $/SM | 6475.50
19 | Staircase rail | 15.17 | SM | 47.60 | $/SM | 722.09
20 | Staircase Tile | 26.88 | SM | 45.22 | $/SM | 1215.51
21 | Window Stone | 51.44 | SM | 47.60 | $/SM | 2448.54
22 | Granite Stone | 8.00 | SM | 119.00 | $/SM | 952.00
Total Bid Price |  |  |  |  |  | 168565.52

## Slide 95: Conclusion
We will do comparison between all slab systems in Quantities and costs.
Quantities Comparison
Footings
Footings |  |  |  | 
Item description | Solid Sab system | Flat Plate system | Two-way Ribbed Slab system (Waffle) | One-way Ribbed slab system
Volume of Excavation (m3) | 326.63 | 329.70 | 301.48 | 314.70
Total Concrete Volume (m3) | 28.56 | 29.17 | 24.70 | 27.05
Volume of framework (m3) | 1.72 | 1.73 | 1.53 | 1.67
Reinforcing (tones) | 0.83 | 0.83 | 0.75 | 0.81
Flat Plat System have the largest quantities of concrete and steel with small differences.

## Slide 96: Conclusion
Quantities Comparison
Column Necks
Column Neck |  |  |  | 
Item description | Solid Sab system | Flat Plate system | Two-way Ribbed Slab system (Waffle) | One-way Ribbed slab system
Total Concrete Volume (m3) | 2.07 | 2.28 | 2.06 | 2.11
Volume of framework (m3) | 0.95 | 1.01 | 0.99 | 0.96
Reinforcing (tones) | 0.51 | 0.58 | 0.42 | 0.56
Flat Plat System have the largest quantities of concrete and steel with small differences.

## Slide 97: Conclusion
Quantities Comparison
Columns
Column |  |  |  | 
Item description | Solid Sab system | Flat Plate system | Two-way Ribbed Slab system (Waffle) | One-way Ribbed slab system
Total Concrete Volume (m3) | 13.11 | 14.42 | 12.79 | 13.30
Volume of framework (m3) | 6.15 | 6.55 | 5.95 | 6.20
Reinforcing (tones) | 2.18 | 2.48 | 2.24 | 2.22
Flat Plat System have the largest quantities of concrete and steel with small differences.

## Slide 98: Conclusion
Quantities Comparison
Floor Slabs
One-way Ribbed slab system has the largest quantity of concrete. On the other hand Two – Way Ribbed system has the largest quantity of steel.
Floor Slabs |  |  |  | 
Item description | Solid Sab system | Flat Plate system | Two-way Ribbed Slab system (Waffle) | One-way Ribbed slab system
Total Concrete Volume (m3) | 61.05 | 81.40 | 70.59 | 84.77
Volume of framework (m3) | 20.69 | 20.69 | 20.69 | 20.69
Reinforcing (tones) | 6.21 | 6.97 | 7.13 | 6.42
No. of Blocks | 0 | 0 | 2236.24 | 1923.60

## Slide 99: Conclusion
Quantities Comparison
Frames
Flat Plate system has the smallest quantities of steel and concrete in frames (Drop).
Frames |  |  |  | 
Item description | Solid Sab system | Flat Plate system | Two-way Ribbed Slab system (Waffle) | One-way Ribbed slab system
Total Concrete Volume (m3) | 14.06 | 0.00 | 0.00 | 0.00
Volume of framework (m3) | 3.64 | 0.00 | 0.00 | 0.00
Reinforcing (tones) | 3.63 | 2.44 | 4.72 | 5.03

## Slide 100: Conclusion
Price Comparison
We decide to compare between them according to 1 m2 of slab since area of slab is constant for all
The nonstructural elements will be eliminated because they are the same for all systems, so we will calculate the price for each structural element per 1 m2 of slab and finally the total price per 1 m2 for each system:
For nonstructural elements, Total Price per 1 m2 = 298.56 $

## Slide 101: Conclusion
Slab Systems |  |  |  | 
Item Discription | Solid Slab system | Flat Plate system | Two-way Ribbed Slab system(Waffle) | One-way Ribbed slab system
Labor cost ($) | 41651 | 38396 | 41571 | 40303
Material cost ($) | 99952 | 93143.00 | 94797 | 96754
Equipment Cost ($) | 4384 | 4443.00 | 4193 | 4312
Total Direct Cost ($) | 145987 | 135982.00 | 140561 | 141369
% Labor | 28.53 | 28.24 | 29.58 | 28.51
% Equipment | 3 | 3.27 | 2.98 | 3.05
% Material | 68.47 | 68.49 | 67.44 | 68.44

## Slide 102: Conclusion
Price Comparison
Slab Systems |  |  |  | 
Item Description | Solid Sab system | Flat Plate system | Two-way Ribbed Slab system (Waffle) | One-way Ribbed slab system
Excavation for footings | 13.75 | 13.94 | 13.15 | 13.53
Footings | 11.39 | 11.60 | 9.94 | 10.86
Column Neck | 2.78 | 3.10 | 2.54 | 2.92
Tie Beams | 11.24 | 11.24 | 11.25 | 11.24
Ground Slab | 7.59 | 7.59 | 7.59 | 7.59
Columns | 14.84 | 16.47 | 14.76 | 15.07
Floors Slab | 85.43 | 58.61 | 71.71 | 71.47
Frames | 13.29 | 6.39 | 12.34 | 13.16
Total Price From Structural elements ($/m2) | 160.31 | 128.94 | 143.28 | 145.84
Total Price ($/m2) | 458.87 | 427.5 | 441.84 | 444.4
After of all, we can notice that the least total price system is Flat Plate Slab with Total Price = 162450 $

## Slide 103: The end
Thank You