## Slide 1: Graduation Project I Analysis and Redesign of Water Distribution Network and Design of WasteWater Collection network for Asira AL-Shamaliyah Village By: Ayman Bdair Karam Sawalha Mohammad Odaily Under supervision of Dr. Anan Jayousi

## Slide 2: Outline
Project objectives
Study area
Questionnaire Analysis
Data collection and calculation
Results of the current water network
Future water consumption and demand needed
Redesign the water network
Design of wastewater collection network

## Slide 3: Project objectives
Analyze the existing water distribution network in Asira AL-Shamaliyah Village.
Redesign the water network for the future demand.
Design the wastewater collection network for Asira AL-Shamaliyah Village
Determine the cost of constructing these networks.

## Slide 4: Methodology

## Slide 5: Study area Asira AL-Shamaliyah Village
It is located to the north of the city of Nablus, at by some distance 7 kilometers away, and had an average height of (648 meters) above sea level.
It has an area of 29,033 denims and a population of about 9960 capita in 2017.

## Slide 6: Study aria AL-Shamaliyah Village
The lowest temperature reaches at average of 10.2 degrees in the month of January , the highest temperature reaches at average of 26.8 degrees in the month of August.
Average relative humidity in the year is 60.5
Average annual rainfall at 588.9 mm
Average speed of wind amounted to 5 kilometers per hour.
Asira ash Shamaliya is provided with water by Nablus Municipality through the public water network.

## Slide 7: Questionnaire Analysis
The purpose of questionnaire:
Study the existing situation.
Knowledge the consumption of water bar month for each family.
Knowledge of the services provided to citizens.
Knowledge of the health, environment and social status in the village.
An important sources of information that can be used during the study.
The main component of the questioner is family size ,
consumption per family in cubic meter ,
water resources that the family use,
and common problems in the network.
35 questioners were been distribute. The distribution of the questioner were been unbiased and random.

## Slide 8: Questionnaire analysis
Average family size = 6.1 capita
water consumption =78.22 L/C/day

## Slide 9: Questionnaire analysis
Consumption (L/C. d) vs Family size
when the number of family member’s increases, the consumption of water will decrease. So that, the demand on water will decrease.

## Slide 10: Questionnaire analysis
Consumption(L/c/day) vs house area.
when the area of house increases. Then, the consumption of water for capita will increase.

## Slide 11: Questionnaire analysis
the Consumption (L/C/d) vs Income of family
when the income of family increase, the consumption of water will increase

## Slide 12: Questionnaire analysis

## Slide 13: Questionnaire analysis

## Slide 14: Questionnaire analysis

## Slide 15: Questionnaire analysis

## Slide 16
Analysis and Redesign of Water Distribution Network

## Slide 17: Simulation Model (Water CAD)
WaterCAD which is the software program used for plane, design, analysis and optimize water distribution network.

## Slide 18: Data collection and calculation

## Slide 19: Data collection and calculation
Total consumption (Demand) = (9960 capita *78.22 Litter/capita/day) / (1000 litter/m³)
Total Demand = 780 m³/day.
UFD = 26%
Supply =
= = 1054 m3 /day.
Population density
(Da*A.a) + (Db*A.b) = total population
( Da*A.a) + (0.5Da*A.b) = 9960 capita

## Slide 20: Data collection and calculation

## Slide 21: Data collection and calculation
Unsteady state case for Asira

## Slide 22: Result and discussion
Pressure at 6:00 am
According to specifications the allowable pressure is within the range (20-120 ) m H2O.

## Slide 23: Result and discussion
Velocity at 6:00 am
The allowable range for velocity is (0.1-3.0)m/s, but there a many of pipes have a velocity under the range specifically

## Slide 24: Future water distribution Network
Future population
The population in 2007 is 7556 capita
proportionality constant“ k “ is 2.8% by
the future population in Asira up year 2037 can be determined by this equation:
P(t)= P0 * ekt
So the population in 2037 = 17503 capita.

## Slide 25: Future water distribution Network
Future water consumption and demand needed
From the Word Health Organization (WHO), the average municipal consumption is 120 L/C/Day.
Consumption (demand) = 120 L/C/Day * 17503 capita / 1000 = 2100.36 m3/Day
Supply = demand / 1-UFD = 2100.36 / 1-0.15 = 2471 m3/day
to estimate the future water demand for each node, the nodal resent water demand will multiply by a factor, which equa
Future demand for each node = current demand * factor
Factor = *
= *
= 2.34

## Slide 26: Future water distribution Network
Redesign the water network
replace the pipes in other diameters to dispense put a pump

## Slide 27: Result and discussion
Pressure at 6:00 am

## Slide 28: Result and discussion
Velocity at 6:00am

## Slide 29
Design of water distribution and sewer collection systems

## Slide 30: Simulation Model (sewerCAD)
This program is ideal for system design and the rehabilitation of sanitary sewers

## Slide 31: Design criteria
Cover
According to PWA standards; the minimum cover for sewer pipes is 1 m and the recommended maximum depth for pipes is approximately 5.0 m
Slope of pipe
As per PWA standards, slop of pipes shall be within the limits 1% -15%.
Flow Velocities
As per PWA standards, flow velocities shall be within the limits 0.3- 3 m/s.

## Slide 32: Data input(Sewercad)
Elevation from contour map
Water Consumption = 120 L /c.d
Wastewater generation coefficient= 0.8
For material: use PVC
Manning coefficient = 0.013
Section type = circular

## Slide 33: pattern

## Slide 34: Load calculations

## Slide 36: wet well

## Slide 37: pump definition

## Slide 38: Rebuild the model
Increase the infiltration
50%
Increase the dimeter for the main counduit

## Slide 40: Slope (sewer network)

## Slide 41: Average cover(sewer network)

## Slide 42: Velocity(sewer network)