## Slide 1: Useful Life Of Artificial Shoulder
2
+
Graduation Project 2

## Slide 2: Students: 1. Nofal Nofal 2. Mohammad Zamel 3.Montaser Salameh
2
+
2
+
Advisor: Dr. Iyad Assaf

## Slide 3: Outline
2
+
Introduction
Methodology
Force and Material
Finite Element
Result and Conclusion

## Slide 4: Introduction
2
+
What is the Shoulder Replacement ?
Shoulder replacement is a surgical procedure in which all or part of the glenohumeral joint is replaced by a prosthetic implant. Such joint replacement surgery generally is conducted to relieve arthritis pain or fix severe physical joint damage.

## Slide 5: Title
Types of Shoulder Replacement
Total Shoulder Replacement
Partial Shoulder Replacement
Shoulder Replacement Parts
Screw
Baseplate
Glenosphere
Humeral Cup
Humeral Stem

## Slide 6: Material Requirements
To use materials in a human body it must be considered these points :
Biocompatible and produce minimal rejection.
High Mechanical properties of the material in order to withstand the forces affecting the shoulder. such as (yield strength, tensile strength, fatigue strength, fracture hardness, and ductility ).
Density and cost : recommended to use lightweight components and responsible price.
Must be nonmagnetic: used medical diagnostic tool is magnetic resonance imaging ,The presence of any magnetic materials implanted in the patient will disrupt the applied magnetic field.

## Slide 7: Material Used
Component | Material
Baseplate | Titanium Alloy
Glenosphere | CoCr Mo alloy
Humeral Cup | UHMWPE
Humeral Stem | Titanium Alloy
Screws | Titanium Alloy

## Slide 8: Wear Of The Polyethylene
The wear of the polyethylene part causes instability leading to the dislocation of the artificial Shoulder, and the long-term used causes a weariness.
It is necessary to find a suitable solution for the problem of erosion of this piece of Polyethylene and increase its life span and this is the main aim of this research.
Most of the artificial shoulder has useful life range between 10 to 20 years.

## Slide 9: Methodology
1. Studying Shoulder joint in general with its parts and components.
2. After that we will discuss the Free body diagram and the relation between forces acts on the Joint to found these forces.
3. Use finite element software “Solid work” to study the stresses and deformations during different situations.
the fatigue life of the shoulder could be determined by Fatigue formulas.

## Slide 10
We choose the Solidwork program to make our simulation to create a 3D model.
so we could change the material that we choose and see the output stress and deformations so that we use it to obtain the fatigue and see how much it affect the lifetime.

## Slide 11
To do analysis, Our team used different material as shown on table below.

## Slide 12: Force analysis
The picture below illustrates the force on shoulder.

## Slide 13
And this photo show us the range of motion Flexion, Extension, Abduction, Internal and External Rotations

## Slide 14
Sample Of Calculations
F1 and F2 Is the applied force
σmin and σmax from Solidworks

## Slide 15: Finite Elements
finite element method (FEM), is a numerical method for solving problems of engineering and mathematical physics. To solve the problem, it subdivides a large problem into smaller, simpler parts that are called finite elements.

## Slide 16
Using Solidwork we made these parts
Baseplate
Glenosphere
Humeral Cup
Humeral Stem
Screw

## Slide 17
After run a detected material and run simulation

## Slide 18
At our project we focused on Polyethylene part and Voss Mass Result

## Slide 19: Result
Using the SolidWorks analysis, we have been able to design a cartilage of up to 42 years old.

## Slide 20: Conclusion
This table shows that a material that has an ultimate tensile strength of 14𝑀𝑃𝑎, it will serve for 40-50 years, and this material is not precisely defined in this project.

## Slide 21: THANK YOU
2
+
Ready for your questions